## Slide 1: Team #2 Solar Car Project
Detailed Design Review

## Slide 2: Team Member
Mechanical Engineers
Electrical Engineers
Keith Dalick
Emiliano Pantner
Adrian Cires
Shishir Rajbhandari
James Barge
Zachary Prisland

## Slide 3: Body

## Slide 4: Tensile Testing 12K Carbon
Sample | Ultimate Testing (MPa) | Tensile Modulus (GPa) | Elongation (%)
1 | 149.40 | 5.51 | 5.18
2 | 154.22 | 5.30 | 4.39
3 | 124.09 | 5.66 | 3.337
4 | 120.46 | 5.17 | 5.81

## Slide 5: Making the Carbon Fiber

## Slide 6: Suspension System

## Slide 7: Current Status
Control arms designed
Short/Long arm design
  Lower control arm
    12.5 inches wide by 12.5 inches long
  Upper control arm
    12 inches wide by 12 inches long
  Maintains position of the contact patch in a straight vertical line under bump and rebound conditions
Attached to body and upright using Heim links

## Slide 8: Control Arm
Old Design
New Design

## Slide 9: Lower Control Arm

## Slide 10: Shocks
Old Shock
New Shock (FOX Van RC)

## Slide 11: Fox Shox Vanilla R Coil Shock
2005 model
7.875 X 500 X 2.30
0.85 lbs
Externally adjustable rebound damping
Adjustable coil spring preload

## Slide 12: Test Plan
Component testing
  Hiem joint
  Control arm
  Mounting Brackets
  Upright arm
  Front Suspension
  Rear Suspension
Suspension system finite element analysis (FEA)
Suspension system virtual simulation

## Slide 13: Braking System

## Slide 14: Current Progress
Sponsored by Wilwood Engineering
Discount prices on various brake components
  Brake Calipers
  Master Cylinders

## Slide 15: Brake Caliper
Go-Kart brake caliper
Suitable for solar car’s lightweight
Features:
  Self retracting and adjusting piston
  Steel piston for reduced heat transfer

## Slide 16: Master Cylinder
Go-Kart master cylinder
Specifically designed for use with selected caliper
Features
  Adjustable lever ratio
  Lightweight aluminum cylinder

## Slide 17: Brake Rotor
Brake rotor will be custom built
  To fit new spindle
Modeled in SolidWorks
  FEA tests for heat dissipation/stress
Utilize machine shop for fabrication

## Slide 18: Power Generation System

## Slide 19: Power Generation

## Slide 20: FLEXS SOLAR CELLS : PT15-300
Voltage | 15.4 V
Current | 200 mA (0.2 A)
Voltage (oc) | 19.0 V
Current (sc) | 240 mA (0.24 A)
Thickness | 1.1 mm
Total size | 10.6 in. x 12.8 in.
Weight | 3.3 oz (94.5 g)

## Slide 21: SOLAR ARRAY – PT15

## Slide 22: Test – Solar
Test solar module for rated Voc (V) and rated Isc (I)
Test solar array for rated Voc (V) and rated Isc (I)
Solar array should be covered to measure the current

## Slide 23: MPPT
DRIVETEK RACE
AERL 600 B

## Slide 24: TEST - MPPT
Test MPPT for input and output voltage (V)
Test MPPT charges the battery bank

## Slide 25: REGENARATIVE BRAKING

## Slide 26: Control System

## Slide 27: Current Status
Power control system components have been purchased
Problems with motor controller communication
Component testing in progress

## Slide 28: Master Control Unit
Power control code is complete
Code to transmit data to motor controller is complete
User input code in progress
Code to process motor controller data in progress

## Slide 29: Dashboard

## Slide 30: Power Control

## Slide 31: Power Control

## Slide 32: Lights
Front lights controlled by rocker switch on dashboard
Brake lights controlled using a relay activated by motor controller
Electronic LED flashers used to control turn indicators

## Slide 33: Test Plan
MCU Software Simulation
Power system component testing
Dashboard component testing
Power system integration
Dashboard integration
MCU/Motor controller integration
Electrical system integration

## Slide 34: Management System

## Slide 35: Overview
Management System
Stored Energy
Propulsion
Batteries
Protection Circuit
Wall Charging
State of Charge
Motor Controller
Motor

## Slide 36: Battery Box Update
Dividing batteries into three separate boxes
Built out of fiberglass
All boxes will be placed at the front of the car
Quick disconnects for each individual box
Dimension | Size
Length | 20"
Width | 6"
Height | 8"

## Slide 37: Battery Risks
Protection Type | Restraining Value
Over Voltage | 4.25 V
Under Voltage | 2.5 V
Over Current | 120 A
Over Temperature | 75 °C
Operating in unsafe conditions
Incorrect wire gauges
Lack of proper insulation
Any incidental contact with driver

## Slide 38: State of Charge
Dashboard display
Battery fuel gauge
Shunt line current measurements
Microcontroller interface capabilities

## Slide 39: Budget & Schedule

## Slide 40: Budget
System | Cost
Body | $7,396
Suspension | $665
Braking | $840
Power Generation | $8,807
Control System | $636
Management System | $609
Grand Total | $18,953
Donations | $7,486
Net Total | $11,467
Budget Estimate after Donations: $11,467
Budget given by University: $5,000
Budget Deficit: $6,467

## Slide 41: Major Milestones
System level design review November 15, 2010
Assemble lower body December 16, 2010 (February 2, 2011)
Assemble upper body January 21, 2011
(TBA)
Detailed design review and test plan January 27, 2011
Configure lower body February 21, 2011
Install solar arrays February 23, 2011
Total body configuration March 15, 2011
Final testing March 29, 2011

## Slide 42: Questions???