## Slide 1: Air Flow Unlimited
Group 13
Joseph Cognato
Jonathan Glynn
Matthew Hartman
Ramon Villarreal

## Slide 2: Intro
Airfoil structure analysis
Airfoil force calculations and material selection
Shape evaluation for the carts
Spring selection and material choices for the carts
User interface preliminary design

## Slide 3: Air blower
Air flow rate is 310 cubic feet per minute.
Gives 40 miles per hour air flow at the exit.
2 Blowers in total run off of a 120 AC outlet.
Further evaluation will be used to get the best approximation of the air speed at specific points in the display.

## Slide 4: Airfoil Display

## Slide 5: Airfoil Display

## Slide 6: Airfoil Display

## Slide 7: Airfoil Design 1
NACA 4412

## Slide 8: Airfoil Design 2
NACA 63-010A

## Slide 9: Airfoil Design 3
NACA 2408

## Slide 10: Lift
Chart: Lift vs. Attack Angle
| 0 | 2.5 | 5 | 7.5 | 10 | 12.5 | 15 | 17.5 | 20
NACA 2408 | 0.122 | 0.256 | 0.377 | 0.489 | 0.592 | 0.669 | 0.697 | 0.662 | 0.541
NACA 4412 | 0.234 | 0.362 | 0.479 | 0.586 | 0.684 | 0.756 | 0.776 | 0.73 | 0.594

## Slide 11: Drag
Chart: Drag vs. Attack Angle
| 0 | 2.5 | 5 | 7.5 | 10 | 12.5 | 15 | 17.5 | 20
NACA 2408 | 0.014 | 0.037 | 0.071 | 0.115 | 0.169 | 0.222 | 0.26 | 0.273 | 0.254
NACA 4412 | 0.031 | 0.064 | 0.107 | 0.157 | 0.213 | 0.263 | 0.289 | 0.283 | 0.24

## Slide 12: Comparison
NACA 2408
NACA 4412
Max. lift ~0.7
Max. Drag ~0.27
Smaller surface area
Simpler shape
Max. lift ~0.78
Max. Drag ~0.3
Larger surface area
Slightly heavier

## Slide 13: Airfoil Material
Combination of materials
Hollow Center
Carbon Fiber (CFRP)
Balsa
Bamboo

## Slide 14: Carts Attachments
Two attachments spherical, and square
Drag force for a sphere with radius 2in. 0.7349 N
Drag force for a square with sides 4in in length 2.09 N
The cart only weights 226 grams so the attachments will be able to produce movement

## Slide 15: Attachment materials
light materials desired to optimize force produced
polymer clay can be used to sculpt hollow designs
Light weight and inexpensive

## Slide 16: COMSOL MultiPhysics
Based on attachments
Velocity profile
Visualization of vortices
Distribution of wake
Display of drag

## Slide 17: COMSOL MultiPhysics contd.

## Slide 18: Spring
For the max force of 2.09N this spring will provide adequate movement
usable for both circle and square carts

## Slide 19: Display Potentials
For both mechanical displays there will be an independent control and monitor.
Robust designs for both are a must.
Potentiometers instead of buttons or switches are safer, and limit the input.
Monitors instead of touch screens for a cheaper and safer alternative.

## Slide 20: Future
Motor selection after final choices of materials and formatting for carts and airfoils
Configuration between control inputs and mechanisms
Selection of hardware for display and user controls
Measure the actual air speed and mass flow with a pitot-static probe
Use COMSOL to evaluate the airfoil at different attack angles

## Slide 21: Questions

## Slide 22: References
http://www.ae.illinois.edu/m-selig/ads/coord_database.html#N
http://www.grc.nasa.gov/WWW/k-12/airplane/foil3.html
http://www.leespring.com/browse_catalog.asp?rbunitOfMeasure=Metric&springType=E&partnum=&UnitOfMeasure=metric&specsCriteria=&subType=&isMIL=&pageNumber=2