## Slide 1: Design Review #1
RASC-AL RoboOps Competition
Team 11: SpaceHex
Ricardo Asencio Daniel Bucken Jason Rhodan | Myles Bean Parker Harwood Matthew Wilson

## Slide 2: Overview
Selected to compete as of 12/21/2012
Awarded $5,000 of $10,000 grant 1/22/2013
Procured most of necessary hardware

## Slide 3: Overview
Continued study of expected environment
Constructing/fabricating mechanical components for new rover, Space-Hex
Locomotion programming using old rover, Hexcavator
Participating in Education/Public-Outreach event at Challenger Learning Center on 2/16/2013
Next NASA deliverable due 3/15/2013 (Report+Video; worth $5,000 grant)

## Slide 4: Revised Scheduling
Hexcavator walking on new computing hardware by end of month
Sample Extraction Module (SEM) built and operational by end of month
Cameras and Networking hardware integrated by mid March

## Slide 5: Design Changes
Camera Boom
  Carbon Fiber tube for increased rigidity
Leg Mounts
  Lightened
  Simplified to reduce fabrication time

## Slide 6: Gripper
Gripper
  Combination chain and gear drive train
  22 N (5lbf) of pinching force

## Slide 7: Graphical User Interface (GUI)
Robot IP
Command
SEM Controls
Locomotion Controls
Camera Selection
Camera Display (Web Browser)
Sensor Readouts

## Slide 8: Carbon Fiber Legs
First prototype legs have been made using XRL leg mold.
11 layers of CF, 6 at 90° and 5 at 45°
Findings: approximately 20 layers of CF will be needed for the full scale legs for Space-Hex

## Slide 9: Build Update: Frame
Aluminum tubing has been welded
All mount locations have been drilled
Waiting on sheet of aluminum to machine and weld for motor mounts

## Slide 10: Build Update: SEM
All components for the arm’s motion are complete
Final parts for gripper arrive later this week
Machining of gripper is already underway

## Slide 11: SEM in Motion

## Slide 12: SEM Coding
All movement functions for SEM have been coded and tested on similar hardware
Motor drivers and encoders for SEM have been ordered

## Slide 13: FPGA Hardware
Prototyped circuit successfully transferred to Xula2
PWM signal is reliably produced
Decoders give reliable results
Still some issues

## Slide 14: Rasberry Pi (Software Updates)
In Progress
  SPI communication is prone to errors due to motor noise
  PID algorithm in progress
    Syncs motor speeds
Buehler algorithm for walking
  Requires PID working
Turning Gait
System integration

## Slide 15: Buehler Clock

## Slide 16: Budget
First phase of purchases are completed
Second phase will be completed with second installment of the NASA Grant
  Batteries and backup batteries
 | Misumi | CISCOR (FAMU) | Space Grant & CISCOR FSU | NASA
Initial | $1,000 | $1,800 | $2,200 | $5,000
Remaining | $313 | $1,227 | $242 | $0

## Slide 17
Sponsors

## Slide 18
Questions
?