## Slide 1: Smart Material Museum Exhibit Spring Final Presentation
Senior Design Group 13
Glen Ashworth
Daniel Roque
Isaac Piersall
Laura Wainikainen

## Slide 2: Overview
Problem/Intro
Challenger Center Requirements
Background
Overall Design
Breakdown/Flowcharts
Electronic Components
Stand and Target Layouts
Video
Budget
Closing

## Slide 3: Problem/Intro
Design, build, and test a museum exhibit
Smart material
  piezoceramic
Interactive and entertaining

## Slide 4: Sponsor: Challenger Learning Center
Located on Kleman Plaza in downtown Tallahassee
Home to an IMAX 3D Theater, space mission simulator, and Downtown Digital Dome Theatre & Planetarium

## Slide 5: Challenger Center Requirements
Simple and safe
Space themed
Sized appropriately
Budget $1500

## Slide 6: Background/Inspiration
What is smart material?
Piezoceramic specifics
  MFC (macrofiber composite)
  Electrical Mechanical

## Slide 7: Background/Inspiration
Various applications
  Micro-positioning and vibration damping of optics
  Signal sensors
  Monitoring support structures
Use in space
  Satellites
  Improves communication

## Slide 8: General View of Lobby

## Slide 9: View of Exhibit
Exhibit Stand with Joystick and Controls
User Input (Joystick control and arcade buttons)
Joystick microswitches turn on/off
Target laser switched on by yellow button
Arduino reads microswitches

## Slide 10: View of Exhibit
Laser switched on and aimed at a target
Arduino provides input signal to amplifiers
Amplifiers power piezoelectric materials
Piezoelectric materials bend, reflecting the laser at the proper angle

## Slide 11: View of Exhibit
Target with light sensors for each direction of motion
Location of pan/tilt kit with a separate laser mounted on top
Laser hits target light sensors
Light sensors signal fed to the second Arduino

## Slide 12: Map View
Laser mounted on pan/tilt servo motors
Arduino powers the pan and tilt servos, which move according to which light sensor is hit by the laser
Output laser is displayed on the map

## Slide 13: Electronics
Smart Material Corp
MFC M4010-P1
  elongator
  operates from -500 to 1500 v
  environmentally sealed package
  flexible, durable, and damage tolerant
  conforms to surfaces
Emco C10 amplifiers
  Input voltage: 11.5-16 V
  Power: 1 Watt
  output: 0-1000v @ 0-1 mA
  programming voltage: 0-5

## Slide 14: Electronics Cont.
Arduino Uno
  Based on the ATmega328
  16 digital inputs/outputs
    6 are PWM
  6 A-D converters
Power Supplies
  6 v, 2 amp for the satellite section
  12 v, 3 amp for the piezo section

## Slide 15: Electronics Cont.
Joystick
  4 microswitches, ea. rated for 2 A @250v
  durable contruction
Servos
  operating voltage: 4.8-6 v
  operating range: ~170 deg
Photoresistors
  120 to 1100 ohms
    close light source to ambient light
  used with resistors to create a voltage divider

## Slide 16: Electronics Cont.
Laser Pointers
  operate up to 1mW of power
  Class 2: considered safe during normal use
    blink reflex of eye will prevent damage
Assorted Resistors
  used as pull-up resistors for the input
  used with capacitors to make a RC low pass filter
Arcade Buttons
  Durable (tested to 10,000,000 cycles)
  microswitches rated to 3A @ 120V

## Slide 17: User Interface
Piezoelectric MFC
Power Source
Arduino Uno
C10 Amplifiers
Outgoing
Laser Light Beam
Mirror

## Slide 18: Exhibit Stand
Pan/tilt kit

## Slide 19: Videos
Laser Movement: http://youtu.be/W8oDQ-zhKU8
Piezoelectric Material: http://youtu.be/9JU9q-LVN-E

## Slide 20: Satellite Target
Incoming
Laser Light Beam
Photocell
Array
Arduino
Uno
Pan/Tilt Bracket
Servo
Motors
Green Laser
Outgoing
Laser Beam

## Slide 21: Video
Laser controlled pan/tilt kit: http://youtu.be/UP5KaqaDGHQ

## Slide 22: Challenges Encountered
Analog to Digital Converter (Joystick)
  Digital Joystick
Adjustable arms to hold MFCs
Sawdust

## Slide 23: Safety
Electronics Components Encased
Limit in Coding
  0-255
Height of Satellite Target

## Slide 24: Cost Analysis
Budget: $1500
Remaining Funds: $780
Item | Price
Piezoelectric MFCs | $ 120
Amplifiers | $ 340
Microcontrollers | $ 60
Miscellaneous Electronics | $ 150
Exhibit Stand | $ 50
Total | $ 720

## Slide 25: Recommendations for Future Work
Light sensors on Florida map
Wireless control station inside of “Mission Control”
Webcam placed on satellite facing map

## Slide 26: What’s Next?
Complete satellite target
Acrylic provided by Challenger Learning Center (4/19/13)
Assembly at Challenger Learning Center
Open House Saturday at 10:00AM
NASA Space Grant Assignments
  Final Report
  Video Clips

## Slide 27
Questions?