## Slide 1
Final Presentation-Spring ‘13
Team 6: Autonomous Aerial Vehicle
AUVSI 2013 Student Unmanned Air Systems Competition
Team Members: Ken Anderson, Arielle Duen, Eric Milo, Ernandes Nascimento,
Cristopher Timmons, Robert Woodruff & Matthew Yasensky
Project Advisors: Dr. Chiang Shih, Dr. Michael P. Frank, Dr. Kamal Amin

## Slide 2: Today’s Topics
Team History
Competition Overview and Needs Assessment
Flight Progress
Autopilot and Navigation
Camera/Gimbal System
Imaging Processing
Schedule/Budget
Summary

## Slide 3: Team History
Fall Semester
  Half of Team Studying in Brazil
  FIPSE
    Fund for the Improvement of Post-Secondary Education
    Exchange Program
      Florida State University
      Universidade Federal de Itajubá, Minas Gerais, Brazil
    Promotes the Development of
      Engineering Curriculum
      Mentored Internships
      International Collaborative Design Projects
Spring Semester
  Additional Team Member

## Slide 4: Needs Assessment
Need for Advancement of Autonomous Technology
  Military Missions
  Search and Rescue
  Private Sector Automation
Recent News has Given Drone Technology a Negative Spin
  Collegiate Involvement

## Slide 5: Project/Competition Overview
AUVSI-Competition Project
  Association for Unmanned Vehicle Systems International
Search and Rescue
  Natural Disaster Scenario
I.S.R.
  Intelligence
  Surveillance
  Reconnaissance

## Slide 6: Competition Objectives
  Waypoint Navigation
  Coordinate Change
  Autonomous Takeoff and Landing
  Autonomous Area Search for Ground Targets
  Image Recognition of Ground Targets
  Safety Precautions

## Slide 7: Aircraft Functionality
Mechanical Systems

## Slide 8: Airframe Concepts

## Slide 9: Airframe/Propulsion System
Senior Telemaster
94 in wingspan
1330 sq inches wing area
17 lbs (fully loaded)
25/55 mph cruise/top speed
Magnum XL 91 Nitro
4-stroke/0.91 cu inch
2,000-12,000 practical RPM
22 oz fuel = 50 min of flight

## Slide 10: Achieving Flight Time
Fuel Tank
Feeder tank
Engine
Pressure Line
Fuel Line
Fuel Tank Configuration Concept:
  ≈2.5 min per 1 oz fuel
  16 oz + 6 oz = 22 oz
  Estimated 55 min flight time
Fuel Tanks Installed
  Demonstrated 50 min flight time

## Slide 11: Learning to Fly
11
Real Flight Simulator:
  20+ hours of flight experience
Buddy Box Practice:
  Multiple practice flights

## Slide 12: AMA Membership
12
Academy of Model Aeronautics
  -Requirement to fly in the competition and Tallahassee
AMA Benefits:
  -$2.5 million Comprehensive General Liability Protection
  -$25,000 Accidental/Medical coverage
  -$1,000 Fire, Theft, and Vandalism coverage

## Slide 13: Navigation Systems
Autopilot

## Slide 14: Ardupilot Mega 2.5
5.2 V0.5 V
200 mA
3 axis gyro
Accelerometer
Magnetometer
Barometer
Arduino compatible
Onboard 4 MP Dataflash chip for automatic data logging
Digital compass powered by Honeywell’s HMC5883L-TR chip

## Slide 15: 3DR GPS uBlock LEA-6
3DR Radio Telemetry Kit
900 MHz
200 dBm transmit power
250 kbps air data rate
Adaptive time division multiplexing
Built in error correcting
Approx. 1 mile range
5 Hz update rate
3.3 V regulator
I2C EEPROM for configuration storage

## Slide 19: Safety Features
Futaba 6J 6 Channel Digital Prop. RC System Transmitter
The plane will return to home and loiter around home after 20 seconds of lost signal
The plane must perform a controlled crash after 3 minutes of lost signal

## Slide 20: Camera Attachment
Gimbal System

## Slide 21
Gimbal System
  Gimbal Concept
  Redesigning the Sytem
    First system was oversized
      Large camera and gimbal
      Scaled down camera and gimbal
      Eliminated unnecessary components
    Latest design features
      Wider angle of view
      More concise
      Less weight, CG dislocation
      Higher ground clearance

## Slide 22: Gimbal System
  System Implemented
  System works properly on test flight
    Autopilot is able to control servos
    Servos are calibrated correctly
  Vibrations
    Last tests with damping materials were not as good as expected
    Newer tests are currently being done
      Rubber Bands

## Slide 23: Gimbal System
  Angular Correction Video

## Slide 24: Camera System
Image Processing

## Slide 25: Image Processing – Top Level
CCD
Camera
5.8GHz Video Transmitter
5.8GHz Video Receiver
Composite-to-USB Encoder

## Slide 26: Transmission Subsystem
Power Supply
  Rechargeable Li-Po Battery
  11.1 V, 2200 mAH
Video Transmitter
  Composite video (NTSC)
  5.8 GHz
  400 mW
Camera
  Sony CCD
  700 TVL Resolution
11.1 V Li-Po Battery

## Slide 27: Receiving Subsystem
Video Receiver
  R5800DX
  5.8 GHz sampling frequency
USB Encoder
  Input: Composite Video
  Output: USB
Asus Laptop
  Intel Core i5 Processor
  4 GB RAM memory
USB Encoder
AC Wall Outlet

## Slide 28: Software Subsystem
Yes
Duplicate of previous target?
Disregard Data
No
Save to Output File
Orientation
Location of Target
Char Color
Char Shape
Target Color
Target Shape
No
Yes
Is there a target present?
Match GPS data to image
Video Data
GPS Data
Acquire next frame of video
Extract Target Data
Store Data

## Slide 29: Image Processing - Results
Image Processing from in-flight video

## Slide 30: Budget
Chart: 
| Mechanical | Electrical | Miscallaneous
 | 268.58 | 1340.39 | 50.19
FIPSE Budget = $2000
Remaining = $340

## Slide 31: Schedule – Spring Semester
31

## Slide 32: Summary
FIPSE
  A unique experience over international boundaries
  Exposure to interesting challenges
  Expanded skill-set of our team
What we have
  All hardware necessary to meet thresholds of competition
  A UAV capable of autonomous flight and real-time image processing

## Slide 33: Summary Cont’d
Sony KPC Camera
Gimbal System
Autopilot System
  3-Axis Gyroscope
  3-Axis Magnetometer
Ublox GPS
Telemetry Transmitter
Radio Receiver
Video Transmitter
Electronics Power Supply
Magnum XL Engine
Pitot Probe

## Slide 34: Summary Cont’d
Remaining threshold
What we could have done differently
  Consider needs, not only what is available
    We allowed for 60 minute flight time, which may not have been necessary
Future recommendations
  New vehicle
  Electric Motor
  Have a Pilot
  Computer Engineer

## Slide 35: Thanks and Appreciation
Dr. Shih
Dr. Amin
Dr. Frank
Mechanical Faculty
Electrical Faculty
Hobbytown USA
Seminole RC Club
Senior Design TA’s
SENIOR CLASS 2013

## Slide 36
Questions?

## Slide 37: Budget