## Slide 1
“Wear It” Impact Baseball Vest
Garth Fletcher
Kyler Hast
Kyle Meredith
Maria Miro
Ryne Wickery
Cecilia Wong
February 13, 2014
Advisors
Dr. K. Amin
Dr. D. Olawale
Team Members
Sponsor
Gavin Boone

## Slide 2
Background
Updated Scope
Analysis
Design
Material Selection
Testing
Ergonomics
Updated Schedule
Overview
Kyler Hast

## Slide 3
Batter may incur severe or painful injuries from being hit by a baseball.
These types of injuries may deter younger children from playing baseball.
With an effective protective collar injuries to the spine and neck can be prevented.
No current protection is available for the neck region.
Background
Kyler Hast

## Slide 4
Design a collar to prevent injury from baseball impact.
Design the collar so it does not hinder motion/performance.
Design collar to be integrated into current vests.
Updated Scope
Kyler Hast

## Slide 5
Analysis
Impact time
    2.455*10-3 sec
Force of ball at 100mph
    2.581 kN (580 lbf)
Surface area of ball compressed
    0.503 in2
Impact Energy = 141 J
Kyler Hast

## Slide 6
Collar Design
Final design will be selected from one of the following designs
Final selection will be based on finite element results
Ryne Wickery

## Slide 7
Crown Neck Plate
Ryne Wickery

## Slide 8
Arched Neck Plate
Ryne Wickery

## Slide 9
Flat Neck Plate
Ryne Wickery

## Slide 10
Final
Material Selection
Ryne Wickery

## Slide 11
Will be used for the hard shell of the collar
Thermoplastic
Relatively large strength-to-density ratio
Currently used in bull riding protection vests, and also in ballistic protection
High Density Polyethylene
Ryne Wickery

## Slide 12
Padding material for the collar
Used in current protective gear
Water resistant
    Won’t absorb sweat
Can be formed to collar shape
Recoverable
Relatively lightweight
EVA Foam
Maria Miro

## Slide 13
Ergonomics
Comfort
    Foam will be comfortable to player
Fit
    Thermoplastic, and elastic foam will allow collar to be molded as desired [Retain mobility]
Safety
    Collar will protect player from damage caused by impact
Chemical
    Polyethylene and EVA will not react with skin of player that would cause rash or disturbance.
Maria Miro

## Slide 14
Future Plans
Finite Element Analysis
    Will be used to Select Final Design
    Will allow us to determine material dimension (thickness)
Procurement
    Acquire material samples for compression testing
Compression Testing
    Sample of Collar construction will undergo compression testing to mimic impact.
    This will allow us to confirm conclusions from finite element analysis
Maria Miro

## Slide 15
Maria Miro

## Slide 16
Questions?