## Slide 1: Solar Sausage for Desalination
Sponsor: FAMU-FSU College of Engineering
Advisors: Dr. Michael Devine
Dr. Shangchao Lin
Instructors: Dr. Nikhil Gupta
Dr. Chiang Shih
Group 7: Alexandra Filardo
Joseph Hamel
Alexander Stringer
Crystal Wells

## Slide 2: Overview
The Project
  Objectives and Scope
Solar Sausage
System Overview
  The Design
  The Process
  The Components
  Maintenance
General Calculations
2
Solar Sausage for Water Desalination Joseph Hamel
Past, Present, Future
Business Plan
Challenges Faced
Resources
  Procurements
  Budget
  Manufacturing
Schedule

## Slide 3: The Project
Project Scope
To create a solar desalination system utilizing the Solar Sausage.
Create a system that can be easily mass produced at low cost.
Main Objectives
The system must support a small family
Minimize cost
Make the system user friendly
Make the system easily transportable and easily deconstructed
3
Solar Sausage for Water Desalination Joseph Hamel

## Slide 4: Solar Sausage
Is an inflatable parabolic solar concentrator made of Mylar Polyester
  98% cheaper than traditional parabolic reflectors
The reflective membrane separated two sections
The pressure in the upper section is maintained at . The lower section is maintained at less than the upper section
  The pressure difference results in a focal point
4
Solar Sausage for Water Desalination Joseph Hamel

## Slide 5: System Overview: The Design
Solar Sausage
Condenser
10 ft
Trough
Stand
Storage
Tank
3 ft
5
4 ft
Solar Sausage for Water Desalination Alex Filardo

## Slide 6
6
Solar Sausage for Water Desalination Alex Filardo

## Slide 7: General Layout
Storage Tank
Trough
Condenser
Channels
Bladder
Trough
Solar Sausage
7
Solar Sausage for Water Desalination Alex Filardo

## Slide 8: Storage Tank
The Storage Tank volume is
Filter located in the upper portion of the tank will filter out particles larger than 100 microns
Storage tank will be painted black to maximize heat absorption from the sun
Manually operated valve will control the flow of filtered saline water into the trough
Figure 4. Storage Tank
Filters and hold saline water to feed into the through
8
10 in
13.75 in
6 in
Solar Sausage for Water Desalination Joseph Hamel

## Slide 9: Trough
The trough runs the full length of the solar sausage and has a width of 2 inches
  The focal point is only 3/8th of an inch wide
The troughs volume is
Heat Delivered to Trough
The trough is painted black to maximize heat absorption
Figure 2. Trough
Full Trough
End of Trough where it is bolted to the stand
a)
b)
a)
b)
9
2 in
2 in
10 ft
Solar Sausage for Water Desalination Joseph Hamel

## Slide 10: Condenser/Channels
Is 5 inches wide runs the full length of the trough and sits directly over it
Has a condensing surface area of
As the water condenses it drips down into the channels along the side
One end is raised a few inches higher than the other. Driving the water down to the lower end where it is then collected
Figure 3. Condenser
a) Connected to an elevated Bolt on the Stand.
b) The angle of the raised end drives the water down the channels
b)
a)
a)
b)
10
1 in
1 in
3 in
2.5 in
Solar Sausage for Water Desalination Joseph Hamel

## Slide 11: Bladder
Placed inside oil drums already readily available for customer
Collects clean water from channels
Removed and replaced once filled with potable water
11
Solar Sausage for Water Desalination Alex Filardo

## Slide 12: Expected Worker Maintenance
Bring saline water to Solar Sausage site
Rotate Solar Sausage to align sun with trough
Daily Clean out of salt build up in trough
Replace potable water bladder once full
Rinse saline filter bladder weekly
12
Solar Sausage for Water Desalination Alex Filardo

## Slide 13: General Calculations
Trough Volume
Storage Tank Volume
Total Reflective Surface Area
Heat Delivered to the Trough
Saline Concentration
Start up time
Run time
Total Operating Time
12
Solar Sausage for Water Desalination Alex Filardo

## Slide 14
Past
Completed design/calculations for system
Present
Constructing system and testing Solar Sausage heating to trough
Beginning partnership with business group
Future
Prototype testing to confirm expected performance of design
Troubleshooting/resolving new issues arising during testing
Ordered all parts aside from condenser
Connecting with Engineering Without Borders
Assembled Solar Sausage prototype
Build completed marketing strategy with business group
13
Solar Sausage for Water Desalination Joseph Hamel

## Slide 15: Business Plan
Reach out to potential investors
  Water Aid
  Water for People
  Water for Good
  Global Water
Identify market competition
Continue meeting with business group for successful business plan
14
Solar Sausage for Water Desalination Joseph Hamel

## Slide 16: Challenges Faced/Lessons Learned
Challenges Faced
  Designing the most optimal condenser
  Touching base with Engineering Without Borders
  Preventing contamination of water from aluminum
Lessons Learned
  Building a report and present information of a long-term project
  Building chemistry and working efficiently with group
  Practicing professionalism contacting colleagues and superiors
15
Solar Sausage for Water Desalination Joseph Hamel

## Slide 17: Procurement
Thus far the team has procured items to construct the
  Stands (x2)
  The Trough
These items were procured through McMaster Carr and Metals Supermarket
These items were procured at a cost of
  $499.71
16
Solar Sausage for Water Desalination Alex Filardo

## Slide 18: Budget
18
Solar Sausage for Water Desalination Alex Filardo

## Slide 19: Gantt Chart
19
Solar Sausage for Water Desalination Alex Filardo

## Slide 20: Summary
Goal: create an inexpensive, easily replicated solar desalination system utilizing the Solar Sausage
The system’s design was shown with main components
General calculations, expected maintenance work and future business plans were discussed
The monetary aspects such as procurement and budget are generalized
Timelines and scheduling were defined
20
Solar Sausage for Water Desalination Joseph Hamel

## Slide 21: References
Vendor Purchase(s)
  http://www.mcmaster.com/#
  http://ecommerce.metalsupermarkets.com/MSC-Home.aspx
[1] Engel, Yunus A. Fundamentals of Thermal-fluid Sciences. 4th ed. Singapore: McGrawHill, 2012. Print.
[2] Sinha, Sayontan. "Solar Insolation." Solar Insolation. Web. 21 Oct. 2014.
[3] "Ocean Water: Salinity." Oceanography. Office If Naval Research. Web. 18 Oct. 2014.
21
Solar Sausage for Water Desalination Joseph Hamel

## Slide 22: Questions ???