## Slide 1: Solar Sausage for Desalination
Sponsor: FAMU-FSU College of Engineering
Advisor: Dr. Michael Devine
Dr. Shangchao Lin
Group: Alexandra Filardo
Joseph Hamel
Alexander Stringer
Crystal Wells

## Slide 2: Overview
Sun Tracking System
Testing
  Completed Testing
  Future Testing
  Safety Procedures & Water Quality
Commercialization Plan and Customer Profile
Budget
Schedule
The Project
  Objectives and Scope
Solar Sausage
The System
  Design
  Piping System
  Storage Tank
  Pressure Regulation System
  Operation
  Condenser
  Maintenance

## Slide 3: The Project
Project Scope
Objectives
To create a solar desalination system utilizing an inflatable parabolic reflector called the Solar Sausage
To create a system that can be easily mass produced at low cost.
Produce drinking water with a saline concentration less than 100 ppm
Support a family of 5
Minimize cost
Create a user friendly system that can be easily transported and constructed

## Slide 4: Solar Sausage
Figure 1: Cross-Sectional view of the Sausage
Inflatable parabolic reflector in the shape of a sausage
Made of a clear membrane and a Mylar reflective membrane
When inflated the reflective membrane separates the Solar Sausage into two sections
Upper Pressure:
  Lower Section is less than the top

## Slide 5: The System: Design
Solar Sausage
Stand
Storage Tank
Condenser
Figure 2: System Configuration
Side View
Cross-Sectional View
B)
A)
Trough

## Slide 6: The System: Design
A)
B)
Figure 3: System Configuration Expanded View
Piping System
Interior View

## Slide 7: The System: Storage Tank
Storage Tank will be a five gallon bucket
  Readily available filters
  Approved by U.N for storing water
  Height:
  Diameter:
Bucket will sit on the Storage Tank Platform
  Will be above the stand
Saline water piping system
  A ball valve is used to control the flow
A)
B)
C)
Figure 4: Storage Tank Components
5 Gallon Bucket
Platform
Piping System

## Slide 8: The System: Storage Tank Configuration
The piping system is used to secure the bucket to the platform
A flare nut is used to lock everything in position
Two rubber O-rings are make the storage tank water tight
Figure 5: Simplified Storage Tank Configuration

## Slide 9: The System: Pressure Regulation
11/8” ID plastic tubing
Needle Valve
Tri-Barb
Foot-Pump
Pressure Gauge
Pipe from Solar Sausage
Two systems required
8 Pieces, 4 not shown
Needle Valve allows for precision control of the airflow
Figure 6: Simplified Pressure Regulation System Configuration

## Slide 10: The System: Condenser
Length Width Height
Raised at the storage tank end
  Ideal gradient between to
Guards along the aid in the collection of water vapor
Water exits out the collection pipe
A)
B)
Figure 7: Condenser Section
Raised end
Lowered end and collection point
Interior View

## Slide 11: The System: Sun Tracking
Straps
  Glued to sides of Solar Sausage (shown in red)
  Crossed beneath Solar Sausage
  Attached to weighted bar underneath
Converts linear translation to rotational motion
Direction of rotation of Solar Sausage dependent on bar motion
  Ex. Moving bar to the right produces counterclockwise rotation of Solar Sausage
Figure 8: Simplified Diagram of the sun tracking system.
Notes: This weighted bar & strap system has been used for similar applications previously at Sunnyland Solar (FSU’s previous SS farm)

## Slide 12: The System: Operation
Fill water storage tank with saline water to filter out debris
Notes: Will produce 3 gallons per day

## Slide 13: The System: Operation
Open valve to fill trough with filtered water

## Slide 14: The System Operation
Use the Pressure Regulation System to create focal point and heat the trough

## Slide 15: The System Operation
Water vapor rises into the dome, condenses then collects in the channels

## Slide 16: The System Operation
The gradient drives the water to the collection pipe. The desalinated water is collected in a container of choice by the operator
Desalinated Water

## Slide 17: The System: Maintenance
Daily Maintenance
  Clean Trough of all saline build up
  Clean Condenser of all build up
  Check Solar Sausage for any tearing
Weekly Maintenance
  Rinse saline water filter of all dirt and debris
  Clean desalinated water containers
  Tighten all connections on the pressure regulation system
  Clean Saline Water and Desalinated Water piping systems of all build up

## Slide 18: Testing: Completed Testing
Relationship of Flow Rate and Handle Position | 
Handle Position (degrees) | Average Flow Rate (gal/min)
20 | 0.00
45 | 0.60
60 | 1.44
90 | 3.14
Calibration and Confirmation of Equipment accuracy
  Salinity: Accuracy of 2%
  Thermometer: Accuracy of 1.5%
Relationship of flow rate and valve handle angle
Figure 2: Valve shown at
(a) 0˚ position (Closed) and
(b) 90 ˚ position (Open)
(a)
(b)
Notes: Static calibration of equipment
Equipment accuracy done using distilled water & salt water (500ppm)
3 measurements for each water
each time accuracy percent was consistent
Equipment accuracy for thermometer used by measuring water @ 77F & oil at 300F
3 measurements each time
Flow doesn’t start until 20 degrees due to internal ball valve
60 degrees is ideal flow rate

## Slide 19: Testing: Future Testing
Flash Distillation
  Valve placed at to allow a slow-drip into heated trough
  The evaporation rate will be calculated. This will be repeated in till Flash Distillation is no longer possible
Batch Distillation
  The trough will be filled with , and the time for it to evaporate will be measured
Focal Point Concentration
  Focal point width: -
  Procedure to maintain width
Sun Tracking System
  Procedure to track the sun
    North-South alignment
  Adequate rotation value and frequency
    i.e
Notes: Focal Point Concentration: to maximize results, FP must be > 3/8 in wide and < 2in wide
develop procedure to maintain this width
Sun Tracking System: procedure to track the sun
adequate rotation value & time - a value for # of deg/hour SS must be turned & frequency
Two Types of Distillation to be tested:
Flash Distillation: A process where the water is flash-evaporated
Batch Distillation: A process where a mixture is evaporated in batches

## Slide 20: Testing: Safety & Quality
Safety Procedures
Water Quality
Heat-Resistant gloves will be worn during testing
All temperatures will be taken at a distance with a Pistol-Grip Infrared Thermometer
Trough and Condenser will be allowed 30 minutes to cool after testing before
The saline concentration of the drinking water produced will be measured
Measures saline concentration
ExStik II Salinity Meter will be used
  2% Accuracy

## Slide 21: Business Plan
Commercialization Plan
Customer Profile
1st year: Network
2nd - 4th year: Enter market
5th/6th: development of domestic commercialized systems
Non-profit organizations & humanitarian engineering teams
On-site training by organization or team
Notes: Commercialization Plan:
1 – secure vendors, develop contacts with non-profit organizations (ex. Engineers Without Borders, )
2/3/4 – develop brand recognition, attempt market saturation (product would become more widely known & used)
5/6 – development of domestic commercialized systems
Customer Profile:
Non-profits & engineering-minded humanitarian groups (usually mission-based work)
Small-scale engineering mission teams performing humanitarian work that is able to train current staff
Business Plans
  International market within 4 years
  Domestic mass production within 6 years

## Slide 22: Budget
Chart: Budget Overview
Spent | 1157.14
Available | 3842.86
Chart: Spending Breakdown
| Raw Materials | Accessories | Testing Supplies | Labor
 | 418.98 | 430.23 | 247.93 | 60
Notes: Estimated Cost: ~$700.00/unit
  Current Cost: $438.86 excluding condenser

## Slide 23: Schedule

## Slide 24: Summary
Desalination system utilizing the Solar Sausage technology
Design
  Modular , little maintenance, components, and sun-tracking system
Testing
  Completed: Determine optimal flow rate based on handle position
  Future: Focal point concentration, Sun-tracking system values, Type of distillation
  Safety & Quality: heat-resistant gloves and thermometers used, testing salinity
Business
  International market within 4 years
  Domestic mass production within 6 years
Budget
  23% spent
Currently on Schedule
  Weather conditions

## Slide 25: Questions?
For more information: http://eng.fsu.edu/me/senior_design/2015/team07/