## Slide 1
Sponsored by
Kim Sash &
The Tall Timbers Research Station and Land Conservancy
In partnership with
Dr. Gupta, Dr. Shih, Dr. Clark, Dr. Harvey, Dr. Frank &
The FAMU-FSU College of Engineering
Presented by
Jane Bartley, ME (team leader)
Lester Nandati, Lead ME
Colin Riley, Lead EE
Also featuring
Bridget Leen, ME
Jordan Muntain, ME
Sina Sharifi-raini, EE
The Gopher Tortoise Scope
Notes: JANE

## Slide 2
Background
Subsystems
Project Management
Final Product
Overview
Jane Bartley
Notes: <background
Motivation
Design overview
Project management
Subsystem integration
Final Product
JANE>

## Slide 3
Keystone species
Gopher tortoises can create burrows up to 50 ft long
Declining population
Populations statistics are measured using a scope
Motivation
Figure 2. Gopher tortoise habitat. [2]
Background | Subsystems | Project Management | Final Product
Jane Bartley
Figure 1. Gopher tortoise emerging from his burrow. [1]
Notes: Bullet pts 2 habitat, foresting
JANE

## Slide 4
Burrow conditions
  Wet and muddy
  Cramped with poor visibility
Current scope
  Hard to maneuver down the burrow
  Limited capability
  Not weather resistant
Scoping Process
Figure 4. Tall Timbers’ current gopher tortoise scope
Figure 3. Difficulties with current scoping method.
User Interface
Scope
Background | Subsystems | Project Management | Final Product
Jane Bartley
Notes: Have to bend down to see
JANE

## Slide 5
Specifications
Primary
Secondary
Tertiary
Uses infrared camera
Weighs less than 40 lbs
Measures less than 4 in x 6 in x 10 in
Costs less than $1000 to duplicate
Splash proof
Capable of 8 hours of operation
Temperature and humidity data
Video and image capturing
GPS
Background | Subsystems | Project Management | Final Product
Jane Bartley
Notes: LESTER

## Slide 6
Camera System
Stand-alone IR camera
  7 Infrared LEDs
  Wide angle lens
  680p x 420p
  420 fps
Figure 5. Wide View infrared camera. [3]
Versatility
  Custom build housing
  Compact and affordable
  Panning system with 80° span
Background | Subsystems | Project Management | Final Product
Lester Nandati
Stand-alone IR camera
  7 Infrared LEDs
  Wide angle lens
  680p x 420p
  420 fps
Figure 5. Wide View infrared camera. [3]
Versatility
  Custom build housing
  Compact and affordable
  Panning system with 80° span
Notes: <component determination>
  Under Control functionality
    -Dictate panning system
    -Easier to modif
LESTER

## Slide 7
Aileron system design
  Panning only
  Simpler and more compact
System is placed inside the rover so that the camera is in front of the tracks
Camera Panning
Figure 6. Camera pan assembly.
Background | Subsystems | Project Management | Final Product
Lester Nandati
Notes: JANE
-Should I mention the visibility through the side walls?

## Slide 8
Body Development
Planar Chassis
Casing
  0.125 inch IR transmitting Plexiglas
  Angled front shield
Side boxes
  Temperature sensitive components
  Additional room
  Bearing and axle support
Planar Chassis
Casing
  0.125 inch IR transmitting Plexiglas
  Angled front shield
Side boxes
  Temperature sensitive components
  Additional room
  Bearing and axle support
Planar Chassis
Casing
  0.125 inch IR transmitting Plexiglas
  Angled front shield
Side boxes
  Temperature sensitive components
  Additional room
  Bearing and axle support
Figure 7. Stages of body casing.
Background | Subsystems | Project Management | Final Product
Lester Nandati
Notes: LESTER

## Slide 9
Treads
  Lynxmotion Tracks - Polypropylene/rubber
  Cut width of 2 inch treads in half
90° Gearmotors
  200:1 torque ratio
  Fully enclosed
  Built in clutch
  Machined couplers
Locomotion
Figures 8, 9. Tracks and gearmotors.
Background | Subsystems | Project Management | Final Product
Lester Nandati
Notes: LESTER

## Slide 10
Arduino Micro
7 8-bit PWM channels
32 KB flash memory
16 MHz clock speed
USB 2.0 serial communication
1.9 x 0.7 inches
Rover Electronics
Background | Subsystems | Project Management | Final Product
Colin Riley
Notes: COLIN

## Slide 11
DHT22
Relative Humidity from 0% to 100% with ±0.05% accuracy
Temperatures from -45°C to 125°C with ±0.5°C accuracy
Refreshes every 2 seconds
Rover Electronics
Background | Subsystems | Project Management | Final Product
Colin Riley
Notes: COLIN

## Slide 12
Raspberry Pi B+
4 USB 2.0 ports
32 GB micro SD card
ARM 11 CPU
900 MHz clock speed
User Interface
Background | Subsystems | Project Management | Final Product
Colin Riley
Notes: COLIN

## Slide 13
Logitech Gamepad
Joystick for intuitive rover control
Directional pad to pan camera
Wired, USB connection
User Interface
Rover Motion
Camera Angle
Shutdown
Background | Subsystems | Project Management | Final Product
Colin Riley
Notes: COLIN

## Slide 14
Screen and Driver
7 inches
In-plane switching LCD
1280 x 800 pixels
60 frames/second
User Interface
Background | Subsystems | Project Management | Final Product
Colin Riley
Notes: COLIN

## Slide 15
Rechargeable Li-ion Battery
13.4 - 9 Volt operating range
2.5 hour battery life
5 hours to recharge
800 cycle expected life
User Interface
Background | Subsystems | Project Management | Final Product
Colin Riley
Notes: COLIN

## Slide 16
Tether
Figure 10. Tether internal wiring layout
Background | Subsystems | Project Management | Final Product
Features
  Kevlar
  50 ft long
  0.75 in diameter
  Tensile strength- 440 ksi
8-pin waterproof connection
  Secured at rover and at user interface
  Weight: 0.21 lbs
Features
  Kevlar
  50 ft long
  0.75 in diameter
  Tensile strength- 440 ksi
8-pin waterproof connection
  Secured at rover and at user interface
  Weight: 0.21 lbs
Colin Riley
Notes: JANE

## Slide 17
Small rover carries camera underground
User Interface (UI) displays video and sends gamepad commands
50 foot tether provides
  Power
  Communications
  Video
Top Level Design
Rover
User Interface
Battery
Active USB
RCA Video
Data
Power
Above Ground
Below Ground
Background | Subsystems | Project Management | Final Product
Colin Riley
Notes: Segment pictures with text
COLIN

## Slide 18
Project Management
Sep-Oct
Nov-Dec
Jan-Feb
Mar-Apr
Prototype designing
  Camera
  Data acquisition
  Chassis body
Procurements
  Motor driver
  IR Camera
  Raspberry Pi B+
$221 spent to date
Figure 11. Initial CAD drawings.
Background | Subsystems | Project Management | Final Product
Jane Bartley

## Slide 19
Project Management
Nov-Dec
Sep-Oct
Jan-Feb
Mar-Apr
Final rover design
  Motor selection
  User Interface development
  Subsystems finalized
Procurements
  Gamepad
  ABS and Plexiglass
$474 spent to date
Figure 12. Early prototype with components laid out.
Background | Subsystems | Project Management | Final Product
Jane Bartley

## Slide 20
Project Management
Jan-Feb
Nov-Dec
Sep-Oct
Mar-Apr
Figure 13. Later, refined prototype.
Background | Subsystems | Project Management | Final Product
Jane Bartley
Prototyping
  Communication testing
  Component housing
  Tether
Procurements
  Tether materials
  Battery and charger
$1169 spent to date

## Slide 21
Project Management
Mar-Apr
Nov-Dec
Sep-Oct
Jan-Feb
Final Design
  Assemble and seal
  User interface testing
  Indoor mobility
  Outdoor performance
Procurements
  Pelican casing
$1608 spent to date
Figure 14. Final assembly.
Background | Subsystems | Project Management | Final Product
Jane Bartley

## Slide 22
Product Evaluation
Primary
Secondary
Tertiary
Uses infrared camera
Weighs less than 40 lbs
Measures less than 4 in x 6 in x 10 in
Costs less than $1000 to duplicate
Splash proof
Capable of 8 hours of operation
Temperature and humidity data
Video and image capturing
GPS
Primary
Secondary
Tertiary
Uses infrared camera
Weighs less than 40 lbs
Measures less than 4 in x 6 in x 10 in
Costs less than $1000 to duplicate
Splash proof
Capable of 8 hours of operation
Temperature and humidity data
Video and image capturing
GPS
Primary
Secondary
Tertiary
Uses infrared camera
Weighs less than 40 lbs
Measures less than 4 in x 6 in x 10 in
Costs less than $1000 to duplicate
Splash proof
Capable of 8 hours of operation
Temperature and humidity data
Video and image capturing
GPS
Primary
Secondary
Tertiary
Uses infrared camera
Weighs less than 40 lbs
Measures less than 4 in x 6 in x 10 in
Costs less than $1000 to duplicate
Splash proof
Capable of 8 hours of operation
Temperature and humidity data
Video and image capturing
GPS
Lester Nandati
Background | Subsystems | Project Management | Final Product
Notes: LESTER

## Slide 23
The GT Cruiser
Background | Subsystems | Project Management | Final Product
Lester Nandati
Notes: COLIN

## Slide 24
  Ability to scope smallest burrows
    Lower cost
    Reduction of features
  Comprehensive features
    Expensive
    Large
Product Expansion
Possibilities of adding or removing features
Affordable rover with appropriate functionality and durability
  Ability to scope smallest burrows
    Lower cost
    Reduction of features
  Comprehensive features
    Expensive
    Large
Background | Subsystems | Project Management | Final Product
Lester Nandati
  Ability to scope smallest burrows
    Lower cost
    Reduction of features
  Comprehensive features
    Expensive
    Large
Notes: LESTER

## Slide 25
For more information go to:
http://eng.fsu.edu/me/senior_design/2015/team21/index.html
References
[1] "Gopher Tortoise - Meryman Environmental." Gopher Tortoise. Meryman Environmental, 2015. Web. 14 Apr. 2015. <http://merymanenvironmental.com/gopher-tortoise/>.
[2] "Gopher Tortoise Council." About the Gopher Tortoise. Gopher Tortoise Council, 2015. Web. 14 Apr. 2015. <http://www.gophertortoisecouncil.org/about-the-tortoise/>.
Questions?

## Slide 26
Appendix