## Slide 1: Pedibus Team 22
Team Members:
Kyle Anderson
Stephen Avery
Alejandro San Segundo
Brett Willenbacher
Team No.22
Slide 1 of 25
Alejandro San Segundo
Final Presentation
Sponsor:
Ron Goldstein
Advisor:
Keith Larson
Professors:
Dr. Shih
Dr. Gupta

## Slide 2: The Team
Team Members:
(Left to Right)
Alejandro San Segundo
Brett Willenbacher
Kyle Anderson
Stephen Avery
Team No.22
Slide 2 of 25
Alejandro San Segundo
Final Presentation
Sponsor:
Ron Goldstein
Advisor:
Keith Larson

## Slide 3: What is a Pedibus?
Team No.22
Slide 3 of 25
Alejandro San Segundo
Final Presentation

## Slide 4: Project Definition
Team No.22
Slide 4 of 25
Alejandro San Segundo
Final Presentation
Project Scope
    Design and fabricate a one of a kind multi-user, pedal powered vehicle for the purpose of entertainment around Tallahassee and nearby areas.
Pedibus Requirement | Status
10 pedaling passengers | ✓
Room for extra (non-pedaling) passengers | ✓
Rolling Chassis must be < 1499 lbs (FL law) | ✓
Off the Shelf parts | ✓
Torque output to climb 8° hill grade | ✓
Able to hold 3000 lbs payload | ✓
Free weight transportable | X
Reverse gear capability | ✓
Movable on single rider input | ✓
Anderson welding steel frame members

## Slide 5: The Pedibus 2.0
Team No.22
Slide 5 of 25
Alejandro San Segundo
Final Presentation
CAD renders of complete Pedibus assembly
Completed Pedibus
Notes: Point 1: 10 Peddlers, 1 driver, 1 “bartender”, and 2 non-peddlers
Point 2: Because of Tallahassee’s hills a crawl gear and cruise gears are recomended

## Slide 6: Design Breakdown: Frame
Team No.22
Slide 6 of 25
Stephen Avery
Final Presentation
Frame:
Ladder style frame
A500 box steel construction
CAD renders of finalized frame design
Frame During Initial Fabrication

## Slide 7: Design Breakdown: Frame
Team No.22
Slide 7 of 25
Stephen Avery
Final Presentation
Design Considerations:
Manufacturing
Material Type
Bracing Configuration
Weight
    Size
    Component Placement
Frame Finite Element Analysis Sample (in.)

## Slide 8: Design Breakdown: Steering
Team No.22
Slide 8 of 25
Kyle Anderson
Final Presentation
Steering:
Rack and pinion straight axle set up
Curb to curb < 45ft
Brass bushings used for smooth rotation

## Slide 9: Design Breakdown: Steering
Team No.22
Slide 9 of 25
Kyle Anderson
Final Presentation
Steering:
Rack and pinion straight axle set up
Curb to curb < 45ft
Brass bushings used for smooth rotation

## Slide 10: Design Breakdown: Drivetrain
Team No.22
Slide 10 of 25
Stephen Avery
Final Presentation
Specifications:
Dual Driveshaft to Manual Transaxle Design
            6 forward speeds + Reverse
            Individually supported axle shafts
Industrial Chain Drive
CAD render of rear axle
CAD render dual shaft design mounted on pillow blocks

## Slide 11: Design Breakdown: Drivetrain
Team No.22
Slide 11 of 25
Stephen Avery
Final Presentation
Freewheeled driveshaft allow for individual cadence and no back drivability
Dual drive shaft design eliminates chain crossing
Reduces shaft torque by dividing over two
Freewheel sprocket mounted onto shaft
Dual shaft design mounted on pillow blocks

## Slide 12: Design Breakdown: Electronics
Team No.22
Slide 12 of 25
Stephen Avery
Final Presentation
Primary Control Panel:
Modular Lighting
Remote Charging
Fuse Block with Additional “Hot” Slots
Keyed Battery Shutoff
Driver’s Control Panel:
Voltage Meter
Hazard Lights
Turn signals

## Slide 13: Progress: Pedaling Ergonomics
Team No.22
Slide 13 of 25
Alejandro San Segundo
Final Presentation
Pedaling:
Recumbent stance
Relaxed knee max knee bend angle (<70)
Freewheeled shaft design for coasting
Hibrid recumbent riding stance
Cranks and pedal mounted onto frame
Fully recumbent riding stance

## Slide 14: Progress: Towing Platform
Team No.22
Slide 14 of 25
Kyle Anderson
Final Presentation
Towing:
Torsion Axle implementation
            Electric drum brakes on towing axle
Standard towing hitch mount
Torsion Tow Axle
Towing axle assembly

## Slide 15: Design Breakdown: Woodwork
Team No.22
Slide 15 of 25
Kyle Anderson
Final Presentation
Bartop:
Pressure treated wood top
Coated for Weather protection
Added handrail for rider stability
Bench Seating Arrangement:
Room for non-pedaling passengers
Semi-Recumbent Riding stance
Finished and mounted bar top
Finished and mounted benches

## Slide 16: Design Breakdown: Wheels and Brakes
Team No.22
Slide 16 of 25
Stephen Avery
Final Presentation
Axle | Brakes | Wheels | Tires | Bolt Patterns
Rolling Front | 10” Hydraulic Disc | 16” | Same | 5 on 4.5”
Rolling Rear | 8” Hydraulic Disc |  |  | 
Towing | 10” Electric Drum |  |  | 
Break pedal assembly
Electric drum brakes
Front disk brakes
Mounted wheel assembly

## Slide 17: Design Breakdown: Roof Awning
Team No.22
Slide 17 of 25
Kyle Anderson
Final Presentation
Made by Capital awning Co.
Made of galvanized steel for strength and price
Finished roof assembly
CAD render of roof assembly

## Slide 18: Vehicle Testing
Team No.22
Slide 18 of 25
Alejandro San Segundo
Final Presentation
Performance Test | Result
Pedaling performance (movable by single rider) | Pass
Max speed cadence comfort and vehicle reaction | Pass
Hill Climb (8ᵒ grade climb with 10 passengers) | Pass*
Steering testing (ease of steering/curb-to-curb < 45ft) | Pass
Breaking (max speed to full stop < 25ft) | Pass
*Manufacturing mistake caused failure. Has since been repaired.
The proud team captain aboard his ship

## Slide 19: Procurement
Team No.22
Slide 19 of 25
Brett Willenbacher
Final Presentation
All components, including:
  Fabrication materials
  Drivetrain components
Towing components
Bicycle components
Steering components
Driving/Operation components
Have been purchased and received.
Total Spent: $13,550
Total spent as of 4/16/15
Chart: Pedibus 2.0 Cost Breakdown
| Steel | Misc. Materials | Misc. Parts | Transaxle, Brakes & Wheels | Roof | Bar Top
Steel Misc. Materials Misc. Parts Transaxle, Brakes & Wheels Roof Bar Top | 1155.47 | 1046.27 | 4035.78 | 1397.68 | 2945.5 | 472.5

## Slide 20: Timeline
Team No.22
Slide 20 of 25
Brett Willenbacher
Final Presentation
**Finished on Time

## Slide 21: Project Issues
Team No.22
Slide 21 of 25
Stephen Avery
Final Presentation
Problem | Solution
Rear Axle Key Shear Due to Manufacturing Error. | Replace and Re-machine Right Rear Axle
Lack of Emergency Brake | Automotive Parking Brake on Right Rear Axle
Noisy Floorboards | Insulate Panel Edges/Replace Fasteners
Drivetrain Slip | Replace Belt Drive with Chain Drive
Incorrect Final Gear Ratio | Change Lower Sprocket
Frame Over Legal Width | Cut and Lower Bench Seat Back
Insufficient Bar Top to Knee Clearance | Add Spacers to Bar Top Mounts
Poor Driveshaft Component Fit | Replace Driveshafts with Cold Rolled Steel

## Slide 22: Future Considerations
Team No.22
Slide 22 of 25
Kyle Anderson
Final Presentation
Post Build Suggestions:
Rear Bench
Finish Towing Provisions
Noise Insulation
Paint
Bar Walls
Drink Troughs
Additional Electronics
Fit and Finish

## Slide 23: Project Take-Away
Team No.22
Slide 23 of 25
Stephen Avery
Final Presentation
What was Learned:
Evaluate Man-Power vs. Work Load
Define Technical Requirements
Provide Sufficient Analysis of All Components
Team Communication and Delegation
Customer Involvement
Assign Importance and Priority to Tasks
Sufficient Testing Prior to Implementation

## Slide 24: Summary
Team No.22
Slide 24 of 25
Brett Willenbacher
Final Presentation

## Slide 25
Team No.22
Slide 25 of 25
Brett Willenbacher
Final Presentation
Questions?