## Slide 1: Electronic Synthetic Aperture Radar Imager
Team E#11/M#27 – Milestone #7
Spring 2015 – Final Senior Design Presentation

## Slide 2: Team Agenda
Team Roles & Responsibilities
Project Overview
Electrical System
Power Supply Design
Programming Overview
Signal Processing
Mechanical Analysis
Project Management
Conclusion
Closing Questions

## Slide 3: The Team Structure
Engineer | Jasmine Vanderhorst | Benjamin Mock | Joshua Cushion | Matthew Cammuse | Patrick De la llana | Julia Kim | Malcolm Harmon | Mark Poindexter
Field of Study | Industrial Engineering | Industrial Engineering | Electrical Engineering | Electrical Engineering | Electrical Engineering | Electrical Engineering | Mechanical Engineering | Mechanical Engineering
Tasks | Project Management Team Web Master Technical Writing & Formatting Presentations & Posters | Lead IE & Treasurer Procurement Budget Allocation Safety Analysis Risk Analysis | Lead EE & Radio Frequency Engineer Electrical System Design Testing Strategy & Application | Assistant Project Manager & Co-Lead EE Antenna Array Design Power System Wiring | Co-Lead EE FPGA Programming Timing, Switches, and A-to-D Conversion Coding System Timing | Co-Lead EE & Recording Secretary Signal Processing Image Calibration | Assistant Project Manager Vendor Relations Antenna Frame Design Material Analysis User Manual | Co-Lead ME Vendor Relations Component Box Design Cabling Design Heat Transfer Analysis User Manual

## Slide 4: Project Introduction & Goals
SAR Introduction
What is an SAR?
Synthetic Aperture Radar: Typically, a single rotating antenna is attached to an aircraft flying over a target zone capturing several high resolution images to create a single image map.
Why is an SAR needed?
Typical Use: Environmental Monitoring, Earth-Resource Mapping, and Military Applications
Project Goal
What is the project goal?
To develop a “static, multi-antenna Synthetic Aperture RADAR (SAR) imager”
Project Theory: 20 stationary antennas, creating a single low resolution image for the purpose of detecting metal objects and weapons
How will this type of RADAR be used?
Typical Use: Government Buildings, Schools, Airports, & various other homeland security applications

## Slide 5: Project Overview
Radar Imager Project Scope Matthew Cammuse – Electrical Engineer

## Slide 6: Performance Characteristics
Requirement | Units | Value | Comments
Frequency | GHz | 10.0 +/- 0.1 GHz | Single frequency operation. BW supports 1/PW
Range to scene to be imaged | feet | 20 | 20 foot radius from center of antenna aperture
Scene extent | inches | 40 x 40 | The area to be imaged
Cross range resolution | inches | 2.5 | 1-D in Azimuth and Elevation
Down range resolution | inches | N/A | A future enhancement to performance
Tx Pulse Width (PW) | nS | 20 | 
Transmit Power | W | 0.2 | 
Antenna aperture size | feet | 5 x 5 | Waveguide horns in cross configuration
Pulse Repetition Interval | nS | 100 | 
Receiver Noise Figure | dB | 3 | Does not include front end losses
Image Time | mS | 0.5 | Time to collect 1 set of image data

## Slide 7: Imaging Radar Operational Concept
40 x 40 inch scene
20 [ft] range to scene center
16 - 2.5 inch
1-D Cells in
Azimuth and
Elevation
5 x 5 feet
20nS wide RF
Pulse @ 10 GHz
X-Band Horn (17 dBi)
Antenna Array
Pulsed Transmit/Receive
Imaging Radar
Static parts
COTS components
Digital beam forming
Beams are formed
Digitally with Fourier
Transform, 16 in Azimuth
And 16 in Elevation
PC Display
VGA Connection
16 - Azimuth
16 - Elevation
Antenna Spacing
Tx-Rx –
Rx-Rx –

## Slide 8: Electrical System
Major Electrical Components & Designs Matthew Cammuse – Electrical Engineer
Joshua Cushion – Electrical Engineer

## Slide 9: Electrical System Overview

## Slide 10: Transmit Signal Chain Role
Role:
Generate radio frequency sinusoidal waveform
  Target operating frequency: 10 GHz (X Band)
  Maximum Power: 10 W/m2 = 1 mW/cm2 (FCC Regulations)
  Power in 10322 cm2 (40 in2) Scene Extent = 0.008 mW/cm2
Key Components:
Voltage Controlled Oscillator
Power Amplifier
Frequency Multiplier
Signal Attenuators
SPDT Switch
SP4T Switch
Transmit Antennas

## Slide 11: Transmit Signal Chain – Power
Component | Input Power |  | Output Power |  | Frequency
 | [dBm] | [mW] | [dBm] | [mW] | [GHz]
Voltage Controlled Oscillator (VCO) | 0.000 | 1 | -4.000 | 0.398 | 5
Super Ultra Wideband Amplifier | -4.196 | 0.381 | 21.804 | 151.501 | 5
Single Pole Double Throw (SPDT) Switch | 21.530 | 142.233 | 19.530 | 89.743 | 5
Fixed Attenuator | 19.413 | 87.347 | 9.413 | 8.735 | 5
Frequency Multiplier | 9.413 | 8.735 | -3.088 | 0.491 | 10
Ultra Wide Bandwidth Amplifier | -3.088 | 0.491 | 8.913 | 7.785 | 10
Variable Attenuator | 8.795 | 7.577 | -3.205 | 0.478 | 10
Band Pass Filter | -3.323 | 0.465 | -6.323 | 0.233 | 10
Power Amplifier | -6.518 | 0.223 | 25.482 | 353.319 | 10
Single Pole Four Throw (SP4T) Switch | 25.482 | 353.319 | 22.482 | 177.079 | 10

## Slide 12: Transmit Signal Chain – Test Strategies
Measure and verify each at the output of SP4T switch:
Peak Signal Power
  42dB (attenuation) – 22.92 dBm = 21.804 dBm
Average Signal Power
  Attenuation – measured power/span – 10*log (duty cycle)
    17.749 dBm and 16.839 dBm
Pulse Width = 20nS
  Null Frequency = 50 MHz
  1/null frequency
Period (T) = 65nS
  Frequency = 15.38 GHz
  1/T

## Slide 13: Design Changes – Transmit Signal Chain
VCO:
Role:
  Generate a signal of -4dBm and 5 GHz
Problem:
  Max frequency of signal: 4.631 GHz
  Once multiplied by 2 (9.262 GHz), does not meet minimum passband of BPF (9.75 GHz)
Alternative:
  Used an RF signal generator
  Output signal:
    Power: -4dBm
    Frequency: 5 GHz
Band Pass Filter Performance

## Slide 14: Design Changes – Transmit Signal Chain
FPGA to SPDT Switch:
Role:
  Generate a 20nS pulse with period of 60nS for SPDT switch
Problem:
  PMOD connectors provide low fidelity 20nS pulse
  VHDCI connector provides the correct signal
    Pins too small to solder to
Alternative:
  Use an signal generator until VHDCI breakout board is delivered
VHDCI Breakout Board

## Slide 15: Receive Signal Chain Role
Role:
Receive the reflected radio frequency signal scatterings from target
Convert the received RF signals into digital voltages
Key Components:
Receive Antennas
SP16T Switch
Signal Attenuator
Low Noise Amplifier
IQ Demodulator
Four Analog to Digital Converters

## Slide 16: Receive Signal Chain – Power
Component | Input Power |  | Output Power |  | Frequency
 | [dBm] | [mW] | [dBm] | [mW] | [GHz]
Single Pole Sixteen Throw (SP16T) Switch | -53.251 | 4.731E-06 | -57.951 | 1.603E-06 | 10
Band Pass Filter | -58.068 | 1.560E-06 | -61.068 | 7.820E-07 | 10
Low Noise Amplifier (LNA-SLNA-120-38-22-SMA) | -61.068 | 7.820E-07 | -23.068 | 4.934E-03 | 10
Variable Attenuator (SA4077) | -23.342 | 4.632E-03 | -37.342 | 1.844E-04 | 10
Low Noise Amplifier (LNA-SLNA-180-38-25-SMA) | -37.460 | 1.795E-04 | 0.540 | 1.132 | 10
Radio Frequency (RF) IQ Demodulator | 0.070 | 1.016E+00 | -6.930 | 0.203 | 10

## Slide 17: Receive Signal Chain – Test Strategies
Measure power and frequency of signal input into RF channel of IQ demodulator
Measure the output voltage from the I and Q channels of IQ demodulator as the corner reflector moves within the scene extent

## Slide 18: Design Changes – Receive Signal Chain
Level Shift Circuit:
Role:
  Shift the voltage range from IQ demodulator from ±100mV to 0 - 200mV
  Allows the 2 ADCs to sample negative I and Q voltages once shifted
Alternative:
  Sampled I, I’, Q, Q’ channels from IQ demodulator
  Used 4 ADCs and updated software to only sample the positive I and Q voltages
Before
LO
RF
IQ Demodulator
Q
Q’
I
I’
FPGA Demo Board
Level Shift Circuit
ADC
ADC
After
FPGA Demo Board
LO
RF
IQ Demodulator
Q
Q’
I
I’
ADC
ADC
ADC
ADC

## Slide 19: IQ Demodulator (LO) Chain – Power
Component | Input Power |  | Output Power |  | Frequency
 | [dBm] | [mW] | [dBm] | [mW] | [GHz]
Voltage Controlled Oscillator (VCO) | 0.000 | 1.000 | -4.000 | 0.398 | 5
Super Ultra Wideband Amplifier | -4.196 | 0.381 | 21.804 | 151.501 | 5
Single Pole Double Throw (SPDT) Switch | 21.530 | 142.233 | 19.530 | 89.743 | 5
Fixed Attenuator | 19.413 | 87.347 | 9.413 | 8.735 | 5
Frequency Multiplier | 9.217 | 8.350 | -3.283 | 0.470 | 10
Ultra Wide Bandwidth Amplifier | -3.283 | 0.470 | 8.717 | 7.442 | 10
Fixed Attenuator | 8.599 | 7.243 | 5.599 | 3.630 | 10
LO (IQ Demodulator) | 5.129 | 3.258 | - | - | 10

## Slide 20: IQ Demodulator LO Signal Chain-Test Strategies
Measure and verify each at the input of LO channel:
Peak Signal Power
  42dB (attenuation) – 37.262 dBm = 4.738 dBm
Average Signal Power
  Attenuation – measured power/span – 10*log (duty cycle)
    4.629 dBm and 4.819 dBm
Period (T) = 65nS
  Frequency = 15.38 GHz
  1/T
Pulse Width = 40nS
  Null Frequency = 50 MHz
  1/null frequency

## Slide 21: Power Supply
Power Overview
Matthew Cammuse– Electrical Engineer

## Slide 22: Black Box Power Supply
QTY | Part Name | V+(V) | I+ (mA) | V-(V) | I-(mA)
1 | VCO | 5 | 45 | - | -
1 | SPDT Switch | 5 | 1.4 | - | -
1 | SP4T Switch | 5 | 160 | -5 | 50
1 | SP16T Switch | 5 | 550(max) | -12 | 200(max)
1 | IQ Demodulator | 5 | 110 | -5 | -
1 | Super Ultra Wideband Amplifier | 12 | 400(max) | - | -
2 | Ultra Wide Bandwidth Amplifier | 12 | 62(typ) 68(max) | - | -
1 | Low Noise Amplifier SLNA-120-38-22-SMA | 12 | 250 | - | -
1 | Low Noise Amplifier SLNA-180-38-25-SMA | 12 | 250(min) 280(typ) 320(max) | - | -
1 | Power Amplifier | 15 | 900(typ) 1100(max) | - | -
1 | FPGA Board | USB Powered |  |  | 
Black Box Power Supply
19 [V] Input
ON-OFF Switch

## Slide 23: Power Supply Block Diagram
Electrical Wiring
Positive Voltage – Red wire
Negative Voltage – White wire
Ground – Black
Twisted Pairings
Regulators

## Slide 24: Voltage Regulators
Positive Voltage (+V)
Negative Voltage (-V)
Linear Technology: LTC4008 Battery Charger
Output voltage based on R7 and R12 resistors
Pi filter
Digikey: DC-DC Converter
Output voltage based on controlled resistor
Voltage [V] | Resistor | [Ω]
+5 | R7 | 154k
 | R12 | 47.5k
+12 | R7 | 100k
 | R12 | 11.0k
+15 | R7 | 130k
 | R12 | 11.0k
Voltage [V] | (RSET) [Ω]
-5 | 2k
-12 | 28.8k

## Slide 25: Programming Overview
Major Coding Sequences
Patrick Delallana – Electrical & Computer Engineer

## Slide 26: Software Design Summary
Tasks
  Splitting up of programming tasks into major priorities
Purpose
  Purpose and description of each task
Testing
  Methods that were used to test the software for each task
Results
  System demonstration results for each task
Status
  Status with regards to completion of project

## Slide 27: Task 1: System Timing
Description
  Controls the SPDT, SP4T, and SP16T switch
  Outputs pulse that transmits to the target
Explanation
  20 nS pulse to transmit to target
  SPDT same timing as pulse, logic 1 on, logic 0 off
  SP4T has logic 0 being on, logic 1 being off
  SP16T has logic 0 being on, logic 1 being off

## Slide 28: Task 1: System Timing
Testing
  Code was tested using an oscilloscope to check for correct outputs.
  Switches on FPGA were used to change the different combinations for transmit receive.
Results
  System timing code was able to control the switches for the system. The demonstration for this code was successful.
Status
  This code is complete, and needs no further work.

## Slide 29: Task 2: Analog to Digital Conversion Code
Purpose
  Converts analog voltage ranging from 0 to 3.3 volts into digital binary combination that is stored onto the FPGA.
  Converts four signals I, Ibar, Q, Qbar from IQ demodulator.
  Result is a 12 bit binary combination.
Explanation
  Two states were used, idle and read.
  When idle, a signal was output showing A/D was not reading
  When read, a signal was output showing A/D was reading and a counter was used to check how many bits were being used and how many were left.

## Slide 30: Task 2: Analog to Digital Conversion Code
Testing
  DC power supply was used as test for input voltage
  7 segment display was used to read voltages in hex.
  Pushbuttons were used to display different voltages from IQ demodulator.
Results
  Analog to Digital Conversion code was able to convert and display the different voltages from the IQ demodulator in the system demonstration.
Status
  This code is complete, and needs no further work.

## Slide 31: Task 3: VGA Code
Description
  Perform the basis functions for angles, and break down into real and imaginary parts
  Gives amplitude and phase corresponding to each angle
  Parse the display into columns of 16, with each column representing an angle
  Performs the fast Fourier transform of the incoming energy
Explanation
  HSYNC (horizontal) and VSYNC (vertical ) counters to label where pixels light up
  Lookup table for sine and cosine values of different angles

## Slide 32: Task 3: VGA Code
Testing
  Code was tested by checking to see if varying input voltage from DC power supply would light up the VGA display depending on amplitude.
  Code was checked in CAPS to see if signal reflected off corner reflector would light up VGA display
Results
  Input signal from the IQ demodulator was able to light up the VGA display depending on amplitude of signal. This would only let you know something is reflecting, not where it is.

## Slide 33: Task 3: VGA Code - Steps
Completed Steps
  Pixel illumination
  Lookup table
Steps that need to be taken to ensure completion
  Parse the lighting up of pixels into 16 columns
  Write basis functions in VHDL
  Complex multiplication of results of basis functions in VHDL

## Slide 34: Signal Overview
Signal Processing Julia Kim – Electrical Engineer

## Slide 35: Signal Processing
Sixteen Phase Centers from each Tx/Rx Pair to Scene
Variable d is distance between phase centers
θ is the angle from a line with origin at center of array that is 90° to antenna ray to a line from origin at the center of the array to a point elsewhere in the scene
represents the 16 θs that go to 16 points in the scene

## Slide 36: Signal Processing – Basis Functions
For image formation, the sum of the energy from some of the scatterers is taken and they are decomposed by multiplying them by the basis functions.
The basis function represents the energy that will come in from a different angle, so if it is multiplied by the total energy, it decomposes it into just that part.
Chart: Basis Functions
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
f(θ1) | -2.9487 | -5.8974 | -8.8462 | -11.7949 | -14.7436 | -17.6923 | -20.641 | -23.5898 | -26.5385 | -29.4872 | -32.4359 | -35.3846 | -38.3334 | -41.2821 | -44.2308 | -47.1795
f(θ2) | -2.5582 | -5.1164 | -7.6745 | -10.2327 | -12.7909 | -15.3491 | -17.9072 | -20.4654 | -23.0236 | -25.5818 | -28.14 | -30.6981 | -33.2563 | -35.8145 | -38.3727 | -40.9309
f(θ3) | -2.1665 | -4.333 | -6.4995 | -8.6661 | -10.8326 | -12.9991 | -15.1656 | -17.3321 | -19.4986 | -21.6651 | -23.8317 | -25.9982 | -28.1647 | -30.3312 | -32.4977 | -34.6642
f(θ4) | -1.7739 | -3.5478 | -5.3217 | -7.0956 | -8.8695 | -10.6434 | -12.4173 | -14.1912 | -15.9651 | -17.739 | -19.5129 | -21.2868 | -23.0607 | -24.8346 | -26.6085 | -28.3824
f(θ5) | -1.3805 | -2.761 | -4.1415 | -5.522 | -6.9025 | -8.283 | -9.6636 | -11.0441 | -12.4246 | -13.8051 | -15.1856 | -16.5661 | -17.9466 | -19.3271 | -20.7076 | -22.0881
f(θ6) | -0.98651 | -1.973 | -2.9595 | -3.946 | -4.9325 | -5.9191 | -6.9056 | -7.8921 | -8.8786 | -9.8651 | -10.8516 | -11.8381 | -12.8246 | -13.8111 | -14.7976 | -15.7842
f(θ7) | -0.59208 | -1.1842 | -1.7762 | -2.3683 | -2.9604 | -3.5525 | -4.1446 | -4.7366 | -5.3287 | -5.9208 | -6.5129 | -7.1049 | -7.697 | -8.2891 | -8.8812 | -9.4733
f(θ8) | -0.19739 | -0.39478 | -0.59217 | -0.78955 | -0.98694 | -1.1843 | -1.3817 | -1.5791 | -1.7765 | -1.9739 | -2.1713 | -2.3687 | -2.5661 | -2.7634 | -2.9608 | -3.1582
f(θ9) | 0.19739 | 0.39478 | 0.59217 | 0.78955 | 0.98694 | 1.1843 | 1.3817 | 1.5791 | 1.7765 | 1.9739 | 2.1713 | 2.3687 | 2.5661 | 2.7634 | 2.9608 | 3.1582
f(θ10) | 0.59208 | 1.1842 | 1.7762 | 2.3683 | 2.9604 | 3.5525 | 4.1446 | 4.7366 | 5.3287 | 5.9208 | 6.5129 | 7.1049 | 7.697 | 8.2891 | 8.8812 | 9.4733
f(θ11) | 0.98651 | 1.973 | 2.9595 | 3.946 | 4.9325 | 5.9191 | 6.9056 | 7.8921 | 8.8786 | 9.8651 | 10.8516 | 11.8381 | 12.8246 | 13.8111 | 14.7976 | 15.7842
f(θ12) | 1.3805 | 2.761 | 4.1415 | 5.522 | 6.9025 | 8.283 | 9.6636 | 11.0441 | 12.4246 | 13.8051 | 15.1856 | 16.5661 | 17.9466 | 19.3271 | 20.7076 | 22.0881

## Slide 37: Signal Processing End Goal
Fourier transform is used to decompose the waveform into the amounts of energy that come in from different angles.
Basically a 1-D image that tells the user where the energy is coming in from different angles in the scene
Chart: Amplitude vs Angle
| -9 | -7.8 | -6.6 | -5.3999999999999995 | -4.1999999999999993 | -2.9999999999999991 | -1.7999999999999992 | -0.5999999999999992 | 0.60000000000000075 | 1.8000000000000007 | 3.0000000000000009 | 4.2000000000000011 | 5.4000000000000012 | 6.6000000000000014 | 7.8000000000000016 | 9.0000000000000018
 | 23.9779 | 0.55059 | -9.3086 | 23.9378 | -10.2584 | -10.6046 | -12.5153 | 24.1211 | -14.0733 | -14.586 | -14.8213 | -15.7154 | 24.1322 | -16.9156 | -10.0392 | -7.712

## Slide 38: Mechanical Overview
Mark Poindexter – Mechanical Engineer Malcolm Harmon – Mechanical Engineer

## Slide 39
Scale: 1(Low) – 5 (High) (Constructability) | Design 1 | Design 2
Electrical Components | 4 | 3
Structure Mounting | 3 | 3
Prior Design
Analysis
Scale: 1(Low) – 5(High) (Horn Alignment) |  | 
Phase Centers | 5 | 3
Horn Adjustability | 4 | 4

## Slide 40: Restructured Body Design
Horn Placement Component Box | Horn Shield Back Plate Cover

## Slide 41: Antenna Structure Design
Component Box
Part # | Part Name
SAR - 1 | Comp. Box Lid
SAR - 2 | Comp. Box
SAR - 3 | Channel To Stand
SAR - 4 | Stand
SAR - 5 | Channel Connector
SAR - 6 | Vertical Horn Cover
SAR - 7 | Left Horn Cover
SAR - 8 | Right Horn Cover
SAR - 9 | Quadrant Panel

## Slide 42: Component Box
Rotated Lid for easy access to Components
Manually mounted on structure for most convenient placement

## Slide 43: Heat Analysis – Component Box
Power Supplied: 34.8 W
Box Surface Area: 12.7 ft2
Heat Flux: 2.7 W/ft2
Temperature Rise: 13.5 2.8

## Slide 44: Antenna Structure Design
Horn Covers
Part # | Part Name
SAR - 1 | Comp. Box Lid
SAR - 2 | Comp. Box
SAR - 3 | Channel To Stand
SAR - 4 | Stand
SAR - 5 | Channel Connector
SAR - 6 | Vertical Horn Cover
SAR - 7 | Left Horn Cover
SAR - 8 | Right Horn Cover
SAR - 9 | Quadrant Panel

## Slide 45: Antenna Structure Design
Structure Frame and Stand
Part # | Part Name
SAR - 1 | Comp. Box Lid
SAR - 2 | Comp. Box
SAR - 3 | Channel To Stand
SAR - 4 | Stand
SAR - 5 | Channel Connector
SAR - 6 | Vertical Horn Cover
SAR - 7 | Left Horn Cover
SAR - 8 | Right Horn Cover
SAR - 9 | Quadrant Panel

## Slide 46: Final Antenna Structure

## Slide 47
Stress Analysis - Antenna Structure
DRAMATIZED MAX DISPLACEMENT IN INCHES
Max Displacement
1.1x10-6 in
Quadrant Panel
Max Dis.
9.0x10-7 in
Horn Covers
Stand to Structure Connector
Max Displacement 8.1x10-7 in
Stand
Max Displacement
5.5x10-5 in

## Slide 48: Horn Holders
Nut threaded rods to compress horn holders
Rotate about threaded rods axis for alignment
Threaded rod welded to horn holders

## Slide 49: Trihedral
Triangular planes are joined together to form a triangular pocket to receive and reflect waves

## Slide 50: Results – Horn Alignment

## Slide 51: Project Management
Budget Assessment, Bill of Materials, Schedule
Benjamin Mock – Industrial Engineer
Jasmine Vanderhorst – Industrial Engineer

## Slide 52: Resource Allocation
Initial Projection
Northrop Grumman sponsored up to $50,000
Projected $38,000 expense
Left a $12,000 buffer
Final Evaluation
Chart: SAR Imager Budget
| Electrical Components | Test Equipment | Mechanical/Misc | Remaining
 | 31730.83 | 7070.95 | 3728.6465 | 7472.0635

## Slide 53: Project Flow – Parallel Schedule

## Slide 54: Project Schedule
Fall 2014
Designed RF Electrical System
Antenna Design & Analysis
Mechanical Structure Design & Analysis
Performed Component Analysis
Procurement Process Initiated
Spring 2015 – Post Midterm Hardware Demonstration
Signal Power Levels & Pulse Quality Testing & Verification
  Transmit Chain 3/23
  LO IQ Demodulator 3/23
  Receive 3/27
Test Timing Switches
  SPDT & SP4T – 3/25
  SP16T – delivered 3/27; tested 3/29
A-to-D Converter Test – 3/27

## Slide 55: Project Schedule
Spring 2015
IQ Demodulator output correct voltages for I & Q channels – 3/31
Verify FPGA Code performs A/D Conversion of I, I’, Q, and Q’ – 4/1
Single Antenna detects a returned pulse from Transmit Chain – 4/2
Major Milestones
  NG Sponsor Visit – 4/1 – 4/3
  Assemble Mechanical Structure – 4/1
  Correctly Transmit RF Pulse at 20 foot distance – 4/2
  Integrate Electrical System – 4/3
    4 Transmit, 16 Receive, Assembled Component Box, Power Supply
  Test & Calibrate SAR System – 4/3
  Successfully Demonstrate Full System Setup – 4/9

## Slide 56: Future Recommendations

## Slide 57: Project Conclusion
Completion Status and Conclusion
Jasmine Vanderhorst – Industrial Engineer

## Slide 58: Project Completion Status
Electrical Component Design
  Percent Complete: 100%
Signal Processing Calculations
  Percent Complete: 100%
Programming
  Percent Complete: 75%
  Needed: VHDL Code for Signal Processing Functions
Structural Design
  Percent Complete: 100%

## Slide 59: Conclusion
Transmit/receive path was achieved
  Measured results from testing were close to theoretical results
Pulses were coded and implemented effectively for transmit and receive
  Output voltages from IQ demodulator were obtained successfully and displayed
Efficient power supply box was designed and set up
Theoretical calculations for signal processing were realized
Structure for antennas and component box were manufactured
  Heat and stress analyses were realized for structure

## Slide 60: Final Product

## Slide 61: Thank You!
Questions & Comments