## Slide 1: Electronic Synthetic Aperture Radar Imager
Team E#11/M#27 - Milestone #2
Project Proposal and Statement of Work

## Slide 2: Agenda
Project Overview
Team Qualifications
System Breakdown
  Electrical System
    Power Supply & Distribution
    FPGA Programming
  Antenna Design
  Mechanical Design
Detailed Schedule
Detailed Budget
Detailed Risk Assessment

## Slide 3: Project Overview
Signal Processing Engineer – Julia Kim
Electrical Engineering

## Slide 4: Problem Statement
Problem: To create a physical schematic of a radar system with SAR theory using commercial-off-the-shelf (COTS) components.
Theoretically, an SAR Imager requires a mobile transmission and receiving antenna to capture a greater range and/or clearer image of what is being targeted.

## Slide 5: SAR Imager
SAR carried by the Sandia Twin Otter aircraft.
Data is collected at ranges of 2 – 15 km.

## Slide 6: Problem Statement
Solution: Team will use multiple stationary antennas that transmit and receive signals.
  ECE will design a stationary schematic of a radar system with 20 antennas.
  ME will design the physical structure for the antennas and the associated horns that go with them.
  IE will manage human factors, risk analysis, project schedule, and overall budget.

## Slide 7: Intended Use and Users
Intended Use: Theoretical implementation and testing.
  Primary use: Check for the transmission and receiving of pulse by the antennas.
Intended Users: Student members of the team.
  As a research project, it is intended to be an operating physical schematic of the project.

## Slide 8: Team Qualifications
Project Manager: Jasmine Vanderhorst
Industrial Engineer

## Slide 9: Team Qualifications
Project Manager (PM) – Jasmine Vanderhorst (IE)
  Courses: Eng. Management, Business Ethics, Industrial Tools
  Experience: 4 Internships – program & project management
Asst. (PM) & Antenna Engineer – Matthew Cammuse (EE)
  Courses: Electromagnetic Fields I & II, Digital Comm., Digital Logic, Microprocessors, Circuits I & II
  Experience: NSWCDD Internship - Electromagnetic and Radio Frequency Department

## Slide 10: Team Qualifications (cont’d.)
Asst PM & Antenna Structure – Malcolm Harmon (ME)
  Courses: Mechanics & Materials, 3 year Certification in AutoCAD
  Experience: 3-Dimensional Software Experience, Building Manager
Lead Engineer & Programmer – Patrick De la Llana (ECE)
  Courses: Digital Logic, Data Structures, Control Systems, Digital Communications, and Microprocessors
  Experience: CAPS (Center for Advanced Power Systems) research

## Slide 11: Team Qualifications (cont’d.)
Co-Lead Industrial Engineer & Treasurer– Benjamin Mock (IE)
  Courses: Manuf. Process, Engineering Materials, Engineering Management, Human Factors, and Ergonomics
  Experience: Treasurer of 2 organizations, Southeast District Parliamentarian for 1 organization, time management, risk forecasting, and technical writing.
Co-Lead Electrical & RF Engineer – Joshua Cushion (EE)
  Courses: Electronics I & II Labs, Power Electronics
  Experience: 3 Internships – Digital & Analog Circuit Design & Analysis

## Slide 12: Team Qualifications (cont’d.)
Signal Processing Engineer & Document Control – Julia Kim (EE)
  Courses: Power Electronics, Fundamentals of Power Systems, and Power Systems I, Signals & Systems
  Experience: Lab work in Advanced Circuits and Electronics
Co-Lead Mechanical Engineer & Antenna Structure – Mark Poindexter (ME)
  Courses: ME Tools & Lab, Mechanical Systems I & II, and Dynamic Systems II
  Experience: designing with Pro E Software, work with small & large machines and automotive repairs

## Slide 13: System Breakdown
RF Engineer: Joshua Cushion
Electrical Engineering

## Slide 14: Project Subsystems
Electrical System
  Radio Frequency Circuit Components
  Power Supply Printed Circuit Board (PCB)
  Field Programmable Gate Array (FPGA) Board
Antenna Design
Mechanical Structure

## Slide 15: Electrical System
RF Engineer: Joshua Cushion
Electrical Engineering

## Slide 16: Block Diagram – Simple Model
Joshua Cushion
Simple Model

## Slide 17: Block Diagram – Advanced Model
Joshua Cushion
Advanced Model

## Slide 18: Concept Generation – Electrical System
Advanced Model
Advantages :
  Does not include test equipment
  Image processing is done while system is running
Disadvantages:
  Heavy dependence on the FPGA
    More FPGA programming tasks
  High risk of timing issues
Simple Model
Advantages :
  Very little dependence on the FPGA
    Less FPGA programming tasks
  More reliable switching time for switches
Disadvantages:
  Requires test equipment
    Oscilloscope
    Waveform generator
  Image processing is done after a complete cycle

## Slide 19: Major Circuit Components
Voltage Controlled Oscillator (VCO)
  Creates the high frequency transmit signal
  Specifications:
    Operating frequency: 5 – 10 GHz
    Output power: +20 dBm
    Input Voltage: 8 - 15 V
IQ Demodulator
  Represents the phase and amplitude
  of the RF input as a output voltage
  Specifications
    LO/RF frequency: 6 – 10 GHz
    DC offset: (-8) – (+8) mV
    Input voltage: ±5 V
IQ Demodulator:AD60100B
VCO: HMC-C029

## Slide 20: Major Circuit Components
Switches
  Single Pole Double Throw (SPDT)
  Single Pole Four Throw (SP4T)
  Single Pole 16 Throw (SP16T)
Specifications
  Operating frequency
  Switching times
  Output power
  Supply Voltage
SP4T: HMC-C071
SP16T: SWL01016S
SPDT: HMC-C058

## Slide 21: Major Task: Radar Range Equation Parameters
Radar Range Equation
Radar’s ability to detect a target at a certain range from the radar
Determine the signal power and noise power

## Slide 22: Signal to Noise Ratio
Signal Power
S =
Peak Transmit Power (Pt)
Transmit Path Gain (G)
  Calculate for entire chain
Effective Area of Receive Antenna
Noise Power
N = kTSBn
Cascaded model of TX and RX paths
System Noise Temperature (TS)
  TS = T1 + + +…
Gain (G) /Loss (L)
  Check component datasheets

## Slide 23: Power Supply and Distribution
Signal Processing Engineer – Julia Kim
Electrical Engineering

## Slide 24: Concept Generation
Goal: To efficiently supply and distribute power to the components in the electrical system
One main power supply input
Options:
  Solder less bread board with Through-Hole Technology (THT) components
  Design a printed circuit board (PCB) with soldered components

## Slide 25: Proposed Design
Printed Circuit Board (PCB)
Requirements
  Accept input from a main power supply
  13 output connections, one for each component
  Supply the required input voltage and current for each component
  Operate within the specified temperature range for each component

## Slide 26: Statement of Work
Tasks:
  Gather info for each component:
    Max, min, typical
      Input voltage
      Input current
      Input power
      Operating temperatures

## Slide 27: FPGA Programming
Lead Programmer: Patrick de la Llana
Electrical & Computer Engineering

## Slide 28: Concept Generation & Selection: FPGA
Digilent Nexys 3
  Newer version of Nexys 2
Specifications:
  USB port
  8-bit VGA Display
  100MHz clock
  Pmod capability

## Slide 29: FPGA: Needs & Wants
100 MHz clock
  Switching edge needs to be 10ns
Pmod Capability
  For the purpose of plug in A/D and D/A converters.
USB port
  Desired for simplicity.
VGA port
  VGA display of image.

## Slide 30: Tasks of FPGA
Generate Signal
Control Timing
  SPDT - Transmit and Receive Modes
  SP4T – Transmit Antennas.
  SP16T – Receive Antennas
Store Data
  Voltages and phases from the IQ demodulator into data.
Image processing
  16 point Fast Fourier transform
  End result a 1-Dimensional display of pixels divided into 16 columns.

## Slide 31: Major Goals
Create Timing Diagram
  Sequential mapping of signals to match timing.
Interface Control Document (ICD) Chart
  Make sure all interfaces are compatible
    (voltage, cable type, etc.).
Test code when component arrives.
Research more into FPGA and LabVIEW compatibility.

## Slide 32: Antenna Design
Antenna Engineer: Matt Cammuse
Electrical Engineering

## Slide 33: Antenna Instruments & Conditions
Instruments
Horn Antenna
  X-Band: 10 GHz
Waveguide-to-Coaxial adapter
Conditions
Gain = 26 dBi

## Slide 34: Preferred Horn Antenna
Company: Advanced Receiver
Antenna Type: X-Band Horns
Model No: MA86551
Center Frequency: 10.525 GHz
Frequency Range: 8-12.4 GHz
Nominal Gain: 17 dBi
H-Plane (Azimuth) beamwidth: 25°
E-Plane (Altitude) beamwidth: 25°
RF Connection: Mates with UG-39/U
Price: $20.00
Quantity: 20
Total Cost: $400.00
Azimuth Range = 106 in. [8.8 ft.]
Altitude Range = 106 in. [8.8 ft.]
Scene Extent ≈ 9 feet x 9 feet

## Slide 35: Alternative Horn Antennas
    Advanced Technical Materials: High Band – Model No. 90-443-6
Price per horn: $465.50
Frequency Range: 8.20-12.4 GHz
Gain: 24 dBi
H-Plane (Azimuth) beamwidth: 10.6°
E-Plane (Altitude) beamwidth: 8.8°
Height: 7 in.
Width: 10 in.
Length: 20.2 in
    Advanced Technical Materials: High Band – Model No. 75-443-6
Price per horn: $522.50
Frequency Range: 10-15 GHz
Gain: 24 dBi
H-Plane (Azimuth) beamwidth: 10.5°
E-Plane (Altitude) beamwidth: 8.9°
Height: 5.73 in.
Width: 8.07 in.
Length: 17 in.

## Slide 36: Waveguide-to-Coaxial Adapter
    WR90 Waveguide Isolator X-Band 8.2 to 12.4 GHz
Frequency Range: 8.2-12.4 GHz
Price: $79.95
Configured with Isolator
  Reduces leakage
    Flann 16094-NF | WR90 to N-Female Waveguide Adapter X-Band
Frequency Range: 8.2-12.4 GHz
Square Non-Choke Flange
Price: $129.95
    Omega Laboratories Model 108 - WR90 to N-Female Waveguide Adapter
Frequency Range: 8-12.4 GHz
Square Non-Choke Flange
Price: $129.95

## Slide 37: Overall Structure
Linear Antenna Apertures (2)
  Transmit – 4
  Receive – 16
T-shape design
  Apertures crossing
Vertical Aperture  Altitude
Horizontal Aperture  Azimuth
32 Phase Centers

## Slide 38: Antenna Design - Aperture
Transmits Antennas (Tx) – 2
  Location: Ends of array
Receive Antennas (Rx) – 8
  Location: Between transmit antennas
16 Phase Centers
  Midpoint between Tx and Rx
Antenna Spacing
  Transmit-to-Receive Spacing = 7.09 in
  Receive-to-Transmit Spacing = 3.54 in
  Prevents grating lobes
  Array Factor

## Slide 39: Major Tasks
Calculate required Beamwidth and Gain
Find capable instruments
  Horn antennas
  Waveguide-to-coaxial
Determine spacing between antennas

## Slide 40: Mechanical Design
Antenna Structure Engineers:
Mark Poindexter & Malcolm Harmon
Mechanical Engineering

## Slide 41: Structure – Design 1
Horn Alignment
  T Configuration
Horn Placement
  Adjustability
Electrical Components
  Detachable Box
Material
  Aluminum Based Metal
Stand
  Saw Horse

## Slide 42: Structure – Design 2
Horn Alignment
  Cylindrical Web Configuration
Horn Placement
  Adjustability
Electrical Components
  Detachable Horn Cover
Material
  Galvanized Steel Based Metal
Stand
  Tripod

## Slide 43
Scale: 1 - 5 (Constructability) | Design 1 | Design 2
Phase Centers | 5 | 3
Horn Adjustability | 4 | 4
Horn Coverage | 2 | 4
Electrical Components | 4 | 3
Structure Mounting | 3 | 3
Comparison

## Slide 44: Material Selection
Scale 1-4 | Weight | Overall Strength | Machinability | Cost | Total
Aluminum | 3 | 2 | 1 | 2 | 8
Galvanized Steel | 4 | 1 | 2 | 1 | 8
ABS | 1 | 3 | 3 | 4 | 11
PLA | 2 | 4 | 4 | 3 | 13

## Slide 45: Synthetic Aperture Radar – Final Design
Choosing the Features
Parts Retained
Design 1 | Design 2
Horn Placement Component Box | Horn Shield Back Plate Cover
Blended Parts
Final Design
Wall Mount Design Stand
New Features
Final Design
ABS Plastic

## Slide 46: Retain Parts
Horn Placement Component Box | Horn Shield Back Plate Cover

## Slide 47: Parts Blended
Wall Mount | Quad Stand

## Slide 48: Complete Detailed Schedule
Project Manager: Jasmine Vanderhorst
Industrial Engineer

## Slide 49: Project Main Tasks
Frequency Justification
Antenna Design
FPGA Programming ­
Trade-Off analysis
Simulation: Timing
Radar Range Equation
Transmit Path
Receive Path
Cabling Design
Conceptual Mechanical Design
Finalize Mechanical Design
Power Budget
Testing
Generate Interface Control Document
System Calibration
Generate Final Performance Characteristics

## Slide 50: Critical Path – Antenna Design

## Slide 51: Critical Path – FPGA Programming

## Slide 52: Critical Path – Analysis

## Slide 53: Critical Path – Mechanical & Power

## Slide 54: Critical Path – Calibration

## Slide 55: Complete Detailed Budget
Co-Lead Engineer & Treasurer –
Benjamin Mock
Industrial Engineer

## Slide 56: Major Component Cost - 1
Component | Distributor | Quantity | Unit Cost | Total Cost
FPGA | Digilent | 1 | $140.00 | $140.00
Antenna Horns | Advanced Receiver | 20 | $20.00 | $400.00
VCO | Hittite | 1 | $1,100.95 | $1,100.95
Power Amplifier | Fairview Microwave | 1 | $2,420.27 | $2,420.27

## Slide 57: Major Component Cost - 2
Component | Distributor | Quantity | Unit Cost | Total Cost
Low Noise Amplifier | Fairview Microwave | 1 | $1,512.67 | $1,512.67
D/A Conv. | Digilent | 1 | $28.99 | $28.99
A/D Conv. | Digilent | 1 | $37.00 | $37.00
Freq. Mult. | Mini-Circuit | 1 | $41.95 | $41.95

## Slide 58: Major Component Cost - 3
Component | Distributor | Quantity | Unit Cost | Total Cost
SPDT | Hittite | 1 | $69.95 | $69.95
SP4T | UMCC | 1 | $79.95 | $79.95
SP16T | UMCC | 1 | $25.95 | $25.95
Var. Atten. | Narda | 2 | $6.00 | $12.00

## Slide 59: Major Component Cost - 5
Component | Distributor | Quantity | Unit Cost | Total Cost
IQ Demodul. | Polyphase Microwave | 1 | $1,512.67 | $1,512.67

## Slide 60: Major Component Cost - 6
Component Subtotal |  | $9,043.96
Overhead | 20.00% | $1,808.79
Total Expense |  | $10,852.75
 | (Risk Mitigation Maximum) | $19,896.71

## Slide 61: Project Expenses
Primary Tentative Expenses
  RADAR Absorbing Foam & Support
  Cabling
  Mechanical Structure Fabrication
  Trihedral Reflectors
Secondary Tentative Expenses
  Storage Apparatus
  Assembly Tooling
  3-D Printing Order
  Overhead
  Mannequin

## Slide 62: Personnel Expenses - 1
Baseline Assumptions
  Hourly Rate $30.00
  Hours/Week 12hrs
  Total Weeks 30 (2 semesters)
  Total Hours 360hrs
  Fringe Benefits 29.00%

## Slide 63: Project Expense - 2
Projected Expense
  Cost per Engineer
    $10,800.00
  Fringe per Engineer
    $3,132.00
  Total Cost for Team
    $111,456.00

## Slide 64: Detailed Risk Assessment
Co-Lead Engineer & Treasurer –
Benjamin Mock
Industrial Engineer

## Slide 65: Major Project Risks
Procurement Difficulties
Signal Processing Code
  Dependence on Critical Path
Budget Limitations

## Slide 66: Minor Project Risks
Component Failure
Extraneous noise conflicts with signal processing
  Vibration & Heat Generation
Facility Availability
Non Integrated Circuit components require soldering which may negatively affect component quality

## Slide 67: Questions & Comments
THANK YOU