## Slide 1: Design & Manufacture of Rotorcraft
IME Team#8/ME Team#31
Chabely Amo
Louisny Dufresne
Robert Johnson
Mohammed Nabulsi
Taniwa Ndebele
Victoria Rogers
Kimberlee Steinman
Mitchell Stratton
IME Team #8/ME Team #31 Slide 1 of 32
Kimberlee Steinman
Design & Manufacture of Rotorcraft

## Slide 2: Team Organization
IME Team #8/ME Team #31 Slide 2 of 32
Kimberlee Steinman
Design & Manufacture of Rotorcraft

## Slide 3: Background
IME Team #8/ME Team #31 Slide 3 of 32
Kimberlee Steinman
Design & Manufacture of Rotorcraft
A rotorcraft is a flying machine that uses lift generated by wings called rotor blades that revolve around a mast
Rotary unmanned aerial vehicles often
  fall into one of two classifications:
  High payload capacity but low
    portability
  High portability but a reduced
    payload capacity.
Figure 1. Example of a Quad-rotor [1]

## Slide 4: SWOT Analysis Quadrants
IME Team #8/ ME Team #31 Slide 4 of 32
Kimberlee Steinman
Design & Manufacture of Rotorcraft
Strengths | Weaknesses
Interdisciplinary Group Open Communication Stakeholders and Resources | Large Group Limited Literature Availability
Opportunities | Threats
Increase in Military Demand for Rotorcrafts | Another funded group developing a similar rotorcraft might devalue the results of the project

## Slide 5: SIPOC Analysis Chart
IME Team #8/ME Team #31 Slide 5 of 32
Suppliers | Input | Process | Output | Customers
HPMI, Online retailers, College of Engineering departments. | Group member's knowledge and training in design and manufacturing | Design a rotorcraft that meets the customer's requirements and the manufacturing processes required to create the rotorcraft | Rotorcraft matching our projects goal statement | The Department of Industrial and Manufacturing Engineering and Dr.Okoli
Kimberlee Steinman
Design & Manufacture of Rotorcraft

## Slide 6: Goal Statement and Objective
Design a rotorcraft that can:
  Fit in a military backpack (23”x14.5”x15”)
  Carry a payload of at least 50 pounds
  Be made with commercial off the shelf (COTS) components
  Travel up to approximately 1 mile
  Be easily maintained and used in the field
Design the manufacturing processes to be used in creating the rotorcraft
Build a prototype of the rotorcraft
IME Team #8/ ME Team #31 Slide 6 of 32
Figure 2. Military Backpack [2]
Kimberlee Steinman
Design & Manufacture of Rotorcraft

## Slide 7: House Of Quality
Chabely Amo
Design & Manufacture of Rotorcraft
IME Team #8/ ME Team #31 Slide 7 of 32

## Slide 8: Multi-copter Configuration
IME Team #8/ ME Team #31 Slide 8 of 32
Chabely Amo
Design & Manufacture of Rotorcraft
Two types:
Coaxial Setup (X8)
  Two engines mounted co-axially on the ends of each boom
  Excellent Lifting Power
  Easier Portability
Radial Setup (V8)
  One engine mounted on the
    end of each boom
Figure 3. Multi-copter Configurations [3]

## Slide 9: Designs Analyses and Comparisons
IME Team #8/ME Team #31 Slide 9 of 32
Chabely Amo
Design & Manufacture of Rotorcraft
Design #1  Proposed by Intern Student Cameron Alexander
Design #2  Proposed by the Team
Design #3  Proposed by the Team

## Slide 10: General Design
IME Team #8/ ME Team #31 Slide 10 of 32
Chabely Amo
Design & Manufacture of Rotorcraft
Figure 4. Cameron’s Radial Design
Figure 5. Team’s Coaxial Designs 2 and 3

## Slide 11: Measure Phase Tool: eCalc Analysis
Provides web-based quality services to calculate evaluate and design electric motor driven systems for remote controlled models
Provides Rotorcraft outcome based on:
  Battery
  Speed Controller
  Motor
  Propeller
Guarantees error margin no greater than ±10%
IME Team #8/ME Team #31 Slide 11 of 32
Mohammed Nabulsi
Design & Manufacture of Rotorcraft

## Slide 12: eCalc Multi-Copter Calculator
IME Team #8/ME Team #31 Slide 12 of 32
Mohammed Nabulsi
Design & Manufacture of Rotorcraft

## Slide 13: Motor Comparison
IME Team #8/ ME Team #31 Slide 13 of 32
Mohammed Nabulsi
Design & Manufacture of Rotorcraft
Design | Motor | Kv (RPM/V) | Prop Range | Mass (Lbs.) | Max Current (A) | Max Voltage (V) | Power (W) | Cost ($)
Design #1 | E-Flite Power 52 Brushless Outrunner [6] | 590 | 12”x 8” to 14”x 7” | 0.77 | 65 | 22 | 1650 | 109
Design #2 | E-Flite Power 360 Brushless Outrunner [5] | 180 | 24”x10” to 25”x12” | 2.7 | 130 | 44.4 | 6000 | 359
Design # 3 | E-Flite Power 110 Brushless Outrunner [4] | 295 | 17”x8” to 19”x10” | 1.1 | 65 | 38.4 | 2000 | 139

## Slide 14: Battery Comparison
IME Team #8/ ME Team #31 Slide 14 of 32
Mohammed Nabulsi
Design & Manufacture of Rotorcraft
Design | Battery | Capacity (mAh) | Voltage (V) | Discharge (C) | Weight (Lbs.) | Cost ($)
Design #1 | E-Flight Lipo Pack [9] | 3,200 | 22.2 | 30 | 1.49 | 100
Design #2 | Thunder Power Lipo Pack [8] | 5,000 | 33.3 | 70 | 2.56 | 419
Design #3 | Pulse Lipo Pack [7] | 5,000 | 25.9 | 65 | 2.09 | 196

## Slide 15: Propeller Comparison
IME Team #8/ ME Team #31 Slide 15 of 32
Mohammed Nabulsi
Design & Manufacture of Rotorcraft
Design | Propeller | Prop Size | Weight (Lbs.) | Cost ($)
Design #1 | Plastic [12] | 16.5”x10” | 0.17 | 7
Design #2 | APC Electric [11] | 24”x12” | 0.19 | 19
Design #3 | APC Electric [10] | 18”x10” | 0.18 | 8

## Slide 16: eCalc Results
Design | Lift Payload of 50 Lbs. | Comments
Design #1 | No | -Maximum current is over the limit for the speed controller and the motor -Motor overheat potential -Throttle at 100% (minimal maneuverability)
Design #2 | Yes | -Throttle at 77% (full maneuverability)
Design #3 | Conditionally | -Throttle at 98% (minimal maneuverability)
IME Team #8/ ME Team #31 Slide 16 of 32
Mohammed Nabulsi
Design & Manufacture of Rotorcraft

## Slide 17: Does it Fit in the Backpack?
IME Team #8/ ME Team #31 Slide 17 of 32
Taniwa Ndebele
Design & Manufacture of Rotorcraft
Design | Fit in the Military Backpack
Design #1 | YES
Design #2 | NO
Design #3 | YES

## Slide 18: Rotorcraft Simulation
IME Team #8/ ME Team #31 Slide 18 of 32
Taniwa Ndebele
Design & Manufacture of Rotorcraft

## Slide 19: Design Cost Comparison
IME Team #8/ ME Team #31 Slide 19 of 32
Taniwa Ndebele
Design & Manufacture of Rotorcraft
Chart: Cost ($)
| Design 1 | Design 2 | Design 3
 | 3842 | 7451 | 3645

## Slide 20: Overall Designs Comparisons
Design
Design #1
Design #2
Design
#3
Lift
Payload of 50 lbs.
NO
YES
Conditionally
Fit in the Military
Backpack
YES
NO
YES
Estimated
Weight (lbs.)
32
47
38
Cost
($)
3841
7451
3645
IME Team #8/ ME Team #31 Slide 20 of 32
Taniwa Ndebele
Design & Manufacture of Rotorcraft
2630

## Slide 21: Stress Analysis
Assume arms and base plate will be carbon fiber
Attach 50 pound load to rotorcraft
Team’s analysis shows amount of deformation under load in mm
Cameron Alexander’s analysis shows yield stress
Neither design fails stress analysis
IME Team #8/ ME Team #31 Slide 21 of 32
Victoria Rogers
Design & Manufacture of Rotorcraft

## Slide 22: Base Plate Stress Analysis Comparison
IME Team #8/ ME Team #31 Slide 22 of 32
Victoria Rogers
Design & Manufacture of Rotorcraft
Team’s Design | Cameron Alexander’s Design
Bottom View with Hook
Top View without Hook

## Slide 23: Arms Stress Analysis Comparison
IME Team #8/ ME Team #31 Slide 23 of 32
Victoria Rogers
Design & Manufacture of Rotorcraft
Team’s Design | Cameron Alexander’s Design

## Slide 24: Microcontroller Unit (MCU)
  “Brain” of Rotorcraft
    Controls all main functions
    Code is stored here
    All inputs and outputs move through the MCU
  Will be placed inside the frame
    Prevents crash damage
    Kept safe from adverse weather
    Helps to maintain balance of craft
  Light relative to other parts
IME Team #8/ ME Team #31 Slide 24 of 32
Mitchell Stratton
Design & Manufacture of Rotorcraft
Figure 6. Brain of Rotorcraft

## Slide 25: Arduino Leonardo
20 Digital I/O Ports
12 Analog inputs
C++ Programming Language
Compatible with IMU
IME Team #8/ ME Team #31 Slide 25 of 32
Figure 7. Arduino Leonardo [13]
Mitchell Stratton
Design & Manufacture of Rotorcraft
Voltage (V) | Cost ($) | Size (in) | Weight (g)
7 – 12 | 23 | 2.7 x 2.1 | 20

## Slide 26: Inertial Measurement Unit (IMU)
Contains:
  Gyroscope
  Accelerometer
  Compass
Responsible for Providing orientation data to the MCU
Keeps rotorcraft straight
IME Team #8/ ME Team #31 Slide 26 of 32
Figure 8. Flight Control Panel
Mitchell Stratton
Design & Manufacture of Rotorcraft

## Slide 27: Adafruit 9-DOF IMU Breakout
Compatible with Arduino Leonardo
L3DG20H gyroscope
LSM303DLH accelerometer/compass
3V regulator
IME Team #8/ ME Team #31 Slide 27 of 32
Robert Johnson
Design & Manufacture of Rotorcraft
Figure 9. Adafruit 9-DOF IMU [13]
Cost ($) | Size (in) | Weight (g)
29.95 | 1.5 x 0.9 | 2.8

## Slide 28: RC Controller
Input for electrical design
Must have unique frequency
  Limits interference
IME Team #8/ ME Team #31 Slide 28 of 32
Figure 10. RC Controller
Robert Johnson
Design & Manufacture of Rotorcraft

## Slide 29: Design Flow
IME Team #8/ ME Team #31 Slide 29 of 32
IMU
RC Controller
MCU
Rotors
Robert Johnson
Design & Manufacture of Rotorcraft

## Slide 30: Schedule: Gantt Chart
IME Team #8/ ME Team #31 Slide 30 of 32
Louisny Dufresne
Design & Manufacture of Rotorcraft

## Slide 31: Conclusion
Objective:
Design and Manufacture a Rotorcraft that can:
  Fit in a military backpack (23x14.5x15)
  Can carry a payload of at least 50 pounds
  Made with COTS components (off the shelf)
  Has a range of approximately 1 mile
  Easy to maintain and use in the field
What’s Next:
  Analyze Phase
  Build and Manufacture Design #3
  Perform Ergonomics Analysis
IME Team #8/ ME Team #31 Slide 31 of 32
Louisny Dufresne
Design & Manufacture of Rotorcraft

## Slide 32: References
[1] "FlightGear Forum • View Topic - Four Rotor Helicopter." FlightGear Forum • View Topic - Four Rotor Helicopter. PhpBB Group, n.d. Web. 02 Dec. 2014.
[2] "SMALL MOLLE ASSAULT BACKPACK MILITARY RUCKSACK ARMY NEW." eBay. N.p., n.d. Web. 22 Oct. 2014. <http://www.ebay.com/itm/SMALL-MOLLE-ASSAULT-BACKPACK-MILITARY-RUCKSACK-ARMY-NEW-/170555911038>.
[3] "Multi-Rotor Frame Configurations - CopterCraft.com." CopterCraftcom RSS2. Web. 30 Nov. 2014. <http://www.coptercraft.com/multirotor-frame-configurations/#!prettyPhoto>.
[4] "Power 110 Brushless Outrunner Motor, 295Kv." (EFLM4110A): E-flite. Web. 30 Nov. 2014. <http://www.e-fliterc.com/Products/Default.aspx?ProdID=EFLM4110A>.
[5] "Power 360 Brushless Outrunner Motor, 180Kv." (EFLM4360A): E-flite. Web. 30 Nov. 2014. <http://www.e-fliterc.com/Products/Default.aspx?ProdID=EFLM4360A>.
[6] "Power 52 Brushless Outrunner Motor, 590Kv." (EFLM4052A): E-flite. Web. 30 Nov. 2014. <http://www.e-fliterc.com/Products/Default.aspx?ProdID=EFLM4052A>.
[7] "Lithium Polymer Battery." Wikipedia. Wikimedia Foundation, 29 Nov. 2014. Web. 30 Nov. 2014. <http://en.wikipedia.org/wiki/Lithium_polymer_battery>.
[8] "Pulse Battery." Pulse Battery. Web. 30 Nov. 2014. <http://pulsebattery.com/products_new.php?page=4>.
[9] "Thunder Power RC G8 Pro Force 70C 5000mAh 9-Cell/9S 33.3V LiPo Battery FREE SHIPPING SKU: TP5000-9SPF70." RCToyscom New Products. Web. 30 Nov. 2014. <http://www.rctoys.com/rc-toys-and-parts/TP5000-9SPF70/RC-PARTS-THUNDER-POWER-9-CELL-LITHIUM-BATTERIES.html>.
[10] "APC APCE-18X10, APCE 18X10, Accessories." APC APCE-18X10. Web. 30 Nov. 2014. <https://www.aero-model.com/1_3_69/Accessories_APC-18x10-E-Prop/APCE-18X10.html>.
[11] "APC APCE-24X12, APCE 18X10, Accessories." APC APCE-18X10. Web. 30 Nov. 2014. <https://www.aero-model.com/1_3_69/Accessories_APC-18x10-E-Prop/APCE-18X10.html>.
[12] "USA DEALS." 2Pcs 16.5 X 10 Black Plastic Folding Propeller Blade for RC Helicopter. Web. 30 Nov. 2014. <http://findusadeals.com/deals/B00KHUVK20.html>.
[13] "How To Build A Quadcopter." THE WORLD FROM MY POINT OF VIEW. N.p., n.d. Web. 22 Oct. 2014. <http://akashstevekhanna.wordpress.com/2014/03/01/2899/>.
IME Team #8/ ME Team #31 Slide 32 of 32
Louisny Dufresne
Design & Manufacture of Rotorcraft