## Slide 1: SOAAR UAV: Small Object Avoidance Autonomous Rescue Unmanned Aerial Vehicle
Team 12: Matthias Clarke, Devin justice, Trent Loboda, Cody Rochford, Marcus Yarber, Qinggele ‘Gale’ Yu
Presenters: Devin Justice, Trent Loboda, Cody Rochford
Advisor: Dr. Alvi
Conceptual design
1

## Slide 2: Project Introduction
Conceptual design
2
Devin justice
Association for Unmanned Vehicle Systems International (AUVSI) Student Unmanned Aerial Systems (SUAS) 2017 Competition
“The competition requires students to design, integrate, report on, and demonstrate a UAS capable of autonomous flight and navigation, remote sensing via onboard payload sensors, and execution of a specific set of tasks.”
Figure 2. Mission map for the SUAS 2017 Competition.
Figure 1. Current UAV developed by team 8 in 2016.

## Slide 3: Goal Statement
Develop an autonomous UAV featuring autonomous takeoff and landing, autonomous flight and navigation, target detection and classification, stationary and dynamic object avoidance, and payload delivery.
Objectives:
  Select and develop electronics payload.
  Design, build, and integrate payload delivery mechanism.
  Select and integrate lightweight landing gear configuration.
  Create programs to detect and classify stationary targets.
  Create programs to detect and classify emerging targets.
  Develop control system to autonomously avoid objects.
Conceptual design
3
Devin justice

## Slide 4: Feasibility of Previous UAV
Conceptual design
4
Devin justice
Figure 3. House of Quality to determine feasibility of previous build.

## Slide 5: Electrical Systems Design
Conceptual design
5
Trent Loboda
System Requirement Solution
Autonomy Autopilot component
Navigation GPS
Object detection/avoidance Camera
Communication Multiple antennas
Control system CPU

## Slide 6: Current Systems and New Designs
Remaining Components New Components
PIXHAWK autopilot/flight controller PIXHAWK meets requirements
Integrated 3DR telemetry unit Zubax gnss GPS module
Pixy CMUcam5 camera Sony DCS-W710/B 16MP camera
Spectrum DX8 transmitter and AR8000 receiver Transmitter & receiver meet
  the requirements
No existing CPU ODROID C2 CPU
Conceptual design
6
Trent Loboda

## Slide 7: Component Justification
Figure 4. ODROID C2 Board for Onboard CPU.
Conceptual design
7
Trent Loboda
Companion Computer Selection
After thorough research, the student selected the ODROID C2
board for its robust processing power, low cost, and small size.
 | Odroid C2 | Odroid C1+ | Rpi 2 Model B
GPU | 3x ARM 700Mhz | 2x ARM 600MHz | 1x VideoCore 250MHz
Weight | 40g | 40g | 42g
Price | $40 | $37 | $35
Table 1. CPU Comparison between Odroid C2 and Competitors.

## Slide 8: Component Justification: Camera Selection
Pairwise Comparison matrix
                Needs by importance: Weight
                1. Resolution 0.55
                2. Size 0.27
                3. Power Consumption 0.18
Competition constraint requires object recognition at up to 300ft
Prior camera Pixycam CMUcam5 not powerful enough to accurately recognize distant objects
Conceptual design
8
Trent Loboda
Table 2. Pairwise Comparison Matrix for Camera Selection.

## Slide 9: Component Justification
System Telemetry
Current Configuration Planned replacement
3DR Ublox GPS and compass Zubax gnss GPS
Pro: Team has this component and Pro: Refresh rate meets
it functions competition constraint
Con: The refresh rate does not Con: Team will have to purchase
meet the competition constraint the component
Conceptual design
9
Trent Loboda

## Slide 10: Payload Delivery
Conceptual design
10
Cody rochford
Payload
  8oz sealed water bottle
  Total payload must not exceed 16oz
GPS coordinates for drop
  Must retain 80% of the water
  Points awarded: max(0, (150ft − distance) / 150ft)

## Slide 11: Concept Generation: Morphological Chart
Conceptual design
11
Cody rochford
Sub-Functions | Possible Solutions |  |  | 
Payload Accuracy | Timed Release | Adaptive Control Surface | Ballast Weight | 
Integrate with Aerodynamic Design | Geometry | Shaved Foam Attachment |  | 
Payload Safety | Parachute | Padding | Spring | Strong Case
Release Mechanism | Key Design/Geometry | Direct Servo Interaction | Lock/Pin Mechanism | 
Concept 1
Concept 2
Concept 3
Sub-Functions | Possible Solutions |  |  | 
Payload Accuracy | Timed Release | Adaptive Control Surface | Ballast Weight | 
Integrate with Aerodynamic Design | Geometry | Shaved Foam Attachment |  | 
Payload Safety | Padding | Parachute | Spring | Strong Case
Release Mechanism | Key Design/Geometry | Lock/Pin Mechanism | Direct Servo Interaction | 
Table 3. Morphological Chart for Payload Delivery Mechanism.

## Slide 12: Concept 1
Conceptual design
12
Cody rochford
Figure 5. 3D Model Rendering of Latch-Servo Design.
Advantages:
  Simplistic Design
  Lightweight
Disadvantages:
  Open-Air Design
  Less aerodynamics
  High torqued servo arm
  Bottle Entrapment

## Slide 13: Concept 1 Continued
Figure 6. 3D Model of Latch-Servo Design.
Conceptual design
13
Cody rochford

## Slide 14: Concept 2
Conceptual design
14
Cody rochford
Figure 7. 3D Model Rendering of Geometry Release Design.
Advantages:
  Payload incorporated housing
  Less force on servo arm
  Aerodynamic geometry
  Full enclosure of water bottle
Disadvantages:
  Complex design
  Failure to disengage
  Door failure

## Slide 15: Concept 2 Continued
Figure 8. 3D Model of Geometry Release Design.
Conceptual design
15
Cody rochford

## Slide 16: Concept 3
Conceptual design
16
Cody rochford
Figure 9. 2D Schematic of Servo Mechanism.
Figure 10. 3D Model Rendering of Concept 3 Pin/Hole Design.
Advantages:
  Payload incorporated housing
  Accurate release
  Aerodynamic geometry
  Full enclosure of water bottle
Disadvantages:
  Complex design
  Moving mechanism
  Pin disengagement failure
  Lack of parachute

## Slide 17: Concept 3 Continued
Figure 11. 3D Model of Concept 3 Pin/Hole Design.
Conceptual design
17
Cody rochford

## Slide 18: Payload Delivery Concept Selection
Conceptual design
18
Devin justice
Selection Criteria | Baseline | Concept Design 1 | Concept Design 2 | Concept Design 3
Aerodynamic | 0 | 0 | +1 | +1
Simplicity | 0 | +1 | -1 | -1
Weight | 0 | +1 | -1 | -1
Size | 0 | 0 | 0 | 0
Accuracy | 0 | -1 | -1 | +1
Score | 0 | +1 | -2 | 0
Table 4. Pugh Matrix to select for Payload Delivery Mechanism.

## Slide 19: Future Work
Conceptual design
19
Devin justice
Order and test electronics.
Build and integrate payload delivery mechanism.
Begin writing program for stationary and emerging target detection.
  Upon completion “teach” targets.
Begin object avoidance program.
  Write program to develop trajectory based on object location and size.
Interface with “Interoperablility” system to ensure compatibility.
Test system in varying environments.

## Slide 20: Challenges
Target detection:
  Recognize alphanumeric symbols and shapes, reliant on camera capability and distance.
  Emergent target detection is less prevalent in open source code.
  Recognize objects while flying with the propellers in the horizontal position.
  Development of transitional propeller control system.
Object avoidance:
  Develop evasive maneuvering within the limited flight envelope for flying wing design.
  Write a robust program capable implementation with hardware for realistic application.
Conceptual design
20
Devin justice

## Slide 21: Conclusion
Previous UAV structure, propulsion system, and flight controller have been deemed feasible.
Electronic hardware has been selected.
3-dimensional modeling has been developed for the payload delivery mechanism.
Future work has been outlined and scheduled for the fall and spring semesters.
Conceptual design
21
Devin justice

## Slide 22: References
Competition Rules SUAS 2017. (2017).
K. Aley, J. Denman, D. Fitzpatrick, C. Mard, P. McGlynn, and K. Ijagbemi, "Needs Assessment" Sep. 25, 2015.
K. Aley, J. Denman, D. Fitzpatrick, C. Mard, P. McGlynn, and K. Ijagbemi, "Project Plan & Product Specifications" Oct. 22, 2015.
"Hardkernel," in ODROID. [Online]. Available: http://www.hardkernel.com/main/products/. Accessed: Oct. 6, 2016.
Conceptual design
22
Devin justice

## Slide 23: Questions
Are there any questions?
Conceptual design
23
Devin justice

## Slide 24: Q&A Electrical Systems
Top-Level Design
Conceptual design
24
Figure 12. Top-Level Design of Electronics System.

## Slide 25: CPU Ethernet Performance
Conceptual design
25
Figure 13. ODROID Comparison (Mbit/sec).

## Slide 26: Gantt Chart 2
Conceptual design
26
Table 5. Gantt Chart current date through end of semester.

## Slide 27: Component Justification
Conceptual design
27
Table 6. ODROID Board Specification Comparisons.