## Slide 1: Tree Limbing and Harvesting ROV
Team 15 Presenters:
Ryan Gaylord, Alex Glazer,
Nestor Riguad

## Slide 2: Team Introductions
Nestor Rigaud
ME DESIGN
Christopher Ruiz
TEAM LEADER
Donald Phillips
FINANCIAL ADVISOR
Ryan Gaylord
LEAD
COMMUNICATIONS
Alex Glazer
ME PROGRAMMING

## Slide 3: Recap
Project Scope
A ROV modeled after a Total Tree Harvester head
As the ROV climbs, it will de-limb the tree
Once at a certain height, the ROV will top the tree
As it’s descending, the ROV will section the tree
Alex Glazer

## Slide 4: Target Catalog
Targets were assigned to each component of our functional decomposition and other factors
  Secure to Tree
  Climb the Tree
  De-limb the Tree
  Section the Tree
  Other Targets
Alex Glazer

## Slide 5: Targets
Secure to Tree | Maximum Opening Width | 25 in
 | Minimum Opening Width | 8 in
 | Maximum Clamping Pressure | 790 psi
 | Minimum Clamping Force to Climb Tree | 200 lbf
 | Minimum Clamping Force to Shear Limbs | 5,371 lbf
Climb the Tree | Rate of Climbing Tree | 30 ft/min
 | Maximum Tree Height | 60 ft.
Alex Glazer

## Slide 6: Targets: Securing to Tree
Minimum = 8 in.
Maximum = 25 in
Opening width of ROV
Alex Glazer

## Slide 7: Targets: Securing to Tree
Maximum clamping pressure
  790 psi
Minimum clamping force to climb tree
  200 lbf
Minimum clamping force to shear limbs
  5,371 lbf
Alex Glazer

## Slide 8: Targets
Secure to Tree | Maximum Opening Width | 25 in
 | Minimum Opening Width | 8 in
 | Maximum Clamping Pressure | 790 Psi
 | Minimum Clamping Force to Climb Tree | 200 lbf
 | Minimum Clamping Force to Shear Limbs | 5,371 lbf
Climb the Tree | Rate of Climbing Tree | 30 ft/min
 | Maximum Tree Height | 60 ft.
Alex Glazer

## Slide 9: Targets: Climb the Tree
Max height of tree = 60 ft.
Climbing rate = 30 ft/min
Alex Glazer

## Slide 10: Targets
De-limb the Tree | Precision of Limb Shearing | 0.5 in. from tree
 | Force to Shear Limbs | 5171 lbf
 | De-limbing Rate | 10 seconds/limb
 | Maximum Limb Diameter | 5 in.
 | Minimum Limb Diameter | 1 in.
Section the Tree | Rate of Sectioning Tree | 30 seconds
Alex Glazer

## Slide 11: Targets: De-limb the Tree
Force to shear limbs = 5171 lbf
De-limbing rate =
10 sec/limb
Precision = 0.5 in.
Maximum Limb Diameter
  5 in.
Minimum Limb Diameter
  1 in.
Alex Glazer

## Slide 12: Targets
Section the Tree | Rate of Sectioning the Tree | 30 seconds/cut
Other | Max Weight | 200 lbs
 | Max Number of Controls | 10
 | Maximum Development Cost | $5,000
 | Operation Time per Tree | 1.5 Hours
 | Power Consumption | 130 kW
 | Range of Controller | 150 ft.
Alex Glazer

## Slide 13: Targets
Section the Tree | Rate of Sectioning the Tree | 30 seconds/cut
Other | Max Weight | 200 lbs
 | Max Number of Controls | 10
 | Maximum Development Cost | $5,000
 | Operation Time per Tree | 1.5 Hours
 | Power Consumption | 130 kW
 | Range of Controller | 150 ft.
Alex Glazer

## Slide 14: Concept Generation
Ryan Gaylord

## Slide 15: Concept Generation
A morphological chart uses the functional parameters to explore various solutions for the customer requirements.
Climb
Securing
Movement Type
Limbing
Type
Guide
Electrical
Controller
Sectioning
Direct
Type
Cutting Approach
Ryan Gaylord

## Slide 16: Climb
Securing
Ryan Gaylord

## Slide 17: Climb: Securing
Hydraulics
  Large force to weight ratio but can be complicated
Pneumatics
  Simple, precise, and light but low force to weight ratio
Motor
  No leaks and precise, but weak and risk overheating
Ryan Gaylord

## Slide 18: Climb
Movement Type
Ryan Gaylord

## Slide 19: Climb: Movement Type
Wheels
  Lower cost and simpler design, but low surface contact and difficulty over obstacles
Ryan Gaylord

## Slide 20: Climb: Movement Type
Track
  High surface contact and easily overcomes obstacles, but has many moving parts, adding weight
Ryan Gaylord

## Slide 21: Climbs: Movement Type
Bear Hug Clamp
Ryan Gaylord

## Slide 22: Limbing
Type
Ryan Gaylord

## Slide 23: Limbing: Type
Shear
  Simple design with few moving parts, but would require a greater force
Ryan Gaylord

## Slide 24: Limbing: Type
Chainsaw/Circular Saw
  Requires less force and has many moving parts. Involves a guide
Ryan Gaylord

## Slide 25: Limbing
Guide
Ryan Gaylord

## Slide 26: Limbing: Guide
Tracks
  Allows cutting tool to revolve around the ROV
Stationary
  Cutting tool attached rigidly to the ROV
Prismatic
  Cutting tool attached by a prismatic joint
Ryan Gaylord

## Slide 27: Sectioning
Type
Ryan Gaylord

## Slide 28: Sectioning: Type
Shear
  Uses a wedge at high force
Chainsaw
  Greater cutting length and requires low force
Circular Saw
  Requires low force but a smaller cutting length
Ryan Gaylord

## Slide 29: Sectioning
Cutting Approach
Ryan Gaylord

## Slide 30: Sectioning: Cutting Approach
Horizontal
  Simplest method but little control of where the tree section falls
Ryan Gaylord

## Slide 31: Sectioning: Cutting Approach
45 degree angle
  More complicated than a horizontal cut but more control of the tree fall
Θ=45˚
Ryan Gaylord

## Slide 32: Sectioning: Cutting Approach
V-cut
  Most complicated design but also has the highest precision of tree fall
Ryan Gaylord

## Slide 33: Designs
Nestor Rigaud

## Slide 34: Design 1 (Datum)
Uses spiked wheels for movement type
Uses motors to climb up tree
Pneumatic clamping system
Nestor Rigaud

## Slide 35: Design 1 cont.
A rigid shearing cutting tool
A chainsaw for sectioning the tree
Nestor Rigaud

## Slide 36: Design 2
Uses tread for movement type
Uses motors to clamp and drive the ROV up and down the tree
Chainsaws will de-limb and section the tree
Nestor Rigaud

## Slide 37: Design 2 cont.
Rotating track will guide chainsaw around the tree for de-limbing
Second chainsaw will attached by revolute joint to section the tree.
Nestor Rigaud

## Slide 38: Design 3
Uses bear hug clamping method for movement type
A hydraulic clamping system
Two clamps are connected by a prismatic joint to climb the tree
A shearing blade de-limbs by the hydraulic prismatic joint
Chainsaw will be used to section the tree
https://www.youtube.com/watch?v=Cr_ha4JSCJg&t=48s
Nestor Rigaud

## Slide 39: Tree Harvesting ROV
The Next Step?
Nestor Rigaud

## Slide 40: The Next Step
Concept Selection
  Pugh Matrix
  HOQ
  Pre-Prototyping
    Cardboard
    CAD
Prototyping
  CAD
  Material Selection
Project Plan
Nestor Rigaud

## Slide 41: References
[1] S. (n.d.). Naarva s23 Stroke Harvester. Retrieved November 08, 2017, from http://www.pentinpaja.fi/app/product/view/-/id/65/cat_id/10/set_language/en
[2] Loblolly Pine. (n.d.). Retrieved November 07, 2017, from http://www.wood-database.com/loblolly-pine/
[3] Pinus taeda. (n.d.). Retrieved November 07, 2017, from http://www.conifers.org/pi/Pinus_taeda.php

## Slide 42: Tree Harvesting ROV
QUESTIONS?

## Slide 43: Back-Up Slides
Question 1
What are your designs based on?
[1]

## Slide 44: Back-Up Slides
Question 2
How did you find the force to shear the limbs?
  A book was found called “Tree Harvesting Techniques” that displayed an equation on how much force would be needed to shear a limb off a pine tree. We also benchmarked a tree harvester head using the specs on how much shearing force they put out when de-limbing.

## Slide 45: Back-Up Slides
Question 3
What kind of trees will the ROV be used on?
  Un-deformed straight trees up to 60 ft.
  Mostly pine trees, specifically loblolly since these are the most abundant type of pine tree in the southeast [2] [3]