## Slide 1: Tree Limbing and Harvesting ROV
Team 15 Presenters:
Chris Ruiz, Nestor Rigaud, Donald Phillips

## Slide 2: Team Introductions
Nestor Rigaud
ME DESIGN
Christopher Ruiz
TEAM LEADER
Donald Phillips
FINANCIAL ADVISOR
Ryan Gaylord
LEAD
COMMUNICATIONS
Alex Glazer
ME PROGRAMMING

## Slide 3: Recap
Project Scope
A Remotely Operated Vehicle or (ROV) modeled after a Total Tree Harvester head
As the ROV climbs, it will de-limb the tree
Chris Ruiz

## Slide 4: Concept Selection
Based off the Naarva S23 stroke harvester
Bear hug clamping method
Hydraulic clamping system
Two clamps connected by a prismatic joint to climb the tree
A shearing blade de-limbs by the hydraulic prismatic joint
Chris Ruiz

## Slide 5: Key Targets
Force to Shear Limbs | 2586 lbf
Weight | 100 lb
Opening Width of Clamps | 6-20 in
Min. Clamp Force to Climb | 100 lbf
Min. Clamp Force to Shear | 2686 lbf
Limb Diameter | 1-4 in
Chris Ruiz

## Slide 6: Scaled Down Targets
Force to Shear Limbs | 1800 lbf
Weight | 70 lb
Opening Width of Clamps | 12-16 in
Min. Clamp Force to Climb | 100 lbf
Min. Clamp Force to Shear | 1900 lbf
Limb Diameter | 1-2 in
Chris Ruiz

## Slide 7: ROV
Prototype Components and Information

## Slide 8: Clamping
Hydraulic cylinders for open and close clamps
One cylinder per clamp
One rigid arm per clamp
Nestor Rigaud

## Slide 9: Clamping
Nestor Rigaud

## Slide 10: Climbing/Shearing
2 double acting welded hydraulic cylinders
  Will require less psi to reach target force
  Stroke: 6 in
  Retract length: 14 in
Nestor Rigaud
Notes: https://www.grainger.com/product/MAXIM-Double-Acting-Welded-Style-6FDD1?searchQuery=6fdd1&suggestConfigId=6

## Slide 11: Body
A rectangular shell will be the storage location for all hydraulic and electronic systems
  Manifold and valves
  Circuit Board
  Hose entrance and exit paths
Nestor Rigaud
Notes: https://www.grainger.com/product/MAXIM-Double-Acting-Welded-Style-6FDD1?searchQuery=6fdd1&suggestConfigId=6

## Slide 12: Hydraulic System
Open circuit system
  Continuous flow to build pressure
  Uses relief valve to control pressure (~2400 psi)
Manifold
  3 position valves
  double acting cylinders
Donald Phillips

## Slide 13: Hydraulic System
Pump
Motor
Manifold
Reservoir
Relief Valve
Donald Phillips

## Slide 14: Electrical Controls System
Arduino
  Coded in c
  Used to control the ROV valves
Zigbee/xbee
  Send the wireless signal
Gamepad
  Used to input the action (move up, down, clamp, etc.)
Nestor Rigaud

## Slide 15: Controller action
Up/Down
Emergency shut down
Section off
Open clamps
Close clamps
Nestor Rigaud

## Slide 16: Movement Pseudo Code
If state==‘up’
Open top clamp
Turn valve forward, cylinders move up
If time==cylinder expansion time
Close top clamp
Open bottom clamp
Reverse valve, Cylinders retract
If time==cylinder retraction time
Valve turn neutral
Close bottom clamp
State==idle
Nestor Rigaud

## Slide 17: Potential Problems
Low flowing pump
  Not have proper specs to pump at the recommended speed
Solenoid ports
  Worn from previous usage
Different arrival dates from parts
  One cylinder will be arriving mid march
Donald Phillips

## Slide 18: The Bear
Donald Phillips

## Slide 19: Tree Harvesting ROV
The Next Step
Donald Phillips

## Slide 20: The Next Step
Waiting for parts to ship
  Cylinders, valves, hoses
Machining
Systems testing
  Electronic
  Hydraulic
Building prototype
Testing prototype
Risk assessment
Donald Phillips

## Slide 21: References
[1] S. (n.d.). Naarva s23 Stroke Harvester. Retrieved November 08, 2017, from http://www.pentinpaja.fi/app/product/view/-/id/65/cat_id/10/set_language/en
[2] Loblolly Pine. (n.d.). Retrieved November 07, 2017, from http://www.wood-database.com/loblolly-pine/
[3] Pinus taeda. (n.d.). Retrieved November 07, 2017, from http://www.conifers.org/pi/Pinus_taeda.php

## Slide 22: Tree Harvesting ROV
QUESTIONS?

## Slide 23: Back-Up Slides
Question 1
Where will you be conducting control testing for the ROV?
  Testing will be done at our sponsor’s engineering shop alongside an engineer he has delegated to assist us with the project.
[1]

## Slide 24: Back-Up Slides
Question 2
Why scale down target values?
  Since this class requires us to create a physical mechanism for our projects, a prototype with a smaller scale functionality will show that potential success can be achieved when considering the normal target values.

## Slide 25: Back-Up Slides
Question 3
How much will all this cost? What is the Budget?
  The estimated cost for buying all the parts was close to about $5,000. Fortunately our budget is virtually unlimited according to our sponsor but since his resources has allowed to us to obtain certain parts, We have only used about a third of the estimated cost.