## Slide 1: VDR 2 The Detector Baby
Team 511
Karli Cash, Matthew Zawiski, Shadi Bilal, David Miller
20-Nov-18

## Slide 2: Team Introductions
Matthew Zawiski
Software Engineer
Shadi Bilal
Test Engineer
David Miller
Design Engineer/ Financial Advisor
Karli Cash
Project Manager

## Slide 3: Project Summary
David Miller
Based on the customer needs the devices main function is to alert a parent/caregiver if their child is left inside a automobile with unsafe conditions.
Our design team is tasked with creating a device that parents/caregivers can use to prevent the death of infants who are left behind in cars.
Customer needs were established. The device must detect a passenger and surrounding temperatures, alert the user upon detection, and alert emergency personnel before fatal conditions are met.
Design team held a conference call with our sponsor Lisa Allen to discuss the customer needs & preliminary questions pertaining to the overall landscape of the product.
The preliminary design process begins with stating the targets of the product. From there the concept generation process begins.

## Slide 4: Targets
David Miller
Children tend to experience a fever when their internal body temperature reaches 100 degrees Fahrenheit, heat stroke at 104 degrees Fahrenheit, and death at approximately 107 degrees Fahrenheit (Gaggel, 2018).
Target distance was set for the device to operate at a maximum range of 50 to 100 meters.
Sizing of the secondary device was set to similar dimension of a key fob, which would allow the user to carry the device along with their keys.
  Approximate dimensions : height - 0.025m, width - 0.04 m, length - 0.085 m

## Slide 5: Targets Cont.
Device should be compatible with all car seats.
Detect if baby is in car seat.
Display temperature ranges and passenger vitals.
Alert users and emergency personnel.
Device should not be in power or measuring temperatures when passenger is not present.
David Miller

## Slide 6: Target Testing Methods
The accuracy of temperature detection will be tested using a standard thermometer and comparing readings.
Response range will be tested by measuring the distance the two devices can operate until feedback is no longer received.
To insure devices can operate properly in high temperatures it will be placed in an environment simulating that of a hot car.
Test to ensure device can detect when a passenger is in the car seat.
David Miller
Notes: This test would be repeated multiple times at and above the critical temperature to insure its accuracy.
(continuing on last bullet point)

## Slide 7: Concept Generation
Team brainstormed many ideas to bring the project to life.
There were four main categories to consider:
  Passenger detection device
  Interior temperature detection
  Critical temperature cut-off
  Secondary response device
All ideas were put into a morphological chart.
  Created 192 possible concepts.
David Miller

## Slide 8: Passenger Detection Device
David Miller
Heart Rate Monitor Bracelet
Airbag Detection Weight Technology
Smart Lock Alert
A bracelet that will monitor the passenger’s heart rate.
Alerts when unsafe heart rate is reached.
This will be connected to the alarm system and door locks.
Car doors will not lock until passenger is removed.
When critical, alarm system will sound until passenger is removed.
This will alert the driver, much like an airbag alert.
This occurs when a passenger is left too long in the seat after the engine is shut off.

## Slide 9: Passenger Detection Device Cont.
David Miller
Scale Mechanism
Smart Baby Onesie
Baby Monitor Car Seat Clip
Similar to the airbag concept, except incorporated into the car seat.
Detects presence based off weight measured in car seat.
Clip that connects to the harness on a car seat.
Operates when connected and passenger is present.
Alerts when secondary device is too far away.
Very trendy classic that reads infant vitals and alert abnormalities to the parent.

## Slide 10: Interior Temperature Detection Device
Matthew Zawiski
Positive/Negative Temperature Coefficient Thermistor
Semiconductor-Based Sensor
Thermocouples
Resistance Temperature Detector (RTD) Sensor
Sensor with electrical resistance that raises or lowers with changing temperature.
Used in temperature range of -50℃ to 150℃.
Sensor that also uses an electrical resistance.
Composed of a coil of wire wrapped around a glass or silicone core.
Temperature range of -200℃ to 850℃.
Based off of the Seebeck effect.
Electricity is created, and voltage is translated to read temperature differences between materials.
Temperature range is -270℃ to 1260℃.
Electronic device that is placed on an integrated circuit to measure temperatures.
Temperature range is between -40℃ to 120℃.
Notes: A positive temperature coefficient thermistor’s resistance increases with increasing temperature, while the negative temperature coefficient thermistor’s resistance decreases with increasing temperature.
According to the Seebeck effect, a temperature difference between two metals will create electricity. Thermocouples rely on this phenomenon by creating a loop with
semiconducting metals when inserted between a temperature gradient.
Two diodes are placed between a temperature gradient to measure the voltage across which is proportional to the absolute temperature.

## Slide 11: Critical Temperature Cut-Off
Matthew Zawiski
Rate of Temperature Increase
Maximum/Minimum Absolute Temperature
This first method will be calibrated based off of a neutral temperature and then track rapidly changing temperatures towards both extremes (hot or cold).
Car’s internal temperature can rise from 70 to 115 degrees in about an hour or 0.75 degrees per minute (Jon, 2018).
This second method will work based on a specified temperature at each extreme.
Rise in temperature between the car and infant is approximately 4.5:1 degrees.
Possible fever after the car’s temperature rises above 84 degrees Fahrenheit.
Notes: System calibrated to 84 degrees farenheit

## Slide 12: Secondary Response Device
Matthew Zawiski
Key Fob
Pager
Smart Watch
Phone App
Resembles a car key fob that can be carried on a key ring.
Consists of buttons and a small screen to display messages and temperature inside car.
An app that connects to the primary device for it to send messages.
The app will also provide up-to-date readings of the inside car temperature.
A watch that can be worn to receive quick alerts.
A simple solution that can be attached to the waist and display short messages.

## Slide 13: Concept Selection
Eight designs were chosen for evaluation.
A few selection methods were carried out including:
  House of Quality (HOQ)
  Pugh Matrices
  Analytical Hierarchy Process (AHP)
This gave the final concept to move forward with.
Matthew Zawiski

## Slide 14: House of Quality
Customer needs compared to engineering characteristics based on a 1,3,9 scale.
Pairwise comparison evaluated to determine importance of customer requirements.
Engineering characteristics were ranked based on the calculated relative weight.
Matthew Zawiski
Notes: A 1 being least impactful and 9 being most impactful

## Slide 15: Competitor - Elpho eClip (Inc., E., 2018)
Easy setup and universal with all straps.
Low energy source with the use of Bluetooth.
Alerts user through smart phone app.
Detects when user is more than 15 feet away from the car.
Matthew Zawiski
Monitors temperature in the back of the car while car is on and off.
Baby proof, no choking hazards, baby incapable to turn off device.

## Slide 16: Pugh Matrix #1
Matthew Zawiski
 |  | Concepts |  |  |  |  |  |  | 
Selection Criteria | Elpho eClip | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Detects Minimum Passenger Weight | Datum | Same | Same | Same | Same | Plus | Same | Same | Plus
Detect - Alert - Reaction Time |  | Minus | Same | Minus | Same | Plus | Same | Minus | Plus
Critical Car Temperature |  | Plus | Plus | Plus | Same | Same | Plus | Plus | Plus
Displays Passenger Vitals |  | Plus | Plus | Plus | Same | Same | Same | Plus | Same
Compatibility with Car Seat |  | Minus | Same | Minus | Minus | Same | Same | Minus | Same
Operate in Distance Range |  | Plus | Same | Plus | Same | Plus | Minus | Same | Same
Displays Temperature Ranges |  | Plus | Plus | Plus | Plus | Plus | Same | Plus | Plus
Alert Tone to User |  | Plus | Same | Plus | Same | Plus | Same | Same | Same
Initial Temperature Detection |  | Same | Same | Same | Same | Same | Same | Same | Same
SOS Signal to Emergency Personnel |  | Plus | Plus | Plus | Plus | Plus | Plus | Plus | Plus
# of Pluses |  | 6 | 4 | 6 | 2 | 6 | 2 | 4 | 5
# of Minuses |  | 2 | 0 | 2 | 1 | 0 | 1 | 2 | 0
Notes: Mention elpho e clip on datum
Mention Top 10 engineering characteristics were used most important at the top
Talk about how concept 8 was used for datum because of the differential of 5 with pluses in the most important categories

## Slide 17: Pugh Matrix #2
Matthew Zawiski
 |  | Concepts |  |  |  | 
Selection Criteria | 8 | 1 | 2 | 3 | 5 | 7
Detects Minimum Passenger Weight | Datum | Same | Minus | Minus | Same | Same
Detect - Alert - Reaction Time |  | Minus | Same | Minus | Same | Minus
Critical Car Temperature |  | Same | Same | Same | Minus | Same
Displays Passenger Vitals |  | Plus | Plus | Plus | Same | Plus
Compatibility with Car Seat |  | Minus | Same | Minus | Same | Minus
Operate in Distance Range |  | Plus | Same | Plus | Plus | Same
Displays Temperature Ranges |  | Same | Same | Same | Same | Same
Alert Tone to User |  | Plus | Same | Plus | Same | Same
Initial Temperature Detection |  | Same | Same | Plus | Minus | Plus
SOS Signal to Emergency Personel |  | Same | Same | Same | Same | Same
# of Pluses |  | 3 | 1 | 4 | 1 | 2
# of Minuses |  | 2 | 1 | 3 | 2 | 2
Notes: Concepts 4 and 6 were eliminated.
Concept 8 was shifted to datum for re-evaluation.

## Slide 18: Pugh Matrix #3
Narrowed down to three final designs: 1,2,7
Analytical Hierarchy process was completed next to establish numerical weights for each engineering characteristic and design concept.
Matthew Zawiski
 |  | Concepts |  | 
Selection Criteria | 3 | 1 | 2 | 7
Detects Minimum Passenger Weight | Datum | Plus | Same | Plus
Detect - Alert - Reaction Time |  | Same | Plus | Same
Critical Car Temperature |  | Same | Same | Same
Displays Passenger Vitals |  | Same | Same | Same
Compatibility with Car Seat |  | Same | Plus | Same
Operate in Distance Range |  | Same | Minus | Minus
Displays Temperature Ranges |  | Same | Same | Same
Alert Tone to User |  | Same | Minus | Minus
Initial Temperature Detection |  | Minus | Minus | Same
SOS Signal to Emergency Personel |  | Same | Same | Same
# of Pluses |  | 1 | 2 | 1
# of Minuses |  | 1 | 3 | 2

## Slide 19: Concept Selection
Highest value was initially chosen for the final design, which was concept seven.
  Heart Rate Monitor Bracelet
However, after gauging public opinion, concept two was more practical.
Therefore, concept two was chosen to move forward with.
Matthew Zawiski
Concepts | Alternative Value
1 | 0.1744
2 | 0.2860
7 | 0.5396
Table 1: Alternative Values for the Final Three Concepts

## Slide 20: Final Design
Matthew Zawiski
The final design was determined to be concept 2, which is the combination of:
  A baby monitor attached to the car seat buckles
  A positive/ negative temperature coefficient thermistor
  Rate of temperature increase
  A Key Fob
Team plans on creating a clip system large enough to encompass microcontroller and temperature sensors.
  similar to the standard baby harness clips.
Proximity sensors in the clip ends will tell if clips are secured together indicating the presence of a child.

## Slide 21: Final Design Drawlings
Matthew Zawiski

## Slide 22: Bill of Materials
Matthew Zawiski
Category | Part | Part # | Part Description | Quanity | Units | Cost ($) / Unit | Tax ($) | Shipping Cost ($) | Total Cost ($)
Electronics |  |  |  |  |  |  |  |  | 
 | Arduino UNO REV3 Board | 1 | Microcontroller board | 1 | 2 | 22.00 | 2.64 | 8.50 | 55.14
 | Electronic Component Pack | 2 | Includes resistors, LEDs, buttons,potentiometer | 250 | 1 | 6.86 | 0.41 | 9.98 | 17.25
 | Wires Ribbon Cables Kit for Arduino | 3 | Includes 40 male-female, 40 male-male, 40 female-female | 120 | 1 | 6.98 | 0.42 | 9.98 | 17.38
 | Arduino speaker | 4 | Mini speaker to give off alert sound | 2 | 1 | 8.98 | 0.54 | 9.98 | 19.50
 | Mini Bread Borad | 5 | 170-Point mini bread board to create portable circuits | 2 | 1 | 2.55 | 0.15 | 8.50 | 11.20
 | LCD Display | 6 | Transmissive LCD Character Display to display messages | 1 | 4 | 8.10 | 1.94 | 8.50 | 42.84
 | ECR2032 Battery | 7 | Small battery used for power source | 10 | 1 | 4.60 | 0.28 | 9.98 | 14.86
 | Battery Holder | 8 | 2 terminal battery holder for ECR2032 batteries | 1 | 1 | 5.89 | 0.35 | 9.98 | 16.22
 | Receiver | 9 | 433 MHz reciever, located in the key fob, receives signal from the clip | 1 | 1 | 6.66 | 0.40 | 9.98 | 17.04
 | Transmitter | 10 | Located in the clip, sends a signal to key fob (Sold as kit with reciever) | 1 | 0 | 0.00 | 0.00 | 0.00 | 0.00
 | Power Switch | 11 | Switch to turn device on, off, or put in sleep mode | 10 | 1 | 4.17 | 0.25 | 9.98 | 14.40
Casing |  |  |  |  |  |  |  |  | 
 | 3-D Print Filament | 12 | PLA 3D Printer Filliment - Blue used to 3D print the housing of both devices | 1 | 1 | 19.99 | 1.20 | 9.98 | 31.17
 | Screws | 13 | Screws to keep casings for both devices together | 1100 | 1 | 4.99 | 0.30 | 9.98 | 15.27
 | Key Ring | 14 | Keeps the key fob connected to keychains | 50 | 1 | 3.95 | 0.24 | 9.98 | 14.17
Sensors |  |  |  |  |  |  |  |  | 
 | Reed Magnetic Switch | 15 | Magnetic switch used to determine when clip is connected | 1 | 1 | 0.79 | 0.05 | 7.99 | 8.83
 | Thermistors | 16 | NTC Thermistor Temperature Sensor Module for Arduino to measure temperature | 1 | 1 | 1.87 | 0.11 | 0 | 1.98
Total Cost ($) : | 297.25

## Slide 23: Bill of Materials cont.
Project Composition: 40% Ordering/Receiving Parts 60% Assembling the Device
Yes = 1, No = 0
Currently 2.35 % of the project is completed
Matthew Zawiski
Amount of Category Completed (%) | 5.882 | 5.882 | 5.882
Weight of Importance (%) | 15 | 5 | 20
Total Amount of Project Completed (%) | 2.353 |  | 
Purchased | Shipped | Received
No | No | No
No | No | No
No | No | No
No | No | No
No | No | No
No | No | No
No | No | No
No | No | No
No | No | No
No | No | No
No | No | No
Yes | Yes | Yes
No | No | No
No | No | No
No | No | No
No | No | No
Category | Part | Part #
Electronics |  | 
 | Arduino UNO REV3 Board | 1
 | Electronic Component Pack | 2
 | Wires Ribbon Cables Kit for Arduino | 3
 | Arduino speaker | 4
 | Mini Bread Borad | 5
 | LCD Display | 6
 | ECR2032 Battery | 7
 | Battery Holder | 8
 | Receiver | 9
 | Transmitter | 10
 | Power Switch | 11
Casing |  | 
 | 3-D Print Filament | 12
 | Screws | 13
 | Key Ring | 14
Sensors |  | 
 | Reed Magnetic Switch | 15
 | Thermistors | 16

## Slide 24: Future Work
Risk Assessment
Poster (Summary of Project)
Ordering Parts
  Purchase all parts by end of semester for them to arrive on time
Prototype & Building
  Coding
  Assembly
Testing
David Miller

## Slide 25: References
Geggel, L. (2018, May 24). How Long Does It Take a Parked Car to Reach Deadly Hot
Temperatuers? Retrieved from Live Science: https://www.livescience.com/62651-how-hot-cars-get.html
Inc., E. (2018). eClip: Helping to pervent babies from being left in cars. Retrieved from Kickstarter:
https://www.kickstarter.com/projects/1745478023/eclip-helping-to-prevent-babies-from-being-left-in
Jon. (2018). How hot can the interior of a car get - and how quickly? Retrieved from Heat Kills:
http://heatkills.org/how-hot/
Notes: Not this slide will advance on default after 2 seconds. If you would like to change this then go to the transition tab and under timing change the advance slide settings.

## Slide 26: Questions?

## Slide 27: Backup Sildes
Supporting Slides to the content above.

## Slide 29: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 30: Approved Logos

## Slide 31: Color Palette

## Slide 32: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |