## Slide 1
Team 501: Powder Recovery for Metal Additive Manufacturing
Arlan Ohrt
Kevin Richter
Vincent Giannetti
Noah Tipton
Joshua Dorfman
November 7th, 2019

## Slide 2: Team Introductions
Arlan Ohrt
Project/Systems Engineer
Kevin Richter
Field
Engineer
Noah Tipton
Design
Engineer
Vincent Giannetti
Manufacturing
Engineer
Joshua Dorfman
Field
Engineer

## Slide 3
Sponsor – Air Force Research Labs (AFRL)
AFRL/RWMW – Ordnance Division, Damage Mechanisms Branch (Eglin Air Force Base)
  A global leader in advancing weapons science and technology
Specific Contact - Dr. Philip Flater
  Lead for the metal additive manufacturing lab at AFRL/RWMW
Joshua Dorfman

## Slide 4
Project Description
The objective of this project is to design a device which increases the amount of recovered steel powder in a metal additive manufacturing process. This device should be compatible with existing hardware and processes while ensuring the safety of the operators.
Joshua Dorfman

## Slide 5
The Three ‘R’s
Recover
Recycle
Remove
Joshua Dorfman

## Slide 6
Project Background – Metal Additive Manufacturing
Laser Powder Bed Fusion (LPBF):
Powder Distributed in an Even Layer
Laser Traces Layer Path to “Fuse” Material Together
AFRL’s operating 3D printer is the 3D Systems ProX 300
This process results in a large amount of “unfused” powder. This powder should be recycled.
Joshua Dorfman

## Slide 7
Project Background – Metal Additive Manufacturing
Laser Powder Bed Fusion (LPBF):
Powder Distributed in an Even Layer
Laser Traces Layer Path to “Fuse” Material Together
Joshua Dorfman
This process results in a large amount of “unfused” powder. This powder should be recycled.

## Slide 8
Project Background – Metal Additive Manufacturing
Roller
Overflow
Build Plate
Powder Supply
Joshua Dorfman

## Slide 9
Project Background – The Metal Used
Joshua Dorfman
General Info:
Purchasable from 3D Systems
Particle Size: 10 – 15 μm (Paper thickness is ~ 100 μm)
Martensitic Steel (Magnetic)
17– 4PH Stainless Steel: 17% Chromium, 4% Nickel, Precipitation Hardening

## Slide 10
Project Background – The Metal Used
Joshua Dorfman
General Info:
Purchasable from 3D Systems
Particle Size: 10 – 15 μm (Paper thickness is ~ 100 μm)
Martensitic Steel (Magnetic)
17– 4PH Stainless Steel: 17% Chromium, 4% Nickel, Precipitation Hardening

## Slide 11
Joshua Dorfman
Project Background – Powder Recovery Stages
“Wet Vac Stage”
“Air Powered Stage”
“Built In Stage”

## Slide 12
Joshua Dorfman
Project Background – Powder Recovery Stages
Stage 1 – “Built In Stage”
Built in recovery system
  Vacuum
  Overflow Reservoir
Operation
  Sealed chamber
  Glove to operate vacuum
Significant Powder Recovery

## Slide 13
Joshua Dorfman
Project Background – Powder Recovery Stages
Stage 2 – “Wet Vac Stage”
Removing the part
  Pass the build plate out
Operation
  Use powered air purifying respirator (PAPR)
  Open door and remove part
  Use Ruwac NA35 Immersion Vacuum
No Powder Recovery

## Slide 14
Joshua Dorfman
Project Background – Powder Recovery Stages
Stage 3 – “Air Powered Stage”
Sandblasting cabinet
Operation
  Place part inside the enclosure
  Use compressed air to remove residual powder
No Powder Recovery

## Slide 15
Joshua Dorfman
Project Background – Integration
Where Our System Can Go
“Wet Vac Stage”
“Air Powered Stage”
“Built In Stage”

## Slide 16
Joshua Dorfman
Project Background – Integration
Significant Powder Recovery
No Powder Recovery
Our System
Significant Powder Recovery

## Slide 17
Joshua Dorfman
Project Background – Integration
Our System
Significant Powder Recovery

## Slide 18
Joshua Dorfman
Project Background – Integration
Our System
Significant Powder Recovery

## Slide 19
Noah Tipton
Concept Generation

## Slide 20
Noah Tipton
Concept Generation
Multirotational CNC
Tiny Tube Blower
Spinning Sifter
Hanging Electromagnet
Electrostatic Wand
Encased Low to High Frequency Vibration

## Slide 21
Noah Tipton
Targets and Metrics - Validation
1) Volume
2) Force
Up to Eglin AFB safety standards
Particle Size
1) 250 x 250 x 300 mm
2) 356 N
Passes through 75 μm mesh
Pass Bioenvironmental Engineering Flight (BEF) air test
Metric
Target
Mass
Mass
Greater than 0 grams of separated powder in container
Recover Powder
Manage Powder
Support the Part
Inhibit Powder
Separates powder from the part
Transports powder
to a container
Isolate the powder
from user
Hold the part
in the area
Prevents powder contamination

## Slide 22
Noah Tipton
Targets - Manage the Powder
We can use our product after part removal from the printer
Currently, no powder is recovered after printer removal
Any recovered powder is an improvement
No values have been measured for comparison
No Powder Recovery
Target: Greater than 0 grams of powder

## Slide 23
Noah Tipton
Target - Hold the Part
Build volume: 250 x 250 x 300 mm (~ 1 )
Over assumed part load: 356 N (~80 lb)
Target 1: Allow a volume greater than build volume
Target 2: Hold 356 N or more

## Slide 24
Noah Tipton
Eglin Air Force Base – Bioenvironmental Engineering Flight (BEF) Air Sampling
Contaminants in air must not exceed Occupational Environmental Exposure Limits (OEEL)
Target: Pass the BEF air sample test once product is in use
Target – Isolate the Powder From the User

## Slide 25
Noah Tipton
Recommended to run powder through 75 μm mesh to remove contaminants
Particle shape and chemistry will not be a concern unless prints turn out bad
Target: Recovered powder passes through 75 μm stainless steel mesh
Target – Prevent Powder Contamination

## Slide 26
Arlan Ohrt
Concept Selection

## Slide 27
Arlan Ohrt
Concept Selection
Methods:
House of Quality
Pugh Charts
Analytical Hierarchy Process (AHP)
 |  | Engineering Characteristics |  |  |  |  |  | 
Improvement Direction |  | ↑ | ↑ | ↑ | ↑ | ↑ | ↓ | ↓
Units |  | Gram | Gram | Newton | Cubic Meter | Eglin AFB BEF Test | Pass through Mesh | Seconds
Customer Requirements | Importance Weight Factor | Amount of Separated Powder | Amount of Contained Powder | Supportable Load | Operable Volume | Met Safety Standards | Contamination | Added Time to Overall Process
Separate More Powder From the Part | 4 | 9 | 3 |  | 1 |  |  | 1
Recover the Separated Powder | 3 | 3 | 9 |  | 1 |  |  | 
Prevent Powder Contamination | 5 | 1 | 1 |  |  |  | 9 | 
Hold the Part During Process | 1 | 3 |  | 9 | 9 |  |  | 
Ensure Operator Safety | 5 |  |  | 3 |  | 9 |  | 
Integrate With Current System | 2 |  |  |  |  |  |  | 9
Raw Score | 249 | 53 | 44 | 24 | 16 | 45 | 45 | 22
Relative Weight % |  | 21.29 | 17.67 | 9.64 | 6.43 | 18.07 | 18.07 | 8.84
Rank Order |  | 1 | 4 | 5 | 7 | 2 | 2 | 6

## Slide 28
Arlan Ohrt
Concept Selection
Methods:
House of Quality
Pugh Charts
Analytical Hierarchy Process (AHP)
 |  | Concepts |  |  |  |  |  |  | 
Engineering Characteristics | Current Recovery Process | Tiny Tube Blower | Encased Low to High Frequency Vibration | Hanging Faucet Electromagnet | Electrostatic Brush | CNC Axis Part Mover | Spinning Sifter | Vibration Through all Stages | Multi-Directional Vibration
Amount of Separated Powder | DATUM | + | + | + | + | + | + | + | +
Amount of Contained Powder |  | + | + | + | + | + | + | + | +
Supportable Load |  | S | S | S | S | - | - | - | -
Operable Volume |  | S | S | S | S | S | S | S | S
Met Safety Standards |  | S | S | S | S | S | S | S | S
Contamination |  | S | + | S | S | S | + | S | S
Added Time to Overall Process |  | - | - | - | S | S | - | - | -
Total + |  | 2 | 3 | 2 | 2 | 2 | 3 | 2 | 2
Total - |  | 1 | 1 | 1 | 0 | 1 | 2 | 2 | 2

## Slide 29
Arlan Ohrt
Concept Selection
Methods:
House of Quality
Pugh Charts
Analytical Hierarchy Process (AHP)
 |  | Concepts |  |  |  |  |  |  | 
Engineering Characteristics | Current Recovery Process | Tiny Tube Blower | Encased Low to High Frequency Vibration | Hanging Faucet Electromagnet | Electrostatic Brush | CNC Axis Part Mover | Spinning Sifter | Vibration Through all Stages | Multi-Directional Vibration
Amount of Separated Powder | DATUM | + | + | + | + | + | + | + | +
Amount of Contained Powder |  | + | + | + | + | + | + | + | +
Supportable Load |  | S | S | S | S | - | - | - | -
Operable Volume |  | S | S | S | S | S | S | S | S
Met Safety Standards |  | S | S | S | S | S | S | S | S
Contamination |  | S | + | S | S | S | + | S | S
Added Time to Overall Process |  | - | - | - | S | S | - | - | -
Total + |  | 2 | 3 | 2 | 2 | 2 | 3 | 2 | 2
Total - |  | 1 | 1 | 1 | 0 | 1 | 2 | 2 | 2

## Slide 30
Arlan Ohrt
Concept Selection
Methods:
House of Quality
Pugh Charts
Analytical Hierarchy Process (AHP)
 |  | Concepts |  |  | 
Engineering Characteristics | Electrostatic Brush | Tiny Tube Blower | Encased Low to High Frequency Vibration | Hanging Faucet Electromagnet | CNC Axis Part Mover
Amount of Separated Powder | DATUM | S | + | - | S
Amount of Contained Powder |  | + | + | - | S
Supportable Load |  | S | S | S | -
Operable Volume |  | S | S | S | S
Met Safety Standards |  | S | S | S | S
Contamination |  | + | + | S | +
Added Time to Overall Process |  | S | - | S | S
Total + |  | 2 | 3 | 0 | 1
Total - |  | 0 | 1 | 2 | 1

## Slide 31
Arlan Ohrt
Concept Selection
Methods:
House of Quality
Pugh Charts
Analytical Hierarchy Process (AHP)
 |  | Concepts |  |  | 
Engineering Characteristics | Electrostatic Brush | Tiny Tube Blower | Encased Low to High Frequency Vibration | Hanging Faucet Electromagnet | CNC Axis Part Mover
Amount of Separated Powder | DATUM | S | + | - | S
Amount of Contained Powder |  | + | + | - | S
Supportable Load |  | S | S | S | -
Operable Volume |  | S | S | S | S
Met Safety Standards |  | S | S | S | S
Contamination |  | + | + | S | +
Added Time to Overall Process |  | S | - | S | S
Total + |  | 2 | 3 | 0 | 1
Total - |  | 0 | 1 | 2 | 1

## Slide 32
Arlan Ohrt
Concept Selection
Methods:
House of Quality
Pugh Charts
Analytical Hierarchy Process (AHP)
 |  | Concepts |  |  | 
Engineering Characteristics | Electrostatic Brush | Tiny Tube Blower | Encased Low to High Frequency Vibration | Hanging Faucet Electromagnet | CNC Axis Part Mover
Amount of Separated Powder | DATUM | S | + | - | S
Amount of Contained Powder |  | + | + | - | S
Supportable Load |  | S | S | S | -
Operable Volume |  | S | S | S | S
Met Safety Standards |  | S | S | S | S
Contamination |  | + | + | S | +
Added Time to Overall Process |  | S | - | S | S
Total + |  | 2 | 3 | 0 | 1
Total - |  | 0 | 1 | 2 | 1

## Slide 33
Arlan Ohrt
Concept Selection
Methods:
House of Quality
Pugh Charts
Analytical Hierarchy Process (AHP)
The 19 Matrices of Work Will Not Be Covered

## Slide 34
Arlan Ohrt
Selected Concept
Encased Low to High Frequency Vibration
Function
Separates
Contains
Holds
Isolates
Non-Contaminated
Design Aspect
Vibration
Funnel + Gravity
Upside-Down
Enclosure
Dedicated
Target
Over 0 grams
Force & Volume
BEF Test
75 μm Mesh

## Slide 35
Arlan Ohrt
Selected Concept
Encased Low to High Frequency Vibration
Function
Separates
Contains
Holds
Isolates
Non-Contaminated
Design Aspect
Vibration
Funnel + Gravity
Upside-Down
Enclosure
Dedicated
Target
Over 0 grams
Force & Volume
BEF Test
75 μm Mesh
F

## Slide 36
Arlan Ohrt
Selected Concept
Encased Low to High Frequency Vibration
Function
Separates
Contains
Holds
Isolates
Non-Contaminated
Design Aspect
Vibration
Funnel + Gravity
Upside-Down
Enclosure
Dedicated
Target
Over 0 grams
Force & Volume
BEF Test
75 μm Mesh
F

## Slide 37
Arlan Ohrt
Selected Concept
Encased Low to High Frequency Vibration
Function
Separates
Contains
Holds
Isolates
Non-Contaminated
Design Aspect
Vibration
Funnel + Gravity
Upside-Down
Enclosure
Dedicated
Target
Over 0 grams
Force & Volume
BEF Test
75 μm Mesh
Powder Recovery ONLY

## Slide 38
Arlan Ohrt
Selected Concept
Encased Low to High Frequency Vibration
Function
Separates
Contains
Holds
Isolates
Non-Contaminated
Design Aspect
Vibration
Funnel + Gravity
Upside-Down
Enclosure
Dedicated
Target
Over 0 grams
Force & Volume
BEF Test
75 μm Mesh
Powder Recovery ONLY

## Slide 39
Arlan Ohrt
Refining the Concept

## Slide 40
Arlan Ohrt
Refining the Concept – Post Eglin Visit

## Slide 41
Arlan Ohrt
Refining the Concept – Enclosure
Cart Benefits:
Size
Maneuverability
Dedicated Interior, Free Exterior

## Slide 42
Arlan Ohrt
Refining the Concept – Vibration

## Slide 43
Arlan Ohrt
Refining the Concept – Damping

## Slide 44
Arlan Ohrt
Refining the Concept – Holding Part

## Slide 45
Arlan Ohrt
What is Next?
Future Work:
Continue Refining Design
Continue Specifying Needed Parts
Finalize for Assembly, Testing, and Refinements in the Spring
Explore the utilization of nodal frequency

## Slide 46
Arlan Ohrt
Title Slide Background - https://www.materialise.com/en/blog/when-how-and-where-of-metal-3d-printing
Lost and Found - https://www.portseattle.org/sites/default/files/2019-08/bigstock_lost_1140.jpg?slideshow=true&slideshowAuto=false&slideshowSpeed=4000&speed=350&transition=elastic
Recycle Bin - http://fridandrussell.com/SH_productdetail.asp?Ino=61517U06C&Company=STX
Painter’s Tape - https://www.scotchblue.com/3M/en_US/scotchblue/proper-tape-removal/
3D Systems – https://www.3dsystems.com/3d-printers/prox-dmp-300/specifications
LPBF Demo GIF - https://thescopepopculturescience.blogspot.com/2015_01_01_archive.html
Stainless Steel Properties - https://www.3dsystems.com/materials/metal
nTopology – https://ntopology.com/
PAPR – https://images-na.ssl-images-amazon.com/images/I/4125zPcBPNL.jpg
Sandblaster - https://badboyblasters.com/product/abrasive-media-sand-blaster-bb1050led-bvr-pr-hv-fl-2/
AFRL Sign - https://news.wfsu.org/post/eglin-air-force-base-ready-adjust-hiring-freeze
Electric Vibrator - https://www.mcmaster.com/5808k61
Dampeners - https://www.mcmaster.com/29895t54 , https://www.mcmaster.com/9241k44
References

## Slide 47
Team 501: Powder Recovery for Metal Additive Manufacturing
Arlan Ohrt
Kevin Richter
Vincent Giannetti
Noah Tipton
Joshua Dorfman
November 7th, 2019

## Slide 48
Return
Backup Slides

## Slide 49
Return
Backup Slides
Functional Decomposition
Group Member Contact
nTopology
Precipitation Hardening Explained
17- 4PH Material
3D Systems Printer Specs

## Slide 50
Return

## Slide 51
Return

## Slide 52
Group Contact
Return
Arlan Ohrt
ago16b@my.fsu.edu
Kevin Richter
kr15@my.fsu.edu
Noah Tipton
nrt15@my.fsu.edu
Vincent Giannetti
vjg15b@my.fsu.edu
Joshua Dorfman
jd16s@my.fsu.edu

## Slide 53
Functional Decomposition
Recover Powder
Manage Powder
Holds the part in the area
Transports powder to a container
Separates powder from the part
Insulates the user from powder
Prevents powder contamination
Support the Part
Inhibit Powder
Return

## Slide 54
Precipitation Hardening Explained
The strength and hardness of some materials can be increased by the formation of very small particles
This is done through heat treatments
It is called “Precipitation Hardening” because the process results in very small particles, called “Precipitates”
This works because precipitates help block dislocation motion, which is an important aspect of a materials failure and properties
Return
http://www.engineeringenotes.com/metallurgy/age-hardening-treatment/age-hardening-treatment-of-metals-metallurgy/26376

## Slide 55
17- 4PH Stainless Steel
Return
https://www.3dsystems.com/sites/default/files/2017-06/3D-Systems_17-4_PH_%28B%29_DMP_DATASHEET_US_A4_2017.06.21_WEB.pdf

## Slide 56
Arlan Ohrt

## Slide 57: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 58: Approved Logos

## Slide 59: Color Palette

## Slide 60: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |