## Slide 1
5. Raspberry pi sends data to Arduino from sensors to initiate package retrieval.
Team 311: Autonomous Material Handling Robot
Sebastian Muriel, Alexandar Jen, Walter Caldwell, Tony Zheng
The objective of this project is to create a partially autonomous material handling robot that works in a dark warehouse with conditions unfavorable to human workers.
Dark warehouses with increased automation are more cost effective overtime.
Many warehouse injuries related to overexertion/bodily reactions, contact with equipment, and forklifts.
Estimated average electricity consumption of 6.6kWh per square foot for a warehouse, or roughly 23.7 MJ per square foot.
Autonomous movement
Safely lift 25 pound load
Dark warehouse navigation
Objective
Project Background
Goals
Retrieve and deliver packages to specified drop off location
Obstacle Detection
4. Independently controlled omni-directional wheels
2. Infrared line following
3. Pulley-motor connection for lifting
1. Forklift-style package manipulation
3
1
4
2
The user wirelessly connects to the pi server using the ip tunnel. The NodeJS then communicates the command desired by the user and executes it in the Mongodb database. The result status is then sent back through the tunnel to update the user.
5
6
6. Pi camera scans QR code and initiates pick up.
Notes: Objective
Background/ Motivation
Assumptions
Functional Decomposition
Critical targets
Locomotion
    Omni-directional wheels
    Power Supply
    Motors
  Manipulation
    Forks
    Pulley
    Slider
  Navigation
    Line path
    Ultrasonic Sensor
    Infrared Sensor
    Pi camera + wide lense
  Inventory Tracking
    Arduino
    Raspberry pi
    QR code