## Slide 1
Team 514: Hydrogen Pre-Heater in the Nuclear Thermal Rocket Simulation
Michael Corak – Kevin Hartzog – Fisher Hillburn – Jordan Weid
Background/Motivation
NASA's NTREES (Nuclear Thermal Rocket Element Environment Simulator) currently simulates the conditions found in a nuclear fuel element in a nuclear thermal rocket with a 20-inch test article. The true size on the rocket is 50 inches, so in order to properly simulate varying temperatures across the true length, a pre-heater must be used. The images below show what a temperature profile might look like with axial distance and a comparison of the true length to simulation length.
Governing Physics
Project Description
The objective of this project is to create a device that allows for independent control of the inlet temperatures of hydrogen supply to the test articles and mounts to a variety of test article shapes and sizes.
Selected Design
Induction coil
H2
No radiation heat transfer
Constant heat flux
Ideal gas
All heat transfer on surface of heat exchanger enters fluid
Thermal Resistance Network
Assumptions
Test article
Selected Design Characteristics
Control – Potentiometer
Heating – Induction Heating
Mounting - Composite plate
Heat Exchanger Shape - Cylindrical
Interface to Test Article – Not yet decided
CAD Rendering