## Slide 1
1
Virtual Design Review 2
Team 515
December 1, 2020
Reusable Shock Absorber for New Lunar Lander

## Slide 2: Team Members
2
Josh Blank
Design Engineer
Alex Noll
Mechanical Engineer
Matt Fowler
Systems Engineer
Tristan Jenkins
Design Engineer
Melanie Porter
Dynamics Engineer
Team Members
Tristan Jenkins

## Slide 3: Sponsor & Advisor
Sponsor & Advisor
Project Sponsor
Rachel McCauley
MSFC Advanced Concepts Deputy Manager at NASA
Academic Advisor
Keith Larson
Teaching Faculty I
Tristan Jenkins

## Slide 4
To design a reusable device for the human lander system that will dissipate the impact energy in such a way that it does not damage the vessel or occupants.
Objective
Tristan Jenkins

## Slide 5: Project Description
Project Description
Tristan Jenkins

## Slide 6: Apollo Shock Absorber
Apollo Shock Absorber
LANDING GEAR ASSEMBLY
ALUMINUM HONEYCOMB VISUAL AID
LANDING GEAR PRIMARY STRUT
[1]
[1]
Tristan Jenkins

## Slide 7: Functions
Functions
Shock Absorber
Link
Support
Impact Reduction
Reusability
Absorb Impact Energy
Dampen Vibrations
Transform Energy
Returns to original state
Indicate Reusability
Support Mass
Absorb Shock
Dissipate Energy
Store Energy
Prevent Excessive Rebound
Tristan Jenkins

## Slide 8
Absorb Impact Energy
Functions
Absorb Structural Shock
Support Mass
Return to Original State
Prevent Excessive Rebound
Transform Energy
Dampen Vibrations
Dissipate Energy
Store Energy
~145 kJ
Targets
3 g’s
~25,000 kg
≤ 10 hours
Rebound < 0.5 m
KEfinal = 0
Settling time < 2 s
≤ 10 hours
~145 kJ
Indicate Reusability
Proves 100% Reusability
Withstand Lunar Conditions
Lifespan of 10 years
Metric
System remains elastically ductile when subjected to up to 3 g's of acceleration.
All kinetic energy from impact is absorbed into the system as it brings the structure to rest.
Through dissipation of stored energy and/or active reversion, the system returns exactly to original parameters within the time limit.
Sensors monitor parameter values over time including when parameters return to initial values.
Materials and geometry of the structure statically supports the mass under Earth and Moon gravity without plastic deformation.
Melanie Porter

## Slide 9
Leaf Springs
2
1
Top Concepts
Scissor Jack
Spring Mounted Weights
4
3
Electromagnetic Core
Spider Legs
6
5
Compliant Mesh
Inverted Tripod
8
7
Locking Spring
Concept Generation
Melanie Porter

## Slide 10
Selection Process
Defines the relationship between customer needs and engineering characteristics.
Used to determine the important qualities for the Pugh Chart.
House of Quality
Pugh Charts
Compares multiple concepts at once.
Used Apollo 11 shock absorber as datum and eliminated concepts.
Picked a new datum for second Pugh chart
Melanie Porter
Notes: Before we get into the details of each concept, let’s explain how our selection process worked. We first performed a house of quality to help us understand the relation between customer needs and engineering characteristics. We then used the outcome from the house of quality to set up our Pugh chart. For our first Pugh chart we compared our top 8 ideas to the Apollo class shock absorber. We then pulled out our top 3 ideas and a new datum to compare in our second Pugh chart.

## Slide 11
Leaf Springs
2
1
Top Concepts
Scissor Jack
Spring Mounted Weights
4
3
Electromagnetic Core
Spider Legs
6
5
Compliant Mesh
Inverted Tripod
8
7
Locking Spring
D
Selection Process
Melanie Porter

## Slide 12
Con
Josh Blank
Concept #6
Concept Generation
Spider Legs
Team 515
Page 1/4
Rotary Friction Dampers
Positioning Springs

## Slide 13
Con
Josh Blank
Concept #2
Concept Generation
Leaf Springs
Team 515
Page 2/4
Leaf Springs
Footpad ‘axle’

## Slide 14
Con
Concept #4
Weighted Springs
Team 515
Concept Generation
Josh Blank
Page 3/4

## Slide 15
Con
Concept #7
Concept Generation
Locking Springs
Team 515
Extended
Compressed
Solenoid
Ratchet
Spring Pawl
Josh Blank
Page 4/4

## Slide 16
Concept Selection
Leaf Springs
2
Top Concepts
Spring Mounted Weights
4
7
Locking Spring

Josh Blank

## Slide 17
Locked Spring Design
Temperature variations have little impact.
Recycles impact energy
Effectively absorbs energy and precludes vibrations.
Josh Blank
Concept Selection

## Slide 18
Looking Forward
Locking Mechanism
Testing Methods
3D Drawings
Josh Blank

## Slide 19: Thank You
View of Apollo 14 Lunar Module on the Moon

## Slide 20
References
[1] Rodgers, W. F. (1972). Apollo Experience Report – Lunar Module Landing Gear Subsystem (NASA TN 0-6850). Washington , D.C. : National Aeronautics and Space Administration.
[2] INCO. (1974). Materials for Cryogenic Service: Engineering Properties of Austenitic Stainless Steels. Nickle Development Institute .

## Slide 21: Backup Slides

## Slide 22: Back Up Project Description

## Slide 23: Back Up Functional Decomp
Functional Decomposition Cross Reference Table. Rows more important than columns |  |  |  |  |  |  |  |  |  | 
 | Withstand Shock | Support Weight | Absorb Impact Energy | Dampen Vibrations | Prevent Excessive Rebound | Transform Energy | Dissipate Energy | Store Energy | Return to Origingal State | Sum
Withstand Shock | - | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 7
Support Weight | 0 | - | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 6
Absorb Impact Energy | 1 | 1 | - | 1 | 1 | 1 | 1 | 1 | 1 | 8
Dampen Vibrations | 0 | 0 | 0 | - | 0 | 0 | 1 | 1 | 0 | 2
Prevent Excessive Rebound | 0 | 0 | 0 | 1 | - | 1 | 1 | 1 | 0 | 4
Transform Energy | 0 | 0 | 0 | 1 | 0 | - | 1 | 1 | 0 | 3
Dissipate Energy | 0 | 0 | 0 | 0 | 0 | 0 | - | 1 | 0 | 1
Store Energy | 0 | 0 | 0 | 0 | 0 | 0 | 0 | - | 0 | 0
Return to Origingal State | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | - | 5
Rank | 2 | 3 | 1 | 7 | 5 | 6 | 8 | 9 | 4 | 
Rank | Function
1 | Absorb Impact Energy
2 | Withstand Shock
3 | Support Weight
4 | Return to Original State
5 | Prevent Excessive Rebound
6 | Transform Energy
7 | Dampen Vibrations
8 | Dissipate Energy
9 | Store Energy

## Slide 24: Back Up Concept Selection: HoQ
 | Importance rating | Absorb Impact Energy | Absorb Structural Shock | Support Mass | Return to Original State | Indicate Reusability | Prevent Excessive Rebound | Transform Energy | Dampen Vibrations | Dissipate Energy | Store Energy | Withstand Lunar Conditions
The product can be used indefinitely. | 3 | 3 | 2 | 2 | 3 | 2 |  | 1 | 1 | 1 | 1 | 3
The product is lightweight. | 3 |  |  |  |  |  |  |  |  |  |  | 
The product can be sent to the moon and used repeatedly. | 3 | 3 |  | 1 | 3 | 2 |  |  |  |  |  | 3
No routine maintenance is necessary during remainder of each lunar trip. | 1 |  |  |  | 2 | 1 |  |  |  |  |  | 
Shock absorber dynamic qualities does not change or diminish after an impact. | 2 | 2 | 2 | 1 | 1 |  | 1 | 1 |  | 1 | 1 | 
The product can handle an impact speed of 10 feet per second. | 3 | 3 | 3 |  |  |  |  |  |  |  |  | 
The product can support 25,000 kg. | 2 |  | 3 | 3 |  |  | 2 |  |  |  |  | 
The product can land at up to a 10-degree offset from the z-axis. | 1 |  |  |  |  |  | 1 |  |  |  |  | 
Raw Score (total) | 146 | 31 | 21 | 17 | 21 | 13 | 7 | 5 | 3 | 5 | 5 | 18
Relative weight (%) | 100 | 21.23 | 14.38 | 11.64 | 14.38 | 8.90 | 4.79 | 3.42 | 2.05 | 3.42 | 3.42 | 12.33
Rank Order |  | 1 | 2 | 5 | 3 | 6 | 7 | 8 | 11 | 9 | 10 | 4

## Slide 25: Back Up Concept Selection: Pugh 1
 |  | Concept |  |  |  |  |  |  | 
Selection Criteria | Datum | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Absorb Impact Energy | Apollo Shock Absorbers | - | s | + | + | + | s | + | s
Absorb Structural Shock |  | - | + | - | + | + | - | s | s
Support Mass |  | s | s | - | S | s | s | s | s
Return to Original State |  | + | + | + | + | + | + | + | +
Indicate Reusability |  | + | + | + | - | - | + | s | -
Prevent Excessive Rebound |  | - | - | + | + | + | + | + | +
Transform Energy |  | S | + | s | s | s | + | + | s
Dampen Vibrations |  | + | + | + | + | + | - | + | +
Dissipate Energy |  | s | + | s | s | s | + | s | s
Store Energy |  | s | s | s | + | s | + | + | s
Withstand Lunar Conditions |  | - | + | - | - | - | - | s | +
#of pluses |  | 3 | 6 | 5 | 6 | 5 | 6 | 6 | 3
# of minuses |  | 4 | 1 | 3 | 1 | 1 | 3 | 0 | 1

## Slide 26: Back Up Concept Selection: Pugh 2
 | Concepts |  |  | 
Selection Criteria | Datum | 2 | 7 | 4
Absorb Impact Energy | Spider Legs | + | + | S
Absorb Structural Shock |  | + | + | +
Support Mass |  | s | + | -
Return to Original State |  | + | + | S
Indicate Reusability |  | s | - | +
Prevent Excessive Rebound |  | - | + | +
Transform Energy |  | + | + | +
Dampen Vibrations |  | - | + | +
Dissipate Energy |  | s | + | S
Store Energy |  | + | + | S
Withstand Lunar Conditions |  | s | + | -
#of pluses |  | 5 | 10 | 5
# of minuses |  | 2 | 1 | 2

## Slide 27: Back Up Concept Selection: AHP 1
Criteria Matrix [c] |  |  |  |  |  |  |  | 
Customer Needs | Lightweight | Reusable | Dynamic qualities do not change after impact "hopping" | Reduce to <3Gs acceleration | Consistent tooling | handle impact 10ft/s | can support 25000kg | <10 degree offset from z axis
Lightweight | 1.00 | 0.33 | 0.33 | 0.20 | 3.00 | 0.14 | 0.20 | 0.33
Reusable | 3.00 | 1.00 | 3.00 | 0.33 | 5.00 | 0.20 | 0.33 | 3.00
Dynamic qualities do not change after impact | 3.00 | 0.33 | 1.00 | 0.20 | 3.00 | 0.20 | 0.20 | 0.33
Reduce to <3Gs acceleration | 5.00 | 3.00 | 5.00 | 1.00 | 5.00 | 0.33 | 0.33 | 3.00
Consistent tooling | 0.33 | 0.20 | 0.33 | 0.20 | 1.00 | 0.33 | 0.33 | 0.33
handle impact speed 10ft/s | 7.00 | 5.00 | 5.00 | 3.00 | 3.00 | 1.00 | 3.00 | 5.00
can support 32800kg | 5.00 | 3.00 | 5.00 | 3.00 | 3.00 | 0.33 | 1.00 | 5.00
<10 degree offset from z axis | 3.00 | 0.33 | 3.00 | 0.33 | 3.00 | 0.20 | 0.20 | 1.00
Sum | 27.33 | 13.20 | 22.67 | 8.27 | 26.00 | 2.74 | 5.60 | 18.00

## Slide 28: Back Up Concept Selection: AHP 2
Normalized Matrix |  |  |  |  |  |  |  |  | {W}
Lightweight | 0.04 | 0.03 | 0.01 | 0.02 | 0.12 | 0.05 | 0.04 | 0.02 | 0.0403
Reusable | 0.1098 | 0.0758 | 0.1324 | 0.0403 | 0.1923 | 0.0729 | 0.0595 | 0.1667 | 0.1062
Dynamic qualities do not change after impact | 0.1098 | 0.0253 | 0.0441 | 0.0242 | 0.1154 | 0.0729 | 0.0357 | 0.0185 | 0.0557
Reduce to <3Gs acceleration | 0.1829 | 0.2273 | 0.2206 | 0.1210 | 0.1923 | 0.1215 | 0.0595 | 0.1667 | 0.1615
Consistent tooling | 0.0122 | 0.0152 | 0.0147 | 0.0242 | 0.0385 | 0.1215 | 0.0595 | 0.0185 | 0.0380
handle impact speed 10ft/s | 0.2561 | 0.3788 | 0.2206 | 0.3629 | 0.1154 | 0.3646 | 0.5357 | 0.2778 | 0.3140
can support 32800kg | 0.1829 | 0.2273 | 0.2206 | 0.3629 | 0.1154 | 0.1215 | 0.1786 | 0.2778 | 0.2109
<10 degree offset from z axis | 0.1098 | 0.0253 | 0.1324 | 0.0403 | 0.1154 | 0.0729 | 0.0357 | 0.0556 | 0.0734
Sum | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1.0000

## Slide 29: Back Up Concept Selection: AHP 3
Weighted Sum Vector {Ws} | {W} | {Cons} |  |  | 
0.352 | 0.0403 | 8.737873 |  | n | 8
0.992 | 0.1062 | 9.337189 |  | lambda | 9.181082
0.488 | 0.0557 | 8.754142 |  | RI | 1.4
1.546 | 0.1615 | 9.571901 |  | CI | 0.168726
0.323 | 0.0380 | 8.492243 |  | CR | 0.120519
3.004 | 0.3140 | 9.567303 |  |  | 
2.080 | 0.2109 | 9.863322 |  |  | 
0.670 | 0.0734 | 9.124682 |  |  | 
 | Average: | 9.181082 |  |  | 

## Slide 30: NASA Colors

## Slide 31: Progress Trackers