## Slide 1
1
Design Review 4
Team 515
January 26, 2021
Reusable Shock Absorber for New Lunar Lander

## Slide 2: Team Members
2
Josh Blank
Design Engineer
Alex Noll
Mechanical Engineer
Matt Fowler
Systems Engineer
Tristan Jenkins
Design Engineer
Melanie Porter
Dynamics Engineer
Team Members
Matt Fowler

## Slide 3: Sponsor & Advisor
Sponsor & Advisor
Project Sponsor
Rachel McCauley
MSFC Advanced Concepts Deputy Manager at NASA
Academic Advisor
Keith Larson
Teaching Faculty I
Matt Fowler

## Slide 4
To design a reusable device for the human lander system that will dissipate the impact energy in such a way that it does not damage the vessel or occupants.
Objective
Matt Fowler

## Slide 5: Project Description
Project Description
Matt Fowler

## Slide 6: Functions
Previous Work
Link
#1
Project Scope
Customer Needs
Background Research
Functional Decomp
Targets & Metrics
Concept Generation
Concept Selection
Matt Fowler

## Slide 7
Con
Concept #7
Concept Generation
Locking Springs
Team 515
Extended
Compressed
Solenoid
Ratchet
Spring Pawl
Matt Fowler
Page 1/2

## Slide 8
Con
Concept #7
Concept Generation
Locking Springs
Team 515
Matt Fowler
Page 2/2
Main Spring
Solenoid
Pawl Arm
Linear Ratchet
Extension Spring
Ferromagnetic Core
To Lander

## Slide 9
CAD
Geometric considerations
Material considerations
Fabrication considerations
Melanie Porter
Current Work

## Slide 10
10
Melanie Porter
Solenoid Force
Magnetic Field Generation
Pin Reaction Force
Tooth Reaction Force
Tooth Interface
Pivot Point
Consideration
Tooth Angle
Pawl Springs
Geometric Considerations

## Slide 11
Springs
Structural Pieces
Wear Surfaces
Melanie Porter
Material Considerations

## Slide 12
Circular I-beam and linear ratchet.
Melanie Porter
Fabrication & Assembly
Circular I-beam is slid though top end before spring is loaded in.
Ball end of main cylinder threaded on.

## Slide 13
Complete prototype designs
Upcoming
Melanie Porter
Prototype construction
Determine testing methods and test prototypes

## Slide 14
Melanie Porter
Prototype Construction

## Slide 15
  Geometry
  Spring
  Pawl locking mechanism
Five prototypes → four tests
  Pawl releasing mechanism
  Final prototype (not tested)
Melanie Porter
Prototype Testing

## Slide 16: Thank You!
Notes: It’s about the staff meeting

## Slide 17
References
[1] Rodgers, W. F. (1972). Apollo Experience Report – Lunar Module Landing Gear Subsystem (NASA TN 0-6850). Washington , D.C. : National Aeronautics and Space Administration.
[2] INCO. (1974). Materials for Cryogenic Service: Engineering Properties of Austenitic Stainless Steels. Nickle Development Institute .

## Slide 18: Backup Slides

## Slide 19: Back Up Project Description

## Slide 20: Back Up Functional Decomp
Functional Decomposition Cross Reference Table. Rows more important than columns |  |  |  |  |  |  |  |  |  | 
 | Withstand Shock | Support Weight | Absorb Impact Energy | Dampen Vibrations | Prevent Excessive Rebound | Transform Energy | Dissipate Energy | Store Energy | Return to Origingal State | Sum
Withstand Shock | - | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 7
Support Weight | 0 | - | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 6
Absorb Impact Energy | 1 | 1 | - | 1 | 1 | 1 | 1 | 1 | 1 | 8
Dampen Vibrations | 0 | 0 | 0 | - | 0 | 0 | 1 | 1 | 0 | 2
Prevent Excessive Rebound | 0 | 0 | 0 | 1 | - | 1 | 1 | 1 | 0 | 4
Transform Energy | 0 | 0 | 0 | 1 | 0 | - | 1 | 1 | 0 | 3
Dissipate Energy | 0 | 0 | 0 | 0 | 0 | 0 | - | 1 | 0 | 1
Store Energy | 0 | 0 | 0 | 0 | 0 | 0 | 0 | - | 0 | 0
Return to Origingal State | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | - | 5
Rank | 2 | 3 | 1 | 7 | 5 | 6 | 8 | 9 | 4 | 
Rank | Function
1 | Absorb Impact Energy
2 | Withstand Shock
3 | Support Weight
4 | Return to Original State
5 | Prevent Excessive Rebound
6 | Transform Energy
7 | Dampen Vibrations
8 | Dissipate Energy
9 | Store Energy

## Slide 21: Back Up Concept Selection: HoQ
 | Importance rating | Absorb Impact Energy | Absorb Structural Shock | Support Mass | Return to Original State | Indicate Reusability | Prevent Excessive Rebound | Transform Energy | Dampen Vibrations | Dissipate Energy | Store Energy | Withstand Lunar Conditions
The product can be used indefinitely. | 3 | 3 | 2 | 2 | 3 | 2 |  | 1 | 1 | 1 | 1 | 3
The product is lightweight. | 3 |  |  |  |  |  |  |  |  |  |  | 
The product can be sent to the moon and used repeatedly. | 3 | 3 |  | 1 | 3 | 2 |  |  |  |  |  | 3
No routine maintenance is necessary during remainder of each lunar trip. | 1 |  |  |  | 2 | 1 |  |  |  |  |  | 
Shock absorber dynamic qualities does not change or diminish after an impact. | 2 | 2 | 2 | 1 | 1 |  | 1 | 1 |  | 1 | 1 | 
The product can handle an impact speed of 10 feet per second. | 3 | 3 | 3 |  |  |  |  |  |  |  |  | 
The product can support 25,000 kg. | 2 |  | 3 | 3 |  |  | 2 |  |  |  |  | 
The product can land at up to a 10-degree offset from the z-axis. | 1 |  |  |  |  |  | 1 |  |  |  |  | 
Raw Score (total) | 146 | 31 | 21 | 17 | 21 | 13 | 7 | 5 | 3 | 5 | 5 | 18
Relative weight (%) | 100 | 21.23 | 14.38 | 11.64 | 14.38 | 8.90 | 4.79 | 3.42 | 2.05 | 3.42 | 3.42 | 12.33
Rank Order |  | 1 | 2 | 5 | 3 | 6 | 7 | 8 | 11 | 9 | 10 | 4

## Slide 22: Back Up Concept Selection: Pugh 1
 |  | Concept |  |  |  |  |  |  | 
Selection Criteria | Datum | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Absorb Impact Energy | Apollo Shock Absorbers | - | s | + | + | + | s | + | s
Absorb Structural Shock |  | - | + | - | + | + | - | s | s
Support Mass |  | s | s | - | S | s | s | s | s
Return to Original State |  | + | + | + | + | + | + | + | +
Indicate Reusability |  | + | + | + | - | - | + | s | -
Prevent Excessive Rebound |  | - | - | + | + | + | + | + | +
Transform Energy |  | S | + | s | s | s | + | + | s
Dampen Vibrations |  | + | + | + | + | + | - | + | +
Dissipate Energy |  | s | + | s | s | s | + | s | s
Store Energy |  | s | s | s | + | s | + | + | s
Withstand Lunar Conditions |  | - | + | - | - | - | - | s | +
#of pluses |  | 3 | 6 | 5 | 6 | 5 | 6 | 6 | 3
# of minuses |  | 4 | 1 | 3 | 1 | 1 | 3 | 0 | 1

## Slide 23: Back Up Concept Selection: Pugh 2
 | Concepts |  |  | 
Selection Criteria | Datum | 2 | 7 | 4
Absorb Impact Energy | Spider Legs | + | + | S
Absorb Structural Shock |  | + | + | +
Support Mass |  | s | + | -
Return to Original State |  | + | + | S
Indicate Reusability |  | s | - | +
Prevent Excessive Rebound |  | - | + | +
Transform Energy |  | + | + | +
Dampen Vibrations |  | - | + | +
Dissipate Energy |  | s | + | S
Store Energy |  | + | + | S
Withstand Lunar Conditions |  | s | + | -
#of pluses |  | 5 | 10 | 5
# of minuses |  | 2 | 1 | 2

## Slide 24: Back Up Concept Selection: AHP 1
Criteria Matrix [c] |  |  |  |  |  |  |  | 
Customer Needs | Lightweight | Reusable | Dynamic qualities do not change after impact "hopping" | Reduce to <3Gs acceleration | Consistent tooling | handle impact 10ft/s | can support 25000kg | <10 degree offset from z axis
Lightweight | 1.00 | 0.33 | 0.33 | 0.20 | 3.00 | 0.14 | 0.20 | 0.33
Reusable | 3.00 | 1.00 | 3.00 | 0.33 | 5.00 | 0.20 | 0.33 | 3.00
Dynamic qualities do not change after impact | 3.00 | 0.33 | 1.00 | 0.20 | 3.00 | 0.20 | 0.20 | 0.33
Reduce to <3Gs acceleration | 5.00 | 3.00 | 5.00 | 1.00 | 5.00 | 0.33 | 0.33 | 3.00
Consistent tooling | 0.33 | 0.20 | 0.33 | 0.20 | 1.00 | 0.33 | 0.33 | 0.33
handle impact speed 10ft/s | 7.00 | 5.00 | 5.00 | 3.00 | 3.00 | 1.00 | 3.00 | 5.00
can support 32800kg | 5.00 | 3.00 | 5.00 | 3.00 | 3.00 | 0.33 | 1.00 | 5.00
<10 degree offset from z axis | 3.00 | 0.33 | 3.00 | 0.33 | 3.00 | 0.20 | 0.20 | 1.00
Sum | 27.33 | 13.20 | 22.67 | 8.27 | 26.00 | 2.74 | 5.60 | 18.00

## Slide 25: Back Up Concept Selection: AHP 2
Normalized Matrix |  |  |  |  |  |  |  |  | {W}
Lightweight | 0.04 | 0.03 | 0.01 | 0.02 | 0.12 | 0.05 | 0.04 | 0.02 | 0.0403
Reusable | 0.1098 | 0.0758 | 0.1324 | 0.0403 | 0.1923 | 0.0729 | 0.0595 | 0.1667 | 0.1062
Dynamic qualities do not change after impact | 0.1098 | 0.0253 | 0.0441 | 0.0242 | 0.1154 | 0.0729 | 0.0357 | 0.0185 | 0.0557
Reduce to <3Gs acceleration | 0.1829 | 0.2273 | 0.2206 | 0.1210 | 0.1923 | 0.1215 | 0.0595 | 0.1667 | 0.1615
Consistent tooling | 0.0122 | 0.0152 | 0.0147 | 0.0242 | 0.0385 | 0.1215 | 0.0595 | 0.0185 | 0.0380
handle impact speed 10ft/s | 0.2561 | 0.3788 | 0.2206 | 0.3629 | 0.1154 | 0.3646 | 0.5357 | 0.2778 | 0.3140
can support 32800kg | 0.1829 | 0.2273 | 0.2206 | 0.3629 | 0.1154 | 0.1215 | 0.1786 | 0.2778 | 0.2109
<10 degree offset from z axis | 0.1098 | 0.0253 | 0.1324 | 0.0403 | 0.1154 | 0.0729 | 0.0357 | 0.0556 | 0.0734
Sum | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1.0000

## Slide 26: Back Up Concept Selection: AHP 3
Weighted Sum Vector {Ws} | {W} | {Cons} |  |  | 
0.352 | 0.0403 | 8.737873 |  | n | 8
0.992 | 0.1062 | 9.337189 |  | lambda | 9.181082
0.488 | 0.0557 | 8.754142 |  | RI | 1.4
1.546 | 0.1615 | 9.571901 |  | CI | 0.168726
0.323 | 0.0380 | 8.492243 |  | CR | 0.120519
3.004 | 0.3140 | 9.567303 |  |  | 
2.080 | 0.2109 | 9.863322 |  |  | 
0.670 | 0.0734 | 9.124682 |  |  | 
 | Average: | 9.181082 |  |  | 

## Slide 27: NASA Colors

## Slide 28: Progress Trackers