## Slide 1
4
2
Key Parts
Team 503 | Nicholas Blenker | Tucker Hall | David Wilson
Environmental Test Chamber
Initial Design
The objective of this project is to validate the existing design and deliver an assembly that regulates temperature and humidity for use in a laboratory environment
DUCTWORK
CONTROL
VOLUME
AIR
HANDLING
UNIT
CHAMBER
COMPRESSOR
TREATED AIR
RETURN AIR
Air Conditioning Unit:
Cools from 45° to 0° Celsius
Heating Strips:
Heat can reach 65° Celsius
Humidifier:
Ranges from 0% to 100% relative humidity
Collection System:
Funnels condensation and refills the humidifier tank
Controller:
Centralizes and automates system control
Targets
Design Changes
Floor-Mounted AHU
Detachable Side Ducts
16,800 BTU A/C
Industrial Humidifier
1
2
3
4
Automotive testing
Weapons testing
Electronics testing
Perishable food storage
Medical product testing
Final Design
Applications
10°C ≤ T ≤ 50°C
0% ≤ RH ≤ 95%
Within 1% of desired
values
Compressor exchange
within 15 minutes
No human interaction
Sponsor: William Bilbow | Advisor: Keith Larson