## Slide 1
Articulating Nose Cone
Jed Fazler | Noah Moffeit | Nicholas Samuda | Robert Smith
Notes: https://visualhunt.com/f7/photo/32891036558/2ed24545c0/

## Slide 2: Team 504 Introductions
Nicholas Samuda
Noah Moffeit
Test Engineer
Robert Smith
Research Engineer
Nicholas Samuda
Systems Engineer
Jed Fazler
Field Engineer

## Slide 3: Sponsor and Advisor
Dr. Rajan Kumar
Dr. Jonas Gustavsson
Nicholas Samuda
Notes: Our project sponsor is Dr. Rajan Kumar, he is an Associate Professor at the FAMU-FSU college of engineering and the Director of the Florida Center for Advanced Aero-Propulsion. Our project advisor is Dr. Jonas Gustavsson who works as an Associate Scientist at FCAAP.

## Slide 4: Project Scope
Design the method of articulation for a nose cone during testing in a low-speed wind tunnel while keeping a smooth edge transition.
Nicholas Samuda

## Slide 5: Project Considerations
Importance placed on the applicability of the design at larger scales
Tunnel Testing
Real World Use
Nicholas Samuda

## Slide 6: Critical Targets and Metrics
θ
Articulate the nose cone to obtain a pitch and yaw of ± 20°
Keep transition edges smooth between nose and body
Nicholas Samuda

## Slide 7: Concept Generation
Nose Pulleys
Linear Actuators
Polar Controller
2 DOF Gear Box
Rotating Contact Surfaces
Basic Rotating Nose
Nicholas Samuda

## Slide 8: Preliminary Design: Polar Control
5
2
1
4
6
7
3
Worm Gear
1
Spur Gear
2
Pin Slot Link
3
Stepper Motor
7
Pin Holders
4
Motor Mount
6
Sliding Pin
5
Nicholas Samuda

## Slide 9: Selected Design: Concentric Surfaces
Implements the use of two angled surfaces for articulation
- Uses two stepper motors for rotation and deflection
- Requires a universal joint at the concentric surfaces
Nicholas Samuda

## Slide 10: 3D Printing and Prototyping
Noah Moffeit
10° concentric surfaces
Universal joint
Ball and socket pins
20° of rotation achieved

## Slide 11: Gap Handling
- Investigate flexible materials for the nose to body interface
- Gap could possibly cause issues with stability of flow
- Attempted Solutions:
  Silicon
  3-D Printed TPU Filament
  Multi-Filament 3-D print
Gap
Noah Moffeit

## Slide 12: Gap Handling: Cast Resin
Noah Moffeit
A silicon resin was cast in a 3D printed mold
  High flexibility that allows for bending
  Bubbles developed inside the resin creating possible stress concentrations
  Pinching occurs at moderate to high deflection

## Slide 13: Gap Handling: 3D Printed Flex
NinjaFlex 3D Printer Filament
  Promising flex characteristics
  Will have to test multiple thicknesses
  Requires calibration and time to print
Noah Moffeit

## Slide 14: Gap Handling: Spring Sleeve
A mixed material 3d print has been designed to allow for spring-like flexibility while retaining rigidity
  Multiple sleeves in production by the Air Force Research Laboratory
  Restricted by the deflection angle
Noah Moffeit

## Slide 15: Nose Deflection Process
Noah Moffeit
Operation allows for 20° of deflection
The deflection is then directed into the desired position
  Working towards rotating and deflecting in unison

## Slide 16: Contact Surface Operation
Noah Moffeit
- Universal joint highlighted in red
  Allows for power translation
Custom collar designed to prevent axial translation

## Slide 17: Combating Friction
Inherent friction between concentric surfaces
Solutions
  Washer and retaining clip
  Solid lubricants
  Bearings
Two face-mounted bearings used to rotate outer surfaces
Noah Moffeit

## Slide 18: Benchtop Testing
Calibrate motor rotation
Develop code to control
Noah Moffeit
Determine nose deflection for motor rotation

## Slide 19: Future Work
Noah Moffeit
Test model within the tunnel
Continue prototyping bendable sleeves
Finalize machining and test fittings
Make final purchases

## Slide 20
Thanks for listening
Jed Fazler | Noah Moffeit | Nicholas Samuda | Robert Smith
`
Jed Fazler
Noah Moffeit
Robert Smith
Nicholas
Samuda

## Slide 21: Project Description and Key Goals
This project aims to create a technology that can be applied to many projectile configurations, allowing the projectile to maneuver adaptively through unforeseen, hazardous environments. The technology developed will detect said obstacles or conditions and actuate the projectile autonomously.
The key goals were selected to itemize the main objectives that must be accomplished over the duration of the project based on the project’s description and advice from the project’s sponsor. The following are the goals or milestones we have derived to ensure the project’s completion:
  Conceptualize and research 5 different innovative ways to maneuver a projectile.
  Choose one of these designs to expand upon and develop into a working design.
  Develop innovative technologies that can be implemented into the projectile allowing for smart capabilities.
  Develop a way for the projectile to adapt to its environment or obstacles through autonomous actions.
  Construct a scaled down model of the projectile for use in wind tunnel testing to verify desired aerodynamic characteristics of design.
  Construct a prototype projectile to test actuation of the smart functionality within the projectile.

## Slide 22: Market
The primary market for this project was seen as the company or organization that the product would be directly constructed for and would use the product.
Primary Markets:
  Florida Center for Advanced Aero Propulsion (FCAAP)
The secondary markets are a makeup of other companies or organizations who may benefit from or would be interested in purchasing the results of this project.
Secondary Markets:
  Air Force Office of Scientific Research (AFOSR)
  Lockheed Martin
  Raytheon Technologies
  Northrop Grumman

## Slide 23: Assumptions
Propulsion
Deployment
Storage
It is assumed that:
Projectile deployment
Entailing storage
Transportation
Initial launch
will be facilitated by technologies already implemented in the projectile. It is also assumed that the projectile will remain within earth’s atmospheric conditions for its use.

## Slide 24: Stakeholders
Dr. Shayne McConomy
Dr. Rajan Kumar
Dr. Jonas Gustavsson
FCAAP
FAMU-FSU College of Engineering
The stakeholders for this project include all parties who will have influenced the design of the technologies produced by the project as well as those who have invested time and other resources into the project.

## Slide 25: Customer Needs
How do you think current control surfaces and their actuation can be improved? | Current control surfaces require clean flow, which is not realistic at high angles of attack, so that’s something. | Projectile accommodates for attached flow over control surfaces.
What draw backs come with standard fin deflections as a control surface? | Must have clean flow to actuate properly. Size and weight that come with actuation mechanism | Projectile control surfaces will be suitable effective even in detached flow.
What Mach numbers would be expected for this projectile? | FCAAP polysonic wind tunnel can’t go faster than Mach 5. We’ll probably test Mach 4. | The projectile can withstand Mach 4.
What slenderness ratio of the projectile would be appropriate? | Would be nice if it could be tied into what we have done already. Matching a baseline design here at FCAAP. 8-10 | The projectile uses a basic axisymmetric body configuration based on previously tested models.

## Slide 26: Customer Needs
Do we need to worry about designing the method of propulsion? | Don’t worry about designing the propulsion as we cannot have it modeled in the wind tunnel. | Propulsion is beyond the scope of this project.
By the end of this project, what level of manufacturing should be accomplished to demonstrate our results? | Small model for testing control surfaces in wind tunnel, larger model for demonstration purposes and sensing capabilities. Radar sensors possible option. | The projectile is modelled for aerodynamic testing and then prototyped for proof of actuation.
What conditions do you expect the projectile to operate in? | Projectile should go where the target goes. High angles of attack. Initial deployment shockwaves and vortices. Vibrations in supersonic can affect and disrupt the electronics. | The projectile has a way to rapidly adapt to the conditions that exist during deployment.
Should the projectile be able to actuate without user input? | Yes | The projectile is automatically operated.

## Slide 27: Customer Needs
Should favorable aerodynamic characteristics be prioritized over functionality? | No, it should accomplish the task while minimizing negative effects. Compare to previous results. | Maintaining aerodynamic characteristics is secondary to maintaining control surface effectiveness.
What is considered a “harsh” or “hazardous” | Vortices, and shockwaves off the parent aircraft. High angles of attack | The missile adapts to high pitch angles.
What will be the preferred method of flow visualization? | It looks good. Better for showing actuation effects. Could be done with shadow graph in the wind tunnel. Not necessary but helpful. | Flow visualization will be done through other tests such as shadowgraph or oil flow.
Will the projectile also have to accommodate targeting? | Does not necessarily need to sense targets, could also sense high angles of attack. | The missile can sense its angle of attack in various scenarios.

## Slide 28: Functional Decomposition
Jed Fazler
POWER
Transmission
Storage
Transfers power to components
Provides power for components

## Slide 29: Functional Decomposition
Jed Fazler
SENSING
Signaling
Sensors
Transmits response signal
Monitors sensor data
Interprets sensor data

## Slide 30: Functional Decomposition
Jed Fazler
ACTUATION
Mechanical
Flow
Controls roll
Maintains flow attachment
Controls pitch
Controls yaw

## Slide 31: Functional Decomposition
Jed Fazler
STRUCTURE
Protects components
Maintains integrity

## Slide 32
Jed Fazler
Robert Smith
Noah Moffeit
Nicholas
Samuda

## Slide 33: Color Palette
How do you think current control surfaces and their actuation can be improved? | Current control surfaces require clean flow, which is not realistic at high angles of attack, so that’s something. | Projectile accommodates for attached flow over control surfaces.
What draw backs come with standard fin deflections as a control surface? | Must have clean flow to actuate properly. Size and weight that come with actuation mechanism | Projectile control surfaces will be suitable effective even in detached flow.
What Mach numbers would be expected for this projectile? | FCAAP polysonic wind tunnel can’t go faster than Mach 5. We’ll probably test Mach 4. | The projectile can withstand Mach 4.
What slenderness ratio of the projectile would be appropriate? | Would be nice if it could be tied into what we have done already. Matching a baseline design here at FCAAP. 8-10 | The projectile uses a basic axisymmetric body configuration based on previously tested models.

## Slide 39
Robert Smith
Nose Pulleys
Linear Actuators
Polar Controller
2 DOF Gear Box
Rotating Contact Surfaces
Basic Rotating Nose