## Slide 1
In-Space Cryogenic
Propellant Storage
Anna Gilliard | Liam McConnell | Samantha Myers | Brandon Young
Team 512

## Slide 2: Team Introductions
Anna Gilliard
Fluids Engineer
Brandon Young
Materials Engineer
Liam McConnell
Cryogenics Engineer
Samantha Myers
Controls Engineer
Anna Gilliard

## Slide 3: Sponsor and Advisor
Wei Guo
FAMU-FSU College of Engineering
Rachel McCauley
NASA Marshall Space Flight Center
Travis Belcher
NASA Marshall Space Flight Center
Anna Gilliard

## Slide 4: Project Objective
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work
The objective of this project is to design a storage tank for cryogenic propellant that increases storage time, reduces fuel loss, and reduces heat transfer.

## Slide 5: Key Goals
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work

## Slide 6: Key Goals
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work
Maintain temperature

## Slide 7: Key Goals
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work
Maintain temperature
Maintain pressure

## Slide 8: Key Goals
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work
Reduce fuel loss
Maintain temperature
Maintain pressure

## Slide 9: Key Goals
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work
Reduce fuel loss
Maintain temperature
Reduce heat transfer
Maintain pressure

## Slide 10: Key Goals
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work
Reduce fuel loss
Develop a prototype
Maintain pressure
Maintain temperature
Reduce heat transfer

## Slide 11: Assumptions
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work
Test with liquid nitrogen
Withstands Earth, space, and lift-off conditions
Lunar mission of two weeks

## Slide 12: Critical Targets and Metrics
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work

## Slide 13: Critical Targets and Metrics
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work
Maintain temperature of 77 K

## Slide 14: Critical Targets and Metrics
Anna Gilliard
Maintain temperature of 77 K
Maintain structural integrity for two weeks
Summary
Design Update
Testing
Timeline
Current Work

## Slide 15: Critical Targets and Metrics
Anna Gilliard
Maintain temperature of 77 K
Maintain structural integrity for two weeks
Maintain pressure of ~30 psi
Summary
Design Update
Testing
Timeline
Current Work

## Slide 16: Concept Generation
Anna Gilliard
Summary
Design Update
Testing
Timeline
Current Work
All high-fidelity concepts are assuming double-shell, pill shaped tank.

## Slide 17: Concept Generation
Anna Gilliard
Multi-Layer Insulation
All high-fidelity concepts are assuming double-shell, pill shaped tank.
Summary
Design Update
Testing
Timeline
Current Work

## Slide 18: Concept Generation
Anna Gilliard
Ceramic Supports
Multi-Layer Insulation
All high-fidelity concepts are assuming double-shell, pill shaped tank.
Summary
Design Update
Testing
Timeline
Current Work

## Slide 19: Concept Generation
Anna Gilliard
Ceramic Supports
Film Reflecting Radiation
Multi-Layer Insulation
All high-fidelity concepts are assuming double-shell, pill shaped tank.
Summary
Design Update
Testing
Timeline
Current Work

## Slide 20: Original Design
Liam McConnell
Double-shell, pill shaped tank with MLI, vacuum between layers, reflective layer on the outside surface
Summary
Design Update
Testing
Timeline
Current Work
Notes: This model based mostly on conclusions made by other researchers through testing

## Slide 21: Current Prototype Design
Liam McConnell
Summary
Design Update
Testing
Timeline
Current Work
Inner and Outer Tanks
Vent
Top Flange
Bolts
G10-CR
Cross Valve
Clamps
Pressure Relief Valve
Stainless Steel Pipes
Top Flange
Sectioned View
Front View

## Slide 22
Liam McConnell
Current Prototype Design
Summary
Design Update
Testing
Timeline
Current Work
Prototype Dimensions
Outer tank diameter: 10.125 in.
Outer tank height: 13 in.
Inner tank diameter: 6.625 in.
Inner tank height: 10 in.
Sectioned View
Front View

## Slide 23: Design Comparison
Liam McConnell
Liquid Nitrogen
Flat Endcaps
Active Vacuum
Stainless Steel 304
Volume of ~6 gal
Foam Insulation
Liquid Hydrogen
Spherical Endcaps
Sealed Vacuum
Aluminum 2219
Volume of ~300,000 gal
MLI
Final Design
Prototype
G10-CR Supports
Reflective Outer Layer
Summary
Design Update
Testing
Timeline
Current Work

## Slide 24: Testing Procedure
Liam McConnell
Summary
Design Update
Testing
Timeline
Current Work
1. Open all end caps
2. Fill tank with line through port
3. Close fill port and end caps
4. Record mass flow rate from vents and record mass every 8 hours

## Slide 25: Testing Procedure
Liam McConnell
Summary
Design Update
Testing
Timeline
Current Work
Recording Mass Flow Rate
  Flowmeter
  Graduated cylinder and water displacement
  Weight of tank
Recording Mass of Fluid
  Scale

## Slide 26: Purchasing
Liam McConnell
Summary
Design Update
Testing
Timeline
Current Work
Inner tank
Outer tank
Vacuum connection
G10-Cr pipe
Pressure relief valve
2’x2’ Stainless Steel Sheet
Bolts
Vent
External connection fittings
Foam insulation
Cross valve

## Slide 27: Current Challenges
Liam McConnell
Summary
Design Update
Testing
Timeline
Current Work
Insulation change
External connections in lab fitting to tank
Editing tank design to simplify construction for machine shop
Computer recording mass flow rate

## Slide 28: Timeline
Liam McConnell
Receive Materials
Feb. 25
Begin Testing
Mar. 15
Engineering Design Day
April 7
Begin Prototype Construction
Mar. 4
Final Report
April 12
Summary
Design Update
Testing
Timeline
Current Work

## Slide 29
In-Space Cryogenic
Propellant Storage
Anna Gilliard | Liam McConnell | Samantha Myers | Brandon Young
Team 512
Notes: End on this slide for questions
​

## Slide 32: Customer Needs
Anna Gilliard
How long will the container be in space?
Select a hypothetical mission.
What type of fuel will be stored?
Either liquid hydrogen or oxygen will be used.
What conditions are we designing for?
The container must operate under all possible conditions.
What scale should be used?
It should be scalable to contain the required amount of fluid.
Notes: Next, we obtained our customer needs by asking our sponsor questions and interpreting their answers.
When asked how long we should design for the container be in space, NASA left our project relatively open ended, so we decided to design for a hypothetical mission to determine the duration.
The type of fuel that will be used in practice is either liquid hydrogen or liquid oxygen. These are the most common fuel types used in an RL10 engine. The RL10 engine is one of the commonly used for spacecraft at NASA.
We are designing for all possible conditions that the container could be under. In our case, this includes conditions on Earth, during the launch of the rocket, and in space. We must also account for the tank being filled and emptied. With the fluids being at such low temperatures, the material will expand and contract to some degree, so we need to ensure that the material we choose will not be subject to failure.
Finally, we need our prototype to scale to hold the required amount of propellant.

## Slide 33: Customer Needs
Team Question | Provided Answer | Interpreted Need
Are we expected to fabricate the storage container? | Yes, prototype a scaled model. | The prototype has the ability to scale to a larger size.
What improvements can be made to current products? | Extend the amount of time the fuel can be stored. | The container has the ability to increase time maintained at cryogenic temperature and pressure.
Are we expected to perform experiments and present data to validate our design? | Yes, prototyping and testing are the main goal NASA has for this project. | The system has the ability to be validated for scientific calculations and design choices.
How long will the container be in space? | This factor is up to the group. | The system has the capability to be used on a hypothetical mission of a determined length.
Does NASA have a previous model that the group can improve? | NASA wants to see original ideas. It would be best to start from scratch. | The system has the capability to store cryogenic propellant with different materials and systems than previous models.
What type of fuel will be stored? | Liquid hydrogen or liquid oxygen. | Cryogenic container has the ability to hold liquid hydrogen or liquid oxygen and maintain them at the appropriate temperature and pressure.
What would be considered a successful project? | Improve how the container handles outside heat sources. | The container has the ability to decrease the rate of heat transfer more significantly in comparison to current state-of-the-art.
Are we designing for Earth, Mars, or the moon? | This factor is up to the group. | The cryogenic tank has the ability to store the propellant properly for the mission that the team decides to design for.
Does our design have to mount onto the ship in a certain way? | The storage container should work with existing state-of-the-art support structures. | Container has the ability to connect with other parts of the ship for structure.

## Slide 34: Functional Decomposition
Samantha Myers
In-Space Cryogenic Propellant Storage Container
Notes: From our background research, assumptions, and customer needs, we broke down the project into major and minor functions.

## Slide 35: Functional Decomposition
In-Space Cryogenic Propellant Storage Container
Stores
Insulates
Communicates to User
Connects
Samantha Myers
Notes: The main functions of our in-space cryogenic propellant storage container are to store the cryogen, insulate it from heat transfer, communicate to the user, and to be able to physically connect.

## Slide 36: Functional Decomposition
Stores
Samantha Myers
Hold Cryogenic Fluid
Prevent Fuel Loss
Maintains Pressure
Notes: The first main function is to store the fuel. To successfully store the cryogen, the container must prevent fuel loss, maintain a desired pressure, and contain the fluid.

## Slide 37: Functional Decomposition
In-Space Cryogenic Propellant Storage Container
Stores
Insulates
Communicates to User
Connects
Samantha Myers
Notes: The second major function to break down is insulation.

## Slide 38: Functional Decomposition
Insulates
Samantha Myers
Decrease Heat Absorption
Increase Heat Loss
Notes: In order to successfully insulate the propellant, the storage must increase heat loss from the system and decrease heat absorption into the system.

## Slide 39: Functional Decomposition
In-Space Cryogenic Propellant Storage Container
Stores
Insulates
Communicates to User
Connects
Samantha Myers
Notes: The third major function to break down is communicating to the user.

## Slide 40: Functional Decomposition
Communicates to User
Samantha Myers
Displays on Container
Sends Information
Notes: To successfully communicate to the user, the container must send information and display the information on the container.

## Slide 41: Functional Decomposition
In-Space Cryogenic Propellant Storage Container
Stores
Insulates
Communicates to User
Connects
Samantha Myers
Notes: The last major function of the storage container is to physically connect.

## Slide 42: Functional Decomposition
Samantha Myers
Attaches Inner and Outer Shell
Attaches to Interior of Spacecraft
Connects
Notes: To successfully connect, the storage must be attachable to the spacecraft, meaning some type of hole or way to attach struts or other connectors. It must also connect the inner and outer shells of the double-shell tank, ideally with minimal conduction.

## Slide 43: Functional Decomposition
In-Space Cryogenic Storage Container
Stores
Communicates with User
Connects
Insulates
Holds cryogenic fluid without failure
Maintains pressure
Prevents fuel loss
Increases pressure
Decreases pressure
Minimize heat transfer
Reduce heat absorption through radiation
Reduce heat transfer through conduction
Sends information
Displays information
Attaches to interior of spacecraft
Attaches inner and outer shell
Connects metal
Connects tubes

## Slide 44: Concept Selection
Name
Summary
Design Update
Testing
Timeline
House of Quality
Pugh Chart
Analytical Hierarchy Process

## Slide 45: Functions and Targets
Samantha Myers
Summary
Design Update
Testing
Timeline
Stores
Insulates
Connects

## Slide 46: Targets and Metrics
Withstand 6 Gs of force
Maintain structural integrity for two weeks
Maintain pressure of 80 – 90 psi
Less than 1% mass boil off per day
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Brandon Young

## Slide 47: Targets and Metrics
Reflect all but 10 kJ of energy per square meter per day
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Brandon Young
Notes: Deleted: Inner shell receives less than 10 kJ of energy per day

## Slide 48: Targets and Metrics
Information display synced to instruments to an accuracy of 1 second
Gauges or dials are clear and easy to read
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Brandon Young
Minimum 300 nit display, and14-point font size
If the shells become brittle, the user will be alerted with a 80 decibel alarm
If the container leaks, the user will be alerted within 5 seconds with a 80 decibel alarm
Notes: If the shells become brittle, the user will be alerted with a 80 decibel alarm
If the container leaks, the user will be alerted within 5 seconds with a 80 decibel alarm

## Slide 49: Targets and Metrics
Tank is fixed on inner walls of spaceship
Inner struts withstand 6 Gs of force
Useable for up to 5 missions
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Brandon Young

## Slide 50: Critical Targets and Metrics
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Brandon Young
Withstand 6 Gs of Force
Maintain structural integrity for two weeks
Maintain pressure of 80 – 90 psi
Reflect all but 10kJ of energy per square meter per day

## Slide 51: Targets and Metrics
Function | Target
Holds cryogenic fluid without failure | Withstand 3 Gs of force on takeoff Maintain structural integrity for two weeks
Maintains pressure | Keep pressure between 80 and 90 psi for entire mission
Prevents fuel loss | Less than 1% per day mass boil off for the duration of the mission
Increases heat dissipated | Dispel all but 10 kJ of energy per unit volume per day
Decreases heat transfer | Inner tank will be subject to less than 10 kJ of energy per day
Communicate to user | Information display synchronized to instruments to the accuracy of a second
Displays on container | Digital presentation: at least 300 nit displays, 14-point font size or larger Analog Presentation: Gauges or dials clear and easy to read
Attaches to space craft interior | Attaching brackets can withstand 3 Gs of force upon takeoff Tank is fixed on inner walls of spaceship
Attaches inner and outer shell | Inner Struts can withstand 3 Gs of force on takeoff Useable for up to five missions If the storage container leaks, alerts user within 5 seconds with 80 decibels If metal becomes too brittle alert user with 80 decibels

## Slide 52: Concept Generation
Morphological Chart
Geometry | Number of Layers | Thickness | Insulation
Cylinder | One | Thick | Coolant
Sphere | Two | Thin | Vacuum
Pill | Three |  | Foam
 |  |  | Powder
 |  |  | Fiber
 |  |  | Multi-layer

## Slide 53: Concept Generation
Brainstorming
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Liam McConnell
Notes: Brainstorming – coming up with random ideas
Morphological chart – using a chart to combine basic ideas into more complex ideas
Biomimicry – Looking at nature for inspiration on insulation and shape

## Slide 54: Concept Generation
Brainstorming
Morphological Chart
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Liam McConnell
 | A | B | C
A | A | AB | AC
B | AB | B | BC
C | AC | BC | C
Notes: Brainstorming – coming up with random ideas
Morphological chart – using a chart to combine basic ideas into more complex ideas
Biomimicry – Looking at nature for inspiration on insulation and shape

## Slide 55: Concept Generation
Morphological Chart
Biomimicry
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Liam McConnell
Brainstorming
Notes: Brainstorming – coming up with random ideas
Morphological chart – using a chart to combine basic ideas into more complex ideas
Biomimicry – Looking at nature for inspiration on insulation and shape

## Slide 56: Concept Generation
Anna Gilliard
Double-Shell with Foam Insulation
Pill Shape with Powder Insulation
Triple-Shell with Vacuum
Double-Shell Tank with Vacuum
Double-Shell with Glass Bead Insulation
Summary
Design Update
Testing
Timeline
Validation

## Slide 57: House of Quality
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Time
Safety
Volume
Ease of Use
Cost
Surface Area
Durability
Liam McConnell
Notes: Compares customer needs to characteristics

## Slide 58: House of Quality
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Time
Safety
Volume
Liam McConnell

## Slide 59: Pugh Charts
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
MLI
Foam Insulation
Double-Shell Vacuum
Glass Bead Insulation
Film Insulation
Spherical Shape
Powder Insulation
Liam McConnell
Notes: Compares concepts to engineering characteristics

## Slide 60: Pugh Charts
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
MLI
Foam Insulation
Powder Insulation
Liam McConnell

## Slide 61: Analytical Hierarchy Process
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Time
Safety
Volume
Ease of Use
Cost
Surface Area
Durability
Liam McConnell
Notes: MLI, Ceramic supports, reflective film
Compares engineering characteristics vs themselves

## Slide 62: Analytical Hierarchy Process
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Time
Safety
Volume
Liam McConnell
Notes: MLI, Ceramic supports, reflective film

## Slide 63: Analytical Hierarchy Process
Summary
Targets and Metrics
Concept Generation
Concept Selection
Future Work
Design Rank | Design | Normalized Score
1 | Multi-Layer Insulation | 0.444
2 | Foam Insulation | 0.283
3 | Powder Insulation | 0.274
Safety
Volume
Time
Liam McConnell

## Slide 64: Concept Selection
Binary Comparison Chart |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | Total
1 | - | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 7
2 | 0 | - | 1 | 0 | 0 | 0 | 0 | 0 | 1
3 | 0 | 0 | - | 0 | 0 | 1 | 1 | 0 | 2
4 | 0 | 1 | 1 | - | 0 | 0 | 0 | 0 | 2
5 | 0 | 1 | 1 | 1 | - | 1 | 1 | 1 | 6
6 | 0 | 1 | 0 | 1 | 0 | - | 1 | 1 | 4
7 | 0 | 1 | 0 | 1 | 0 | 0 | - | 1 | 3
8 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | - | 3

## Slide 65: Concept Selection
1 – Increase Storage Time | a – Volume
2 – Validate Design Choices | b – Surface Area
3 – Use of Hypothetical Mission | c – Time
4 – Store Cryogenic Propellant | d – Safety
5 – Maintain Temperature | e – Durability
6 – Maintain Pressure | f – Ease of Use
7 – Reduce Heat Transfer | g - Cost
8 – Connect to Existing Systems | 

## Slide 66: Concept Selection
A – MLI in a Vacuum, Pill Shape | E – Powder Insulation – Pill Shape
B – Foam Insulation – Pill shape | F – Spherical Shape
C – Film Insulation – Pill Shape | G – Glass Bead Insulation – Pill Shape
D – Double Shell Vacuum – Pill Shape | 

## Slide 67: Concept Selection

## Slide 68: Concept Selection

## Slide 69: Concept Selection

## Slide 70: Concept Selection

## Slide 71: Concept Selection

## Slide 72: Concept Selection
Concept | Alternative Value | Rank
MLI - Pill Shape | 0.444 | 1
Foam Insulation - Pill Shape | 0.283 | 2
Powder Insulation Supports | 0.274 | 3

## Slide 73: Heat Leak Calculations
Liam McConnell
Qrad [W] | 1.3453
Qcond_pipe [W] | 4.3241
Qcond_G10 [W] | 1.6904
Qtotal [W] | 7.3598
Mass flow rate [kg/hr] | 0.1325
Time [hr] | 32.994
Time [day] | 1.3747
Prototype with MLI and Vacuum
Summary
Design Update
Testing
Timeline
Validation

## Slide 74: Calculations
Radiation (Qrad= 0.5*e*As*sigma*(T14 – T24)) | 
e | 0.075
As (m^2) | 0.192186712
sigma (W/m^2K^4) | 5.67E-08
T1 (K) | 300
T2 (K) | 77
Q_dot_rad (W) | 3.295594838

## Slide 75: Calculations
Conduction (Qcond= k*Ac*(T1-T2)/L) *PER SUPPORT* | 
k (W/m*K) | 0.228
Ac (m^2) | 0.000475
T1 (K) | 300
T2 (K) | 77
L (m) | 0.0428625
Q_dot_cond (W) | 0.563450569
number of supports | 3
Q_dot_cond_tot (W) | 1.690351706

## Slide 76: Calculations
Foam Heat Leak with Vacuum | 
T1 [K] | 300
T3 [K] | 77
k1 [W/mK] | 16
L1 | 0.125
k2 [W/mK] | 0.04
L2 | 1.375
q [W/m2] | 6.485798682
Surface Area [m2] | 0.192186712
Q [W] | 1.246484323

## Slide 77: Heat Leak Calculations
Liam McConnell
Summary
Design Update
Testing
Timeline
Validation
Prototype without Insulation
Qrad [W] | 3.2956
Qcond_pipe [W] | 4.3241
Qcond_G10 [W] | 1.6904
Qtotal [W] | 9.3101
Mass flow rate [kg/hr] | 0.1676
Time [hr] | 26.082
Time [day] | 1.0867

## Slide 78: Heat Leak Calculations
Liam McConnell
Summary
Design Update
Testing
Timeline
Validation
Prototype with Foam and Vacuum
Qrad [W] | 1.2465
Qcond_pipe [W] | 4.3241
Qcond_G10 [W] | 1.6904
Qtotal [W] | 7.2609
Mass flow rate [kg/hr] | 0.1307
Time [hr] | 33.443
Time [day] | 1.3934