## Slide 1
Team 517
Bianca Marius, Finnbar Rooney, Nicholas Walker
Team: 517
Making the MagLab Greener:
Optimizing the HVAC
Notes: Good Afternoon, our project is about making the MagLab greener.

## Slide 2: Team Introductions
Nicholas Walker
Design Engineer
Bianca Marius
Thermal Fluids Engineer
Finnbar Rooney
Materials Engineer
Nicholas Walker

## Slide 3: Sponsor and Advisor
Engineering Mentor
Cameron Griffith
Trane Sales Associates
Academic Advisor
Juan Ordóñez, Ph.D.
Full Professor
Nicholas Walker

## Slide 4: Objective
The objective of the project is to reduce the carbon emissions in the National High Magnetic Field Laboratory
Nicholas Walker
Notes: Bianca Marius

## Slide 5
Background
Nicholas Walker
Notes: So first off the definition of Greenhouse gas(or carbon) emissions are human activities strengthening the greenhouse effect which then causes a hotter climate change. The biggest cause of this is from carbon dioxide produced by burning fossil fuels: the most prominent being coal, oil, and natural gas.
This chart shows that the total US Greenhous Gas Emission transportation at 29%; however, electricity is right behind it at 25%. HVAC system accounts for 40% of a commercial buildings total energy use.
Bianca Marius

## Slide 6: Key Goals
Current Expenditures
Develop Solutions
Reduce Cost
Nicholas Walker
Notes: The key goals of our plan is to
Explore the current expenditures for Innovation Park Explore and the pre covid expenditures from the Maglab
Innovate the most effective potential solutions for improving the HVAC efficiency at Innovation Park
And then by taking into account of all the parts and manual installation and operation of these proposed ideas, determine Which solutions are the most cost effective.

## Slide 7: Markets
MagLab Utilities Facilitators
Trane
Nicholas Walker
Notes: Primary Markets are the mag lab and innovation park utilities facilitators along with Trane as these are who our solution is specifically geared towards and essentially being sold to first.
Trane

## Slide 8: Assumptions
Pre COVID-19 Data
Only HVAC
Nicholas Walker
Notes: Using Pre-Covid Data- covid 19 reduced the amount of MagLab contractors and skewed the energy usage data, so we will use data from 2019 before to interpolate the normal energy consumption
Only focusing on decreasing electricity use through HVAC- were not going to try to decrease the energy consumption of the magnets or the electricity habits of the building we are only focusing on a solution that incorporates the HVAC system to reduce electricity consumption and increase efficiency
Have access to all the necessary data- we will not have to add sensors to gather data. We will be able to collect the necessary data from the current sources

## Slide 9: Stakeholders
Cameron Griffith
Trane
FAMU-FSU COE
Nicholas Walker
Notes: Our stakeholders are our sponsor, Cameron Griffith, Trane, and the FAMU FSU College of Engineering.

## Slide 10: Functional Decomposition
Reduce
Reuse
Recycle
Nicholas Walker
Notes: The main functions for our project are the classic techniques to reduce carbon emissions. Reduce, reuse, recycle.
Reduce - reducing the energy that the MagLab , increase the energy efficiency
Reusing – reuse byproduct of one system for another, capture energy from other sources
Finally recycling use byproducts of one system for another

## Slide 11: Targets
Reduce 15% of energy usage
Reuse 10% of the byproduct of a system
Recycle 25% of waste
Nicholas Walker

## Slide 12: Concept Generation
Finnbar Rooney
Chill Water System Schematic
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 13: Concept Generation
Nicholas Walker
Chill Water System Schematic
Medium Fidelity Concept:
Adding a cooling tank
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 14: Concept Generation
Nicholas Walker
Chill Water System Schematic
High Fidelity Concept:
Optimizing the chillers
Medium Fidelity Concept:
Add a 5th chiller
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 15: Concept Generation
Chill Water System Schematic
High Fidelity Concept:
Variable speed fans on the cooling tower
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 16: Concept Generation
Nicholas Walker
Chill Water System Schematic
High Fidelity Concept:
Optimizing the water pumps
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 17: Concept Generation
Chill Water System Schematic
Finnbar Rooney
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 18: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 19: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 20: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 21: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 22: Concept Selection: Pugh Chart
 | Datum | Concepts |  | 
Selection Criteria | Adding a 5th Chiller | Optimizing Pumps | Variable Speed Cooling Fans | Optimizing Chillers
Implementation |  | + | S | +
Sustainable |  | + | S | +
Price |  | + | + | +
Life Span |  | - | - | -
Number of Pluses |  | 3 | 1 | 3
Number of Minuses |  | 1 | 1 | 1
Finnbar Rooney

## Slide 23: Concept Selection: Pugh Chart
 | Datum | Concepts |  | 
Selection Criteria | Adding a 5th Chiller | Optimizing Pumps | Variable Speed Cooling Fans | Optimizing Chillers
Implementation |  | + | S | +
Sustainable |  | + | S | +
Price |  | + | + | +
Life Span |  | - | - | -
Number of Pluses |  | 3 | 1 | 3
Number of Minuses |  | 1 | 1 | 1
Finnbar Rooney

## Slide 24: Concept Selection: Pugh Chart
 | Datum | Concepts |  | 
Selection Criteria | Adding a 5th Chiller | Optimizing Pumps | Variable Speed Cooling Fans | Optimizing Chillers
Implementation |  | + | S | +
Sustainable |  | + | S | +
Price |  | + | + | +
Life Span |  | - | - | -
Number of Pluses |  | 3 | 1 | 3
Number of Minuses |  | 1 | 1 | 1
Finnbar Rooney

## Slide 25: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 26: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 27: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 28: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 29: Final Selection
Finnbar Rooney
Concepts | Optimizing Pumps | Variable Speed Controlling Pumps | Optimizing Chillers
Alternative Value | 0.3183 | 0.3020 | 0.3165

## Slide 30: Additional Considerations
How does our sponsor feel about our selection?
  At first, apprehensive
  Overall satisfied
Cameron would like us to look at continuing this concept to serve the rest of the COE
Finnbar Rooney

## Slide 31: Next Steps
Research how to run the pumps on a temperature or magnet power
Organizing an assessment of the risks with this project
Consider validation techniques
Finnbar Rooney
Notes: Our next steps are to improve the efficiency of the MagLab HVAC systems. We will do this by first finding out all we can about the HVAC systems and ways we can improve it. Then we will generate concepts on how to improve the efficiency. Then we will select one of those concepts for our design project.

## Slide 32: References
Haughney, K. (2021, August 2). FSU breaks ground on new research facility. Florida State University News. Retrieved October 15, 2021, from https://news.fsu.edu/news/university-news/2021/08/02/fsu-breaks-ground-on-new-research-facility/.
Nicholas Walker

## Slide 33: Embodiment
Upcoming Presenter’s Name

## Slide 35: Background
Bianca Marius
Notes: For a quick overview on what the Maglab is: it’s a facility that has the world’s largest and highest-powered magnet in the world. It’s funded by National Science Foundation and the state of Florida, and each year more than 2,000 scientists come from across the globe to use their facilities. It focuses on using magnetic fields to conduct research on topics including physics, biology, bioengineering, chemistry, geochemistry, and biochemistry. It’s uses a lot of energy to run its operations, specifically 8% of Tallahassee’s electricity.
Now Trane is involved in supplying it’s HVAC system. Trane is a manufacturer of heating, ventilating, air conditioning systems; and they build management systems and controls. They rank consistently above average in customer satisfaction and dependability because of the quality of its components and the lifespan of its system is around 15-20 years.

## Slide 36: Secondary Market
Bianca Marius
FAMU and FSU
Building Contractors
Notes: And our secondary market are famu and fsu main campuses because then they can modify and change their techniques similarly to the primary market inorder to achieve the same result of reducing their carbon footprint while still saving money.
Also, building contractors are involved here as their job is to construct, modify, or demolish a structure and using our solution they could earn more capital by implementing it in future contracts.

## Slide 37: Progress
Two Directions
IRCB
MagLab Facilities
Nicholas Walker
Notes: Now our team has a decision to make.
We need to either design a way to transport the chill water from the MagLab to IRCB
or improve the efficiency of the existing MagLab facilities.
Both of these directions reduce carbon emissions therefore satisfying the original scope. Our team has selected to improve the existing facilities

## Slide 38: Progress
Interdisciplinary Research and Commercialization Building (IRCB)
Nicholas Walker
Notes: There is a new building coming to the Innovation park.
The Interdisciplinary Research and Commercialization Building will begin construction in 2024.
The current plan is to use the chill water from the MagLab to cool the new building. Chill water would be pumped from the MagLab and used in IRCB’s HVAC system. This method would reduce the amount of carbon emissions because using one building’s HVAC to cool two buildings consumes less energy than having each building provide their own cooling. Think of it like carpooling. Using one car for two people saves on fuel emissions. This is the same basic
New building without HVAC.

## Slide 39: Manufacturing
Upcoming Presenter’s Name

## Slide 41: Testing
Upcoming Presenter’s Name

## Slide 43: Project Management

## Slide 44: # Most Important Points
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.

## Slide 45: Lessons Learned

## Slide 46: Reference
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.

## Slide 47: Questions (be sure to design your own)

## Slide 48: Backup Slides

## Slide 49: Functional Decomp Backup

## Slide 52: Concept Selection Backup

## Slide 55: Detailed Math Backup

## Slide 58: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 59: Approved Logos

## Slide 60: Color Palette

## Slide 61: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |