## Slide 1
Team 517
Bianca Marius, Finnbar Rooney, Nicholas Walker
Team: 517
Making the MagLab Greener:
Optimizing the HVAC
Notes: Good Afternoon, our project is about making the MagLab greener. Specifically, we're focusing on optimizing the HVAC.

## Slide 2: Team Introductions
Nicholas Walker
Design Engineer
Bianca Marius
Thermal Fluids Engineer
Finnbar Rooney
Materials Engineer
Nicholas Walker
Notes: My name is Bianca Marius, I'm the thermal fluids engineer. This is Finnbar Rooney, our materials engineer and Nicholas Walker our design engineer.

## Slide 3: Sponsor and Advisor
Engineering Mentor
Cameron Griffith
Trane Sales Associates
Academic Advisor
Juan Ordóñez, Ph.D.
Full Professor
Nicholas Walker
Notes: Our sponsor is Cameron Griffith, a sales associate at Trane. And our advisor is Dr. Juan Ordonez, a full professor at the FAMU-FSU college of engineering.

## Slide 4: Objective
The objective of the project is to reduce the carbon emissions of the Innovation Park
Nicholas Walker
Notes: Bianca Marius
The main objective of this project is to reduce the carbon emissions of Innovation Park.

## Slide 5
Background
Nicholas Walker
Notes: So first off the definition of Greenhouse gas(or carbon) emissions are human activities strengthening the greenhouse effect which then causes a hotter climate change. The biggest cause of this is from carbon dioxide produced by burning fossil fuels: the most prominent being coal, oil, and natural gas.
This chart shows that the total US Greenhous Gas Emission transportation at 29%; however, electricity is right behind it at 25%. HVAC system accounts for 40% of a commercial buildings total energy use.
Bianca Marius

## Slide 6: Key Goals
Current Expenditures
Develop Solutions
Reduce Cost
Nicholas Walker
Notes: The key goals of our plan is to
Explore the current expenditures for Innovation Park Explore and the pre covid expenditures from the Maglab
Innovate the most effective potential solutions for improving the HVAC efficiency at Innovation Park
And then by taking into account of all the parts and manual installation and operation of these proposed ideas, determine Which solutions are the most cost effective.

## Slide 7: Markets
Innovation Park
Trane
Nicholas Walker
Notes: Primary Markets are the mag lab and innovation park utilities facilitators along with Trane as these are who our solution is specifically geared towards and essentially being sold to first.
Trane

## Slide 8: Assumptions
Pre COVID-19 Data
Only HVAC
Nicholas Walker
Notes: Using Pre-Covid Data- covid 19 reduced the amount of MagLab contractors and skewed the energy usage data, so we will use data from 2019 before to interpolate the normal energy consumption
Only focusing on decreasing electricity use through HVAC-
were not going to try to decrease the energy consumption of the magnets or the electricity habits of the building
We are only focusing on a solution that incorporates the HVAC system to reduce electricity consumption and increase efficiency
Have access to all the necessary data- we will not have to add sensors to gather data. We will be able to collect the necessary data from the current sources

## Slide 9: Functional Decomposition
Reduce
Reuse
Recycle
Nicholas Walker
Notes: The main functions for our project to reduce, reuse, recycle.
Reduce - reducing the energy that the MagLab , increase the energy efficiency
Reusing - reuse by product of one system for another, capture energy from other sources
Finally recycling use byproducts of one system for another

## Slide 10: Concept Generation
Chill Water System Schematic
Nicholas Walker
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 11: Final Selection
Nicholas Walker
Concepts | Optimizing Pumps | Variable Speed Controlling Fans | Optimizing Chillers
Alternative Value | 0.3183 | 0.3020 | 0.3165

## Slide 12: Additional Considerations
How does our sponsor feel about our selection?
At first, apprehensive
But overall satisfied
Cameron would like us to look at continuing this concept to serve the rest of the Innovation Park.
Nicholas Walker

## Slide 13: Three Main Parts
Create a tabletop validation technique to present on Senior Design day.
Redesign the cooling system for the magnets at the MagLab.
Move chill water to IRCB.
Nicholas Walker
13

## Slide 14: Redesigning the MagLab Cooling System
The pumps run with the assumption that the magnets are drawing max power.
Cooling them more accurately will reduce energy and save money.
Bianca Marius

## Slide 15: Redesigning the MagLab Cooling System
Find the optimized minimum safe value
Propose an automatic system to control the pumps
Bianca Marius

## Slide 16: Move Chill Water to IRCB
Determine the cooling requirement for IRCB.
From the cooling requirement, calculate the amount of chill water needed.
Design a method to transfer that amount to IRCB.
Bianca Marius

## Slide 17: Progress on IRCB
IRCB requires 800 tons of cooling capacity
This requires 1371 gpm of chilled water to cool
This would require pipes of roughly 6 ½ inches in inner diameter
Bianca Marius

## Slide 18: Over a 30 Year Lifetime
16 million kWh of electricity
10 million kWh
kg of CO2
2 million dollars
Bianca Marius

## Slide 19: Validation Technique
Bianca Marius
Heating Element
Cooling Block
Reservoir
As the heat increases…
The voltage provided to the pump also increases.

## Slide 20: Validation Technique
Bianca Marius
Heating Element
Cooling Block
Reservoir
As the heat decreases…
The voltage provided to the pump also decrease, saving energy.

## Slide 21: Validation Technique
Progress:
Hardware has been ordered
Still Need:
Electronics
Bianca Marius

## Slide 22: References
Affiliated Engineers. (2019). Florida State University Research Park Central Utilities Study. Tallahassee.
Bianca Marius

## Slide 23: Thank you
Finnbar Rooney
Nicholas Walker
Bianca Marius

## Slide 24: What We still need
Determine cost of pipes
Determine cost of installing pipes

## Slide 25: Targets
Reduce 15% of
Reuse 10% of the byproduct of a system
Recycle 25% of waste
Bianca Marius

## Slide 26: Progress on Validation Technique
Hardware parts have been ordered
Still figuring out the electronics that are associated with controlling the pump
Voltage Limiter

## Slide 27: Future Work
Plan a way to cool the magnets at the MagLab

## Slide 28: References
Haughney, K. (2021, August 2). FSU breaks ground on new research facility. Florida State University News. Retrieved October 15, 2021, from https://news.fsu.edu/news/university-news/2021/08/02/fsu-breaks-ground-on-new-research-facility/.
Nicholas Walker

## Slide 29: Concept Generation
Finnbar Rooney
Chill Water System Schematic
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 30: Concept Generation
Nicholas Walker
Chill Water System Schematic
Medium Fidelity Concept:
Adding a cooling tank
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 31: Concept Generation
Nicholas Walker
Chill Water System Schematic
High Fidelity Concept:
Optimizing the chillers
Medium Fidelity Concept:
Add a 5th chiller
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 32: Concept Generation
Chill Water System Schematic
High Fidelity Concept:
Variable speed fans on the cooling tower
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 33: Concept Generation
Nicholas Walker
Chill Water System Schematic
High Fidelity Concept:
Optimizing the water pumps
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 34: Embodiment
Upcoming Presenter’s Name

## Slide 36: Background
Bianca Marius
Notes: For a quick overview on what the Maglab is: it’s a facility that has the world’s largest and highest-powered magnet in the world. It’s funded by National Science Foundation and the state of Florida, and each year more than 2,000 scientists come from across the globe to use their facilities. It focuses on using magnetic fields to conduct research on topics including physics, biology, bioengineering, chemistry, geochemistry, and biochemistry. It’s uses a lot of energy to run its operations, specifically 8% of Tallahassee’s electricity.
Now Trane is involved in supplying it’s HVAC system. Trane is a manufacturer of heating, ventilating, air conditioning systems; and they build management systems and controls. They rank consistently above average in customer satisfaction and dependability because of the quality of its components and the lifespan of its system is around 15-20 years.

## Slide 37: Stakeholders
Cameron Griffith
Trane
FAMU-FSU COE
Nicholas Walker
Notes: Our stakeholders are our sponsor, Cameron Griffith, Trane, and the FAMU FSU College of Engineering.

## Slide 38: Secondary Market
Bianca Marius
FAMU and FSU
Building Contractors
Notes: And our secondary market are famu and fsu main campuses because then they can modify and change their techniques similarly to the primary market inorder to achieve the same result of reducing their carbon footprint while still saving money.
Also, building contractors are involved here as their job is to construct, modify, or demolish a structure and using our solution they could earn more capital by implementing it in future contracts.

## Slide 39: Progress
Two Directions
IRCB
MagLab Facilities
Nicholas Walker
Notes: Now our team has a decision to make.
We need to either design a way to transport the chill water from the MagLab to IRCB
or improve the efficiency of the existing MagLab facilities.
Both of these directions reduce carbon emissions therefore satisfying the original scope. Our team has selected to improve the existing facilities

## Slide 40: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 41: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 42: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 43: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 44: Concept Selection: Pugh Chart
 | Datum | Concepts |  | 
Selection Criteria | Adding a 5th Chiller | Optimizing Pumps | Variable Speed Cooling Fans | Optimizing Chillers
Implementation |  | + | S | +
Sustainable |  | + | S | +
Price |  | + | + | +
Life Span |  | - | - | -
Number of Pluses |  | 3 | 1 | 3
Number of Minuses |  | 1 | 1 | 1
Finnbar Rooney

## Slide 45: Concept Selection: Pugh Chart
 | Datum | Concepts |  | 
Selection Criteria | Adding a 5th Chiller | Optimizing Pumps | Variable Speed Cooling Fans | Optimizing Chillers
Implementation |  | + | S | +
Sustainable |  | + | S | +
Price |  | + | + | +
Life Span |  | - | - | -
Number of Pluses |  | 3 | 1 | 3
Number of Minuses |  | 1 | 1 | 1
Finnbar Rooney

## Slide 46: Concept Selection: Pugh Chart
 | Datum | Concepts |  | 
Selection Criteria | Adding a 5th Chiller | Optimizing Pumps | Variable Speed Cooling Fans | Optimizing Chillers
Implementation |  | + | S | +
Sustainable |  | + | S | +
Price |  | + | + | +
Life Span |  | - | - | -
Number of Pluses |  | 3 | 1 | 3
Number of Minuses |  | 1 | 1 | 1
Finnbar Rooney

## Slide 47: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 48: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 49: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 50: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 51: Progress
Interdisciplinary Research and Commercialization Building (IRCB)
Nicholas Walker
Notes: There is a new building coming to the Innovation park.
The Interdisciplinary Research and Commercialization Building will begin construction in 2024.
The current plan is to use the chill water from the MagLab to cool the new building. Chill water would be pumped from the MagLab and used in IRCB’s HVAC system. This method would reduce the amount of carbon emissions because using one building’s HVAC to cool two buildings consumes less energy than having each building provide their own cooling. Think of it like carpooling. Using one car for two people saves on fuel emissions. This is the same basic
New building without HVAC.

## Slide 52: Manufacturing
Upcoming Presenter’s Name

## Slide 54: Testing
Upcoming Presenter’s Name

## Slide 56: Project Management

## Slide 57: # Most Important Points
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.

## Slide 58: Lessons Learned

## Slide 59: Reference
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.

## Slide 60: Questions (be sure to design your own)

## Slide 61: Backup Slides

## Slide 62: Functional Decomp Backup

## Slide 65: Concept Selection Backup

## Slide 68: Detailed Math Backup

## Slide 71: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 72: Approved Logos

## Slide 73: Color Palette

## Slide 74: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |