## Slide 1
Team 517
Bianca Marius, Finnbar Rooney, Nicholas Walker
Team: 517
Making the MagLab Greener:
Optimizing the HVAC
Notes: Good Afternoon, our project is about making the MagLab greener. Specifically, we're focusing on optimizing the HVAC.

## Slide 2: Team Introductions
Nicholas Walker
Design Engineer
Bianca Marius
Thermal Fluids Engineer
Finnbar Rooney
Materials Engineer
Finnbar Rooney
Notes: My name is Bianca Marius, I'm the thermal fluids engineer. This is Finnbar Rooney, our materials engineer and Nicholas Walker our design engineer.

## Slide 3: Sponsor and Advisor
Company Sponsor
Cameron Griffith
Trane Sales Associates
Academic Advisor
Juan Ordóñez, Ph.D.
Full Professor
Finnbar Rooney
Notes: Our sponsor is Cameron Griffith, a sales associate at Trane. And our advisor is Dr. Juan Ordonez, a full professor at the FAMU-FSU college of engineering.

## Slide 4: Objective
The objective of the project is to reduce the carbon emissions of the Innovation Park
Finnbar Rooney
Notes: Bianca Marius
The main objective of this project is to reduce the carbon emissions of Innovation Park.

## Slide 5
Background
Finnbar Rooney
Notes: So first off the definition of Greenhouse gas(or carbon) emissions are human activities strengthening the greenhouse effect which then causes a hotter climate change. The biggest cause of this is from carbon dioxide produced by burning fossil fuels: the most prominent being coal, oil, and natural gas.
This chart shows that the total US Greenhous Gas Emission transportation at 29%; however, electricity is right behind it at 25%. HVAC system accounts for 40% of a commercial buildings total energy use.
Bianca Marius

## Slide 6: Key Goals
Current Expenditures
Develop Solutions
Reduce Cost
Finnbar Rooney
Notes: The key goals of our plan is to
Explore the current expenditures for Innovation Park Explore and the pre covid expenditures from the Maglab
Innovate the most effective potential solutions for improving the HVAC efficiency at Innovation Park
And then by taking into account of all the parts and manual installation and operation of these proposed ideas, determine Which solutions are the most cost effective.

## Slide 7: Markets
Finnbar Rooney
Notes: Primary Markets are the mag lab and innovation park utilities facilitators along with Trane as these are who our solution is specifically geared towards and essentially being sold to first.
Trane

## Slide 8: Assumptions
Pre COVID-19 Data
Only HVAC
Finnbar Rooney
Notes: Using Pre-Covid Data- covid 19 reduced the amount of MagLab contractors and skewed the energy usage data, so we will use data from 2019 before to interpolate the normal energy consumption
Only focusing on decreasing electricity use through HVAC-
were not going to try to decrease the energy consumption of the magnets or the electricity habits of the building
We are only focusing on a solution that incorporates the HVAC system to reduce electricity consumption and increase efficiency
Have access to all the necessary data- we will not have to add sensors to gather data. We will be able to collect the necessary data from the current sources

## Slide 9: Functional Decomposition
Reduce
Reuse
Recycle
Finnbar Rooney
Notes: The main functions for our project to reduce, reuse, recycle.
Reduce - reducing the energy that the MagLab , increase the energy efficiency
Reusing - reuse by product of one system for another, capture energy from other sources
Finally recycling use byproducts of one system for another

## Slide 10: Concept Generation
Finnbar Rooney
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 11: Final Selection
Finnbar Rooney
Concepts | Optimizing Pumps | Variable Speed Controlling Fans | Optimizing Chillers
Alternative Value | 0.3183 | 0.3020 | 0.3165

## Slide 12: Additional Considerations
Interdisciplinary Research and Commercialization Building
Finnbar Rooney

## Slide 13: Three Main Parts
Create a tabletop validation technique represent our design
Redesign the cooling system for the magnets at the MagLab.
Move chill water to IRCB.
Nicholas Walker
13

## Slide 14: Redesigning the MagLab Cooling System
The pumps run with the assumption that the magnets are drawing max power.
Cooling them more accurately will reduce energy and save money.
Nicholas Walker
Notes: So how we'll be doing is redesigning the Maglab's cooling system: currently they run with the assumption that the magnets are using their maximum power.
So we're trying to figure out how to cool them more accurately to reduce the energy used and therefore save more money.
For the Maglab's cooling system, the pumps currently run under the assumption that the magnets are always being used at maximum power. But this is not true, so we want to figure out how to cool them more accurately in order to reduce the energy usage and then as a result save more money.

## Slide 15: Redesigning the MagLab Cooling System
Find the optimized minimum safe value
Propose an automatic system to control the pumps
Nicholas Walker
Notes: What we mean when we say we want to find the minimum optimized safe value is that we want to find the lowest possible voltage that can be provided to the pumps in order to keep the system running safely. Because these pumps are used to push cool water past the magnets in order to keep them cool, because when the magnets are in use, they heat up. And like most systems that heat up when in use, we need something in place to keep it cooled down.
Using graphs and data provided to us on the Maglab's cooling pumps, we'll try to find the minimum safe value for the pumps.
\\The magnets will put out a certain amount of heat and we're trying to find the value of what is the least amount of voltage that can be supplied in order to keep these magnets from overheating.
We want to propose an automated system in order to keep this process running instead of having a person manually figure out what the amount of voltage will be needed
Problem to solution explanation:

## Slide 16: Magnet Cooling Costs
Nicholas Walker
Found monthly KW used
Calculate using a cost of $1.88 Per KW

## Slide 17: Cost
Nicholas Walker
Monthly KW Used | Monthly Cost
499.17 | $844.45

## Slide 18: Optimized Pumps
Used a percentage of the heat flow required to determine what percentage of the pump was needed
Calculated the optimized cost
Nicholas Walker

## Slide 19: Optimized Cost
Nicholas Walker
Optimized Monthly KW Used | Optimized Monthly Cost
55.38 | $104.11

## Slide 20: Comparison
Nicholas Walker
Notes: The Optimized saves 73.5% of the total Power usage per

## Slide 21: Savings
Save 393.80 KW
4,725.5 KW in a year
$740 Monthly
Saves $8,884 in a year
Nicholas Walker

## Slide 22: Move Chill Water to IRCB
Determine the cooling requirement for IRCB.
From the cooling requirement, calculate the amount of chill water needed.
Design a method to transfer that amount to IRCB.
Bianca Marius
Notes: So the next part of this plan is that we need to figure out how to move the chill water from the MagLab to IRCB. First we need to determine the amount of cooling required for IRCB, in other words we need to figure out what this specific commercial building will need in order to keep its contractors cool. And then from this we need to calculate the amount of chill water needed.
Then we need to design a method to transfer that chill water from the Maglab to IRCB.

## Slide 23: Progress on IRCB
IRCB requires 800 tons of cooling capacity
This requires 1371 gpm of chilled water to cool
This would require pipes of roughly 6 ½ inches in inner diameter
Bianca Marius
Notes: Now for a progress update on IRCB. From a report provided to us by John Kynoch done by the affiliated engineers on this project we know that IRCB requires 800 tons of cooling capacity. To keep up with this cooling capacity it will need 1371 gpm of chilled water being pumped. And this would then require pipes with roughly 6.5 inches for their inner diameter as that is the standard size for pipes used in these types of chill water systems.

## Slide 24: Pump Power Requirement
Work done by the pump on the fluid:
Modified Bernoulli's Equation:
Simplified:
Known:
Assumptions:
No minor pressure losses (entries, exits, fittings, and valves)
No change in height
Bianca Marius
Variable | Value | Units
L | 182.22 | m
ρwater | 1000 | kg/m3
D | 0.1651 | m
ṁ | 86.4 | kg/s
Notes: Next we wanted to figure out how much power it would take to keep this system running. The equation to find power is the volumetric flow rate multiplied by the pressure loss. To find the pressure loss we used a modified version of the Bernoulli's Equation. It simplifies out to being...this equation. The knowns in the equation include L...
Which is the distance between IRCB and the Maglab, 200 yards. The D in this equation is the diameter of the pipe, estimated to be 6.5 inches. The rho represents density, which we know will be the density of water 1000 kg/m3.
And the unknown is f, the friction factor, which can be calculated.
The mu is dynamic viscosity, again based off of water.

## Slide 25: Finding the Friction Factor
First figure out whether the flow is laminar or turbulent with the Reynold’s Number
Use Chen Correlation to find the friction factor
Bianca Marius
Known:​ ​
ƒ= f(ReD , ε, D)
Variable | Value | Units
µwater | 8.9 x 10-4 | Pa•s
ε | 1.5 x 10-6 | m
D | 0.1651 | m
ṁ | 86.4 | kg/s
ReD = 4ṁ πµD
____
Notes: There are several equations that can be used to find the friction factor. This is because the equation you use is based off of whether or not the flow is laminar or turbulent. In order to figure out the status of the flow you need to find the value of the reynolds number. The reynolds number is this equation shown here. We used the one farthest to the right being 4 times mdot, the mass flow rate, over pi, mu, and D the diameter.
Mu is the dynamic viscosity of the water, which was found to be 8.9x10^-4 meters. Plugging these in, the Reynold's number was found to be higher than 2,000 which means that the flow is turbulent.
We can then use the Chen Correlation to find the friction factor for this flow.
The three variables in this equation are epsilon, the relative roughness, which comes from the pipe material?? Found to be 1.5x10^-6m, D the diameter of the pipe, and the Reynold's #.
Then we were able to calculate the pressure loss which came out to
So we plug these in and find the friction factor value, then we have all of the variables needed to plug in to the equation to find the pressure loss.

## Slide 26: Estimated Power Needed
Figure out the volumetric flow rate:
Power Required:
V̇*Δp = 9630 W
Bianca Marius
V̇=AV
V= ṁ
(ρA)
Known:​
Variable | Value | Unit
ṁ | 86.4 | kg/s
A | 0.0214 | m2
ρwater | 1000 | kg/m3
Δp | 111500 | Pa
___
Notes: Now the only thing left to find the power is the volumetric flow rate. Which again is v dot.
Which we can find using the formula V dot is equal to the area times the velocity of the flow.
The velocity is found from mdot over density times the area.
Finally we were able to find the power which ended up being around 9700W.

## Slide 27: Piping Cost Analysis
Material(All 6") | Cost per foot | Total Cost
PVC | $5.28-$7.79 | $3165-$4675
HDPE | $6.97-$10.21 | $4182-$6126
Stainless Steel | $39-$268.07 | $23400-160,842
Carbon Steel | $42.45-$61 | $25,470-$36,600
Bianca Marius
Notes: Next we performed a cost analysis on different material that could be used to make the pipes. We chose some of the most commonly used ones including PVC, HDPE, Stainless Steel, and Carbon Steel. It was found that the one with the lowest average cost was PVC.
And what will we do with this information?

## Slide 28: Over a 30 Year Lifetime
16 million kWh of electricity
10 million kg of CO2
2 million dollars
Bianca Marius
Reference: Affiliated Engineers. (2019). Florida State University Research Park Central Utilities Study. Tallahassee.
Notes: According to this plan, done by the study, we'll save over 16 million kWh of electricity over a 30 year lifetime, along with saving 10 million kWh kg of CO2 and $2 million dollars.
How are 2 million dollars being saved?
In this 2 million dollars includes, installed costs, operational costs both annual and non-annual, residual value, and annual energy expenditures.

## Slide 29: Validation Technique
Finnbar Rooney
Heating Element
Cooling Block
Reservoir
As the heat increases…
The voltage provided to the pump also increases.
Notes: Now for our table top technique, we want a system that replicates how as the heat increases, the voltage provided to the pump will also increases.
Heating element=magnets
Reservoir=cooling towers
Pumps=pumps

## Slide 30: Validation Technique
Finnbar Rooney
Heating Element
Cooling Block
Reservoir
As the heat decreases…
The voltage provided to the pump also decrease, saving energy.

## Slide 31: Validation Technique
Finnbar Rooney
MAX6675 Thermocouple
12V Gikfun R385 Pump
Arduino Mega
Notes: For a progress update on our prototype some parts we've ordered are a 3.5 gallon polyethylene pail, a submersible pump and PVC tubing for the water, cold plate with copper tubes to transfer the water over the hot plate that represents the magnet.

## Slide 32: Lessons Learned
Projects are hard!
Multiple stakeholders
Very complicated very quickly
Future work will focus on perfecting the validation technique
Finnbar Rooney

## Slide 33: Thank you
Finnbar Rooney
Nicholas Walker
Bianca Marius

## Slide 34: References
Affiliated Engineers. (2019). Florida State University Research Park Central Utilities Study. Tallahassee.
Bianca Marius

## Slide 35: Validation Technique
Progress:
Hardware has been ordered
Still Need:
Electronics
Bianca Marius
Notes: For a progress update on our prototype some parts we've ordered are a 3.5 gallon polyethylene pail, a submersible pump and PVC tubing for the water, cold plate with copper tubes to transfer the water over the hot plate that represents the magnet.

## Slide 36: Targets
Reduce 15% of
Reuse 10% of the byproduct of a system
Recycle 25% of waste
Bianca Marius

## Slide 37: Progress on Validation Technique
Hardware parts have been ordered
Still figuring out the electronics that are associated with controlling the pump
Voltage Limiter

## Slide 38: Future Work
Plan a way to cool the magnets at the MagLab

## Slide 39: References
Haughney, K. (2021, August 2). FSU breaks ground on new research facility. Florida State University News. Retrieved October 15, 2021, from https://news.fsu.edu/news/university-news/2021/08/02/fsu-breaks-ground-on-new-research-facility/.
Nicholas Walker

## Slide 40: Concept Generation
Finnbar Rooney
Chill Water System Schematic
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 41: Concept Generation
Nicholas Walker
Chill Water System Schematic
Medium Fidelity Concept:
Adding a cooling tank
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 42: Concept Generation
Nicholas Walker
Chill Water System Schematic
High Fidelity Concept:
Optimizing the chillers
Medium Fidelity Concept:
Add a 5th chiller
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 43: Concept Generation
Chill Water System Schematic
High Fidelity Concept:
Variable speed fans on the cooling tower
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 44: Concept Generation
Nicholas Walker
Chill Water System Schematic
High Fidelity Concept:
Optimizing the water pumps
Notes: John Kynoch took us on a tour of the maglab
Chillers –
Cool down water by transferring heat to the condenser system
-4 chillers made by trane
-2000 GPM of 40 degree water
-2 billion ice cubes
-8000 tons of cooling power
Condenser system
-takes the heat from the chilled water
Rejects heat into atmosphere with 4 cell cooling tower
4 condenser pumps pump 6000 GPM through chillers and back to heating tower
Heat exchanger system
- Water from chiller pumped into hear exchanger at 3000 GPM
-hot water from the magnets comes in 2 heat exchanger and transfers heat to the chilled water
can transfer 56MW of heat in the time the water transfers
-water enters more than 120 degrees leaves at 42 degrees
Heated water then pimped into the chiller
Chilled Water Storage Tank
Two chilled water storage tanks
One is 3 million gallons
One in 1.3 million gallons
Act as thermal energy storage and buffer for chillers
Additional 58,000 ton hours of cooling power
HVAC System
-takes up to 2400 GPM
-uses chilled water to cool the air that blows thoughout the building

## Slide 45: Embodiment
Upcoming Presenter’s Name

## Slide 47: Background
Bianca Marius
Notes: For a quick overview on what the Maglab is: it’s a facility that has the world’s largest and highest-powered magnet in the world. It’s funded by National Science Foundation and the state of Florida, and each year more than 2,000 scientists come from across the globe to use their facilities. It focuses on using magnetic fields to conduct research on topics including physics, biology, bioengineering, chemistry, geochemistry, and biochemistry. It’s uses a lot of energy to run its operations, specifically 8% of Tallahassee’s electricity.
Now Trane is involved in supplying it’s HVAC system. Trane is a manufacturer of heating, ventilating, air conditioning systems; and they build management systems and controls. They rank consistently above average in customer satisfaction and dependability because of the quality of its components and the lifespan of its system is around 15-20 years.

## Slide 48: Stakeholders
Cameron Griffith
Trane
FAMU-FSU COE
Nicholas Walker
Notes: Our stakeholders are our sponsor, Cameron Griffith, Trane, and the FAMU FSU College of Engineering.

## Slide 49: Secondary Market
Bianca Marius
FAMU and FSU
Building Contractors
Notes: And our secondary market are famu and fsu main campuses because then they can modify and change their techniques similarly to the primary market inorder to achieve the same result of reducing their carbon footprint while still saving money.
Also, building contractors are involved here as their job is to construct, modify, or demolish a structure and using our solution they could earn more capital by implementing it in future contracts.

## Slide 50: Progress
Two Directions
IRCB
MagLab Facilities
Nicholas Walker
Notes: Now our team has a decision to make.
We need to either design a way to transport the chill water from the MagLab to IRCB
or improve the efficiency of the existing MagLab facilities.
Both of these directions reduce carbon emissions therefore satisfying the original scope. Our team has selected to improve the existing facilities

## Slide 51: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 52: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 53: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 54: Concept Selection: House of Quality
House of Quality |  | Engineering Characteristics |  |  | 
Improvement Directions |  |  |  |  | 
Units |  | n/a | Joules | $ | Years
Customer Requirements | Importance Weight Factor | Implementation | Sustainable | Price | Life Span
Learn Engineering Tools | 2 | 9 | 3 | 1 | -
Reduce Power Consumption | 3 | 1 | 9 | 3 | -
Implemented at the MagLab | 2 | 3 | - | - | -
Benefit the COE | 1 | - | 3 | 3 | 1
Low Initial Cost | 2 | 3 | - | 3 | -
Raw Score (78) |  | 33 | 27 | 17 | 1
Relative Weight % |  | 42.3 | 34.6 | 21.7 | 1.28
Rank Order |  | 1 | 2 | 3 | 4
Finnbar Rooney

## Slide 55: Concept Selection: Pugh Chart
 | Datum | Concepts |  | 
Selection Criteria | Adding a 5th Chiller | Optimizing Pumps | Variable Speed Cooling Fans | Optimizing Chillers
Implementation |  | + | S | +
Sustainable |  | + | S | +
Price |  | + | + | +
Life Span |  | - | - | -
Number of Pluses |  | 3 | 1 | 3
Number of Minuses |  | 1 | 1 | 1
Finnbar Rooney

## Slide 56: Concept Selection: Pugh Chart
 | Datum | Concepts |  | 
Selection Criteria | Adding a 5th Chiller | Optimizing Pumps | Variable Speed Cooling Fans | Optimizing Chillers
Implementation |  | + | S | +
Sustainable |  | + | S | +
Price |  | + | + | +
Life Span |  | - | - | -
Number of Pluses |  | 3 | 1 | 3
Number of Minuses |  | 1 | 1 | 1
Finnbar Rooney

## Slide 57: Concept Selection: Pugh Chart
 | Datum | Concepts |  | 
Selection Criteria | Adding a 5th Chiller | Optimizing Pumps | Variable Speed Cooling Fans | Optimizing Chillers
Implementation |  | + | S | +
Sustainable |  | + | S | +
Price |  | + | + | +
Life Span |  | - | - | -
Number of Pluses |  | 3 | 1 | 3
Number of Minuses |  | 1 | 1 | 1
Finnbar Rooney

## Slide 58: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 59: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 60: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 61: Concept Selection: AHP
Normalized AHP | Implementation | Sustainable | Price | Life Span | Criteria Weights
Implementation | 0.67 | 0.80 | 0.35 | 0.40 | 0.555
Sustainable | 0.13 | 0.16 | 0.45 | 0.52 | 0.315
Price | 0.1 | 0.02 | 0.05 | 0.02 | 0.0475
Life Span | 0.1 | 0.02 | 0.15 | 0.06 | 0.0825
Sum | 1.0 | 1.0 | 1.0 | 1.0 | 1.0
Finnbar Rooney

## Slide 62: Progress
Interdisciplinary Research and Commercialization Building (IRCB)
Nicholas Walker
Notes: There is a new building coming to the Innovation park.
The Interdisciplinary Research and Commercialization Building will begin construction in 2024.
The current plan is to use the chill water from the MagLab to cool the new building. Chill water would be pumped from the MagLab and used in IRCB’s HVAC system. This method would reduce the amount of carbon emissions because using one building’s HVAC to cool two buildings consumes less energy than having each building provide their own cooling. Think of it like carpooling. Using one car for two people saves on fuel emissions. This is the same basic
New building without HVAC.

## Slide 63: Manufacturing
Upcoming Presenter’s Name

## Slide 65: Testing
Upcoming Presenter’s Name

## Slide 67: Project Management

## Slide 68: # Most Important Points
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.
The quick brown fox jumps over the lazy dog.

## Slide 69: Lessons Learned

## Slide 70: Reference
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies, purus lectus malesuada libero, sit amet commodo magna eros quis urna.

## Slide 71: Questions (be sure to design your own)

## Slide 72: Backup Slides

## Slide 73: Functional Decomp Backup

## Slide 76: Concept Selection Backup

## Slide 79: Detailed Math Backup

## Slide 82: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 83: Approved Logos

## Slide 84: Color Palette

## Slide 85: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |