## Slide 1
NASA STUDENT LAUNCH
SD T501: The Zenith Program

## Slide 2: Zenith Program Leads
Zachary L. Isriel
Role: Program Director
Engineering Interests: Human spaceflight, spacecraft R&D, commercial launch
Jedreck Acquissa
Role: Recovery & Avionics System Lead
Engineering Interests: Fluid Design and Food Manufacturing
Mark A. Ioffredo
Role: Payload System Lead
Engineering Interests: Fluid Design and Aerodynamics
Peyton C. Breland
Role: Propulsion & Vehicle Design Lead
Engineering Interests: Fluid Design, Flight Vehicle Design and Manufacturing
Dylan A. Gardner
Role: STEM Engagement Lead
Engineering Interests: Fluid design, Heat Transfer, and Manufacturing

## Slide 3
Project Overview

## Slide 4: Stakeholders and Roles
National Aeronautics and Space Administration
Launch Service Client
Competition Organizer
Shayne McConomy,
Ph.D.
Functional Manager
ME Senior Design Coordinator
Project Sponsor
William Oates,
Ph.D.
Project Investor
ME Department Chair
Chiang Shih,
Ph.D.
Project Advisor
AME Center Director
AIAA Student Org. Advisor

## Slide 5: Objective
Fly a dual deployment, high-power solid rocket to an altitude of 4,600 ft that will deploy a payload capable of receiving and executing a string of radio frequency commands, after the vehicle has safely recovered within 2500 feet of the launch pad.

## Slide 6: Flight Objective Overview
80-85° Deg
Zenith I
Phase I:
Vehicle fully assembled and launch ready
Phase II:
High velocity ascent with spin stabilization

## Slide 7
Zenith I
Flight Profile Overview
80-85° Deg
Phase II:
High velocity ascent with spin stabilization
Phase I:
Vehicle fully assembled and launch ready
Phase III:
Apogee (4600 ft) first separation (drogue deployment)
7
Peyton Breland

## Slide 8
Phase II:
High velocity ascent with spin stabilization
Phase III:
Apogee (4600 ft) first separation (drogue deployment)
Zenith I
8
Peyton Breland

## Slide 9
Phase III:
Apogee (4600 ft) first separation (drogue deployment)
Zenith I
9
Peyton Breland

## Slide 10
Phase III:
Apogee (4600 ft) first separation (drogue deployment)
Zenith I
Phase IV:
High velocity descent phase
10
Peyton Breland

## Slide 11
Zenith I
Phase III:
Apogee (4600 ft) first separation (drogue deployment)
Phase IV:
High velocity descent phase
Phase V:
Main Chute + Payload Deployment (~550 ft)
11
Peyton Breland

## Slide 12
Zenith I
Phase V:
Main Chute + Payload Deployment (~550 ft)
Phase IV:
High velocity descent phase
12
Peyton Breland

## Slide 13
Phase V:
Main Chute + Payload Deployment (~550 ft)
Phase IV:
High velocity descent phase
13
Zenith I
Peyton Breland

## Slide 14
Phase V:
Main Chute + Payload Deployment (~550 ft)
Zenith I
14
Phase VI:
Low velocity descent till landing
Peyton Breland

## Slide 15
Phase V:
Main Chute + Payload Deployment (~550 ft)
Zenith I
Phase VI:
Low velocity descent till landing
15
Peyton Breland
Phase VII:
Payload completes series of tasks

## Slide 16
Phase VII:
Payload completes series of tasks
16
Peyton Breland
Zenith I
Phase VI:
Low velocity descent till landing

## Slide 17: Project Scope – Key Goals
Be awarded for at least one of the competition categories
From apogee to touchdown in under 85 seconds
Payload completes the desired series of tasks
Successful and accurate flight tests
Reach within 100 ft of the proposed 4600 ft apogee
Maintain a mid-flight stability margin between 3 and 4 calibers

## Slide 18
Launch Vehicle Design

## Slide 19: Design Concepts
Vehicle Concept 1
Vehicle Concept 2
Vehicle Concept 3

## Slide 20: Design Concepts
Vehicle Concept 1
Payload
Ogive Nose Cone
Drogue Chute
AV Bay
Main Chute
Aluminum Thrust Plate
Threaded Rods
Vehicle Concept 2
Vehicle Concept 3
Mass w/ motor: 33.64 lbs (15257 g)
Stability Margin @ 20 mph wind speeds: 1.12 cal
Apogee (max altitude): 5484 feet
Length: 80.5 inches (~6 feet 7 inches)

## Slide 21: Design Concepts
Vehicle Concept 1
Vehicle Concept 2
Vehicle Concept 3

## Slide 22: Design Concepts
Mass w/ motor: 42.42 lbs (19241 g)
Stability Margin @ 20 mph wind speeds: 1.45 cal
Apogee (max altitude): 4048 feet
Length: 85 inches (~7 feet 1 inch)
LD-Haack Series Nose Cone
Payload
Drogue Chute
AV Bay
Main Chute
Threaded Rods
Aluminum Thrust Plate
Vehicle Concept 1
Vehicle Concept 3
Vehicle Concept 2

## Slide 23: Design Concepts
Vehicle Concept 1
Vehicle Concept 2
Vehicle Concept 3

## Slide 24: Design Concepts
Vehicle Concept 3
Mass w/ motor: 38.30 lbs (17372 g)
Stability Margin @ 20 mph wind speeds: 2.25 cal
Apogee (max altitude): 4533 feet
Length: 99 inches (~8 feet 3 inch)
LD-Haack Series Nose Cone
Payload
AV Bay
Threaded Rods
Main Chute
Drogue Chute
3D Printed Thrust Plate and Tail Cone Config.
Vehicle Concept 2
Vehicle Concept 1

## Slide 25: Launch Vehicle Final Design
99.5 in.
6.154 in.
Weight: 38.30 lb
Target Altitude: 4600 ft
Max Velocity: 545 ft/s
Sections held together by #4-40 Nylon shear pins (~ 39 lbf required for each pin)

## Slide 26: Launch Vehicle Sections
Top Section
Nose cone + Upper Payload Bay
Middle Section
Avionics Bay
Bottom Section
Lower Payload Bay + Fin Can
99 in.
6.154 in.
Weight: 38.30 lb
Target Altitude: 4600 ft
Max Velocity: 545 ft/s
Sections held together by #4-40 Nylon shear pins (~ 39 lbf required for each pin)

## Slide 27: Launch Vehicle Sections
55 in.
Nose cone
3 sections for printing feasibility
Upper Payload Bay
Stores:
  Main parachute (Fruity Chutes 84” Iris Ultra Standard)
  32 ft of recovery harness
  Payload

## Slide 28: Launch Vehicle Sections
Top Section
Nose cone + Upper Payload Bay
Middle Section
Avionics Bay
Bottom Section
Lower Payload Bay + Fin Can

## Slide 29: Launch Vehicle Sections
Top Section
Nose cone + Upper Payload Bay
Bottom Section
Lower Payload Bay + Fin Can
12.75 in.
Avionics Bay
Stores:
  Flight computers + batteries
  GPS transmitters
  CO2 ejection cartridges
2.75 in.
Altimeters: Entacore AIM 4

## Slide 30: Launch Vehicle Sections
Top Section
Nose cone + Upper Payload Bay
Middle Section
Avionics Bay
Bottom Section
Lower Payload Bay + Fin Can

## Slide 31: Launch Vehicle Sections
Top Section
Nose cone + Upper Payload Bay
Middle Section
Avionics Bay
43.5 in.
Lower Payload Bay
Stores:
  Drogue parachute (Fruity Chutes 24” Classic Elliptical)
  16 ft of recovery harness
Fin Can
1.5° canted fins for spin stabilization
Fins mounted into centering rings
3D printed tail cone to minimize drag

## Slide 32
Payload Design

## Slide 33: Payload Concepts
Payload Concept 1
Payload Concept 2
Payload Concept 3

## Slide 34: Payload Concepts
Payload Concept 1
Payload Concept 2
Payload Concept 3
Movement- Stationary
Camera Actuation- Servo Motor
Inner Airframe Housing- Free inside payload bay

## Slide 35: Payload Concepts
Payload Concept 1
Payload Concept 2
Payload Concept 3

## Slide 36: Payload Concepts
Payload Concept 1
Payload Concept 3
Payload Concept 2
Movement- 2-wheel DC motor drive
Camera Actuation- Turns camera by moving wheels independently
Inner Airframe Housing- No housing

## Slide 37: Payload Concepts
Payload Concept 1
Payload Concept 2
Payload Concept 3

## Slide 38: Payload Concepts
Payload Concept 3
Payload Concept 2
Payload Concept 1
Movement- Stationary
Camera Actuation- Stepper motor
Inner Airframe Housing- Free inside payload bay

## Slide 39: Payload Final Design
144-148 MHz Receiver
3D printed base
Lexan camera shroud
4 Eye Bolts
4.2 in
5.5 in
4.5 in

## Slide 40: Payload Design
ArduCam Mini
Stepper Motor
Arduino Mega Controller
3D-Printed Camera Mount
Electronics House

## Slide 41
Subscale Vehicle

## Slide 42: 3D Printing

## Slide 43: Subscale Launch!

## Slide 44: Flight Result: Partial Success
Vehicle recovered with no damage
Recovery ~1 mile from launch site
Two good chutes, two good charge firings. Improperly timed main parachute

## Slide 45: Post-Flight Data Analysis
Predicted Altitude: 3,182 ft
Achieved Altitude: 3,279 ft
Deviation = 3.05%

## Slide 46
STEM Engagement Plans

## Slide 47: STEM Engagement
Types
Education-Direct Engagement: Hands-on activities where participants engage in learning a STEM related concept
Education-Indirect Engagement: Participants are engaged in learning a STEM concept through instructor-led presentations
Outreach-Direct Engagement: Participants don’t learn STEM concepts but get hands-on exposure to STEM related topics or hardware
Outreach-Indirect Engagement: Participants will interact with team members in an informal setting
Goals
STEM Engagement Activity reports completed before Flight Readiness Review (03/06/2023)
Engage a total of 250 participants
Properly convey STEM concepts to the participating parties
Stimulate interest for future NASA Student Launch divisions

## Slide 49
STEM Engagement Dates

## Slide 50
STEM Engagement Dates
Challenger Learning Center
02/23/2023
Engagement Type: Outreach-direct
Engagement Description: Set up booth to showcase project and opportunities with NASA student launch.

## Slide 51
Mag-Lab Open House
02/25/2023

## Slide 52
Sail High School
02/28/2023

## Slide 53
School of Arts and Sciences
Date TBA

## Slide 54
Project Timeline, Future Work, & Budget

## Slide 55: Budget
Projected Cost:
$7,891.14
Project Budget:
$8,000.00

## Slide 56
Projected Cost:
$7,891.14
Project Budget:
$8,000.00
- $3036.95 (sub-scale development)
- $2858.69 (full-scale + payload development)
Remaining Expenditure:
- $1911.55 (competition transportation/lodging)
- $7807.19
$192.82

## Slide 57: Expense Distribution

## Slide 58: Expense Distribution

## Slide 59: Timeline / Future work
Flight Readiness Review
Operation
Manual
Web Page
Completion
Engineering Design Day

## Slide 60: Timeline / Future work
Flight Readiness
Review
Report final design modifications since CDR
Includes final assembly and launch operations checklists
Report results of full-scale demonstration flight

## Slide 61: Timeline / Future work
Operation
Manual
Web Page
Completion
Engineering Design Day
Launch Competition

## Slide 62: Timeline / Future work
Operation
Manual
List manufacturing and assembly instructions
Detail pre- and post-flight procedures
Includes all operations checklists developed

## Slide 63: Timeline / Future work
Web Page
Completion
Engineering Design Day
Launch Competition
Final Presentation

## Slide 64: Timeline / Future work
Web Page
Completion
Update with latest NASA and SD deliverables
Correct minor formatting errors and typos
Verify hyperlink functionality for deliverable downloads and team member LinkedIns

## Slide 65: Timeline / Future work
Engineering Design Day
Launch Competition
Final Presentation
Post-Launch Assessment Review

## Slide 66: Timeline / Future work
Engineering Design Day
Design project showcase at COE
Oral presentations (VDR6)
Poster presentations

## Slide 67: Timeline / Future work
Launch Competition
Final Presentation
Post-Launch Assessment Review
SL Award Ceremony

## Slide 68: Timeline / Future work

## Slide 69
THANK YOU

## Slide 70: COPY THIS SLIDE
Point
Point

## Slide 71
COPY THIS SLIDE!