## Slide 1: Smart Projectile
Jack Corbin | Prosley Dorcely | Emily Groth
Deepkumar Patel | Aaron Weingarten

## Slide 2
Prosley Dorcely
Jack Corbin
Emily Groth
Deepkumar Patel
Aaron Weingarten
Team 509
Deepkumar Patel

## Slide 3
Dr. Rajan Kumar
Sponsor
Dr. Jonas Gustavsson
Advisor
Robert Smith
Advisor
Sponsor and Advisor
Deepkumar Patel

## Slide 4: Objective
The objective of the project is to create a scale model of a projectile with an articulating nose cone and deflectable fins for subsonic wind tunnel testing.
Deepkumar Patel

## Slide 5: FCAAP Existing Model
Previous project just dealt with nose deflection.
Emily Groth
Excess weight caused sagging
Fins are not deflectable​
​
Excess current lead to overheating and reduced test time​
Vibration from articulation mechanism​

## Slide 6
Critical Targets and Metrics
θ
Nose deflection between 0 to 5 degrees with resolution ±0.1
Dynamic deflectable fins between 0 to 30 degrees
Time constant optimized to less than 0.5 seconds
Emily Groth

## Slide 7: Assumptions
Assumption 1
Assumption 2
Gravitational force will be far greater than the aerodynamic forces.
Assumption 3
No shockwaves will be produced (subsonic and incompressible)
Model has access to an outside power supply and controls.
Emily Groth

## Slide 8: Nose Cone Light Weighting
Original Model:
Weight: 270g
Simple light weighting can be machined in house
Sintering Light Weight Model:
Weight: 148g
Complex geometries require a method of additive manufacturing
Emily Groth

## Slide 9: Nose Cone Light Weighting
Emily Groth
Lessons Learned:
Companies treat projects differently based on the customer
More material needs to be added for future parts
Material is acceptable for wind tunnel use

## Slide 10: Back Body Constraints
Requirements:
5 grams or less
Under 0.65 in Diameter
Diameter of support shaft is 0.5 inches
Inner diameter of outer body is 1.8 inches
Jack Corbin

## Slide 11: Motor Selection
FEETECH Sub-Micro Servo FS0403-FB
Plastic Miter Gears
Steel Shaft
Specially modified to provide access to the feedback potentiometer to directly measure output position
Specs:
1.5 grams
0.79 x 0.76 x 0.33 in
Jack Corbin

## Slide 12: Gear Selection
Specs:
18 teeth
Nylon plastic
Gear pitch: 48
FEETECH Sub-Micro Servo FS0403-FB
Plastic Miter Gears
Steel Shaft
Jack Corbin

## Slide 13
Shaft Selection
Specs:
Multipurpose 304 Stainless Steel Rod
0.125" Diameter
FEETECH Sub-Micro Servo FS0403-FB
Plastic Miter Gears
Steel Shaft
Jack Corbin

## Slide 14: Fin Attachment
Jack Corbin
Fins
Attachment
Back Body
Hole is drilled
center of gravity

## Slide 15: Gear Connections
Jack Corbin
Fins
Attachment
Back Body
Shaft connects gears to Servo motors

## Slide 16: Fin Assembly
Jack Corbin
Fins
Attachment
Back Body
Cross section of top and bottom fin connection between the gears, shafts, and motors

## Slide 17
Prosley Dorcely
Housing Insert and Gear Support

## Slide 18: Back Body Design
Issues with the model:
1.Securing housing within body
2. Bearings
Prosley Dorcely

## Slide 19: Final Design
Prosley Dorcely

## Slide 20: Future Testing
Aaron Weingarten
Time Testing
0.5 second
Deflection
Nose Testing
between 0 to 5 degrees with resolution ± 0.1
Fin Testing
between 0 to 30
degrees with
resolution ± 0.1
θ

## Slide 21: Budget
Item​ | Price​
6 FEETECH sub-micro servo FS0307​ | $39.00​
15 FEETECH sub-micro servo fs0403-fb with position feedback​ | $153.75
10 plastic miter gears​ | $79.90​
1 1/8-inch stainless steel rod (1 ft) | $1.92
Xometry​ for the Nose Cone | $1000.00​
8 Light Duty Dry-Running Flanged Sleeve Bearing | $38.24
Budget | $5000.00
Spent | $1312.81
Left | $3687.19
Aaron Weingarten

## Slide 22: Incomplete Work
Machining of the fins
Machining of the back body
Assembly of the machined projectile parts
Back body wind tunnel test
Aaron Weingarten

## Slide 23: Lessons Learned
  Ask more questions up front concerning the constraints of the project
  Identify the exact goal of the project from an earlier stage
  Avoid constraining the project too early
  Begin communication with the machinist at an earlier stage in the project to identify design flaws
  Prototype early to root out key design problems
Aaron Weingarten

## Slide 24: Next Steps
Aaron Weingarten
April
Assembly
Final Testing
Senior Design Day
Celebration

## Slide 25: Summary
  To create a scale model of a projectile with an articulating nose cone and deflectable fins for subsonic wind tunnel testing
Objective
  Nose Cone Deflection of up to 5 degrees
  Fin Deflection of up to 30 degrees
  Time Constant of 0.5 seconds
Targets
  For the nose cone a stepper motor was implemented to control the deflection and for the fin deflection servo motors were used along with a gear train
Design
  The nose cone was modified from last year's project to achieve a deflection of 5 degrees
  The fins haven't achieved deflectability yet
Outcomes
  We haven't been able to machine some necessary parts for the back body which hasn't allowed us to perform testing currently
Incomplete Work
Deepkumar Patel

## Slide 26: Summary
  To create a scale model of a projectile with an articulating nose cone and deflectable fins for subsonic wind tunnel testing
Objective
  Nose Cone Deflection of up to 5 degrees
  Fin Deflection of up to 30 degrees
  Time Constant of 0.5 seconds
Targets
  For the nose cone a stepper motor was implemented to control the deflection and for the fin deflection servo motors were used along with a gear train
Design
  The nose cone was modified from last year's project to achieve a deflection of 5 degrees
  The fins haven't achieved deflectability yet
Outcomes
  We haven't been able to machine some necessary parts for the back body which hasn't allowed us to perform testing currently
Incomplete Work
Deepkumar Patel

## Slide 27: Summary
  To create a scale model of a projectile with an articulating nose cone and deflectable fins for subsonic wind tunnel testing
Objective
  Nose Cone Deflection of up to 5 degrees
  Fin Deflection of up to 30 degrees
  Time Constant of 0.5 seconds
Targets
  For the nose cone a stepper motor was implemented to control the deflection and for the fin deflection servo motors were used along with a gear train
Design
  The nose cone was modified from last year's project to achieve a deflection of 5 degrees
  The fins haven't achieved deflectability yet
Outcomes
  We haven't been able to machine some necessary parts for the back body which hasn't allowed us to perform testing currently
Incomplete Work
Deepkumar Patel

## Slide 28: Summary
  To create a scale model of a projectile with an articulating nose cone and deflectable fins for subsonic wind tunnel testing
Objective
  Nose Cone Deflection of up to 5 degrees
  Fin Deflection of up to 30 degrees
  Time Constant of 0.5 seconds
Targets
  For the nose cone a stepper motor was implemented to control the deflection and for the fin deflection servo motors were used along with a gear train
Design
  The nose cone was modified from last year's project to achieve a deflection of 5 degrees
  The fins haven't achieved deflectability yet
Outcomes
  We haven't been able to machine some necessary parts for the back body which hasn't allowed us to perform testing currently
Incomplete Work
Deepkumar Patel

## Slide 29: Summary
  To create a scale model of a projectile with an articulating nose cone and deflectable fins for subsonic wind tunnel testing
Objective
  Nose Cone Deflection of up to 5 degrees
  Fin Deflection of up to 30 degrees
  Time Constant of 0.5 seconds
Targets
  For the nose cone a stepper motor was implemented to control the deflection and for the fin deflection servo motors were used along with a gear train
Design
  The nose cone was modified from last year's project to achieve a deflection of 5 degrees
  The fins haven't achieved deflectability yet
Outcomes
  We haven't been able to machine some necessary parts for the back body which hasn't allowed us to perform testing currently
Incomplete Work
Deepkumar Patel

## Slide 30
Thanks for listening
Jack
Corbin
Prosley Dorcely
Deepkumar Patel
Aaron
Weingarten
Emily
Groth
Deepkumar Patel

## Slide 31: Concept Selection
Concept | Alternative Value
Smart projectile has an interior pulley system that deflects the nose cone to alter flight path | 0.258482
Smart projectile uses articulating nose cone and dynamically deflectable fins for flight control | 0.47494
Smart projectile uses thrust vectoring nozzles to articulate the nose cone to a desired deflection | 0.266536
Emily Groth

## Slide 32: Markets and Stakeholders
Air Force
Boeing
Raytheon
Lockheed Martin
General Dynamics
College of Engineering
Dr. Jonas Gustavsson
Dr. Rajan Kumar
Dr. Shayne McConomy
Dr. Suvranu De
FCAAP
Emily Groth

## Slide 33: Motor Configuration
CAD model for the motors and gears configuration
Angled View
Back View
Prosley Dorcely

## Slide 34: Gear Selection (Clean up make more presentable)
Plastic Miter Gears
18 teeth
Nylon plastic
Gear pitch: 48
Jack Corbin

## Slide 35: Fin Attachment
Method 1
Weld a large short shaft to end of fin
Brittle connection
Possible manufacturing problem when cleaning up connection surface
Method 2
Drill hole in each fin and insert a smaller shaft inside
Might be weaker and compromise the fin
Shaft would fail from bending
Jack Corbin

## Slide 36
Right Side View
Back View
Prosley Dorcely
Back Body Configuration
Prosley Dorcely

## Slide 37: Motor Selection
Specially modified to provide access to the feedback potentiometer through a fourth (green) wire, allowing you to directly measure the position of the output.
FEETECH Sub-Micro Servo FS0403-FB
Specs:
5 Grams
0.79 x 0.76 x 0.33 in
Positional Feed back
Jack Corbin

## Slide 38: Medium Fidelity Concepts
Concept # | Concept Description
3 | An interior pulley system that deflects the nose cone to alter flight path
23 | Multi-shape fin which can be altered to allow it to find the target and change flight path
59 | Uses an internal mass for mechanical control to alter flight path
69 | Morphing fins that can widen and thin out depending on the forces they are trying to exert
83 | Thrust vectoring nozzles to articulate the nose cone to a desired deflection
Deepkumar Patel

## Slide 39: High Fidelity Concepts
Concept # | Concept Description
27 | Smart projectile uses deflectable thrusters to change flight path
34 | Smart projectile uses articulating nose cone and dynamically deflectable fins for flight control
53 | Smart projectile rapidly ejects and retracts internal mass to change flight path
Deepkumar Patel

## Slide 40: Parts that are re-machined
Back fin body
Prosley Dorcely
Fins

## Slide 41: Fin Deflection
Implement four small motors to control each individual fin
Lack of space in the rear portion of the model
Need to find motors that are small enough to fit in body and have high precision
Aaron Weingarten

## Slide 42: Fin Motor Configuration 1 (Update with new CAD)
Right Side View
Back View
Prosley Dorcely

## Slide 43: Nose Cone Light Weighting (Update on Sintering?)
Original Model:
Weight: 270g
Simple light weighting can be machined in house
Alternative Drilling Model:
Weight: 260g
Small weight reduction not worth extra complexity
Emily Groth

## Slide 44: Future Work
Prosley Dorcely

## Slide 45: Customer Needs Backup

## Slide 46: Markets Backup
Primary Market
  FCAAP (Florida Center for Advanced Aero Propulsion)
Secondary Markets
  Air Force Office of Scientific Research (AFOSR)
  Air Force Research Laboratory (AFRL)
  Lockheed Martin
  General Dynamics
  Raytheon Technologies
  Boeing
  Northrop Grumman

## Slide 47: Stakeholders Backup
Florida Center for Advanced Aero Propulsion
FAMU-FSU College of Engineering
Dr. Rajan Kumar
Dr. Jonas Gustavsson
Dr. Shayne McConomy
Dr. Suvranu De

## Slide 48: Standard Shapes
Summary Box
Text box 1
Outlined Text Box

## Slide 49: Approved Logos

## Slide 50: Color Palette

## Slide 51: APA Tables
Category 1 | Category 2 | Category 3 | Category 4 | Category 5
Item 1 |  |  |  | 
Item 2 |  |  |  | 
Item 3 |  |  |  | 
Item 4 |  |  |  | 
 | Category 2 |  |  | Category 3 | 
Category 1 | subcategory 1 | subcategory 2 |  | subcategory 1 | subcategory 2
Item 1 |  |  |  |  | 
Item 2 |  |  |  |  | 
Item 3 |  |  |  |  | 
Item 4 |  |  |  |  |