## Slide 1: Design Review 5
Team 510

## Slide 2: Team Introduction
Ebony Bland
Austin Bruen
Garfield Murphy
Davis Goolsby
Emilio Manzo

## Slide 3: Sponsors and Advisors
Project Liaison from Florida Power and Light
Project Advisor from FAMU FSU College of Engineering
Austin Bruen
Scarlet Luis
Dr. Simone Hruda

## Slide 4: Project Objective
Develop a fuse-switching device that switches out broken or damaged fuses on utility poles
Austin Bruen

## Slide 5
Fuse Switching
Fuse Cutout
Blown Fuse
Fuse Switching
Austin Bruen

## Slide 6: Key Goals
Easy operation &
User friendly
Fuse Switching and
Restoration
Easily Transportable
Austin Bruen

## Slide 7: Assumptions
Pole Size of 35- 40ft
Safe Weather Conditions
Work with one fuse type
Assumptions
Austin Bruen

## Slide 8: Targets and Metrics
3 Degrees of Freedom
Support a max load of 5 pounds
Extends of 10 ft
Components weigh less than 50lbs
Soft Tissue Damage Under Grade 1
Austin Bruen

## Slide 9: Final Design
Automated Telescoping Pole with a Detachable Foldable Robotic Arm
Telescoping Base
Robotic Arm
Garfield Murphy

## Slide 10: Material Selection
PLA used for all the 3D printed parts
PVC pipes used for telescoping pole and final arm links
Garfield Murphy

## Slide 11: Base Progress – Current Prototype
Arbitrary dimensions with vague idea of mechanism.
Goal was to investigate feasibility.
Garfield Murphy

## Slide 12: Base Progress – Current Prototype
Dimensions needed to reach desired height and accommodate for robotic arm.
Goal was to begin 3D printing prototypes before custom fabricating.
Garfield Murphy

## Slide 13: Base Progress – Current Prototype
PVC prototype to reach revised goal of 10ft.
Goal is to validate feasibility of the pulley mechanism and PVC as the working material.
Garfield Murphy

## Slide 14: Base Progress – Current Prototype
Provides flat surface to mount pulleys.
Press fits to PVC and provides ground for steel wire.
Offsets ground to match pulley height.
Garfield Murphy

## Slide 15: Base Progress – Current Prototype
Wire and pulleys will be steel for the prototype. Insulated options are available on the market.
PVC attachment will be 3D printed.
Garfield Murphy

## Slide 16: Robotic Arm - Initial Concept
Ebony Bland
Create a robotic arm with 3 degrees a freedom that would allow user to replace the fuse as if they were using their own arm.
Z
X
Y
Z
X
Y

## Slide 17: Robotic Arm – Initial Concept
Stepper motors connected to timing belts and pulleys will be used to actuate the rotation of the shoulder and elbow.
A gripper actuated by a servo motor will open and close along the x axis.
Ebony Bland

## Slide 18: Robotic Arm – Conceptual Prototypes
Three models were made to demonstrate the concept of the robotic arm. The two latter models were working prototypes that used stepper motors with Lego gears and chains. Several issues arose in these models.
Ebony Bland

## Slide 19: Robotic Arm – Final Design
We currently have a CAD model for a final design that will address the issues experienced with previous prototypes.
40-inch reach
18 -inch
Ebony Bland

## Slide 20: Robotic Arm – Final Design
Ebony Bland

## Slide 21: Robotic Arm – Final Design
Shoulder Linkage for rotation about z and x rotation
Ebony Bland
Elbow Linkage for rotation about x axis
End effector mount for gripper and camera installation

## Slide 22: Robotic Arm Design – Controller
Smartphone App
Base
Gripper
Joint 3: Elbow Rotation
Joint 2: Shoulder X Rotation
Joint 1: Shoulder Z Rotation
Smartphone
ON
Gripper
OFF
Ebony Bland

## Slide 23: Budget
Austin Bruen
Chart: Breakdown of Money Spent
| Base | Arm | Misc
 | 109.05 | 678.07 | 157.12
Chart: Updated Budget
| Total Spent | Total Left
 | 1001.329 | 998.671

## Slide 24: Arm Budget
Austin Bruen
Chart: 
| Stepper Motors/Motor Drivers | Timing Belt | Gearbox | Gripper | PVC | Batteries and Power Adapters
 | 172.98 | 79.28 | 194.27 | 19.99 | 42.63 | 168.92
PVC
Gripper
Battery and Power Adapters
Stepper Motor and Motor Drivers
Gearbox
Timing Belt

## Slide 25: Base Budget
Austin Bruen
Chart: 
| PVC Pipe | Pulley and Cable | Hand Winch | Base
Price | 34.98 | 28.98 | 29.99 | 15.51
PVC
Base
Hand Winch
Cable and Pulley

## Slide 26: Future Work
Austin Bruen
Testing
Final Designs
Troubleshooting
Validate Metrics
Presentation

## Slide 27: Questions
Austin Bruen

## Slide 28: References
Brain, M. (n.d.). How Power Grids Work. Retrieved from Clark Science Center at Smith College: https://www.science.smith.edu/~jcardell/Courses/EGR220/ElecPwr_HSW.html#:~:text=Fuses%20must%20be%20replaced%20each,panel%20like%20the%20one%20above
Csanyi, E. (2013, January 28). How to manipulate energized conductors with hot stick. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/manipulating-energized-conductors-with-hot-stick
Csanyi, E. (2020, October 12). How primary feeder, distribution transformer, fuses and service operate in radial networks. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/primary-feeder-distribution-transformer-fuses-service
Eaton Corporation. (n.d.). Eaton Website. Retrieved from Fuses: fundamentals of fuses: https://www.eaton.com/us/en-us/products/medium-voltage-power-distribution-control-systems/utility-fuses/fuses--fundamentals-of-fuses.html
Hastings Hot Line Tools & Equipment. (2021, March). Hastings Catalog. Retrieved from Hastings Website: https://www.hfgp.com/fb-catalog/
King-Homan, L. (2020, August 3). How Does That Work? Hot Stick. Retrieved from The Wire: Energy news from Omaha Public Power District: https://oppdthewire.com/hot-stick-how-works-2020-oppd/
N

## Slide 29: Backup Slides

## Slide 30: Targets and Metrics
Soft Tissue Damage Under Grade 1
Remove and Replace Fuse Tube
Transportable
Communication with the User
Under 50 Pounds Per Component
Emilio Manzo
Soft Tissue Damage Under Grade 1
Communicates with user
Components weigh less than 50lbs
Remove and Replace Fuse Link

## Slide 31: Robotic Arm - Controller
Soft Tissue Damage Under Grade 1
Remove and Replace Fuse Tube
Transportable
Communication with the User
Under 50 Pounds Per Component
Emilio Manzo

## Slide 32: Robotic Arm Design – Controller
The goal:
Base
Gripper
Joint 3
Joint 2
Joint 1
Video Feed
ON
Gripper
Smartphone

## Slide 33: Targets and Metrics – Critical targets
Support a max load of 5 pounds
3 Degrees of Freedom
Extends of 10 ft
Emilio Manzo

## Slide 34: Assumptions
Work with one fuse type
Pole Size of 35- 40ft
Transportation
Safe Weather Conditions
Training
Emilio Manzo
Assumptions

## Slide 35: Concept Generation and Selection
Austin Bruen

## Slide 36: Project Scope
Background
Key Goals
Markets
Assumptions
Stakeholders
Garfield Murphy

## Slide 37
CUSTOMER NEEDS
- INTERPRETED NEEDS
Garfield Murphy

## Slide 38: Sponsors and Advisors
Scarlet Luis
Project Liaison from Florida Power and Light
Dr. Simone Hruda
Project Advisor from FAMU FSU College of Engineering
Davis Goolsby

## Slide 39: Brief Project Summary
Develop a device that is remotely controlled and can be operated to perform fuse switching operations for restoration purposes
Garfield Murphy

## Slide 40: Robotic Arm – Final Design
We currently have a CAD model for a final design that will address the issues experienced with previous prototypes.
Ebony Bland

## Slide 41: Key Goals
Easy Operation &
User Friendly
Fuse Switching and
Restoration
Easily Transportable
1
2
3
Garfield Murphy

## Slide 42: Key Goals
Easy Operation &
User Friendly
Fuse Switching and
Restoration
Easily Transportable
1
2
3
Emilio Manzo

## Slide 43
Ebony – Ill do this slide
Davis Goolsby

## Slide 44: Functional Decomposition: Smart Integration
Performs Fuse Switching Operation
Has an Ergonomic Design
Considers Transportation/Storage
Mitigates Soft Tissue Damage
Compact Design
Ability to Extend, Retract, & Pivot
Automate Some or All of Process
Transportable by Bucket Truck & Personal Vehicle
Reach Inaccessible Area
Fuse Switching Operation
Ergonomic
Transportation
& Storage
Compact Design
Reach inaccessible
areas
Automatic Operation
Extends/Descends
Emilio Manzo

## Slide 45: Methods of Validation for Targets
Emilio Manzo
Stopwatch test
Tape measure
CAD Stress Analysis

## Slide 46: Concept Generation Tools
Brain Storming
Biomimicry
Crapshoot
Austin Bruen

## Slide 47: Concept Selection – House of Quality
Binary Comparison
House of Quality
Austin Bruen
Binary Piecewise Comparison |  |  |  |  |  |  |  |  |  |  |  | 
Customer Needs | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | Total
1) Automates Fuse Switching | - | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 6
2) Reach Areas Inaccessible by Bucket Truck | 1 | - | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 7
3) Operate in Multiple Operating Environments | 0 | 0 | - | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 2
4) Transportable via Bucket Truck | 0 | 0 | 1 | - | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 5
5) Transportable via Passenger Vehicle | 0 | 0 | 0 | 0 | - | 0 | 0 | 0 | 0 | 0 | 0 | 0
6) Mitigate Soft Tissue Damage | 1 | 1 | 1 | 1 | 1 | - | 1 | 1 | 0 | 0 | 1 | 8
7) Maintain a Device Weight < 50 lbs. | 0 | 0 | 1 | 0 | 1 | 0 | - | 1 | 0 | 0 | 1 | 4
8) Ergonomic Carrying Design | 0 | 0 | 0 | 0 | 1 | 0 | 0 | - | 0 | 0 | 0 | 1
9) Minimum Length of 40 ft. | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | - | 1 | 1 | 10
10) Support a Weight of 14 lbs. | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | - | 1 | 9
11) Operable from 10 ft. Away | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | - | 3
Total | 4 | 3 | 8 | 5 | 10 | 2 | 6 | 9 | 0 | 1 | 7 | n-1=10
Engineering Characteristics |  |  |  |  |  |  |  |  |  |  |  | 
Improvement Direction |  | ↑ | ↑ | ↑ | ↓ | ↑ | ↓ | ↓ | ↓ | ↓ | ↑ | ↑
Units |  | ft | lbf | DOF | ft | ft | s | s | s | n/a | min. | W
Customer Requirements | Importance Weight Factor | Reach Fuse Tube Location | Maximum Installation Time of 15 Minutes | Have 3 Degrees of Freedom | Max Storage length of 4 feet | Min. Communication Length of 50 ft. | Measures Power Consumption Every 20 Seconds | Device Implements User Commands Within 1 Second | Device Stops Operation Within 2 Seconds of Stop Command | Contains 7 User-Interaction Elements | Operable for 30 Min. at a Time | Motor has sufficient Power to Perform Device Operation
1) Automates Fuse Switching | 6 |  | 5 | 5 |  | 3 |  | 3 |  |  | 5 | 9
2) Reach Areas Inaccessible by Bucket Truck | 7 |  |  |  |  |  |  |  |  |  | 3 | 
3) Operate in Multiple Operating Environments | 2 |  |  | 3 |  | 5 |  | 1 |  |  |  | 
4) Transportable via Bucket Truck | 5 | 3 |  |  | 9 |  |  |  |  |  |  | 
5) Transportable via Passenger Vehicle | 0 | 1 |  |  | 9 |  |  |  |  |  |  | 
6) Mitigate Soft Tissue Damage | 8 |  | 1 |  |  |  |  | 1 | 3 |  | 1 | 
7) Maintain a Device Weight < 50 lbs. | 4 |  |  |  |  |  |  |  |  |  |  | 
8) Ergonomic Design | 1 |  |  |  | 3 |  |  |  |  | 9 |  | 
9) Minimum Length of 40 ft. | 10 | 9 |  |  |  |  |  |  |  |  |  | 
10) Support a Weight of 14 lbs. | 9 | 3 |  | 1 |  |  |  |  |  |  |  | 
11) Operable from 10 ft. Away | 3 | 3 |  |  |  | 9 |  | 5 | 5 |  |  | 
Raw Score | 531 | 141 | 38 | 45 | 48 | 55 | 0 | 43 | 39 | 9 | 59 | 54
Relative Weight % |  | 26.554 | 7.156 | 8.475 | 9.040 | 10.358 | 0.000 | 8.098 | 7.345 | 1.695 | 11.111 | 10.169
Rank Order |  | 1 | 9 | 6 | 5 | 3 | 11 | 7 | 8 | 10 | 2 | 4
Minimum Length of 40ft
Support a Weight of 14 pounds
Mitigates soft tissue damage
Important Customer Requirements

## Slide 48: Concept Selection – House of Quality
House of Quality
Austin Bruen
Engineering Characteristics |  |  |  |  |  |  |  |  |  |  |  | 
Improvement Direction |  | ↑ | ↑ | ↑ | ↓ | ↑ | ↓ | ↓ | ↓ | ↓ | ↑ | ↑
Units |  | ft | lbf | DOF | ft | ft | s | s | s | n/a | min. | W
Customer Requirements | Importance Weight Factor | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
1 | 6 |  | 5 | 5 |  | 3 |  | 3 |  |  | 5 | 9
2 | 7 |  |  |  |  |  |  |  |  |  | 3 | 
3 | 2 |  |  | 3 |  | 5 |  | 1 |  |  |  | 
4 | 5 | 3 |  |  | 9 |  |  |  |  |  |  | 
5 | 0 | 1 |  |  | 9 |  |  |  |  |  |  | 
6 | 8 |  | 1 |  |  |  |  | 1 | 3 |  | 1 | 
7 | 4 |  |  |  |  |  |  |  |  |  |  | 
8 | 1 |  |  |  | 3 |  |  |  |  | 9 |  | 
9 | 10 | 9 |  |  |  |  |  |  |  |  |  | 
10 | 9 | 3 |  | 1 |  |  |  |  |  |  |  | 
11 | 3 | 3 |  |  |  | 9 |  | 5 | 5 |  |  | 
Raw Score | 531 | 141 | 38 | 45 | 48 | 55 | 0 | 43 | 39 | 9 | 59 | 54
Relative Weight % |  | 26.55 | 7.16 | 8.47 | 9.04 | 10.36 | 0.00 | 8.10 | 7.34 | 1.69 | 11.11 | 10.17
Rank Order |  | 1 | 9 | 6 | 5 | 3 | 11 | 7 | 8 | 10 | 2 | 4
1 | Reach Fuse Tube Location
2 | Maximum Installation Time of 15 Minutes
3 | Have 3 Degrees of Freedom
4 | Max Storage length of 4 feet
5 | Min. Communication Length of 50 ft.
6 | Measures Power Consumption Every 20 Seconds
7 | Device Implements User Commands Within 1 Second
8 | Device Stops Operation Within 2 Seconds of Stop Command
9 | Contains 7 User-Interaction Elements
10 | Operable for 30 Min. at a Time
11 | Motor has sufficient Power to Perform Device Operation
Reach Fuse Location
Operable for at least 30 minutes
Minimum communication length of 50ft
Important Engineering Characteristics

## Slide 49: Concept Selection – Pugh Charts
Emilio Manzo
 |  | Concepts |  |  |  |  |  |  | 
Selection Criteria | BLUE STRIPE Telescopic Hot Stick | 2 | 4 | 5 | 41 | 52 | 57 | 64 | 80
Reach Fuse Tube Location | Datum | - | S | + | S | + | S | + | S
Installation Time |  | - | S | + | + | - | - | + | +
Degrees of Freedom |  | + | S | + | - | - | - | - | +
Storage Length |  | + | S | + | - | S | S | - | -
Communication Distance |  | - | S | + | - | - | + | + | +
Device Responsiveness |  | - | S | - | - | S | - | - | -
Emergency Stop Time |  | + | S | + | - | S | + | - | +
Operation Time On a Single Charge |  | - | - | - | - | - | - | - | -
Motor Power |  | + | + | + | - | - | + | + | +
Support Fuse Weight |  | - | + | - | + | - | + | + | +
 | # of Plus(+) | 4 | 2 | 7 | 2 | 1 | 4 | 5 | 5
 | # of Minus(-) | 6 | 0 | 3 | 7 | 6 | 4 | 5 | 4
 |  | Concepts |  |  |  | 
Selection Criteria | 64 | 2 | 4 | 5 | 57 | 80
Reach Fuse Tube Location | Datum | - | + | + | + | S
Installation Time |  | - | + | + | + | +
Degrees of Freedom |  | + | S | + | - | +
Storage Length |  | + | + | + | - | +
Communication Distance |  | - | - | + | - | -
Device Responsiveness |  | - | S | + | - | +
Emergency Stop Time |  | + | S | + | - | +
Operation Time On a Single Charge |  | - | + | - | + | +
Motor Power |  | - | - | - | - | -
Support Fuse Weight |  | - | + | - | - | -
 | # of Plus(+) | 3 | 5 | 7 | 3 | 6
 | # of Minus(-) | 6 | 2 | 3 | 7 | 3

## Slide 50: Concept Selection – Pugh Charts
Emilio Manzo
 |  | Concepts |  |  |  | 
Selection Criteria | 64 | 2 | 4 | 5 | 57 | 80
Reach Fuse Tube Location | Datum | - | + | + | + | S
Installation Time |  | - | + | + | + | +
Degrees of Freedom |  | + | S | + | - | +
Storage Length |  | + | + | + | - | +
Communication Distance |  | - | - | + | - | -
Device Responsiveness |  | - | S | + | - | +
Emergency Stop Time |  | + | S | + | - | +
Operation Time On a Single Charge |  | - | + | - | + | +
Motor Power |  | - | - | - | - | -
Support Fuse Weight |  | - | + | - | - | -
 | # of Plus(+) | 3 | 5 | 7 | 3 | 6
 | # of Minus(-) | 6 | 2 | 3 | 7 | 3

## Slide 51: Concept Selection – Analytical Hierarchy Process
AHP – Criteria Weights
AHP – Pairwise comparison
Consistency Check |  |  | Consistency Comparison |  | 
Ws | Cons V |  | Avg Consist | Con Index | Con Ratio
1.43 | 3.21 |  | 3.208 | 0.104 | 0.200
0.35 | 3.20 |  |  |  | 
1.43 | 3.21 |  |  |  | 
Garfield Murphy

## Slide 52: Concept Selection – Analytical Hierarchy Process
Garfield Murphy
Final Rating Matrix |  |  |  |  |  |  |  |  | 
Concept | Reach Fuse Tube | Installation Time | DoF | Storage Length | Communication Distance | Responsiveness | Emergency Stop time | Support fuse weight | Operation on Charge
# 4 | 0.45 | 0.27 | 1.06 | 0.39 | 0.21 | 0.70 | 0.19 | 0.19 | 0.18
# 5 | 0.09 | 0.11 | 0.52 | 0.54 | 0.94 | 0.13 | 1.85 | 0.84 | 2.15
# 80 | 0.45 | 1.06 | 0.19 | 0.31 | 0.62 | 0.29 | 0.92 | 0.91 | 1.22
Concept | Alternate Value
# 4 | 1.97
# 5 | 6.12
# 80 | 4.31
Chart: Alternative Values
| # 4 | # 5 | # 80
Alternative Values | 1.9698 | 6.1156 | 4.3095

## Slide 53: Concept Selection – Final Choices
Concept 4:
External Support
Concept 4:
Robotic Arm Attachment
Concept 5:
Drone
Emilio Manzo

## Slide 54: Questions
Garfield Murphy

## Slide 55: Concept Selection – Pugh Charts
Austin Bruen
 |  | Concepts |  |  |  |  |  |  | 
Selection Criteria | BLUE STRIPE Telescopic Hot Stick | 2 | 4 | 5 | 41 | 52 | 57 | 64 | 80
Reach Fuse Tube Location | Datum | - | S | + | S | + | S | + | S
Installation Time |  | - | S | + | + | - | - | + | +
Degrees of Freedom |  | + | S | + | - | - | - | - | +
Storage Length |  | + | S | + | - | S | S | - | -
Communication Distance |  | - | S | + | - | - | + | + | +
Device Responsiveness |  | - | S | - | - | S | - | - | -
Emergency Stop Time |  | + | S | + | - | S | + | - | +
Operation Time On a Single Charge |  | - | - | - | - | - | - | - | -
Motor Power |  | + | + | + | - | - | + | + | +
Support Fuse Weight |  | - | + | - | + | - | + | + | +
 | # of Plus(+) | 4 | 2 | 7 | 2 | 1 | 4 | 5 | 5
 | # of Minus(-) | 6 | 0 | 3 | 7 | 6 | 4 | 5 | 4
 |  | Concepts |  |  |  | 
Selection Criteria | 64 | 2 | 4 | 5 | 57 | 80
Reach Fuse Tube Location | Datum | - | + | + | + | S
Installation Time |  | - | + | + | + | +
Degrees of Freedom |  | + | S | + | - | +
Storage Length |  | + | + | + | - | +
Communication Distance |  | - | - | + | - | -
Device Responsiveness |  | - | S | + | - | +
Emergency Stop Time |  | + | S | + | - | +
Operation Time On a Single Charge |  | - | + | - | + | +
Motor Power |  | - | - | - | - | -
Support Fuse Weight |  | - | + | - | - | -
 | # of Plus(+) | 3 | 5 | 7 | 3 | 6
 | # of Minus(-) | 6 | 2 | 3 | 7 | 3

## Slide 56
Reach Fuse Location
Operable for at least 30 minutes
Minimum communication length of 50ft
Important Engineering Characteristics

## Slide 57: Markets
Municipalities
Electric Companies
Contractors
Public Safety
Construction
Davis Goolsby
Primary Markets:
Secondary Markets:

## Slide 58: Stakeholders
 | Investors | Decision-Makers | Advisers | Receivers
Sponsor | Florida Power and Light, NextEra Energy | Florida Power and Light, NextEra Energy | Scarlett Luis (Engineer at FPL) | Florida Power and Light, NextEra Energy
Manager | Scarlett Luis (Engineer at FPL) | Scarlett Luis (Engineer at FPL) | Dr. McConomy | Florida Power and Light, NextEra Energy
Experts | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Dr. Hruda | Florida Power and Light employed Operators
Operators | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Kyle Bush (FPL Project Manager) | Florida Power and Light employed Operators
Davis Goolsby

## Slide 59
CUSTOMER NEEDS
Questions | Statements | Interpreted Needs
Intended User? | Typical users are linemen and engineers doing field work. | The device needs to be easy operate to in a field environment.
Operating Environment ? | Residential areas. Design device for ideal weather conditions | Used in safe weather conditions
Current Dimensions of the Product? | Approximately 4 feet long when fully collapsed. | Device fits inside Bucket truck for transportation
Ebony Bland

## Slide 60: Future Work
Concept Generation
Concept Selection
Targets
Risk
Assessment
Bill of Materials
Spring
Plans
Davis Goolsby

## Slide 61: References
Brain, M. (n.d.). How Power Grids Work. Retrieved from Clark Science Center at Smith College: https://www.science.smith.edu/~jcardell/Courses/EGR220/ElecPwr_HSW.html#:~:text=Fuses%20must%20be%20replaced%20each,panel%20like%20the%20one%20above
Csanyi, E. (2013, January 28). How to manipulate energized conductors with hot stick. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/manipulating-energized-conductors-with-hot-stick
Csanyi, E. (2020, October 12). How primary feeder, distribution transformer, fuses and service operate in radial networks. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/primary-feeder-distribution-transformer-fuses-service
Eaton Corporation. (n.d.). Eaton Website. Retrieved from Fuses: fundamentals of fuses: https://www.eaton.com/us/en-us/products/medium-voltage-power-distribution-control-systems/utility-fuses/fuses--fundamentals-of-fuses.html
Hastings Hot Line Tools & Equipment. (2021, March). Hastings Catalog. Retrieved from Hastings Website: https://www.hfgp.com/fb-catalog/
King-Homan, L. (2020, August 3). How Does That Work? Hot Stick. Retrieved from The Wire: Energy news from Omaha Public Power District: https://oppdthewire.com/hot-stick-how-works-2020-oppd/
Davis Goolsby

## Slide 62: Project Scope
Background
Key Goals
Markets
Assumptions
Stakeholders
Garfield Murphy

## Slide 63: Markets, Stakeholders, Assumptions
 | Investors | Decision-Makers | Advisers | Receivers
Sponsor | Florida Power and Light, NextEra Energy | Florida Power and Light, NextEra Energy | Scarlett Luis (Engineer at FPL) | Florida Power and Light, NextEra Energy
Manager | Scarlett Luis (Engineer at FPL) | Scarlett Luis (Engineer at FPL) | Dr. McConomy | Florida Power and Light, NextEra Energy
Experts | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Dr. Hruda | Florida Power and Light employed Operators
Operators | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Kyle Bush (FPL Project Manager) | Florida Power and Light employed Operators
Fuse Types
Safe Weather Conditions
Pole Sizes
Transportation
Training
Garfield Murphy

## Slide 64: Base Design
Davis Goolsby

## Slide 65: Material selection
Emilio Manzo

## Slide 66: Material Selection
Emilio Manzo
PLA USED FOR ALL THE 3D PRINTED PARTS
PVC PIPES USED FOR TELESCOPING POLE AND FINAL ARM LINKS

## Slide 67: Future Work
=
Emilio Manzo
3D Print Base
3D Print Arm
Testing
Final Designs
Troubleshooting
Validate Metrics
Presentation

## Slide 68: Final Design
Automated Telescoping Pole with a Detachable Foldable Robotic Arm
Ebony – Ill do this slide
Davis Goolsby