## Slide 1: Design Review 6
Team 510

## Slide 2: Team Introduction
Ebony Bland
Austin Bruen
Garfield Murphy
Davis Goolsby
Emilio Manzo
Emilio Manzo

## Slide 3: Sponsors and Advisors
Project Liaison from Florida Power and Light
Project Advisor from FAMU FSU College of Engineering
Emilio Manzo
Scarlet Luis
Dr. Simone Hruda

## Slide 4: Project Objective
Develop a fuse-switching device that switches out broken or damaged fuses on utility poles
Austin Bruen

## Slide 5
Fuse Switching
Fuse Cutout
Blown Fuse
Fuse Switching
Austin Bruen

## Slide 6: Key Goals
Easy operation &
User friendly
Fuse Switching and
Restoration
Easily Transportable
Austin Bruen

## Slide 7: Assumptions
Pole Size of 35- 40ft
Safe Weather Conditions
Work with one fuse type
Assumptions
Garfield Murphy

## Slide 8: Design Requirements
3 Degrees of Freedom
Support a max load of 5 pounds
Extends of 10 ft
Components weigh less than 50lbs
Soft Tissue Damage Under Grade 1
Garfield Murphy

## Slide 9: Performance Requirements
Device Battery Life
Preform Fuse Switching
Remotely Controlled
Communication with User
Garfield Murphy

## Slide 10: Final Design
Automated Telescoping Pole with a Detachable Foldable Robotic Arm
Telescoping Base
Robotic Arm
Garfield Murphy

## Slide 11: Material Selection
PLA used for all the 3D printed parts
PVC pipes used for telescoping pole and final arm links
Garfield Murphy

## Slide 12: Base Design Progression
Arbitrary dimensions with vague idea of mechanism.
Goal was to investigate feasibility.
Davis Goolsby

## Slide 13: Base Progress – Current Prototype
Dimensions needed to reach desired height and accommodate for robotic arm.
Goal was to begin 3D printing prototypes before custom fabricating.
Davis Goolsby

## Slide 14: Base Progress – Current Prototype
PVC prototype to reach revised goal of 10ft.
Goal is to validate feasibility of the pulley mechanism and PVC as the working material.
Davis Goolsby

## Slide 15: Base Progress – Current Prototype
Provides flat surface to mount pulleys.
Press fits to PVC and provides ground for steel wire.
Offsets connection point to match pulley height.
Davis Goolsby

## Slide 16: Base Progress – Current Prototype
Wire and pulleys will be steel for the prototype. Insulated options are available on the market.
PVC attachment will be 3D printed.
Davis Goolsby

## Slide 17
Base Progress – Current Prototype
Davis Goolsby

## Slide 18
Telescoping Base - Current Issues & Plans:
Davis Goolsby
Connection to robotic arm.
Validation.
Imperfections in vertical slots.

## Slide 19: Robotic Arm – Conceptual Prototypes
Three models were made to demonstrate the concept of the robotic arm. The two latter models were working prototypes that used stepper motors with Lego gears and chains. Several issues arose in these models.
Ebony Bland

## Slide 20: Robotic Arm – Final Design
We currently have a CAD model for a final design that will address the issues experienced with previous prototypes.
Ebony Bland

## Slide 21: Robotic Arm – Final Design
Ebony Bland
Shoulder Z Linkage
Shoulder X Linkage
Elbow Linkage
Forearm Link and Mounting Plate

## Slide 22: Robotic Arm – Final Design
Shoulder Linkage for rotation about z and x rotation
Ebony Bland
Elbow Linkage for rotation about x axis
End effector mount for gripper and camera installation

## Slide 23: Designing 3D printed Parts
Ebony Bland
Had limited printing space so we had to break larger pieces down and redesign certain parts. Also used heat inserts to connect parts.

## Slide 24: Controller – Initial Design
Stepper Motor
Motor Driver
Breadboard with Buttons
Emilio Manzo

## Slide 25: Controller – Initial Design
Emilio Manzo

## Slide 26: Controller – Wireless Implementation
Wi-Fi:
Internet Control
Bluetooth:
Wireless Controller
Bluetooth:
Smartphone App
Emilio Manzo

## Slide 27: Tests for Targets and Metrics – Base
Ebony Bland
How can we determine the base and arm actually work ? How can we prove how well the arm can work ?
Base tests:
How easy is it for a person to crank winch in a manual setting ?
  Survey, force sensor to measure force required,
Reach desired ten feet.
Be within the weight limit.
Test winch safety measure.
Test deflection under load.
Determined force needed to manually winch.

## Slide 28: Tests for targets and metrics
Ebony Bland
Perform Fuse Switching
Repeatability
Time to
switch fuse
Measure
battery life
Device
weight
Easy to use
Remotely Controlled
Lifting
capability
Person’s ability
to learn
how to use
Connection
range
Notes: How can we determine the base and arm actually work ? How can we prove how well the arm can work ?
Base tests:
Arm tests:
Target – work from remote distance – how far can controller interact with arm ?
-possible test is to test connection range, have LEDS to indicate arm is connected to controller at 1-yard distances
Target - Repeatability of task to switch fuse within full battery charge in manual mode
- control arm to remove and replace blown fuse as many times as possible until battery dies
- how many times ? And length of time for battery life
- do all batteries last same time?
Target- length of time to switch fuse
- measure length of time to remove a fuse when in range of fuse
- measure how long it takes to put new fuse it and snap it in
Target – lifting capability to hold fuse
- how long can it hold it ?
Target – replacing fuse
- how much force is needed at end effector to snap fuse back in
Target – idle current draw
- how much current is used to keep arm in a default position (not in motion) (important when being telescoped up and down in-between removing and replacing fuse)
- use multimeter to measure current draw while in default position from each motor, camera, etc for est time it would take to get to desired base height.
- also for while holding fuse for time it would take to descend with telescoping base
- which component battery will die first ?
Target – battery life
-while is use and idle
Target –ease of use
-how long does it take normal person to w/ min training to remove and replace fuse ?
- how easy it for a person with min training to understand controls
- do a test with 2-3 ppl and get survey rating and measure time
-how easy is it to use base prototype?

## Slide 29: Budget
Austin Bruen
Chart: Updated Budget
| Total Spent | Total Left
 | 1001.329 | 998.671
Chart: 
| Total After Tax | Budget Left
 | 1114.75 | 885.25

## Slide 30: Arm Budget
Austin Bruen
Electronics
Timing Belt
Chart: 
| Electronics | Timing Belt | Building Materials | Miscellaneous
Price | 613.14 | 109.01 | 127.11 | 92.93
Building Materials
Miscellaneous

## Slide 31: Base Budget
Austin Bruen
PVC
Hand Winch
Cable and Pulley
Chart: 
| PVC Pipe | Pulley and Cable | Hand Winch | Base
Price: | 34.98 | 28.98 | 29.99 | 15.51
Base

## Slide 32: Lessons Learned – Ebony Bland
Ebony Bland
Tolerances are Important
How to delegate tasks
How to work in a multidisciplinary team

## Slide 33: Lessons Learned – Austin Bruen
Austin Bruen
How to be more efficient with my communication
How to work with epoxy.
How to use excel more efficiently

## Slide 34: Lessons Learned – Davis Goolsby
Davis Goolsby
There’s always a good tool for the job.
Know where you need to be precise and where you don’t.
CAD models are good but not great for communication.

## Slide 35: Lessons Learned – Emilio Manzo
Emilio Manzo
Working in an interdisciplinary team
Building a Website
Programming Large Stepper Motors
Adapting and revising a design based on sponsor feedback

## Slide 36: Lessons Learned – Garfield Murphy
Garfield Murphy
The balance between thoroughness of design considerations and making progress on design
The dangers of dividing tasks without a plan integration
The importance of thoroughly reviewing and the work of others
The dangers of dividing tasks without a plan integration
The balance between thoroughness of design considerations and making progress on design
The importance of thoroughly reviewing and the work of others

## Slide 37: Future Work
Garfield Murphy
Testing
Final Designs
Troubleshooting
Validate Metrics
Presentation

## Slide 38: Questions
Garfield Murphy

## Slide 39: References
Brain, M. (n.d.). How Power Grids Work. Retrieved from Clark Science Center at Smith College: https://www.science.smith.edu/~jcardell/Courses/EGR220/ElecPwr_HSW.html#:~:text=Fuses%20must%20be%20replaced%20each,panel%20like%20the%20one%20above
Csanyi, E. (2013, January 28). How to manipulate energized conductors with hot stick. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/manipulating-energized-conductors-with-hot-stick
Csanyi, E. (2020, October 12). How primary feeder, distribution transformer, fuses and service operate in radial networks. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/primary-feeder-distribution-transformer-fuses-service
Eaton Corporation. (n.d.). Eaton Website. Retrieved from Fuses: fundamentals of fuses: https://www.eaton.com/us/en-us/products/medium-voltage-power-distribution-control-systems/utility-fuses/fuses--fundamentals-of-fuses.html
Hastings Hot Line Tools & Equipment. (2021, March). Hastings Catalog. Retrieved from Hastings Website: https://www.hfgp.com/fb-catalog/
King-Homan, L. (2020, August 3). How Does That Work? Hot Stick. Retrieved from The Wire: Energy news from Omaha Public Power District: https://oppdthewire.com/hot-stick-how-works-2020-oppd/
N

## Slide 40: Backup Slides

## Slide 41: Lessons Learned – be specific and summarize
Austin Bruen

## Slide 42: Miscellaneous Budget
Austin Bruen
Laser Leveler
Bluetooth RF Transceiver
Cable Ties
Battery Charger
Rotary Tool
Epoxy
Chart: 
| Misc: | Expoxy | Lazar Leveler | Rotary Tool | Zipties | Bluetooth RF transciever | Battery Charger
 | 39.99 | 28.98 | 23.96 | 6.99 | 12.99 | 35

## Slide 43: Robotic Arm - Initial Concept
Ebony Bland
Create a robotic arm with 3 degrees a freedom that would allow user to replace the fuse as if they were using their own arm.
Z
X
Y
Z
X
Y

## Slide 44: Robotic Arm – Initial Concept
Stepper motors connected to timing belts and pulleys will be used to actuate the rotation of the shoulder and elbow.
A gripper actuated by a servo motor will open and close along the x axis.
Ebony Bland

## Slide 45: Targets and Metrics
Soft Tissue Damage Under Grade 1
Remove and Replace Fuse Tube
Transportable
Communication with the User
Under 50 Pounds Per Component
Emilio Manzo
Soft Tissue Damage Under Grade 1
Communicates with user
Components weigh less than 50lbs
Remove and Replace Fuse Link

## Slide 46: Robotic Arm - Controller
Soft Tissue Damage Under Grade 1
Remove and Replace Fuse Tube
Transportable
Communication with the User
Under 50 Pounds Per Component
Emilio Manzo

## Slide 47: Robotic Arm Design – Controller
The goal:
Base
Gripper
Joint 3
Joint 2
Joint 1
Video Feed
ON
Gripper
Smartphone

## Slide 48: Targets and Metrics – Critical targets
Support a max load of 5 pounds
3 Degrees of Freedom
Extends of 10 ft
Emilio Manzo

## Slide 49: Assumptions
Work with one fuse type
Pole Size of 35- 40ft
Transportation
Safe Weather Conditions
Training
Emilio Manzo
Assumptions

## Slide 50: Concept Generation and Selection
Austin Bruen

## Slide 51: Project Scope
Background
Key Goals
Markets
Assumptions
Stakeholders
Garfield Murphy

## Slide 52
CUSTOMER NEEDS
- INTERPRETED NEEDS
Garfield Murphy

## Slide 54: Sponsors and Advisors
Scarlet Luis
Project Liaison from Florida Power and Light
Dr. Simone Hruda
Project Advisor from FAMU FSU College of Engineering
Davis Goolsby

## Slide 55: Brief Project Summary
Develop a device that is remotely controlled and can be operated to perform fuse switching operations for restoration purposes
Garfield Murphy

## Slide 56: Robotic Arm – Final Design
We currently have a CAD model for a final design that will address the issues experienced with previous prototypes.
Ebony Bland

## Slide 57: Key Goals
Easy Operation &
User Friendly
Fuse Switching and
Restoration
Easily Transportable
1
2
3
Garfield Murphy

## Slide 58: Key Goals
Easy Operation &
User Friendly
Fuse Switching and
Restoration
Easily Transportable
1
2
3
Emilio Manzo

## Slide 59
Ebony – Ill do this slide
Davis Goolsby

## Slide 60: Functional Decomposition: Smart Integration
Performs Fuse Switching Operation
Has an Ergonomic Design
Considers Transportation/Storage
Mitigates Soft Tissue Damage
Compact Design
Ability to Extend, Retract, & Pivot
Automate Some or All of Process
Transportable by Bucket Truck & Personal Vehicle
Reach Inaccessible Area
Fuse Switching Operation
Ergonomic
Transportation
& Storage
Compact Design
Reach inaccessible
areas
Automatic Operation
Extends/Descends
Emilio Manzo

## Slide 61: Methods of Validation for Targets
Emilio Manzo
Stopwatch test
Tape measure
CAD Stress Analysis

## Slide 62: Concept Generation Tools
Brain Storming
Biomimicry
Crapshoot
Austin Bruen

## Slide 63: Concept Selection – House of Quality
Binary Comparison
House of Quality
Austin Bruen
Binary Piecewise Comparison |  |  |  |  |  |  |  |  |  |  |  | 
Customer Needs | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | Total
1) Automates Fuse Switching | - | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 6
2) Reach Areas Inaccessible by Bucket Truck | 1 | - | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 7
3) Operate in Multiple Operating Environments | 0 | 0 | - | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 2
4) Transportable via Bucket Truck | 0 | 0 | 1 | - | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 5
5) Transportable via Passenger Vehicle | 0 | 0 | 0 | 0 | - | 0 | 0 | 0 | 0 | 0 | 0 | 0
6) Mitigate Soft Tissue Damage | 1 | 1 | 1 | 1 | 1 | - | 1 | 1 | 0 | 0 | 1 | 8
7) Maintain a Device Weight < 50 lbs. | 0 | 0 | 1 | 0 | 1 | 0 | - | 1 | 0 | 0 | 1 | 4
8) Ergonomic Carrying Design | 0 | 0 | 0 | 0 | 1 | 0 | 0 | - | 0 | 0 | 0 | 1
9) Minimum Length of 40 ft. | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | - | 1 | 1 | 10
10) Support a Weight of 14 lbs. | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | - | 1 | 9
11) Operable from 10 ft. Away | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | - | 3
Total | 4 | 3 | 8 | 5 | 10 | 2 | 6 | 9 | 0 | 1 | 7 | n-1=10
Engineering Characteristics |  |  |  |  |  |  |  |  |  |  |  | 
Improvement Direction |  | ↑ | ↑ | ↑ | ↓ | ↑ | ↓ | ↓ | ↓ | ↓ | ↑ | ↑
Units |  | ft | lbf | DOF | ft | ft | s | s | s | n/a | min. | W
Customer Requirements | Importance Weight Factor | Reach Fuse Tube Location | Maximum Installation Time of 15 Minutes | Have 3 Degrees of Freedom | Max Storage length of 4 feet | Min. Communication Length of 50 ft. | Measures Power Consumption Every 20 Seconds | Device Implements User Commands Within 1 Second | Device Stops Operation Within 2 Seconds of Stop Command | Contains 7 User-Interaction Elements | Operable for 30 Min. at a Time | Motor has sufficient Power to Perform Device Operation
1) Automates Fuse Switching | 6 |  | 5 | 5 |  | 3 |  | 3 |  |  | 5 | 9
2) Reach Areas Inaccessible by Bucket Truck | 7 |  |  |  |  |  |  |  |  |  | 3 | 
3) Operate in Multiple Operating Environments | 2 |  |  | 3 |  | 5 |  | 1 |  |  |  | 
4) Transportable via Bucket Truck | 5 | 3 |  |  | 9 |  |  |  |  |  |  | 
5) Transportable via Passenger Vehicle | 0 | 1 |  |  | 9 |  |  |  |  |  |  | 
6) Mitigate Soft Tissue Damage | 8 |  | 1 |  |  |  |  | 1 | 3 |  | 1 | 
7) Maintain a Device Weight < 50 lbs. | 4 |  |  |  |  |  |  |  |  |  |  | 
8) Ergonomic Design | 1 |  |  |  | 3 |  |  |  |  | 9 |  | 
9) Minimum Length of 40 ft. | 10 | 9 |  |  |  |  |  |  |  |  |  | 
10) Support a Weight of 14 lbs. | 9 | 3 |  | 1 |  |  |  |  |  |  |  | 
11) Operable from 10 ft. Away | 3 | 3 |  |  |  | 9 |  | 5 | 5 |  |  | 
Raw Score | 531 | 141 | 38 | 45 | 48 | 55 | 0 | 43 | 39 | 9 | 59 | 54
Relative Weight % |  | 26.554 | 7.156 | 8.475 | 9.040 | 10.358 | 0.000 | 8.098 | 7.345 | 1.695 | 11.111 | 10.169
Rank Order |  | 1 | 9 | 6 | 5 | 3 | 11 | 7 | 8 | 10 | 2 | 4
Minimum Length of 40ft
Support a Weight of 14 pounds
Mitigates soft tissue damage
Important Customer Requirements

## Slide 64: Concept Selection – House of Quality
House of Quality
Austin Bruen
Engineering Characteristics |  |  |  |  |  |  |  |  |  |  |  | 
Improvement Direction |  | ↑ | ↑ | ↑ | ↓ | ↑ | ↓ | ↓ | ↓ | ↓ | ↑ | ↑
Units |  | ft | lbf | DOF | ft | ft | s | s | s | n/a | min. | W
Customer Requirements | Importance Weight Factor | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
1 | 6 |  | 5 | 5 |  | 3 |  | 3 |  |  | 5 | 9
2 | 7 |  |  |  |  |  |  |  |  |  | 3 | 
3 | 2 |  |  | 3 |  | 5 |  | 1 |  |  |  | 
4 | 5 | 3 |  |  | 9 |  |  |  |  |  |  | 
5 | 0 | 1 |  |  | 9 |  |  |  |  |  |  | 
6 | 8 |  | 1 |  |  |  |  | 1 | 3 |  | 1 | 
7 | 4 |  |  |  |  |  |  |  |  |  |  | 
8 | 1 |  |  |  | 3 |  |  |  |  | 9 |  | 
9 | 10 | 9 |  |  |  |  |  |  |  |  |  | 
10 | 9 | 3 |  | 1 |  |  |  |  |  |  |  | 
11 | 3 | 3 |  |  |  | 9 |  | 5 | 5 |  |  | 
Raw Score | 531 | 141 | 38 | 45 | 48 | 55 | 0 | 43 | 39 | 9 | 59 | 54
Relative Weight % |  | 26.55 | 7.16 | 8.47 | 9.04 | 10.36 | 0.00 | 8.10 | 7.34 | 1.69 | 11.11 | 10.17
Rank Order |  | 1 | 9 | 6 | 5 | 3 | 11 | 7 | 8 | 10 | 2 | 4
1 | Reach Fuse Tube Location
2 | Maximum Installation Time of 15 Minutes
3 | Have 3 Degrees of Freedom
4 | Max Storage length of 4 feet
5 | Min. Communication Length of 50 ft.
6 | Measures Power Consumption Every 20 Seconds
7 | Device Implements User Commands Within 1 Second
8 | Device Stops Operation Within 2 Seconds of Stop Command
9 | Contains 7 User-Interaction Elements
10 | Operable for 30 Min. at a Time
11 | Motor has sufficient Power to Perform Device Operation
Reach Fuse Location
Operable for at least 30 minutes
Minimum communication length of 50ft
Important Engineering Characteristics

## Slide 65: Concept Selection – Pugh Charts
Emilio Manzo
 |  | Concepts |  |  |  |  |  |  | 
Selection Criteria | BLUE STRIPE Telescopic Hot Stick | 2 | 4 | 5 | 41 | 52 | 57 | 64 | 80
Reach Fuse Tube Location | Datum | - | S | + | S | + | S | + | S
Installation Time |  | - | S | + | + | - | - | + | +
Degrees of Freedom |  | + | S | + | - | - | - | - | +
Storage Length |  | + | S | + | - | S | S | - | -
Communication Distance |  | - | S | + | - | - | + | + | +
Device Responsiveness |  | - | S | - | - | S | - | - | -
Emergency Stop Time |  | + | S | + | - | S | + | - | +
Operation Time On a Single Charge |  | - | - | - | - | - | - | - | -
Motor Power |  | + | + | + | - | - | + | + | +
Support Fuse Weight |  | - | + | - | + | - | + | + | +
 | # of Plus(+) | 4 | 2 | 7 | 2 | 1 | 4 | 5 | 5
 | # of Minus(-) | 6 | 0 | 3 | 7 | 6 | 4 | 5 | 4
 |  | Concepts |  |  |  | 
Selection Criteria | 64 | 2 | 4 | 5 | 57 | 80
Reach Fuse Tube Location | Datum | - | + | + | + | S
Installation Time |  | - | + | + | + | +
Degrees of Freedom |  | + | S | + | - | +
Storage Length |  | + | + | + | - | +
Communication Distance |  | - | - | + | - | -
Device Responsiveness |  | - | S | + | - | +
Emergency Stop Time |  | + | S | + | - | +
Operation Time On a Single Charge |  | - | + | - | + | +
Motor Power |  | - | - | - | - | -
Support Fuse Weight |  | - | + | - | - | -
 | # of Plus(+) | 3 | 5 | 7 | 3 | 6
 | # of Minus(-) | 6 | 2 | 3 | 7 | 3

## Slide 66: Concept Selection – Pugh Charts
Emilio Manzo
 |  | Concepts |  |  |  | 
Selection Criteria | 64 | 2 | 4 | 5 | 57 | 80
Reach Fuse Tube Location | Datum | - | + | + | + | S
Installation Time |  | - | + | + | + | +
Degrees of Freedom |  | + | S | + | - | +
Storage Length |  | + | + | + | - | +
Communication Distance |  | - | - | + | - | -
Device Responsiveness |  | - | S | + | - | +
Emergency Stop Time |  | + | S | + | - | +
Operation Time On a Single Charge |  | - | + | - | + | +
Motor Power |  | - | - | - | - | -
Support Fuse Weight |  | - | + | - | - | -
 | # of Plus(+) | 3 | 5 | 7 | 3 | 6
 | # of Minus(-) | 6 | 2 | 3 | 7 | 3

## Slide 67: Concept Selection – Analytical Hierarchy Process
AHP – Criteria Weights
AHP – Pairwise comparison
Consistency Check |  |  | Consistency Comparison |  | 
Ws | Cons V |  | Avg Consist | Con Index | Con Ratio
1.43 | 3.21 |  | 3.208 | 0.104 | 0.200
0.35 | 3.20 |  |  |  | 
1.43 | 3.21 |  |  |  | 
Garfield Murphy

## Slide 68: Concept Selection – Analytical Hierarchy Process
Garfield Murphy
Final Rating Matrix |  |  |  |  |  |  |  |  | 
Concept | Reach Fuse Tube | Installation Time | DoF | Storage Length | Communication Distance | Responsiveness | Emergency Stop time | Support fuse weight | Operation on Charge
# 4 | 0.45 | 0.27 | 1.06 | 0.39 | 0.21 | 0.70 | 0.19 | 0.19 | 0.18
# 5 | 0.09 | 0.11 | 0.52 | 0.54 | 0.94 | 0.13 | 1.85 | 0.84 | 2.15
# 80 | 0.45 | 1.06 | 0.19 | 0.31 | 0.62 | 0.29 | 0.92 | 0.91 | 1.22
Concept | Alternate Value
# 4 | 1.97
# 5 | 6.12
# 80 | 4.31
Chart: Alternative Values
| # 4 | # 5 | # 80
Alternative Values | 1.9698 | 6.1156 | 4.3095

## Slide 69: Concept Selection – Final Choices
Concept 4:
External Support
Concept 4:
Robotic Arm Attachment
Concept 5:
Drone
Emilio Manzo

## Slide 70: Questions
Garfield Murphy

## Slide 71: Concept Selection – Pugh Charts
Austin Bruen
 |  | Concepts |  |  |  |  |  |  | 
Selection Criteria | BLUE STRIPE Telescopic Hot Stick | 2 | 4 | 5 | 41 | 52 | 57 | 64 | 80
Reach Fuse Tube Location | Datum | - | S | + | S | + | S | + | S
Installation Time |  | - | S | + | + | - | - | + | +
Degrees of Freedom |  | + | S | + | - | - | - | - | +
Storage Length |  | + | S | + | - | S | S | - | -
Communication Distance |  | - | S | + | - | - | + | + | +
Device Responsiveness |  | - | S | - | - | S | - | - | -
Emergency Stop Time |  | + | S | + | - | S | + | - | +
Operation Time On a Single Charge |  | - | - | - | - | - | - | - | -
Motor Power |  | + | + | + | - | - | + | + | +
Support Fuse Weight |  | - | + | - | + | - | + | + | +
 | # of Plus(+) | 4 | 2 | 7 | 2 | 1 | 4 | 5 | 5
 | # of Minus(-) | 6 | 0 | 3 | 7 | 6 | 4 | 5 | 4
 |  | Concepts |  |  |  | 
Selection Criteria | 64 | 2 | 4 | 5 | 57 | 80
Reach Fuse Tube Location | Datum | - | + | + | + | S
Installation Time |  | - | + | + | + | +
Degrees of Freedom |  | + | S | + | - | +
Storage Length |  | + | + | + | - | +
Communication Distance |  | - | - | + | - | -
Device Responsiveness |  | - | S | + | - | +
Emergency Stop Time |  | + | S | + | - | +
Operation Time On a Single Charge |  | - | + | - | + | +
Motor Power |  | - | - | - | - | -
Support Fuse Weight |  | - | + | - | - | -
 | # of Plus(+) | 3 | 5 | 7 | 3 | 6
 | # of Minus(-) | 6 | 2 | 3 | 7 | 3

## Slide 72
Reach Fuse Location
Operable for at least 30 minutes
Minimum communication length of 50ft
Important Engineering Characteristics

## Slide 73: Markets
Municipalities
Electric Companies
Contractors
Public Safety
Construction
Davis Goolsby
Primary Markets:
Secondary Markets:

## Slide 74: Stakeholders
 | Investors | Decision-Makers | Advisers | Receivers
Sponsor | Florida Power and Light, NextEra Energy | Florida Power and Light, NextEra Energy | Scarlett Luis (Engineer at FPL) | Florida Power and Light, NextEra Energy
Manager | Scarlett Luis (Engineer at FPL) | Scarlett Luis (Engineer at FPL) | Dr. McConomy | Florida Power and Light, NextEra Energy
Experts | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Dr. Hruda | Florida Power and Light employed Operators
Operators | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Kyle Bush (FPL Project Manager) | Florida Power and Light employed Operators
Davis Goolsby

## Slide 75
CUSTOMER NEEDS
Questions | Statements | Interpreted Needs
Intended User? | Typical users are linemen and engineers doing field work. | The device needs to be easy operate to in a field environment.
Operating Environment ? | Residential areas. Design device for ideal weather conditions | Used in safe weather conditions
Current Dimensions of the Product? | Approximately 4 feet long when fully collapsed. | Device fits inside Bucket truck for transportation
Ebony Bland

## Slide 76: Future Work
Concept Generation
Concept Selection
Targets
Risk
Assessment
Bill of Materials
Spring
Plans
Davis Goolsby

## Slide 77: References
Brain, M. (n.d.). How Power Grids Work. Retrieved from Clark Science Center at Smith College: https://www.science.smith.edu/~jcardell/Courses/EGR220/ElecPwr_HSW.html#:~:text=Fuses%20must%20be%20replaced%20each,panel%20like%20the%20one%20above
Csanyi, E. (2013, January 28). How to manipulate energized conductors with hot stick. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/manipulating-energized-conductors-with-hot-stick
Csanyi, E. (2020, October 12). How primary feeder, distribution transformer, fuses and service operate in radial networks. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/primary-feeder-distribution-transformer-fuses-service
Eaton Corporation. (n.d.). Eaton Website. Retrieved from Fuses: fundamentals of fuses: https://www.eaton.com/us/en-us/products/medium-voltage-power-distribution-control-systems/utility-fuses/fuses--fundamentals-of-fuses.html
Hastings Hot Line Tools & Equipment. (2021, March). Hastings Catalog. Retrieved from Hastings Website: https://www.hfgp.com/fb-catalog/
King-Homan, L. (2020, August 3). How Does That Work? Hot Stick. Retrieved from The Wire: Energy news from Omaha Public Power District: https://oppdthewire.com/hot-stick-how-works-2020-oppd/
Davis Goolsby

## Slide 78: Project Scope
Background
Key Goals
Markets
Assumptions
Stakeholders
Garfield Murphy

## Slide 79: Markets, Stakeholders, Assumptions
 | Investors | Decision-Makers | Advisers | Receivers
Sponsor | Florida Power and Light, NextEra Energy | Florida Power and Light, NextEra Energy | Scarlett Luis (Engineer at FPL) | Florida Power and Light, NextEra Energy
Manager | Scarlett Luis (Engineer at FPL) | Scarlett Luis (Engineer at FPL) | Dr. McConomy | Florida Power and Light, NextEra Energy
Experts | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Dr. Hruda | Florida Power and Light employed Operators
Operators | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Kyle Bush (FPL Project Manager) | Florida Power and Light employed Operators
Fuse Types
Safe Weather Conditions
Pole Sizes
Transportation
Training
Garfield Murphy

## Slide 80: Base Design
Davis Goolsby

## Slide 81: Material selection
Emilio Manzo

## Slide 82: Material Selection
Emilio Manzo
PLA USED FOR ALL THE 3D PRINTED PARTS
PVC PIPES USED FOR TELESCOPING POLE AND FINAL ARM LINKS

## Slide 83: Future Work
=
Emilio Manzo
3D Print Base
3D Print Arm
Testing
Final Designs
Troubleshooting
Validate Metrics
Presentation

## Slide 84: Final Design
Automated Telescoping Pole with a Detachable Foldable Robotic Arm
Ebony – Ill do this slide
Davis Goolsby