## Slide 1: VDR2
Team 510

## Slide 2: Team Introduction
Ebony Bland
Emilio Manzo
Austin Bruen
Emilio Manzo
Garfield Murphy
Davis Goolsby

## Slide 3: Project Scope
Background
Key Goals
Markets
Assumptions
Stakeholders
Garfield Murphy

## Slide 4: Brief Project Summary
Develop a device that is remotely controlled and can be operated to perform fuse switching operations for restoration purposes
Garfield Murphy

## Slide 5: Key Goals
Easy Operation &
User Friendly
Fuse Switching and
Restoration
Easily Transportable
1
2
3
Garfield Murphy

## Slide 6: Markets, Stakeholders, Assumptions
 | Investors | Decision-Makers | Advisers | Receivers
Sponsor | Florida Power and Light, NextEra Energy | Florida Power and Light, NextEra Energy | Scarlett Luis (Engineer at FPL) | Florida Power and Light, NextEra Energy
Manager | Scarlett Luis (Engineer at FPL) | Scarlett Luis (Engineer at FPL) | Dr. McConomy | Florida Power and Light, NextEra Energy
Experts | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Dr. Hruda | Florida Power and Light employed Operators
Operators | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Kyle Bush (FPL Project Manager) | Florida Power and Light employed Operators
Fuse Types
Safe Weather Conditions
Pole Sizes
Transportation
Training
Garfield Murphy

## Slide 7
CUSTOMER NEEDS
- INTERPRETED NEEDS
Garfield Murphy

## Slide 8: Functional Decomposition: Smart Integration
Performs Fuse Switching Operation
Has an Ergonomic Design
Considers Transportation/Storage
Mitigates Soft Tissue Damage
Compact Design
Ability to Extend, Retract, & Pivot
Automate Some or All of Process
Transportable by Bucket Truck & Personal Vehicle
Reach Inaccessible Area
Fuse Switching Operation
Ergonomic
Transportation
& Storage
Compact Design
Reach inaccessible
areas
Automatic Operation
Extends/Descends
Emilio Manzo

## Slide 9: Targets and Metrics
Soft Tissue Damage Under Grade 1
Preform Fuse Switching and Restoration
Transportable
Communication with the User
Under 50 Pounds
Emilio Manzo

## Slide 10: Targets and Metrics – Critical targets
Supports a Load of 14 Pounds
3 Degrees of Freedom
Extends of 35-40 ft
Emilio Manzo

## Slide 11: Methods of Validation for Targets
Emilio Manzo
Stopwatch test
Tape measure
CAD Stress Analysis

## Slide 12: Concept Generation Tools
Brain Storming
Biomimicry
Crapshoot
Austin Bruen

## Slide 13: Concept Generation
Austin Bruen

## Slide 14: High Fidelity Concepts
Automated telescoping with a Foldable Robotic Arm
Pole Climber Device
Inflatable Tube Device
Austin Bruen

## Slide 15: Concept Selection – House of Quality
Binary Comparison
House of Quality
Austin Bruen
Binary Piecewise Comparison |  |  |  |  |  |  |  |  |  |  |  | 
Customer Needs | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | Total
1) Automates Fuse Switching | - | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 6
2) Reach Areas Inaccessible by Bucket Truck | 1 | - | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 7
3) Operate in Multiple Operating Environments | 0 | 0 | - | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 2
4) Transportable via Bucket Truck | 0 | 0 | 1 | - | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 5
5) Transportable via Passenger Vehicle | 0 | 0 | 0 | 0 | - | 0 | 0 | 0 | 0 | 0 | 0 | 0
6) Mitigate Soft Tissue Damage | 1 | 1 | 1 | 1 | 1 | - | 1 | 1 | 0 | 0 | 1 | 8
7) Maintain a Device Weight < 50 lbs. | 0 | 0 | 1 | 0 | 1 | 0 | - | 1 | 0 | 0 | 1 | 4
8) Ergonomic Carrying Design | 0 | 0 | 0 | 0 | 1 | 0 | 0 | - | 0 | 0 | 0 | 1
9) Minimum Length of 40 ft. | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | - | 1 | 1 | 10
10) Support a Weight of 14 lbs. | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | - | 1 | 9
11) Operable from 10 ft. Away | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | - | 3
Total | 4 | 3 | 8 | 5 | 10 | 2 | 6 | 9 | 0 | 1 | 7 | n-1=10
Engineering Characteristics |  |  |  |  |  |  |  |  |  |  |  | 
Improvement Direction |  | ↑ | ↑ | ↑ | ↓ | ↑ | ↓ | ↓ | ↓ | ↓ | ↑ | ↑
Units |  | ft | lbf | DOF | ft | ft | s | s | s | n/a | min. | W
Customer Requirements | Importance Weight Factor | Reach Fuse Tube Location | Maximum Installation Time of 15 Minutes | Have 3 Degrees of Freedom | Max Storage length of 4 feet | Min. Communication Length of 50 ft. | Measures Power Consumption Every 20 Seconds | Device Implements User Commands Within 1 Second | Device Stops Operation Within 2 Seconds of Stop Command | Contains 7 User-Interaction Elements | Operable for 30 Min. at a Time | Motor has sufficient Power to Perform Device Operation
1) Automates Fuse Switching | 6 |  | 5 | 5 |  | 3 |  | 3 |  |  | 5 | 9
2) Reach Areas Inaccessible by Bucket Truck | 7 |  |  |  |  |  |  |  |  |  | 3 | 
3) Operate in Multiple Operating Environments | 2 |  |  | 3 |  | 5 |  | 1 |  |  |  | 
4) Transportable via Bucket Truck | 5 | 3 |  |  | 9 |  |  |  |  |  |  | 
5) Transportable via Passenger Vehicle | 0 | 1 |  |  | 9 |  |  |  |  |  |  | 
6) Mitigate Soft Tissue Damage | 8 |  | 1 |  |  |  |  | 1 | 3 |  | 1 | 
7) Maintain a Device Weight < 50 lbs. | 4 |  |  |  |  |  |  |  |  |  |  | 
8) Ergonomic Design | 1 |  |  |  | 3 |  |  |  |  | 9 |  | 
9) Minimum Length of 40 ft. | 10 | 9 |  |  |  |  |  |  |  |  |  | 
10) Support a Weight of 14 lbs. | 9 | 3 |  | 1 |  |  |  |  |  |  |  | 
11) Operable from 10 ft. Away | 3 | 3 |  |  |  | 9 |  | 5 | 5 |  |  | 
Raw Score | 531 | 141 | 38 | 45 | 48 | 55 | 0 | 43 | 39 | 9 | 59 | 54
Relative Weight % |  | 26.554 | 7.156 | 8.475 | 9.040 | 10.358 | 0.000 | 8.098 | 7.345 | 1.695 | 11.111 | 10.169
Rank Order |  | 1 | 9 | 6 | 5 | 3 | 11 | 7 | 8 | 10 | 2 | 4
Minimum Length of 40ft
Support a Weight of 14 pounds
Mitigates soft tissue damage
Important Customer Requirements

## Slide 16: Concept Selection – House of Quality
House of Quality
Austin Bruen
Engineering Characteristics |  |  |  |  |  |  |  |  |  |  |  | 
Improvement Direction |  | ↑ | ↑ | ↑ | ↓ | ↑ | ↓ | ↓ | ↓ | ↓ | ↑ | ↑
Units |  | ft | lbf | DOF | ft | ft | s | s | s | n/a | min. | W
Customer Requirements | Importance Weight Factor | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
1 | 6 |  | 5 | 5 |  | 3 |  | 3 |  |  | 5 | 9
2 | 7 |  |  |  |  |  |  |  |  |  | 3 | 
3 | 2 |  |  | 3 |  | 5 |  | 1 |  |  |  | 
4 | 5 | 3 |  |  | 9 |  |  |  |  |  |  | 
5 | 0 | 1 |  |  | 9 |  |  |  |  |  |  | 
6 | 8 |  | 1 |  |  |  |  | 1 | 3 |  | 1 | 
7 | 4 |  |  |  |  |  |  |  |  |  |  | 
8 | 1 |  |  |  | 3 |  |  |  |  | 9 |  | 
9 | 10 | 9 |  |  |  |  |  |  |  |  |  | 
10 | 9 | 3 |  | 1 |  |  |  |  |  |  |  | 
11 | 3 | 3 |  |  |  | 9 |  | 5 | 5 |  |  | 
Raw Score | 531 | 141 | 38 | 45 | 48 | 55 | 0 | 43 | 39 | 9 | 59 | 54
Relative Weight % |  | 26.55 | 7.16 | 8.47 | 9.04 | 10.36 | 0.00 | 8.10 | 7.34 | 1.69 | 11.11 | 10.17
Rank Order |  | 1 | 9 | 6 | 5 | 3 | 11 | 7 | 8 | 10 | 2 | 4
1 | Reach Fuse Tube Location
2 | Maximum Installation Time of 15 Minutes
3 | Have 3 Degrees of Freedom
4 | Max Storage length of 4 feet
5 | Min. Communication Length of 50 ft.
6 | Measures Power Consumption Every 20 Seconds
7 | Device Implements User Commands Within 1 Second
8 | Device Stops Operation Within 2 Seconds of Stop Command
9 | Contains 7 User-Interaction Elements
10 | Operable for 30 Min. at a Time
11 | Motor has sufficient Power to Perform Device Operation
Reach Fuse Location
Operable for at least 30 minutes
Minimum communication length of 50ft
Important Engineering Characteristics

## Slide 17: Concept Selection – Pugh Charts
Emilio Manzo
 |  | Concepts |  |  |  |  |  |  | 
Selection Criteria | BLUE STRIPE Telescopic Hot Stick | 2 | 4 | 5 | 41 | 52 | 57 | 64 | 80
Reach Fuse Tube Location | Datum | - | S | + | S | + | S | + | S
Installation Time |  | - | S | + | + | - | - | + | +
Degrees of Freedom |  | + | S | + | - | - | - | - | +
Storage Length |  | + | S | + | - | S | S | - | -
Communication Distance |  | - | S | + | - | - | + | + | +
Device Responsiveness |  | - | S | - | - | S | - | - | -
Emergency Stop Time |  | + | S | + | - | S | + | - | +
Operation Time On a Single Charge |  | - | - | - | - | - | - | - | -
Motor Power |  | + | + | + | - | - | + | + | +
Support Fuse Weight |  | - | + | - | + | - | + | + | +
 | # of Plus(+) | 4 | 2 | 7 | 2 | 1 | 4 | 5 | 5
 | # of Minus(-) | 6 | 0 | 3 | 7 | 6 | 4 | 5 | 4
 |  | Concepts |  |  |  | 
Selection Criteria | 64 | 2 | 4 | 5 | 57 | 80
Reach Fuse Tube Location | Datum | - | + | + | + | S
Installation Time |  | - | + | + | + | +
Degrees of Freedom |  | + | S | + | - | +
Storage Length |  | + | + | + | - | +
Communication Distance |  | - | - | + | - | -
Device Responsiveness |  | - | S | + | - | +
Emergency Stop Time |  | + | S | + | - | +
Operation Time On a Single Charge |  | - | + | - | + | +
Motor Power |  | - | - | - | - | -
Support Fuse Weight |  | - | + | - | - | -
 | # of Plus(+) | 3 | 5 | 7 | 3 | 6
 | # of Minus(-) | 6 | 2 | 3 | 7 | 3

## Slide 18: Concept Selection – Pugh Charts
Emilio Manzo
 |  | Concepts |  |  |  | 
Selection Criteria | 64 | 2 | 4 | 5 | 57 | 80
Reach Fuse Tube Location | Datum | - | + | + | + | S
Installation Time |  | - | + | + | + | +
Degrees of Freedom |  | + | S | + | - | +
Storage Length |  | + | + | + | - | +
Communication Distance |  | - | - | + | - | -
Device Responsiveness |  | - | S | + | - | +
Emergency Stop Time |  | + | S | + | - | +
Operation Time On a Single Charge |  | - | + | - | + | +
Motor Power |  | - | - | - | - | -
Support Fuse Weight |  | - | + | - | - | -
 | # of Plus(+) | 3 | 5 | 7 | 3 | 6
 | # of Minus(-) | 6 | 2 | 3 | 7 | 3

## Slide 19: Concept Selection – Final Choices
Concept 4:
External Support
Concept 4:
Robotic Arm Attachment
Concept 5:
Drone
Emilio Manzo

## Slide 20: Concept Selection – Analytical Hierarchy Process
AHP – Criteria Weights
AHP – Pairwise comparison
Consistency Check |  |  | Consistency Comparison |  | 
Ws | Cons V |  | Avg Consist | Con Index | Con Ratio
1.43 | 3.21 |  | 3.208 | 0.104 | 0.200
0.35 | 3.20 |  |  |  | 
1.43 | 3.21 |  |  |  | 
Garfield Murphy

## Slide 21: Concept Selection – Analytical Hierarchy Process
Garfield Murphy
Final Rating Matrix |  |  |  |  |  |  |  |  | 
Concept | Reach Fuse Tube | Installation Time | DoF | Storage Length | Communication Distance | Responsiveness | Emergency Stop time | Support fuse weight | Operation on Charge
# 4 | 0.45 | 0.27 | 1.06 | 0.39 | 0.21 | 0.70 | 0.19 | 0.19 | 0.18
# 5 | 0.09 | 0.11 | 0.52 | 0.54 | 0.94 | 0.13 | 1.85 | 0.84 | 2.15
# 80 | 0.45 | 1.06 | 0.19 | 0.31 | 0.62 | 0.29 | 0.92 | 0.91 | 1.22
Concept | Alternate Value
# 4 | 1.97
# 5 | 6.12
# 80 | 4.31
Chart: Alternative Values
| # 4 | # 5 | # 80
Alternative Values | 1.9698 | 6.1156 | 4.3095

## Slide 22: Final Selection
Automated telescoping with a Foldable Robotic Arm and External Support
Garfield Murphy

## Slide 23: Future Work
Risk
Assessment
Bill of Materials
Spring
Plans
Garfield Murphy

## Slide 24: Questions
Garfield Murphy

## Slide 25: References
Brain, M. (n.d.). How Power Grids Work. Retrieved from Clark Science Center at Smith College: https://www.science.smith.edu/~jcardell/Courses/EGR220/ElecPwr_HSW.html#:~:text=Fuses%20must%20be%20replaced%20each,panel%20like%20the%20one%20above
Csanyi, E. (2013, January 28). How to manipulate energized conductors with hot stick. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/manipulating-energized-conductors-with-hot-stick
Csanyi, E. (2020, October 12). How primary feeder, distribution transformer, fuses and service operate in radial networks. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/primary-feeder-distribution-transformer-fuses-service
Eaton Corporation. (n.d.). Eaton Website. Retrieved from Fuses: fundamentals of fuses: https://www.eaton.com/us/en-us/products/medium-voltage-power-distribution-control-systems/utility-fuses/fuses--fundamentals-of-fuses.html
Hastings Hot Line Tools & Equipment. (2021, March). Hastings Catalog. Retrieved from Hastings Website: https://www.hfgp.com/fb-catalog/
King-Homan, L. (2020, August 3). How Does That Work? Hot Stick. Retrieved from The Wire: Energy news from Omaha Public Power District: https://oppdthewire.com/hot-stick-how-works-2020-oppd/

## Slide 26: Backup Slides

## Slide 27: Concept Selection – Pugh Charts
Austin Bruen
 |  | Concepts |  |  |  |  |  |  | 
Selection Criteria | BLUE STRIPE Telescopic Hot Stick | 2 | 4 | 5 | 41 | 52 | 57 | 64 | 80
Reach Fuse Tube Location | Datum | - | S | + | S | + | S | + | S
Installation Time |  | - | S | + | + | - | - | + | +
Degrees of Freedom |  | + | S | + | - | - | - | - | +
Storage Length |  | + | S | + | - | S | S | - | -
Communication Distance |  | - | S | + | - | - | + | + | +
Device Responsiveness |  | - | S | - | - | S | - | - | -
Emergency Stop Time |  | + | S | + | - | S | + | - | +
Operation Time On a Single Charge |  | - | - | - | - | - | - | - | -
Motor Power |  | + | + | + | - | - | + | + | +
Support Fuse Weight |  | - | + | - | + | - | + | + | +
 | # of Plus(+) | 4 | 2 | 7 | 2 | 1 | 4 | 5 | 5
 | # of Minus(-) | 6 | 0 | 3 | 7 | 6 | 4 | 5 | 4
 |  | Concepts |  |  |  | 
Selection Criteria | 64 | 2 | 4 | 5 | 57 | 80
Reach Fuse Tube Location | Datum | - | + | + | + | S
Installation Time |  | - | + | + | + | +
Degrees of Freedom |  | + | S | + | - | +
Storage Length |  | + | + | + | - | +
Communication Distance |  | - | - | + | - | -
Device Responsiveness |  | - | S | + | - | +
Emergency Stop Time |  | + | S | + | - | +
Operation Time On a Single Charge |  | - | + | - | + | +
Motor Power |  | - | - | - | - | -
Support Fuse Weight |  | - | + | - | - | -
 | # of Plus(+) | 3 | 5 | 7 | 3 | 6
 | # of Minus(-) | 6 | 2 | 3 | 7 | 3

## Slide 28
Reach Fuse Location
Operable for at least 30 minutes
Minimum communication length of 50ft
Important Engineering Characteristics

## Slide 29: Markets
Municipalities
Electric Companies
Contractors
Public Safety
Construction
Davis Goolsby
Primary Markets:
Secondary Markets:

## Slide 30: Assumptions
Fuse Types
Pole Sizes
Transportation
Safe Weather Conditions
Training
Davis Goolsby

## Slide 31: Stakeholders
 | Investors | Decision-Makers | Advisers | Receivers
Sponsor | Florida Power and Light, NextEra Energy | Florida Power and Light, NextEra Energy | Scarlett Luis (Engineer at FPL) | Florida Power and Light, NextEra Energy
Manager | Scarlett Luis (Engineer at FPL) | Scarlett Luis (Engineer at FPL) | Dr. McConomy | Florida Power and Light, NextEra Energy
Experts | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Dr. Hruda | Florida Power and Light employed Operators
Operators | Florida Power and Light, NextEra Energy | Kyle Bush (FPL Project Manager) | Kyle Bush (FPL Project Manager) | Florida Power and Light employed Operators
Davis Goolsby

## Slide 32
CUSTOMER NEEDS
Questions | Statements | Interpreted Needs
Intended User? | Typical users are linemen and engineers doing field work. | The device needs to be easy operate to in a field environment.
Operating Environment ? | Residential areas. Design device for ideal weather conditions | Used in safe weather conditions
Current Dimensions of the Product? | Approximately 4 feet long when fully collapsed. | Device fits inside Bucket truck for transportation
Ebony Bland

## Slide 33: Future Work
Concept Generation
Concept Selection
Targets
Risk
Assessment
Bill of Materials
Spring
Plans
Davis Goolsby

## Slide 34: References
Brain, M. (n.d.). How Power Grids Work. Retrieved from Clark Science Center at Smith College: https://www.science.smith.edu/~jcardell/Courses/EGR220/ElecPwr_HSW.html#:~:text=Fuses%20must%20be%20replaced%20each,panel%20like%20the%20one%20above
Csanyi, E. (2013, January 28). How to manipulate energized conductors with hot stick. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/manipulating-energized-conductors-with-hot-stick
Csanyi, E. (2020, October 12). How primary feeder, distribution transformer, fuses and service operate in radial networks. Retrieved from Electrical Engineering Portal: https://electrical-engineering-portal.com/primary-feeder-distribution-transformer-fuses-service
Eaton Corporation. (n.d.). Eaton Website. Retrieved from Fuses: fundamentals of fuses: https://www.eaton.com/us/en-us/products/medium-voltage-power-distribution-control-systems/utility-fuses/fuses--fundamentals-of-fuses.html
Hastings Hot Line Tools & Equipment. (2021, March). Hastings Catalog. Retrieved from Hastings Website: https://www.hfgp.com/fb-catalog/
King-Homan, L. (2020, August 3). How Does That Work? Hot Stick. Retrieved from The Wire: Energy news from Omaha Public Power District: https://oppdthewire.com/hot-stick-how-works-2020-oppd/
Davis Goolsby

## Slide 35: Project Scope
Background
Key Goals
Markets
Assumptions
Stakeholders
Garfield Murphy