## Slide 1
Team 517
Design Review 6
Cameron Barnes | Cole Gutknecht | Tyler Ince-Ingram| Rafael Meza | Michael Wyrick
Notes: Hi everyone, we are Senior Design Team 517 and we are presenting on our project progress so far this year

## Slide 2
Team Overview
Michael
Cameron Barnes
Systems Engineer
Tyler Ince-Ingram
Test Engineer
Michael Wyrick
Design Engineer
Cole Gutknecht
Materials Engineer
Rafael Meza
Dynamics Engineer
Notes: First we will start with some team introductions,

## Slide 3
Sponsor and Advisor
Arthur Werkheiser
Dr. William Oates
Notes: The sponsor for our project is Arthur Werkheiser, Deputy Branch Chief at Marshall Space Flight Center, acting as a liaison between our team and NASA. Our academic advisor is Dr. Oates who has research interests in Mechanics and Materials along with Non-linear control.

## Slide 4
Project Description
Transport Heavy Loads on the Lunar Surface between the Landing Site and Habitation Area
Notes: The objective of our project is to transport heavy loads on the lunar surface between an established landing site and habitation area.

## Slide 5
Background
Notes: NASA’s Artemis project is the start of their plan for sustainable lunar development. The goal is that at some point in the future, we would have lunar bases and habitation areas acting as both scientific exploration centers and also a pitstop on the way to Mars. However, some sort of device will be needed to help transport cargo around these habitats and also unload cargo from the nearby landing site which is where our device would come in.

## Slide 6
ACRONYM:
Heavy Equipment Rover for lunar Mobility, Expansion, and Sustainment
SYMBOLISM:
God of Transportation Protector of Travelers
HERMES
Notes: Our team name for our design is Hermes. The name stands for Heavy Equipment Rover for lunar Mobility, Expansion, and Sustainment. In Greek mythology, Hermes was also the God of Transportation Protector of Travelers which is applicable to our design background.

## Slide 7
Key Goals
Lightweight
Robust
Adaptable
Lifespan
Safe
Notes: The following items are key design goals for our product. It must be lightweight; this is because reduction in weight translates to lower costs of delivery to the moon which will make our design dost effective
It must be a robust design due to challenges surrounding the lunar environment and terrain, regolith and dust can be detrimental to the design if not adequately protected.
The design should have a level of adaptability so that other necessary components such as power and thermal management systems, can be built into the design in the future
The product should last at least one year on the moon to keep transportation costs low making it cost-effective and also to decrease the amount of lunar waste that would be produced from a short-term device.
The device should meet all NASA and United States safety and technical standards and produce a relatively low risk in chance of design failure

## Slide 8
Assumptions
Max payload 1.4 metric tons on Earth
Cost
effective
materials
Maximum distance of 1 km
Standard packaging designed by team
Focus on mechanical design
Notes: In order to make our design possible we had to make the following assumptions
1. The payload will have a maximum mass of 1.4 metric tons on Earth (Full Scale)
2. The materials purchased will be budget-friendly. The end product will be an earth-bound prototype and we will be buying materials suitable to this application.
3. The landing site of the aircraft should be within 1 km of the habitation area where the cargo will be deposited. ---Preferably our device could travel longer distances but it should at a minimum be able to travel this kilometer.
4. Standard packaging will be used on lunar missions and can designed according to the team
5. Certain systems necessary for a fully functioning lunar vehicle can be excluded for the sake of time management of the project. This includes fully functioning power, thermal management, tires/suspension system, and autonomy.

## Slide 9: Targets and Metrics
Survivability
Power
Activation
Structural
Design
Earthbound Scaled Prototype
Notes: Our main targets are power, activation, and structural design based on the functional decomposition of our device. After further consideration survivability falls into that previously discussed assumption and will not be a focus of our design.

## Slide 10
Targets and Metrics
Power
Convert power to movement
Achieves speed of 3.64 ft/s
Notes: Our main power target is that the device is capable of driving at least 4 km/hr

## Slide 11
Target and Metrics
Activation
Lift maximum weight
Stability transporting over rough terrain
Transverses Inclines up to 20 degrees
Targets and Metrics
Lifts 308 pounds
Notes: Our activation targets were designed to ensure our device can still lift, even in unideal situations
Our full-scale device will be expected to lift 1400 kg on earth, using a 1/10th scale, our prototype should successfully lift 257 pounds
Since the lunar surface is full of imperfections its important our device is capable of remaining stable on rocky terrain, a target is that it able to transverse an incline up to 20 degrees

## Slide 12
Structural
Design
Targets and Metrics
Fit within Rocket
Ground Clearance
Structure Weight
At least 6 inches of ground clearance
No more than 175 lbs
Targets and Metrics
Scaled dimensions less than 24 x 29 x 49 in
Notes: The main targets for our structural body are as follows:
Our full-scale device would have to fit in a rocket cargo bay. The target was based on data from the Space X Starship which determines our scaled device should be no more than 24 x 29 x 49 inches
In our order for our device to function correctly and transverse the lunar terrain, we have determined a ground clearance greater than 6 inches
The scaled weight our design should be less than 175 lbs. This would only include the weight of the structural body as the wheels we currently have on our design would not be applicable in space and are not scaled accordingly. Essentially its expected the deive will weigh half of what it can lift

## Slide 13: Concept Generation
5 Medium Fidelity
Concepts
3 High Fidelity
100

## Slide 14: Medium Fidelity Overview
Bipedal
Forklift
Snake
Fang Lift
Modular Cargo Bed
Rear
Lift System
Honeycomb

## Slide 15: High Fidelity Overview
Quadzilla
Assist System
Sunflower
Lift System
Seesaw
Assist System

## Slide 16
Concept Selection Overview
Notes: The team generated 100 ideas and from those narrowed our design to 5 medium fidelity and further into 3 high fidelity concepts. From these 3 high fidelty, it was determined through concept selection that the design ‘Quadzilla’ was the best fit for project objective.

## Slide 17: Initial Design
QUADZILLA
Notes: Here is the initial design of quadzilla that was shown last semester. Although it shares many important qualities with our current design, it has some key differences including a fully enclosed platform with 4 free standing pillars and 8-wheel design . However, we modified this design to be more successful based on our needs

## Slide 18: Current Design
Structural Frame
Aluminum X-beam Structure
Telescoping Channels
Base Adaptability
Carbon Steel Corner Brackets
Notes: We broke up our current design into various subsystems to showcase its functionality.. Here with our structural frame it is made up mostly aluminum x beams acting as the 4 pillars and we chose this material due to it’s light weight to reduce the overall device weight. Channels were implemented on the back end of the device to compact it approximately 3 inches to fit within the constraints of the rocket and reduce it’s overall volume. The benefits to this structural frame is that it can be easily adapted to the lunar model by attaching solar panels and housing them on either the roof or side of the device. Other mechatronic components could be stored above as well to aid with other applications.

## Slide 19: Current Design
Corner Connections
Sleeves around
X-beams
Highly Stress Resistant
Teflon Inserts
Notes: Our corner connections ensure the load is stable and supported. Like I mentioned, these will be made of hollow steel that wraps around the x beams. Initially, as a team we were looking at plastic brackets however we decided that they would fail under the amount of force being exerted on them. So we decided to move froward with the metal brackets. Tephlon inserts will also be included to reduce surface friction.
Arrow to zoomed in

## Slide 20: Current Design
4 Linear Actuators
Supports 75 lbs per actuator
Housing created
4-inch stroke to lift platform
Vertical Mobility
Notes: 4 linear actuators with a 4 inch stroke, will be used and placed on each corner of the platform to raise the platform 4 inches. The load capacity of the actuators will be sufficient enough since the weight would be 75 lbs per actuator. An actuator housing will be designed and manufactured by the machine shop.

## Slide 21: Design Iterations
Wheel and Motor
Initial
Modification
Notes: The wheel coupling design was chosen to remove the need for individual motors at each wheel. To do skid steering the vehicle simply needs two motors which can drive in opposite directions. The drive system is done in halves, with the left front and back wheels being coupled, same with the right half. The coupling design uses a chain to connect the two wheels with sprockets at the axel to a V shaped path with a belt tensioner and a idler gear to guide the movement. Front and back wheels will not be in line because of the 2-1 design so we use a chain derailleur to position our components in line. A 3D printed casing for the mechanism is possible to prevent a chain slip.
The two back wheels will be driven by two remote controlled motors acting independently, the current idea is to incorporate a gear box system to implement an additional gear ratio to the axels using bevel gears like in the picture.

## Slide 22: Platform Design
Picture of Full CAD
Platform
Notes: The platform will be equipped with track wheels to ensure that the vertical motion is smooth with little to no friction. This design would not be ideal for the lunar concept and would need a casing to protect it from regolith. The track would wrap around the x beams and fit into the slots. The forks will be located on the platform and will be equipped with magnets throughout the platform to ensure the package locks into the correct position and to help with swaying. The package will be designed to have a slot where the forks can slide into and lock into place with the use of the magnets. Lock and key mechanism.

## Slide 23: Package Design
Notes: The platform will be equipped with track wheels to ensure that the vertical motion is smooth with little to no friction. This design would not be ideal for the lunar concept and would need a casing to protect it from regolith. The track would wrap around the x beams and fit into the slots. The forks will be located on the platform and will be equipped with magnets throughout the platform to ensure the package locks into the correct position and to help with swaying. The package will be designed to have a slot where the forks can slide into and lock into place with the use of the magnets representing a Lock and key mechanism.

## Slide 24: Operation
Notes: Ride up

## Slide 25: Operation
Notes: Lift up a couple inches, lock into packaging, enough for ground clearance

## Slide 26: Operation
Notes: Transport (Fix this)

## Slide 27: Design Benefits
HERMES
Stable Design
Greatly Reduces its Volumetric Footprint
Low device weight, high lift capability
Adaptable
Notes: HERMES comes with a series of benefits such as; stable design (4 pillar x beam structure and the design being longer rather than taller, similar to a rectangle), is able to reduce its volumetric footprint through the use of the channels on the back of the device to collapse approximately 3 inches which would be about 3 feet in our true model, it features a low device weight due to the materials used along with it’s high lift capability of 330 lbs, the adaptability aspect comes into play where the top of the structure can be used to house solar panels or other electrical components that would be needed on the lunar surface.

## Slide 28: CAD and Stress Analysis
Platform
Bottom Structure
Top Structure
Notes: Conducting Finite Element Analysis (FEA), we were able to see where the stresses would occur on just the structure itself by loading it at the top and then looking at the stresses that would be present when the forks on the platform are loaded. Due to the material properties of the platform the stresses it will undergo will not cause failure when lifting the cargo package. Specifically, we looked at the maximum shear stresses, and the displacement.

## Slide 29
CAD and Stress Analysis
Maximum Shear Stress
Magnitude of Displacement
Units: psi
Units: in.
Single forks withstand 300lbf
Highest stress at actuator contact points
Al6061 Yield Strength:
40,000 psi
Notes: Conducting Finite Element Analysis (FEA), we were able to see where the stresses would occur on just the structure itself by loading it at the top and then looking at the stresses that would be present when the forks on the platform are loaded. Due to the material properties of the platform the stresses it will undergo will not cause failure when lifting the cargo package. Specifically, we looked at the maximum shear stresses, and the displacement.

## Slide 30
CAD and Stress Analysis
Units: psi
Units: in.
Maximum Shear Stress
Magnitude of Displacement
Max Displacement-
.00096 in
Points of weakness identified at corners.
Issue addressed with steel corners.
Notes: Conducting Finite Element Analysis (FEA), we were able to see where the stresses would occur on just the structure itself by loading it at the top and then looking at the stresses that would be present when the forks on the platform are loaded. Due to the material properties of the platform the stresses it will undergo will not cause failure when lifting the cargo package. Specifically, we looked at the maximum shear stresses, and the displacement. On the bottom bar the shear stress is concentrated at the corners of the structure however this justifies the use of brackets coupled with the yield strength of the aluminum will suffice when experience the 300 lb load.

## Slide 31
Structural frame can withstand 300 lbf
Material choice is valid
6.65 ksi < 40 ksi
CAD and Stress Analysis
Units: psi
Units: in.
Maximum Shear Stress
Magnitude of Displacement
Notes: Conducting Finite Element Analysis (FEA), we were able to see where the stresses would occur on just the structure itself by loading it at the top and then looking at the stresses that would be present when the forks on the platform are loaded. Due to the material properties of the platform the stresses it will undergo will not cause failure when lifting the cargo package. Specifically, we looked at the maximum shear stresses, and the displacement. Brackets will help solidify the structure.

## Slide 32: Mechatronics Design
Remote Control
Throttle
Steering
Linear Actuator Switch
Receiver

## Slide 33: Mechatronics Design
Motor Control System
Flysky FS-i6X Controller
FS-iA6B Receiver
Electronic Speed Controller (ESC)

## Slide 34: Mechatronics Design
Motor Control System
Flysky FS-i6X Controller
FS-iA6B Receiver
Electronic Speed Controller (ESC)
Motor
Motor
Motor
Motor

## Slide 35: Mechatronics Design
Actuator Lift System
Motor Driver
Motor Driver
Flysky FS-i6X Controller
FS-iA6B Receiver

## Slide 36: Mechatronics Design
Pseudocode - Throttle
Power On
Engage Throttle
Throttle > 0?
Throttle < 0?
Forward
Reverse
Throttle = 0?
Idle
Throttle
Steering
Linear Actuator Switch
Receiver

## Slide 37: Mechatronics Design
Pseudocode - Steering
Power On
Engage Steering
Steering > 0?
Steering < 0?
Right
Left
Steering = 0?
Idle
Throttle
Steering
Linear Actuator Switch
Receiver

## Slide 38: Mechatronics Design
Pseudocode - Linear Actuator Switch
Power On
Linear Actuator Switch
Switch > 0?
Switch < 0?
Up
Down
Switch = 0?
Idle
Throttle
Steering
Linear Actuator Switch
Receiver

## Slide 39: Testing and Validation
Sand Pit Testing
Measure: Distance and Time
Calculate: Speed
Goal: 3.64 ft/s
231 lbs
308 lbs
150 lbs
75 %
50 %
Future Testing
To Be Validated before April 6th
Variable Load Testing
Measure: Height & Weight
Goal: 4 in, 308 lbs
Sinkage
Measure: Depth
Goal: < 2 in
Structure Weight
Measure: Weight
Goal: 175 lbs
Notes: Regarding testing and validation, a testing rig will be used to ensure the device can effectively handle uneven terrain and a ramp will be included to ensure it meets the critical target of traversing an incline of 20 degrees. Variable loads will be used to test the ability of the device to lift and transport various weights. To assess the linear actuator height, we will be measuring them at the maximum stroke distance and the shortest distance to ensure that the package can be loaded and unloaded successfully.

## Slide 40: Improvements
Notes: Autonomous Driving
Smart Scanning so it will recognize which packages it is picking up and transmit data where the package was dropped off
Further Dust Mitigation Strategies
Horizontal Compatibility so that it is able to pick up packages of none standard sizing

## Slide 41
Rapid Prototyping
Design Around Budget
Seeking Guidance
Recover From Mistakes
Lessons Learned
Finite Element Analysis
Notes: The team generated 100 ideas and from those narrowed our design to 5 medium fidelity and further into 3 high fidelity concepts. From these 3 high fidelty, it was determined through concept selection that the design ‘Quadzilla’ was the best fit for project objective.

## Slide 42
Summary
Notes: Hermes is a design that adequately addresses our key goals. The base frame can be easily adapted in the future, its lightweight, and can transport the maximum load.
We have built a CAD, The Bill of Materials, and have conducted FEA on some of the structural components of our design. I will be looking into further developing testing and validation methods to effectively meet the critical targets and we will soon look forward to finishing the assembly and testing the functionality of our device by Senior Design Day.

## Slide 43: Contact Us!
Cameron
Barnes
Email:
cab19j@fsu.edu
LinkedIn:
Rafael Meza
Email:
rsm19a@fsu.edu
LinkedIn:
Michael Wyrick
Email:
mw20fi@fsu.edu
LinkedIn:
Cole
Gutknecht
Email:
cmg18f@fsu.edu
LinkedIn:
Tyler
Ince-Ingram
Email:
tsi18@fsu.edu
LinkedIn:

## Slide 44: Backup Slides

## Slide 45: BOM

## Slide 46: Budget Breakdown
Chart: 
| Structural Elements | Mechatronic Elements | Misceallaneous | Remaining Budget
Project Budget | 22.59 | 57.55 | 3.58 | 16.28
Structural
Elements
Electrical
Components
Remaining
Budget
Miscellaneous

## Slide 47: Space Applications

## Slide 48: Dust Mitigation
Current Systems
Actuator Vibration:
Kick off some dust

## Slide 49: Future Design Iterations
Dust Compliant
Wire Mesh Covering that would fold (like an accordion)
Located Near Top Connection (Less Weight to hold)
Option 2
Option 1

## Slide 50: Wheel Sinking
Possible Tire Designs

## Slide 51: Material Swaps
Lunar Regolith as a 3D printing Material
Material Strength: 695 HV
White Light Scanning
Titanium
Additive Manufacturing
Material Strength:
Titanium: 140 MPa
Carbon Steel: 350 MPa
Density:
Titanium: 4.51 g/cm^3
Carbon Steel: 7.88 g/cm^3
Why Not Both?
Upcoming Lunar Research has looked into manufacturing material using a mix of Titanium and Regolith Stimulant

## Slide 52
Notes: Capable of moving at 4 km/h, gearbox will be designed with a 3:1 ratio to reduce the power required from the motors. We are still looking into different battery options.

## Slide 53: Current Work
Bill of Materials
Linear Actuators Ordered
Mechanical Components Ordered
Mechatronic Components Ordered
Ordered
Jan. 30th
Feb. 3rd
Notes: We are currently working on making sure all our parts get ordered in a timely manner. We have ordered our linear actuators as we will need them to correctly design their housing. The Mechanical components will be ordered by the end of the month and the Mechatronic components shortly after

## Slide 54
Design Review 3

## Slide 58
CARGO
MiBOX

## Slide 60
Front View
Side View

## Slide 64: Color Palette
How do you think current control surfaces and their actuation can be improved? | Current control surfaces require clean flow, which is not realistic at high angles of attack, so that’s something. | Projectile accommodates for attached flow over control surfaces.
What draw backs come with standard fin deflections as a control surface? | Must have clean flow to actuate properly. Size and weight that come with actuation mechanism | Projectile control surfaces will be suitable effective even in detached flow.
What Mach numbers would be expected for this projectile? | FCAAP polysonic wind tunnel can’t go faster than Mach 5. We’ll probably test Mach 4. | The projectile can withstand Mach 4.
What slenderness ratio of the projectile would be appropriate? | Would be nice if it could be tied into what we have done already. Matching a baseline design here at FCAAP. 8-10 | The projectile uses a basic axisymmetric body configuration based on previously tested models.