## Slide 1: PDR
2024 NASA Student Launch
FAMU-FSU College of Engineering

## Slide 2: Nicholas Hux THE TEAM
Airframe Design
Lead
Jacob Schmitt
Team Lead
Connor Zhou
Recovery & Payload Lead
Atzimba Avellaneda
Fabrication
Lead
Jake Miller
Avionics & Payload Lead

## Slide 3: 01 Vehicle Dimensions & Materials

## Slide 4: Vehicle Dimensions
Total Length – 97.55 in.
Mass – 33.45 lbs.

## Slide 5: Vehicle Dimensions

## Slide 6: Nosecone
Ogive shape
  Low drag and enhance aerodynamics.
  Effective at reducing intensity of shockwaves.
  Reduces likelihood of turbulence and increases stability.
  Simple shape to manufacture
Acrylonitrile Styrene Acrylate
  UV, heat, impact, chemical resistance.
  Ease of 3D printing.
  Lower density.

## Slide 7: Front End with Payload
Payload Housing
Main Chute Housing
G12 Fiberglass
  High strength to weight ratio.
  High heat, moisture, and impact resistance.
  Smoothened surface.

## Slide 8: Avionics Bay
Contents
  Altimeters
  CO2 Ejection charges
  Black powder charges
Plywood bulkheads
  High strength to weight ratio.
  High heat, moisture, and impact resistance.
  Smoothened surface.

## Slide 9: Back End
Contents
  Drogue
  Solid Propellant Motor
  Motor Casing
G12 Fiberglass
  High strength to weight ratio.
  High heat, moisture, and impact resistance.
  Smoothened surface.
Plywood centering rings
  High strength and durability.
  Lightweight
  Easy to work with.

## Slide 10: Nose Cone
Haack Series
Optimized to reduce drag, difficult to manufacture, mass efficient
Elliptical
Low drag, also difficult to manufacture
Ogive
Relatively easy to manufacture, not as mass efficient

## Slide 11: Thrust Structure/ Tail Cone
Aluminum plates provide support and easily mount the fins
Easy to assemble
Tail Cone combined into thrust structure
Parabolic Tail Cone
  Assists in reducing vortices
  Better flight stability
  Mass efficient

## Slide 12: Fin Configuration
Clipped Delta fins utilized
  Easy to manufacture
  Cost efficient
  Properly stabilize vehicle
  Reduces drag loads
  Optimized in Open Rocket
Fin Flutter
  Max vehicle velocity 630 ft/s
  Fin Flutter starts at around 900 ft/s
  Equation used:

## Slide 13: Stability, Pressure, & Gravity 02

## Slide 14: Stability, Pressure, & Gravity
Stability: 2.73 cal ​
  CG: 138 cm from the nose tip​
  CP: 181 cm from the nose tip​
  Distance between CG and CP: 43 cm

## Slide 15: Apogee
Target Apogee is 4940 ft
Simulation with MATLAB code and OpenRocket

## Slide 16: Separation 03

## Slide 17: Separation
First separation stage will take place at apogee, deployment of drogue chute
Second separation stage will take place around 600ft, deployment of main chute.
Shear pins will hold rocket body parts together and shear apart upon CO2 ejection charge firing
Vehicle descends as 3 separate pieces conjoined by 2 parachutes

## Slide 19: Motor Selection 04

## Slide 20: AeroTech L850W
 | Value | Units
Apogee | 4940.945 | feet
Max. Velocity | 422.78 | miles per hour
Time to Apogee | 17.5 | seconds
Flight Time | 37.9 | seconds
Descent Time | 20.4 | seconds

## Slide 22: 05 Thrust, Weight Rail Exit Velocity, Mission Performance

## Slide 23: Thrust, weight, rail exit velocity, and more
Average thrust: 1000 N
Weight : 15kg * 9.81 m/s^2 = 147.15 N
T/F ratio = 6.8:1
Rail exit velocity: 36.4 ft/s
Max Velocity: 617 ft/s
Max Mach Number: 0.56
Max Kinetic Energy: 71.1 lbf-ft

## Slide 24: Alternative Designs 06

## Slide 25: Nosecone, Fins, & Tail Cone Alternatives
Polyethylene Terephthalate Glycol (PETG)
Flexible, virtually unbreakable
Relatively high heat and chemical resistance
Little difficulty printing
More dense
Acrylonitrile Styrene Acrylate (ASA)
Highly resistant
High strength and durability
Little difficulty printing
Less dense

## Slide 26: Fins, & Tail Cone Shape Alternatives
Tail Cone
Conical – very basic, not optimal
Elliptical – Difficult to manufacture
Fins
Elliptical – high velocity
Trapezoidal – easy to manufacture, decent stability

## Slide 27: Airframe Alternatives
Blue Tube 2.0
Flexible, virtually unbreakable
Relatively high heat and chemical resistance
Little difficulty printing
More dense
G12 Fiberglass
Highly resistant
High strength and durability
Little difficulty printing
Less dense

## Slide 28: Alternate Motors Considered
Motor | Manufacturer | Total Impulse (Ns) | Average Thrust (N) | Max Thrust (N) | Burn Time (s) | Weight (g)
L850W | Aerotech | 3,646.2 | 1,00.9 | 1,866.2 | 4.4 | 3,742
L1080BB | Animal Motor Works | 3,686 | 1,112 | 1258 | 3.31 | 3,592
L800-P | Cesaroni | 3731 | 805 | 1024 | 4.63 | 3,510

## Slide 29: Altimeter Alternatives
 | TeleMega | TeleMetrum | Aim 3 | RRC3
Manufacturer | Altus Metrum | Altus Metrum | Entacore | Missile Works
Dimensions (L*W*H) (mm) | 88x32x16 | 27x70x16 | 65x25x15 | 100x23x4
Pyro Channels | 6 | 2 | 2 | 2
Field Output | Beeps, AltOS | Beeps, AltOS | Beeps | Beeps, LCD
Weight (g) | 24.95 | 20.13 | 12.81 | 17.01
Sampling Rate (Hz) | 100 | 100 | 10 | 20
Battery (V) | 3.7 | 3.7 | 3.7 | 3.7
Price | $508.85 | $381.63 | $121.15 | $101.33

## Slide 30: Tracking Alternative
 | TeleGPS | GPS Tracker | EggTimer | AirTag
Manufacturer | Altus Metrum | Featherweight | TX Transmitter | Apple
Dimensions (L*W*H) (mm) | 38 x 25 x 6 | 31 x 20 x 3 | 23 x 76 x 6 | 32 x 32 x 8
Weight (g) | 12.3 | 15.0 | 12.0 | 11.0
Range (km) | 100 | 85 | 9 | N/A
Transmitter Frequency (MHz) | 433 | 915 | 900 | 13.56
Battery | 3.7 | 3.4 – 4.5 | 7.4 | 3
Price | $254.43 | $365 | $110 | $30

## Slide 31: Drogue Alternatives
Drogue | Drag Coefficient | Projected Area (ft^2) | Descent Speed (ft/s) | Descent Time: Apogee to Main Deployment (s) | Wind Drift: Apogee to Main Deployment at 20-mph (ft)
Fruity Chute 15" Classic Elliptical | 1.5 | 1.178 | 117.434 | 37.391 | 1096.810
Fruity Chute 18" Classic Elliptical | 1.5 | 1.696 | 97.861 | 44.870 | 1316.185
Fruity Chute 24" Classic Elliptical | 1.5 | 3.016 | 73.397 | 59.826 | 1754.885
Fruity Chute 30" Classic Elliptical | 1.5 | 4.712 | 58.717 | 74.783 | 2193.619

## Slide 32: Parachute Alternatives
Parachute | Drag Coefficient | Projected Area (ft^2) | Descent Speed (ft/s) | Descent Time from Main Deployment to Ground (s) | Wind Drift from Main Deployment to Ground at 20 MPH (ft) | Kinetic Energy of Heaviest Recovered Section (ft-lb)
Fruity Chute 60" Iris Ultra Standard | 2.2 | 19.027 | 24.129 | 22.794 | 668.632 | 139.363
Fruity Chute 72" Iris Ultra Standard | 2.2 | 27.399 | 20.107 | 27.353 | 802.359 | 96.779
Fruity Chute 84" Iris Ultra Standard | 2.2 | 37.292 | 17.235 | 31.912 | 936.085 | 71.103
Fruity Chute 96" Iris Ultra Standard | 2.2 | 48.708 | 15.081 | 36.471 | 1069.811 | 54.439

## Slide 33: Payload Alternatives
Descent
Singlecopter
Quadcopter
Mechanical Lander
Gas Thruster

## Slide 34: Payload Alternatives
Landing
Legs
Inflatables
Impalement

## Slide 35: Subsystems 07

## Slide 36: Avionics & Recovery Payload Subsystems
Airframe
Fabrication
Flight computers, telemetry, stage separation
Payload design, fabrication, testing
Airframe, nose cone, tail cone, fins, motor
Material selection, fabrication, tooling

## Slide 37: Preliminary Payload Design 08

## Slide 38: Autonomous Transit and Landing for Airdropped Singlecopter (ATLAS)
Systems
Descent
Control
Retention
Landing

## Slide 39: Descent
Uses an electric-powered ducted fan (EDF) to produce thrust
            Up to 7lbs of thrust
Singlecopter design produces significant torque on the vehicle

## Slide 40: Control
Thrust vectoring fins to solve torque problem
Correct for environmental disturbances such as wind
Actuated by servos, which are controlled by flight computer
Compatibility with ArduPilot software

## Slide 41: Landing
Four bar mechanism actuated by servos
Legs designed to maximize landing surface area
Absorbs energy from landing

## Slide 42: Retention
STEMnauts retained in individual capsules spread throughout the vehicle
Distributes mass around the EDF
Payload retained in payload bay

## Slide 43: Payload Mass Estimates
Component | Individual weight (g) | Quantity | Net Weight (g)
EDF/motor | 372 | 1 | 372
2S LiPo Batteries | 280 | 4 | 1120
ESC | 122 | 1 | 122
Receiver | 3 | 1 | 3
GPS | 12 | 1 | 12
Frame | 220 | 1 | 220
Servo | 9 | 7 | 63
Fin | 10 | 4 | 40
Leg Assembly | 80 | 3 | 240
Line Cutter | 22 | 1 | 22
Wire | 50 | 1 | 50
Tether | 5 | 1 | 5
STEMnaut | 3 | 4 | 12
TOTAL |  |  | 2,281.00

## Slide 44: Requirements Compliance Plan 09

## Slide 45: Requirements
Payload is 5 lbs
Stemnauts survive
Vehicle must follow the guidelines:
  Apogee > 4000 ft and < 6000ft
  Max velocity < M1