## Slide 1: Design Review 6
Team 513
Automated Flux Reader (AFR)

## Slide 2: Team Introductions
Andrew Atallah
Hardware & Software
Engineer
Liora Louis
Materials &
Test Engineer
Sean Hemstreet
Design Engineer
Joshua Huls
Systems Engineer
Joshua Huls

## Slide 3: Sponsor and Advisor
Engineering Mentor
William Bilbow
Director of Technology & Project Manager
Engineering Mentor
Cole Gray
Mechanical Design Engineer
Joshua Huls

## Slide 4: Objective
The objective of this project is to design a device that will be capable of fully measuring and recording the magnetic flux of compressor shafts in an automated way that allows for accurate measurements, repeatability, and less overall firsthand work for the operator.
Joshua Huls

## Slide 5: Background
Joshua Huls
Compressors deliver high efficiency and low sound levels
Oil-free magnetic bearing
The use of our project is for the use in new batches and new designs
Previous manual method was inconsistent work intensive

## Slide 6: Key Goals
Automation
Consistency
Adaptability
Accuracy
Joshua Huls

## Slide 7: Assumptions
Device is used over a period of 3 months per year.
Open-source software.
Given one working fluxmeter and sensor.
Testing will be performed at Danfoss.
Operator will be able to load shaft onto device.
Joshua Huls

## Slide 8: Targets and Metrics
Secures Sample
Repeatability
Structural Durability
Data Transfer
Resolution (5mm)
Joshua Huls

## Slide 9: Concept Generation
Anti-Problem
Biomimicry
Brainstorming
Crapshoot
Forced Analogy
Liora Louis
An in-depth process involving multiple team meetings in which team members produced design ideas together and discussed individuals' ideas as a team to compile a list of wildly varying designs.

## Slide 10: Medium Fidelity Concepts
5
4
3
2
1
5
Helical Cage Device
4
Typewriter Rail System Device
3
Robotic Arm Device
2
Roller Conveyor Belt Device
1
Vertical Lathe Device
Liora Louis

## Slide 11: High Fidelity Concepts
3
2
1
1
Horizontal Lathe Device
3
Lean and Peck Sensor Probe Device
2
Horizontal Roller Bearings Device
Liora Louis

## Slide 12: Concept Selection
Binary Pairwise Comparison
House of Quality (HoQ)
Pugh Charts
Analytical Hierarchy Process (AHP)
Liora Louis

## Slide 13: Selected Concept
Horizontal Lathe
Reliable Measurement Feedback
Consistent Measurements
Measures Entire Region
Secures and Levels Sample
Adaptable
Liora Louis

## Slide 14: Initial Design
Two Triangle Bracket Supports
1
Custom Chuck Head Assembly
2
Live Center
3
Tracks to Move the Brackets
4
Linear Guide Rail
5
Design Elements
Liora Louis

## Slide 15: Second Design Iteration
Sean Hemstreet
3
Added 3-inch aluminum blocks
1
2
3
4
Design Benefits

## Slide 16: Second Design Iteration
Sean Hemstreet
3
Added 3-inch aluminum blocks
1
Adjustable tailstock with wheel
2
3
4
Design Benefits

## Slide 17: Second Design Iteration
Sean Hemstreet
3
Added 3-inch aluminum blocks
1
Adjustable tailstock with wheel
2
Singular lever lock for live center
3
4
Design Benefits

## Slide 18: Second Design Iteration
Sean Hemstreet
Added 3-inch aluminum blocks
1
Adjustable tailstock with wheel
2
Singular lever lock for live center
3
Preassembled chuck head
4
Design Benefits

## Slide 19: Final Design Iteration
Sean Hemstreet
1
2
3
Design Updates

## Slide 20: Final Design Iteration
Sean Hemstreet
Chuck head belt cover
1
2
3
Design Updates

## Slide 21: Final Design Iteration
Sean Hemstreet
Chuck head belt cover
1
Using 0.5-inch aluminum blocks
2
3
Design Updates

## Slide 22: Final Design Iteration
Sean Hemstreet
Chuck head belt cover
1
Using 0.5-inch aluminum blocks
2
Measuring the top of the shaft
3
Design Updates

## Slide 23: Fluxmeter Probe Housing
Joshua Huls
Hinge for moving probe out of way during specimen loading
Notes: 2 positions, open and closed to move the sensitive and delicate sensor probe out of the way when loading

## Slide 24: Fluxmeter Probe Housing
Joshua Huls
9.5 mm
8.3 mm
Tapered probe fitting
Notes: Taper to ensure a secure fit for the probe

## Slide 25: Fluxmeter Probe Housing
Joshua Huls
Cavity and holes for fastening housing to linear guide rail
Notes: Not only are fasteners necessary to attach to the linear system as a hole, but a way to feasibly insert and remove the fasteners was needed

## Slide 26: Fluxmeter Probe Housing
Joshua Huls
Probe rest to reinforce sensor probe angel
Notes: As urged by my collogues a rest was implemented into the housing design to reinforce the probe’s angle of detection to better ensure an optimal tangential angle to the shaft and to support the probe if it loses stiffness over time as its predecessor did.

## Slide 27: Operation
Shaft is loaded via crane
Shaft is aligned and secured
Andrew Atallah
Power supply, Arduino, and fluxmeter are plugged in
User opens the program
User selects the type of shaft being measured
Measurements and recordings begin

## Slide 28: Mechatronic Design
Andrew Atallah
Fluxmeter
Stepper Motor 1
Stepper Motor 2
Limit Switch (LS)
Arduino
Motor Driver 2
Motor Driver 1
Power Supply
Start via C++ Application
Platform moves until LS is hit
Measurement is taken
Platform moves along the shaft,
with stops for measurement
taken every 5 mm
Shaft is rotated 5 mm
Steps 3-5 gets repeated until the
shaft completes a full rotation
Data gets sent to an Excel
Template
1
2
3
4
5
6
7

## Slide 29: Testing and Validation
Confirmed the chuck head was large enough
Confirmed the tailstock and live center were strong enough
Confirmed the NEMA 23 motor was more than capable
Andrew Atallah

## Slide 30: Work in Progress
Andrew Atallah
Finish assembly
Finish integrating mechatronics components
Test finalized code on the 3D printed shafts
Test the resolution of device
Refine operations by testing on the real shafts at Danfoss Turbocor

## Slide 31: Improvements
Sean Hemstreet
Install a progress indicator onto device with LCD screen
Implement an auto-leveling sensor for device
Versatile code that can measure future shafts that Danfoss designs
Flux probe mount with adjustable height

## Slide 32: Budget Breakdown
Remaining Budget
Money Spent
Structural Components
Electronics
Sean Hemstreet
Chart: 
| Remaining | Spent | Structural Components | Electronics
 | 9670.3108 | 1701.777 | 627.9122
$9,600
$2,400
$1,700
$700

## Slide 33: Lessons Learned
Sean Hemstreet
Planning ahead is important
Be prepared for setbacks
Ensure parts ordered fit
Challenges are often seen as simple tasks

## Slide 34: Summary
Automated, Accurate, Consistent, Adaptable
Generate and Select Concept
Turn Concept Into Design
Build and Test
Joshua Huls
Notes: Formulate key objectives and goals Consider the problems presented and form possible concepts for solutions to choose from as a team
Determine what is needed to turn the device idea into a reality, find and design parts, systems and operations to accomplish all key goals and handle all foreseen problems
Assemble gathered resources into the final product and verify that is works as expected, while adapting to new and unforeseen problems and circumstances. This stage is where prior planning and group communication with one another and our sponsor have benefited us the most as we have been able to pivot when necessary to ensure at no point the projects brought to a complete stop. And that advancements are being even in between things like order arrivals and use of machining equipment.

## Slide 35: Automated Flux Reader
Andrew Atallah
Sean Hemstreet
Joshua Huls
Liora Louis
Joshua Huls
aatallah@fsu.edu
sph19@fsu.edu
jth18b@fsu.edu
llouis@fsu.edu

## Slide 36
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 37: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 38: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 39
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 40
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 41
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136