## Slide 1
Automated Flux Reader (AFR)
Team 513 | Andrew Atallah | Sean Hemstreet | Joshua Huls | Liora Louis
Danfoss uses magnetic blade shafts to reduce friction in their compressors. Formation of inconsistencies in the magnetized section of the shafts jeopardizes the flux. The current method used to validate the flux of these shafts is unreliable and labor intensive.
For quality purposes the magnetic region of these shafts needs to be measured and mapped. The Automated Flux Reader (AFR) will be used to detect flux deviation within these shafts. The measurements will be spaced out 5 mm apart in the both the axial and circumferential direction.
Inspiration:
Tools:
Motorized Chuck
Tailstock & Live Center
Linear Guide Rail
C++ Application & Arduino
Fluxmeter
Data Collection:
An Arduino controls the linear guide rail and chuck while a C++ application controls the fluxmeter and the measurement process. Signals are then sent between the two to ensure in-sync measurements.
Measurements:
AFR will obtain the magnetic flux density at ~2,600 locations on the test section.
Objective:
To create a system to capture and map the magnetic flux of compressor shafts.
Key Goals:
Automation
Accuracy
Consistency
Adaptability
VTX Compressor:
Tailstock & Live Center
Linear Guide Rail
Motorized Chuck