## Slide 1: Retaining Water Ice in Regolith at Vacuum - T519
Design Review 5
March 7, 2024

## Slide 2: Team Introductions
Luke Leibkuchler
Systems Engineer
Megan Reid
Design Engineer
Katherine Mesa
Fluid Test Engineer
Trent Walker
Thermal Fluids Engineer
Kevin Hernandez Lichtl
Astronautical Engineer
Trent Walker

## Slide 3: Sponsor and Advisor
Annette Gray
NASA-Marshall Space Flight Center
Mentor
Dr. Shayne McConomy
FAMU-FSU College of Engineering
Advisor
Marvin Barnes
NASA-Marshall Space Flight Center
Sponsor
Trent Walker

## Slide 4: Objective
The objective of this project is to mimic the lunar surface environment in a test fixture​
Trent Walker
Notes: “In order to mimic the lunar surface, we need to understand it first”

## Slide 5: Lunar Surface
Surface is made of regolith
Trent Walker
Atmospheric pressure is equivalent to 2.96x10-15 atm
Water is found as ice in shadowed regions on craters
Average temperature ranges from
-183°C to 107°C (90 K to 380 K)
Notes: To verify performance of structures, mechanisms, and processes, NASA created the PLANET Chamber in Huntsville.
Our job is to simulate lunar surface conditions with a regolith simulant (material that has similar chemical comp. to regolith)

## Slide 6: Background
Convert ice into fuel
Lunar Station
Water ice in craters on the poles
Develop technologies to extract ice
Trent Walker
Notes: As we move towards being an interplanetary species
To allow for human travel throughout the solar system, it is believed a lunar colony will be a necessity.
Rather than embarking from Earth, a lunar station will significantly more energy efficient as the moon has a much weaker gravitational force to overcome.
It is believed the moon has water ice hidden in permanently shadowed areas of craters.
Convert H2O --> H2 + O

## Slide 7: Properties of Water
Trent Walker
Notes: Water Phase Diagram
Lots of energy when saying going down to this pressure without sublimating – main reason we are here

## Slide 8
Targets and Metrics
Trent Walker
Water Composition
Prepare a testing sample containing 4-10% water in the regolith-water mixture
Cryogenic Temperatures
Cool sample down to 170K to 200K (-103°C to -73°C )
High Vacuum Pressure
Testing fixture can withstand pressures from 1 atm - 10-10 atm (

## Slide 9
Initial Design
How it Works
Trent Walker
Liquid Nitrogen Drip
Regolith
Flow LN2
LN2 Drips
Sample is cooled
Notes: How do we ensure temperature is maintained?

## Slide 10
Initial Design
Since the Drip Lid must be removed, No Cooling during:
  Experimental setup
  Pump down
  Extraction test in high-vacuum
Main Limitation
Trent Walker
Liquid Nitrogen Drip
Notes: How do we ensure temperature is maintained?

## Slide 11
Liquid Nitrogen Drip
Previous Design Changes
Cryogenic Jacket
Maximize Cooling
Maintain Temperature
Trent Walker
Notes: “to target the limitations found with the nitrogen drip, we decided to combine our top two ideas into one: the nitrogen drip and the cryogenic temperature”

## Slide 12: Previous Design
Trent Walker
Lid
Jacket
Shell
Grate
Bottom

## Slide 13: Final Design
Trent Walker
Lid
Sleeves
Mounts
Grate
Bed

## Slide 14: Final Design
Trent Walker
3/8"
1/2"
3/8"

## Slide 15: Final Design
Trent Walker
#10-24 Tapped
Array of Holes for Liquid Nitrogen

## Slide 16: New Design Changes
Kevin Hernandez-Lichtl
1
Condensed and Simplified
2
Machinability
3
Flow and Pressure Concerns

## Slide 17: Regolith Bed
Teflon Gasket
Welded corners and edges
Flange
Kevin Hernandez-Lichtl
Section View
Exploded View

## Slide 18: Grate Mounts
Gaps to allow for gas flow
Ledge for Grate
Kevin Hernandez-Lichtl

## Slide 19: Grate and Cloth
Perforated Sheet
Kevin Hernandez-Lichtl
Fine Cheesecloth to separate Regolith

## Slide 20: Cooling Sleeves
LN2 Inlet
3/8” Flared Fitting Through Wall Connector
GN2 Outlet
Welded Corners and Edges
Kevin Hernandez-Lichtl

## Slide 21: Drip Lid
Top View
Bottom View
Flange Bolt Holes
Drilled Holes
Kevin Hernandez-Lichtl

## Slide 22: Assembled Section View
Kevin Hernandez-Lichtl

## Slide 23: Assembled Section View
Kevin Hernandez-Lichtl

## Slide 24: Finite Element Analysis (FEA)
Kevin Hernandez-Lichtl
FEA Results:
25psi Inside Pressure
14.7psi Outside
Minimum FOS of 3.45

## Slide 25: Operating Procedure – Pre-Cool
1
Weigh Out Mass of Regolith
Kevin Hernandez-Lichtl

## Slide 26: Operating Procedure – Pre-Cool
1
Weigh Out Mass of Regolith
2
Calculate Necessary Water Volume
Kevin Hernandez-Litchl
+
=

## Slide 27: Operating Procedure – Pre-Cool
+
=
1
Weigh Out Mass of Regolith
2
Calculate Necessary Water Volume
3
Mix Regolith and Water
THE
HOME DEPOT
Kevin Hernandez-Lichtl

## Slide 28: Operating Procedure – Pre-Cool
1
Weigh Out Mass of Regolith
2
Calculate Necessary Water Volume
3
Mix Regolith and Water
4
Add Sample to Bed
Kevin Hernandez-Lichtl

## Slide 29: Operating Procedure – Pre-Cool
1
Weigh Out Mass of Regolith
2
Calculate Necessary Water Volume
3
Mix Regolith and Water
4
Add Sample to Bed
Dry Air
LN2 Lid
5
Purge System with Dry Air
Kevin Hernandez-Lichtl

## Slide 30: Operating Procedure – Cool Down
Sample is ready. Assume at 295K
Luke Leibkuchler
PLANET Chamber
*Not pressurized
A
LN2 Cooling Sleeves Prep
PLANET Chamber
*Not pressurized
Nitrogen Cooling Sleeves

## Slide 31: Operating Procedure – Cool Down
Sample is ready. Assume at 295K
Luke Leibkuchler
GN2 Exit
PLANET Chamber
*Not pressurized
A
LN2 Cooling Sleeves Prep
PLANET Chamber
*Not pressurized
LN2
Nitrogen Cooling Sleeves

## Slide 32: Operating Procedure – Cool Down
Sample is ready. Assume at 295K
Luke Leibkuchler
B
LN2 Sleeves & Drip Lid
LN2
LN2 Cooling Sleeves Still Connected
GN2 Exit
GN2 Exit
PLANET Chamber
*Not pressurized
A
LN2 Cooling Sleeves Prep
PLANET Chamber
*Not pressurized
LN2
Nitrogen Cooling Sleeves

## Slide 33: Operating Procedure – Post Cool
Luke Leibkuchler
LN2 Cooling Sleeves Still Connected
170K-200K Reached

## Slide 34: Operating Procedure – Post Cool
1
Remove LN2 Lid
170K-200K Reached
LN2 Cooling Sleeves Still Connected
Luke Leibkuchler

## Slide 35: Operating Procedure – Post Cool
1
Remove LN2 Lid
2
170K-200K Reached
Experimental Setup
LN2 Cooling Sleeves Still Connected
Luke Leibkuchler

## Slide 36: Operating Procedure – Post Cool
1
Remove LN2 Lid
2
170K-200K Reached
Experimental Setup
3
Ready for Vacuum
LN2 Cooling Sleeves Still Connected
Luke Leibkuchler

## Slide 37: Operating Procedure – Post Cool
1
Remove LN2 Lid
2
170K-200K Reached
Experimental Setup
3
Ready for Vacuum
4
Pump Down
LN2 Cooling Sleeves Still Connected
Luke Leibkuchler

## Slide 38: NASA MSFC Testing
Confirmed testing procedures and feasibility with team
Travel approved and booked
Testing during Spring Break at NASA MSFC
Luke Leibkuchler

## Slide 39: NASA Preparation: Sensors
Moisture Sensors
Thermocouples
Pressure Transducers
Regolith Sample
Test Fixture
Luke Leibkuchler

## Slide 40: NASA Preparation: LabVIEW
Temperature Display
Pressure Display
Water Moisture Display
Luke Leibkuchler

## Slide 41: NASA Preparation: Prelim Tests
Liquid and Gas testing
Luke Leibkuchler

## Slide 42: Bill of Materials
Luke Leibkuchler
Chart: 
| Expenses | Remaining Balance
Balance Sheet | 1745.09 | 254.91

## Slide 43: Contact Information
Kevin Hernandez Lichtl
Luke Leibkuchler
Katherine Mesa
Megan Reid
Trent Walker
Luke Leibkuchler

## Slide 44: Current Design: Grate
Kevin Hernandez-Litchl

## Slide 45: Thank You!
Notes: Targets and Metrics
Concept Generation and Selection
Prototypes
Biweekly Sponsor Meetings
Risk Assessment
Bill of Materials
Spring Project Plan

## Slide 46: Future Work
Fabrication and Assembly
Procurement
Testing Facility Details
Programming
Continue working on COMSOL model
Begin controls programming and LabView
Run preliminary testing to validate sensors and flow
Meet with advising team
Order remaining materials
COMSOL Model
Megan Reid

## Slide 47: NASA MSFC Testing

## Slide 48: Pre-Testing Agenda

## Slide 49: Customer Needs
Katherine Mesa
1
2
3
4
Control water composition and phase within regolith sample
Cool regolith sample to cryogenic temperatures
Maintain uniform water composition and phase along with temperature
Compatible with PLANET chamber apparatus

## Slide 50: PLANET Chamber
High-fidelity lunar surface environment inside a high-vacuum chamber at NASA
Testing Parameters:
Pressure up to 10-8 Torr
LN2 plumbing
Katherine Mesa
Notes: Made of rock chips, mineral fragments, impact and volcanic glasses and a Moon component called “agglutinates”

## Slide 51
Functional Decomposition
NASA Cooling Fixture
Thermal
Controls
Structure
Katherine Mesa

## Slide 52
NASA Cooling Fixture
Thermal
Controls
Structure
Post Pump Down
Control water composition
Cool entire mass to cryogenic temperatures
Critical Functions
Katherine Mesa
Pre Pump Down
Maintain temperature at high vacuum

## Slide 53: Concept Generation
100 Concepts
3 High Fidelity
5 Medium Fidelity
Katherine Mesa

## Slide 54: High Fidelity
Cryogenic Jacket
Retractable Augers
1
3
Liquid Nitrogen Drip
2
Katherine Mesa

## Slide 55: Properties of Water
Trent Walker
Notes: Water Phase Diagram
Lots of energy when saying going down to this pressure without sublimating – main reason we are here

## Slide 56: Concept Selection Analytical Hierarchy
Katherine Mesa
Notes: Binary Pairwise, House of Quality, Pugh Chart, AHP

## Slide 57: Final Selection
Can Cool Entire Bed Evenly
Minimal Impact to PLANET
Ease of Controlling Water Composition
Operates During Ambient Conditions
Liquid
Nitrogen Drip
Katherine Mesa

## Slide 58: Challenges
1
2
3
4
Cooling
Impermeable layers of ice due to rapid freezing
Temperature reaching the core of the sample
Megan Reid

## Slide 59: Challenges
1
2
3
4
Cooling
Liquid Nitrogen
Impermeable layers of ice due to rapid freezing
Temperature reaching the core of the sample
LN2 boil off effects
Expansion rate from LN2 to GN2
Acquiring LN2 for testing
Megan Reid

## Slide 60: Challenges
1
2
3
4
Cooling
Liquid Nitrogen
Safety Valve
Impermeable layers of ice due to rapid freezing
Temperature reaching the core of the sample
LN2 boil off effects
Expansion rate from LN2 to GN2
Acquiring LN2 for testing
Optimal location for pressure safety valve
Megan Reid

## Slide 61: Challenges
1
2
3
4
Cooling
Liquid Nitrogen
Safety Valve
Weight
Impermeable layers of ice due to rapid freezing
Temperature reaching the core of the sample
LN2 boil off effects
Expansion rate from LN2 to GN2
Acquiring LN2 for testing
Optimal location for pressure safety valve
Ease of transporting
Removing the LN2 lid
Megan Reid

## Slide 63: Background
Regolith is the layer of rock and dust on the moon
Highly insulative
Katherine Mesa
Notes: Made of rock chips, mineral fragments, impact and volcanic glasses and a Moon component called “agglutinates”

## Slide 64: Background
Regolith is the layer of rock and dust on the moon
Highly insulative
PLANET Chamber
High-fidelity lunar surface environment inside a high-vacuum chamber at NASA
Katherine Mesa
Notes: Made of rock chips, mineral fragments, impact and volcanic glasses and a Moon component called “agglutinates”

## Slide 65: Customer Needs
Katherine Mesa
1
Control water composition and phase within regolith sample
2
Cool regolith sample to cryogenic temperatures
3
Maintain uniform water composition and phase along with temperature
4
Compatible with PLANET chamber apparatus

## Slide 66: Concept Selection
Trent Walker
Binary Pairwise
House of Quality
Pugh Chart
Analytical Hierarchy

## Slide 67
Katherine Mesa
Regolith Fixture
Notes: Made of rock chips, mineral fragments, impact and volcanic glasses and a Moon component called “agglutinates”

## Slide 68
Katherine Mesa
Regolith Fixture
Notes: Made of rock chips, mineral fragments, impact and volcanic glasses and a Moon component called “agglutinates”

## Slide 69: Preliminary Drip Lid CAD
Top View - Open
Top View - Closed
Kevin Hernandez Lichtl

## Slide 70: Preliminary Drip Lid CAD
Side View - Exploded
Bottom View - Exploded
Kevin Hernandez Lichtl

## Slide 71: Current Design: Assembly
Megan Reid

## Slide 72: Current Design: Lid
Megan Reid
Top View
Bottom View
LN2 Inlet

## Slide 73: Current Design: Jacket
Megan Reid

## Slide 74: Current Design: Grate
Megan Reid

## Slide 75: Current Design: Bottom
Megan Reid
Notes: Sample is mixed and you’re ready to cool it down.

## Slide 76
Katherine Mesa
Simulate lunar surface conditions with a regolith simulant
Cryogenic Temperature
Water Composition and Phase
Our Job
Compatible with PLANET chamber
Notes: Made of rock chips, mineral fragments, impact and volcanic glasses and a Moon component called “agglutinates”

## Slide 77: Liquid Nitrogen Drip
1
3
2
Regolith Bed
LN2 Liquid Drip
LN2 Liquid
Kevin Hernandez Lichtl

## Slide 78: Liquid Nitrogen Drip
1
3
2
Regolith Bed
Pump
LN2 Liquid Drip
LN2 Gas Exit
LN2 Liquid
Kevin Hernandez Lichtl

## Slide 79: Liquid Nitrogen Drip
1
3
2
Regolith Bed
Pump
LN2 Liquid Drip
LN2 Gas Reentry
LN2 Gas Exit
Bottom Grate
LN2 Liquid
Kevin Hernandez Lichtl

## Slide 80: Liquid Nitrogen Drip
1
3
2
Regolith Bed
Pump
LN2 Liquid Drip
LN2 Gas Reentry
LN2 Gas Exit
Bottom Grate
LN2 Liquid
LN2 Gas Exit
Kevin Hernandez Lichtl

## Slide 81
Kevin Hernandez Lichtl

## Slide 82: Operating Procedure – Post Cool
Megan Reid
1
Remove N2 Lid
2.5
Add Styrofoam Lid
LN2 Jacket Still Connected
170K-200K Reached

## Slide 83: PLANET Chamber Planetary, Lunar, and Asteroid Natural Environments Testbed
A high-fidelity lunar surface environment inside a well equipped high-vacuum chamber at NASA’s Marshall Space Flight Center
Megan Reid

## Slide 84: Current Issue
Water ice in regolith will sublimate to gas if not cold enough before high vacuum
Water vapor condenses out of air when cooled before vacuum
Megan Reid
Notes: Water VAPOR, condenses out of air when cooled before vacuum...
affecting regolith-water content

## Slide 85
Key Goals
Thermal Maintenance
PLANET
Chamber
High Vacuum
Regolith
Megan Reid
Notes: Cool regolith simulant bed before and during high vacuum (10^-7 Torr)
Regolith needs to be cooled to a low enough temperature before depressurization so that water ice doesn’t sublimate
Needs to fit within the NASA PLANET Chamber

## Slide 86: Properties of Water
Megan Reid

## Slide 87: Customer Needs
Maintain water in the solid phase
Water will be in the regolith
Water
Phase
Pressure
Uniform
Properties
Monitor
Properties
PLANET
Chamber
Katherine Mesa

## Slide 88: Customer Needs
Maintain water in the solid phase
Water will be in the regolith
Operates in atmospheric to high vacuum pressure
Mimics space environment
Water
Phase
Pressure
Uniform
Properties
Monitor
Properties
PLANET
Chamber
Katherine Mesa

## Slide 89: Customer Needs
Maintain water in the solid phase
Water will be in the regolith
Operates in atmospheric to high vacuum pressure
Mimics space environment
Reaches desired moisture, pressure, and temperature in regolith
Water
Phase
Pressure
Uniform
Properties
Monitor
Properties
PLANET
Chamber
Katherine Mesa

## Slide 90: Customer Needs
Maintain water in the solid phase
Water will be in the regolith
Operates in atmospheric to high vacuum pressure
Mimics space environment
Reaches desired moisture, pressure, and temperature in regolith
Ability to monitor moisture, pressure, and temperature in regolith
Water
Phase
Pressure
Uniform
Properties
Monitor
Properties
PLANET
Chamber
Katherine Mesa

## Slide 91: Customer Needs
Maintain water in the solid phase
Water will be in the regolith
Operates in atmospheric to high vacuum pressure
Mimics space environment
Reaches desired moisture, pressure, and temperature in regolith
Ability to monitor moisture, pressure, and temperature in regolith
Fits into and is compatible with the PLANET Chamber
Water
Phase
Pressure
Uniform
Properties
Monitor
Properties
PLANET
Chamber
Katherine Mesa

## Slide 92: Customer Needs
Maintain Water at Ice in Regolith
Operate in Atmospheric to High Vacuum Pressure
Uniform Moisture, Pressure, and Temperature in Regolith
Ability to Monitor Properties
Operate in PLANET Chamber
Luke Leibkuchler

## Slide 93: Customer Needs
Maintain Water at Ice in Regolith
Operate in Atmospheric to High Vacuum Pressure
Uniform Moisture, Pressure, and Temperature in Regolith
Ability to Monitor Properties
Operate in PLANET Chamber
Luke Leibkuchler

## Slide 94: Customer Needs
Maintain Water at Ice in Regolith
Operate in Atmospheric to High Vacuum Pressure
Uniform Moisture, Pressure, and Temperature in Regolith
Ability to Monitor Properties
Operate in PLANET Chamber
Luke Leibkuchler

## Slide 95: Customer Needs
Maintain Water at Ice in Regolith
Operate in Atmospheric to High Vacuum Pressure
Uniform Moisture, Pressure, and Temperature in Regolith
Ability to Monitor Properties
Operate in PLANET Chamber
Luke Leibkuchler

## Slide 96: Customer Needs
Maintain Water at Ice in Regolith
Operate in Atmospheric to High Vacuum Pressure
Uniform Moisture, Pressure, and Temperature in Regolith
Ability to Monitor Properties
Operate in PLANET Chamber
Luke Leibkuchler

## Slide 97: Customer Needs
Maintain Water at Ice in Regolith
Operate in Atmospheric to High Vacuum Pressure
Uniform Moisture, Pressure, and Temperature in Regolith
Ability to Monitor Properties
Operate in PLANET Chamber
Luke Leibkuchler

## Slide 98: Customer Needs
Maintain Water at Ice
Operate in Atmospheric to High Vacuum Pressure
Uniform Moisture, Pressure, and Temperature in Regolith
Ability to Monitor Properties
Operate in PLANET Chamber

## Slide 99
Functional Decomposition
NASA Regolith Cooling Fixture
Thermal
Controls
Structure
Luke Leibkuchler

## Slide 100
Functional Decomposition
NASA Regolith Cooling Fixture
Thermal
Controls
Structure
Luke Leibkuchler

## Slide 101
Functional Decomposition
Thermal
Pre Pump Down
Post Pump Down
Water in Air
Cool Entire Mass to Cryogenic Temperatures
High Vacuum
Luke Leibkuchler

## Slide 102
Functional Decomposition
NASA Regolith Cooling Fixture
Thermal
Controls
Structure
Luke Leibkuchler

## Slide 103
Functional Decomposition
Controls
User Interface
Motion
Data Acquisition
Display
Hatch
Luke Leibkuchler

## Slide 104
Functional Decomposition
NASA Regolith Cooling Fixture
Thermal
Controls
Structure
Luke Leibkuchler

## Slide 105
Functional Decomposition
Structure
Operate within PLANET
Withstand PLANET
In and Out of Chamber
Within Dimensions
Electrical Components
Integrity at Extreme Conditions
Luke Leibkuchler

## Slide 106: Functional Decomposition
Thermal
Cool entire regolith mass to –180 degC
Prevent water condensation
Pre-Pump Down
Post-Pump Down
Maintain high vacuum pressure within the fixture
Maintain specific regolith-water composition

## Slide 107
Functional Decomposition
Structure
Operate within PLANET chamber
Withstand PLANET conditions
Allows transport in and out of chamber
Fit within chamber dimensions
Maintain structural integrity
Protect electrical/
mechanical components
Withstands high vacuum
Withstands cryogenic temperatures
Allows flow of coolant
Utilizes materials invisible to microwave radiation

## Slide 108
Functional Decomposition
Controls
Motion
DAQ
User Interface
Display
Open hatch for testing
Close hatch after testing
Display temperature data
Display hatch position data
Display water moisture and fixture pressure data
Collect
temperature data
Collect hatch position data
Collect water moisture and fixture pressure data
Collect coolant flow rate data
Display coolant flow rate data

## Slide 109
Customer Needs

## Slide 110
Key Goals
Thermal Maintenance
Megan Reid
Notes: Cool regolith simulant bed before and during high vacuum (10^-7 Torr)
Regolith needs to be cooled to a low enough temperature before depressurization so that water ice doesn’t sublimate
Needs to fit within the NASA PLANET Chamber

## Slide 111
Key Goals
Thermal Maintenance
Regolith
Megan Reid
Notes: Cool regolith simulant bed before and during high vacuum (10^-7 Torr)
Regolith needs to be cooled to a low enough temperature before depressurization so that water ice doesn’t sublimate
Needs to fit within the NASA PLANET Chamber

## Slide 112
Key Goals
Thermal Maintenance
PLANET
Chamber
Regolith
Megan Reid
Notes: Cool regolith simulant bed before and during high vacuum (10^-7 Torr)
Regolith needs to be cooled to a low enough temperature before depressurization so that water ice doesn’t sublimate
Needs to fit within the NASA PLANET Chamber

## Slide 113
Key Goals
Thermal Maintenance
PLANET
Chamber
High Vacuum
Regolith
Megan Reid
Notes: Cool regolith simulant bed before and during high vacuum (10^-7 Torr)
Regolith needs to be cooled to a low enough temperature before depressurization so that water ice doesn’t sublimate
Needs to fit within the NASA PLANET Chamber

## Slide 114
Assumptions
PLANET Chamber
Instrumentation
Regolith Simulant
Megan Reid
Materials provided for final testing at NASA - MSFC
Operating Conditions
Humidity is controlled at 65%
Cooling with Cryogenic Liquids
No extreme conditions
Notes: Following Materials will supplied:
  Liquid Nitrogen
  Regolith Simulant
  Vacuum Chamber
  Instrumentation
Final testing conducted at Marshall Space Flight Center
Humidity is at 65% (controlled)

## Slide 115
Markets & Stakeholders
NASA - MSFC
SpaceX
Boeing
Blue Origin
Other Private Aerospace Companies
Megan Reid
Notes: Primary:
  NASA
Secondary:
  SpaceX, Boeing, or Blue Origin
  Private aerospace companies developing extraction and excavation technologies

## Slide 116
Targets and Metrics
1.33e-4 Pa – 1.33e-5 Pa
173.15 K - 203.15 K
4-10%
Trent Walker
Notes: Units are trash

## Slide 117: Customer Needs
Luke Leibkuchler
Maintain water in the solid phase
Water will be in the regolith
Water
Phase
Pressure
Uniform
Properties
Monitor
Properties
PLANET
Chamber

## Slide 118: Customer Needs
Luke Leibkuchler
Maintain water in the solid phase
Water will be in the regolith
Operates in atmospheric to high vacuum pressure
Mimics space environment
Water
Phase
Pressure
Uniform
Properties
Monitor
Properties
PLANET
Chamber

## Slide 119: Customer Needs
Luke Leibkuchler
Maintain water in the solid phase
Water will be in the regolith
Operates in atmospheric to high vacuum pressure
Mimics space environment
Reaches desired moisture, pressure, and temperature in regolith
Water
Phase
Pressure
Uniform
Properties
Monitor
Properties
PLANET
Chamber

## Slide 120: Customer Needs
Luke Leibkuchler
Maintain water in the solid phase
Water will be in the regolith
Operates in atmospheric to high vacuum pressure
Mimics space environment
Reaches desired moisture, pressure, and temperature in regolith
Ability to monitor moisture, pressure, and temperature in regolith
Water
Phase
Pressure
Uniform
Properties
Monitor
Properties
PLANET
Chamber

## Slide 121: Customer Needs
Luke Leibkuchler
Maintain water in the solid phase
Water will be in the regolith
Operates in atmospheric to high vacuum pressure
Mimics space environment
Reaches desired moisture, pressure, and temperature in regolith
Ability to monitor moisture, pressure, and temperature in regolith
Fits into and is compatible with the PLANET Chamber
Water
Phase
Pressure
Uniform
Properties
Monitor
Properties
PLANET
Chamber

## Slide 122: Future Work
Luke Leibkuchler
Concept
Selection
Target &
Metrics
Concept
Generation
Risk
Assessment
Prototypes
Bill of
Materials
Create prototypes of high-fidelity concepts to aid in selection
Set targets and metrics for system
Generate 100 ideas for solution that fits needs and targets
Select final concept
Create bill of materials
Perform risk assessment
Meet with advising team
Notes: Targets and Metrics
Concept Generation and Selection
Prototypes
Biweekly Sponsor Meetings
Risk Assessment
Bill of Materials
Spring Project Plan

## Slide 123: Preliminary Drip Lid CAD
Top View - Open
Top View - Closed

## Slide 124: Preliminary Drip Lid CAD
Side View - Exploded
Bottom View - Exploded

## Slide 125: Thank You!
Notes: Targets and Metrics
Concept Generation and Selection
Prototypes
Biweekly Sponsor Meetings
Risk Assessment
Bill of Materials
Spring Project Plan

## Slide 126
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 127: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 128: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 129
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 130
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 131
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136