## Slide 1: Team 520 NASA Marshall Space Flight Center: Actively Sealed Cryogenic Coupler (ASCC)
Jason Goldstein, Lauren Roche, Sean Rodney,
Valerie Rodriguez, Nicolas Sgammato
Design Review 6

## Slide 2: Meet The Team
Nicolas Sgammato
Design
Engineer
Jason Goldstein
Materials Engineer
Lauren
Roche
Cryogenics Engineer
Sean Rodney
Test
Engineer
Valerie Rodriguez
Thermal-Fluids Engineer
Valerie Rodriguez

## Slide 3: Sponsors
James C. Buzzell
Propulsion Systems Engineer,
NASA MSFC
Marvin Barnes
Propulsion Systems Engineer,
NASA MSFC
Valerie Rodriguez

## Slide 4: Objective
The objective of this project is to design, build, and test an actively sealed coupler that prevents the leakage of cryogenic fuel during the transfer from depot to vessel for future NASA missions.
Valerie Rodriguez

## Slide 5: Background
Valerie Rodriguez
Cryogenic couplers allow for extended duration of space missions.
Their purpose is to make a sealed and secure connection between the space craft and the fuel source.

## Slide 6: Background
The coupler is to be used for future NASA lunar missions.
The navigation system from the spacecraft guides the receiving half of the coupler to mate with the probe half, mounted on the tanker ship.
Previous designs required human intervention to lock and initiate fuel transfer.
Valerie Rodriguez

## Slide 7
Department of Mechanical Engineering
The actively sealed portion of the design requires the system to seal purely based on the mechanical connection of the two halves.
This avoids from using electronic components in cryogenic conditions and allows for quick connection and disconnection.
Active Sealing
Valerie Rodriguez
Notes: Yassify

## Slide 8: Key Goals
Effective Sealing
90 Day Lunar Mission
Minimize Leakage
Valerie Rodriguez

## Slide 9
Department of Mechanical Engineering
9
Assumptions
Flow rate and tank pressures will be controlled externally by space craft operators.
Misalignment tolerance will not exceed 0.25” total non-concentricity. Vehicle will have capture feature for gross misalignment.
Heat load is negligible due to insulation and through flow time.
Valerie Rodriguez

## Slide 10
Marshall Space Flight Center
Sean Rodney
Markets

## Slide 11
Extend the life of the cryogenic fuel storage in space
Minimize the leakage rate of fuels during the transfer process
Seal activation upon contact of coupler halves
Limit boil-off of fuel due to heat transfer
Protect system from foreign particulate matter
Sean Rodney
Customer Needs

## Slide 12: Functional Decomposition
Sean Rodney
Fueling
Durability
Connection
Disconnection
Thermal Management

## Slide 13
Connection
Maintain sealed connection during fuel transfer
Lock two halves together and allow for flow channel alignment
Sean Rodney

## Slide 14
Durability
Uphold structural durability
Minimize stresses to system components
Sean Rodney

## Slide 15
Fueling
Open and close flow channels
Minimize fuel leakage
Sean Rodney

## Slide 16
Thermal Management
Endure solar radiation
Minimize heat from conduction, convection, and radiation
Sean Rodney

## Slide 17
Disconnection
Disconnect both halves
Maintain sealed connection for excess fuel
Sean Rodney

## Slide 18
Lauren Roche
Concept Generation
100 Concepts
Concept Selection
3 High Fidelity
5 Med. Fidelity
Biomimicry
Crap Shoot
Morphological Chart

## Slide 19
Lauren Roche
Concept Selection
Binary Pairwise Comparison
House of Quality
Pugh Charts
Analytical Hierarchy Process
Final Selection
Notes: BPC: which customer needs are most important to us
HoQ: used the weight of importance for each need to find the engineering characteristics to focus on
Pugh: comparing high and medium fidelity concepts to the market datum and each other
AHP: numerically determine which concept is best for our needs

## Slide 20
Department of Mechanical Engineering
20
Lauren Roche
#99
#82
#81
#80
#79
Medium Fidelity Concepts
Notes: 5 medium fidelity concepts
Solid confidence that these designs would work for our application
99 is a force held lock
The rest are collet locks – both halves would snap together

## Slide 21
Force held + double poppet actuator + double vacuum wall with:
#33
#98
#100
Encapsulated O-rings
Multi-Layered Insulation (MLI)
Encapsulated O-rings
Spray-On Foam Insulation (SOFI)
Teflon Seals
Multi-Layered Insulation (MLI)
High Fidelity Concepts
Lauren Roche
Notes: 3 high fidelity concepts, we had the most confidence that these would be successful.
All three designs feature a force-held double poppet actuator and a double vacuum wall
Variations of sealing and insulating

## Slide 22
Concept #33
Concept #98
Concept #100
Lauren Roche
Alternative Value:
0.473
Alternative Value:
0.322
Alternative Value:
0.205
Analytical Hierarchy Process
Notes: 3 high fidelity concepts were evaluated, and we produced a numerical value for which one would be best
Highest value, meaning it’s the

## Slide 23
#33
Force held double poppet actuator, sealed with encapsulated O-rings, insulated by a double vacuum wall structure and Multi-Layered Insulation (MLI)
Final Selection
Lauren Roche
Notes: Gave us a basic design to move forward with. Based on research and feedback from our sponsor, we implemented many upgrades to get to our current model

## Slide 24
Lauren Roche
Coupler Operation
Notes: Pilot drives the receiver half to mate with the probe half and this connection is held by force
The springs on either side compress, allowing fluid to flow from the depot to the spacecraft

## Slide 25: Initial Concept
Nicolas Sgammato
Probe
Receiver

## Slide 26: Design Evolution
Nicolas Sgammato
Version 1
Version 2
Version 3

## Slide 27: Major Changes
Single 360-degree flow channel on the receiver half
Multiple flow channels on both halves
Nicolas Sgammato

## Slide 28: Major Changes
Nicolas Sgammato
Components split into multiple pieces
Large and complex components

## Slide 29: Major Changes
Nicolas Sgammato
Based on arbitrary dimensions
Adjusted to match standard pipe sizes

## Slide 30: Final Concept
Probe Half
Nicolas Sgammato

## Slide 31: Final Concept
Receiver Half
Nicolas Sgammato

## Slide 32: Components
Nicolas Sgammato
Stainless Steel Springs
Spring-Loaded Actuators

## Slide 33: Components
Nicolas Sgammato
PTFE Gaskets
Spring-Energized PTFE Seals
PTFE O-Ring

## Slide 34: Components
Nicolas Sgammato
KF Fittings
Retaining Rings
Flanges and Hardware

## Slide 35: Manufacturing
Nicolas Sgammato
304 Stainless Steel Pipe

## Slide 36: Manufacturing
Nicolas Sgammato
Machined Components

## Slide 37
Determine air leakage
Analyze pressure of 24-hour period
Estimate leakage of cryogenic fuels
Jason Goldstein
Vacuum Leak Testing
Status:
Training Complete
Pull vacuum on inner chamber

## Slide 38
Status:
Training Complete
Connect coupler to a liquid nitrogen tank
Verify normal operation and determine any points of failure
Control and observe flow through the coupler
Liquid Nitrogen Flow Testing
Jason Goldstein
Evaluate efficacy of design under cryogenic conditions

## Slide 39
Chart: 
| Raw Materials | Seals | Springs | Miscellaneous | Remaining
% of Budget | 0.62 | 0.19 | 0.02 | 0.04 | 0.13
Raw Materials
$1,248.72
Remaining Budget
$221.40
Allocated: $2000
Budget Breakdown
Jason Goldstein
Spent: $1778.60

## Slide 40: Lessons Learned
Communicate with manufacturers early and often
Continuously reevaluate priorities
The project is dynamic and not static
There is some value in every idea
Jason Goldstein

## Slide 41
Implement spray-on foam insulation to external surfaces
Evaluate thermal performance of coupler
Perform more thorough leak testing (helium gas testing)
Suggestions for Improvement
Jason Goldstein

## Slide 42
Summary
Jason Goldstein

## Slide 43
Summary
Jason Goldstein
Objective: create an actively sealed coupler that limits leakage during cryogenic fuel transfer for space missions

## Slide 44
Summary
Jason Goldstein
Our team analyzed the constraints and developed a design that met our goals

## Slide 45
Summary
Jason Goldstein
We have finalized our design and began manufacturing and assembly.

## Slide 46
Summary
Jason Goldstein
We will begin testing following the completion of assembly and safety verification

## Slide 47
Conclusion
Nicolas Sgammato
Over the past two academic semesters, our team collaborated to create a cryogenic coupler that actively seals and limits fuel leakage for a 90-day mission period

## Slide 48
Thank You
James Buzzell and NASA MSFC, Jeremy Phillips and FAMU-FSU CoE Machine Shop, Dr. Wei Guo and Makai Hulse at the National MagLab, and Dr. Shayne McConomy
Nicolas Sgammato

## Slide 49
Connect with Us
Nicolas Sgammato

## Slide 50: Backup Slides

## Slide 51
References
NASA Low Force Quick Disconnect Coupler – Kennedy Space Center
NASA-STD-5012
NASA-STD-5020
AIAA-S-080
Omni-Seal book/manual that Buzz provided us
Name

## Slide 52: Current Priorities
Conduct water leakage test with 3D-printed model of design
Analyze and interpret data from testing to improve the design
Order necessary materials/parts to begin manufacturing and assembly of coupler
Complete cryogenic testing at the National High Magnetic Field Laboratory (NHMFL)
Department of Mechanical Engineering
21
Name
Notes: Previous version is in back up slides. Add or make any changes.

## Slide 53: Future Work
Perform fluid flow simulations using SolidWorks
Conduct durability tests on the final coupler design
Implement spray on foam insulation (SOFI) to outer surface
Department of Mechanical Engineering
22
Name
Notes: Previous version is in back up slides. Add or make any changes.

## Slide 54: Thank You.
Jason Goldstein, Lauren Roche, Sean Rodney,
Valerie Rodriguez, Nicolas Sgammato
520: NASA Actively Sealed Cryogenic Coupler

## Slide 55: Questions?
Jason Goldstein, Lauren Roche, Sean Rodney,
Valerie Rodriguez, Nicolas Sgammato
Not exactly sure If this should be separate from the thank you slide or combined with it. Also not sure exactly how it should look :/

## Slide 56: Flow Rate Testing
In the case testing at the FCAAP lab is denied, fluid dynamics will be simulated in COMSOL.
Testing using PIV would be ideal but main concerns can still be analyzed using this software.
Department of Mechanical Engineering
56
Valerie Rodriguez

## Slide 57: Meet The Team
Nicolas Sgammato
Design Engineer
Jason Goldstein
Materials Engineer
Lauren Roche
Cryogenics Engineer
Sean Rodney
Test Engineer
Valerie Rodriguez
Thermal-Fluids Engineer
Department of Mechanical Engineering
57
Name

## Slide 58: Lunar Refueling Depot
Reduced Cost
Increased Safety
Extended Mission Capabilities

## Slide 59: Problems with Current Designs
Sealing and Leakage
Thermal Radiation
Contamination

## Slide 60: Actively Sealed Coupler
Seals when the two halves make contact

## Slide 61: Background
Cryogenic Fuel Transfer
Deep Space Mission
Lunar Base Fuel Depot
Lauren Roche
Department of Mechanical Engineering
61

## Slide 62: Key Goals
Effective Sealing
90-Day Lunar Mission
Minimize
Leakage
Department of Mechanical Engineering
62
Name
Notes: Highkey what we agreed wed change this to
- Changed to “minimize leakage”

## Slide 63: Customer Needs
Extend life of the cryogenic fuel
Minimize the leakage rate
Seal activation upon contact of coupler halves
Limit Boil Off
System Protection
Valerie Rodriguez

## Slide 64: Customer Needs
Valerie Rodriguez
Minimize the leakage rate
Extend life of the cryogenic fuel
Seal activation upon contact of coupler halves
Limit boil off
System protection

## Slide 65: Functional Decomposition
Coupling System
Durability
Connection
Fueling
Disconnection
Valerie Rodriguez

## Slide 66: Functional Decomposition
Coupling System
Durability
Connection
Fueling
Disconnection
Major Function
Endure Solar Radiation
Mitigate Particulates
Minimize Heat Transfer
Tolerate Vehicle Misalignment
Uphold Structural Durability
Protect Electrical Components
Minor Function
Valerie Rodriguez

## Slide 67: Functional Decomposition
Coupling System
Durability
Connection
Fueling
Disconnection
Major Function
Check Pressure Difference
Level Pressure
Lock two Halves Together
Seal the Connection
Minor Function
Valerie Rodriguez

## Slide 68: Functional Decomposition
Coupling System
Durability
Connection
Fueling
Disconnection
Major Function
Open Pipe Valve
Minimize Fuel Leakage
Close Pipe Valve
Minor Function
Valerie Rodriguez

## Slide 69: Functional Decomposition
Coupling System
Durability
Connection
Fueling
Disconnection
Major Function
Disconnect Both Halves
Purge Excess Fuel
Minor Function
Valerie Rodriguez

## Slide 70
Status Update
Name
Department of Mechanical Engineering
70
Research on materials, locks, insulation, existing designs
Wrapping up concept generation and concept selection
Contact sponsor to get feedback on our top designs

## Slide 71
Department of Mechanical Engineering
71
Fuel Leakage
Measured Using Venturi Flowmeter at the National High Magnetic Field Laboratory (NHMFL)
Target From Critical Targets Table Provided by Sponsor
For Internal Leakage:
≤ 500 SCIM LN2 at 15 and 50 PSID While De-mated
For External Leakage:
≤ 50 SCIM LN2 at 5 and 50 PSIG Internal Pressure
Nicolas Sgammato

## Slide 72
Department of Mechanical Engineering
72
Heat Transfer
Measured Using a Thermocouple in Coupler Interior
Target Derived From Boiling Point of Liquid Nitrogen
Coupler Interior Temperature
≤ 80 K
Nicolas Sgammato

## Slide 73
Department of Mechanical Engineering
73
Coupler Connection
Measured using a Force Transducer Attached to One Half of Coupler
Connection/
Disconnection Force:
≤ 250 LBF
Target Derived From Previous NASA Coupler
Jason Goldstein

## Slide 74
Department of Mechanical Engineering
74
Concept Generation Tactics
Crap Shoot
1
1
1
2
2
2
3
3
3
C
A
B
Biomimicry
Morphological Chart
1
2
3
4
5
A
B
C
D
E
Jason Goldstein

## Slide 75
Seals​
Insulation
Locks
Valves
Department of Mechanical Engineering
75
Terminology
Lauren Roche
Encapsulated O-ring
Teflon Seal
MLI
SOFI
Double vacuum wall
Double poppet valve
Force held
Collet Lock

## Slide 76
Department of Mechanical Engineering
76
High Fidelity Concepts
Concept #33
Force held double poppet actuator, sealed with encapsulated O-rings, insulated by a double vacuum wall structure and Multi-Layered Insulation
Lauren Roche

## Slide 77
Department of Mechanical Engineering
77
High Fidelity Concepts
Concept #98
Force held double poppet actuator, sealed with encapsulated O-rings, insulated by a double vacuum wall structure and Spray-On Foam Insulation (SOFI)
Lauren Roche

## Slide 78
Department of Mechanical Engineering
78
High Fidelity Concepts
Concept #100
Force held double poppet actuator, sealed with Teflon, insulated by a double vacuum wall structure and Multi-Layered Insulation (MLI)
Nicolas Sgammato

## Slide 79
Department of Mechanical Engineering
28
Name
Coupler Operation

## Slide 80
Department of Mechanical Engineering
80
Medium Fidelity Concepts
Nicolas Sgammato
#79
#81
#80
#82
#99

## Slide 81
Double Poppet
Force held lock
Double vacuum & SOFI
Teflon Seals
#99
Department of Mechanical Engineering
81
Medium Fidelity Concepts
Nicolas Sgammato

## Slide 82
Double Poppet
Collet lock
Double vacuum & MLI
Encapsulated Seals
#82
Department of Mechanical Engineering
82
Medium Fidelity Concepts
Jason Goldstein

## Slide 83
Department of Mechanical Engineering
83
Medium Fidelity Concepts
Jason Goldstein
Double Poppet
Collet Lock
Double vacuum & SOFI
Encapsulated Seals
#81

## Slide 84
Pugh Charts- Second Iteration
Concept #100
Selection Criteria
Leakage
Lifetime
Seal
Resilience
Size
Cost
-
S
-
-
S
+
Department of Mechanical Engineering
84
Datum: Concept #33
Force held double poppet actuator, sealed with Teflon, insulated by a double vacuum wall structure and Multi-Layered Insulation (MLI)
Jason Goldstein

## Slide 85
Seals​
Encapsulated O-ring seal​
Teflon Seal
Insulation
MLI
SOFI
Double vacuum wall
Locks
Force held
Collet Lock
Valves
Double poppet valve
Department of Mechanical Engineering
85
Terminology

## Slide 86
Top Concepts
Name
Department of Mechanical Engineering
86
Force held lock with double poppet valve, encapsulated seals, double vacuum and MLI (multi-layered insulation)
Force held lock with double poppet valve, encapsulated seals, double vacuum and SOFI (spray-on foam insulation)
Collet lock with double poppet valve, encapsulated seals, double vacuum and MLI
Collet lock with double poppet valve, encapsulated seal, double vacuum and SOFI

## Slide 87
Department of Mechanical Engineering
87
Pugh Charts- Second Iteration
Selection Criteria
Leakage
Lifetime
Seal
Resilience
Size
Cost
Nicolas Sgammato
Concept #98
S
-
S
-
+
+
Force held double poppet actuator, sealed with encapsulated O-rings, insulated by a double vacuum wall structure and Spray-On Foam Insulation (SOFI)
Datum: Concept #33

## Slide 88
Department of Mechanical Engineering
88
Pugh Charts- Second Iteration
Selection Criteria
Leakage
Lifetime
Seal
Resilience
Size
Cost
Jason Goldstein
Concept #99
-
-
-
-
+
+
Force held double poppet actuator, sealed with Teflon, double vacuum wall structure and Spray-On Foam Insulation (SOFI)
Datum: Concept #33

## Slide 89: High Fidelity Concepts
#33
#98
#100
Force held double poppet actuator, sealed with encapsulated O-rings, insulated by a double vacuum wall structure and Multi-Layered Insulation (MLI)
Force held double poppet actuator, sealed with encapsulated O-rings, insulated by a double vacuum wall structure and Spray-On Foam Insulation (SOFI)
Force held double poppet actuator, sealed with Teflon, insulated by a double vacuum wall structure and Multi-Layered Insulation (MLI)
Notes: Title text looks weird only because of the animation.
- Theres so much going on with the orange and photos… change?

## Slide 90
Department of Mechanical Engineering
90
Analytical Hierarchy Process
Concept #33
Concept #98
Concept #100
Alternative Value:
0.466
Alternative Value:
0.632
Alternative Value:
1.032
Jason Goldstein

## Slide 91
Department of Mechanical Engineering
91
Targets and Metrics
Fuel Leakage Heat Transfer Coupler Connection Structure Integrity
Fuel Leakage Rate from Flowmeter
Interior Temperature from Thermocouple
Connection Force from Transducer
Material Yielding from Tensile Test
Nicolas Sgammato

## Slide 92
Department of Mechanical Engineering
92
High Fidelity Concepts
Force held double – poppet actuator with double vacuum wall insulation structure paired with:
#33:
Encapsulated
O-ring seals and MLI
#48:
#50

## Slide 93
Department of Mechanical Engineering
93
Medium Fidelity Concepts
Double-poppet valve and double vacuum wall
#49 | Force-held lock Teflon seals SOFI
#32 | Collet lock encapsulated O-ring seals MLI
#31 | Collet lock encapsulated O-ring seals SOFI
#30 | Collet lock Teflon seals MLI
Jason Goldstein

## Slide 94
Department of Mechanical Engineering
94
Medium Fidelity Concepts
Jason Goldstein
Double Poppet
Collet Lock
Double vacuum & MLI
Teflon Seals
#80

## Slide 95
Department of Mechanical Engineering
95
Medium Fidelity Concepts
Lauren Roche
Double Poppet
Collet Lock
Double vacuum & SOFI
Teflon Seals
#79

## Slide 96
Department of Mechanical Engineering
96
Concept Selection
Binary Pairwise Comparison
House of Quality
Pugh Charts
Analytical Hierarchy Process
Final Selection
Lauren Roche

## Slide 97
Department of Mechanical Engineering
97
Binary Pairwise Comparison
Compares Customer Needs to Each Other to Determine Relative Importance
Customer Needs | Score
Fluid Loss Prevention | 6
Active Seal | 6
Maintains Pressure | 6
Effective Coupling | 6
Heat Transfer Protection | 5
Particulate Mitigation | 4
Life-Span | 3
Cost | 3
Sizing Parameters | 3
Material Resilience | 2
Reusability | 1
Lauren Roche

## Slide 98
Department of Mechanical Engineering
98
Structural Integrity
Measured using Tensile Testing on Selected Material
Safe Range was Chosen Due to Material Not Yet Being Selected
Plastic Deformation of Chosen Material:
≤ 5%
Jason Goldstein

## Slide 99
Department of Mechanical Engineering
99
House of Quality
Customer Requirements
Life-span
Fluid Loss
Active Seal
Material Resilience
Reusability
Maintains Pressure
Effective Coupling
Heat Transfer
Particulate Mitigation
Channel Sizing Parameters
Cost
Ranked Engineering Characteristics
1. Fuel Leakage
2. Seal
3. Heat Transfer
4. Durability
5. Weight
6. Cost
Nicolas Sgammato

## Slide 100
Pugh Charts- First Iteration
#82
#81
#80
#33
#98
#100
#99
-2
-2
-2
1
1
1
1
Department of Mechanical Engineering
100
Selection Criteria
Leakage
Lifetime
Seal
Resilience
Size
Cost
Datum: NASA Low Separation Force Quick Disconnect
Nicolas Sgammato

## Slide 101
Department of Mechanical Engineering
101
Medium Fidelity Concepts
#49
Force held double poppet actuator, sealed with Teflon, double vacuum wall structure and Spray-On Foam Insulation (SOFI)
Nicolas Sgammato

## Slide 102
Department of Mechanical Engineering
102
Medium Fidelity Concepts
#32
Double poppet actuator with collet lock, sealed with encapsulated O-rings, double vacuum wall structure and Multi-Layer Insulation (MLI)
Nicolas Sgammato

## Slide 103
Department of Mechanical Engineering
103
Medium Fidelity Concepts
#31
Collet locked double poppet actuator, sealed with encapsulated O-rings, double vacuum wall structure and Spray-On Foam Insulation
Jason Goldstein

## Slide 104
Department of Mechanical Engineering
104
Medium Fidelity Concepts
#30
Double poppet-actuator with collet lock, Teflon seals, double vacuum wall structure and Multi-Layer Insulation
Jason Goldstein

## Slide 105
Department of Mechanical Engineering
105
Medium Fidelity Concepts
#29
Double poppet-actuator with collet lock, Teflon seals, double vacuum wall structure and Spray on Foam Insulation
Jason Goldstein

## Slide 106
Department of Mechanical Engineering
106
High Fidelity Concepts
Concept #33
Concept #48
Concept #50

## Slide 107
Department of Mechanical Engineering
107
High Fidelity Concepts
Force-held lock with double-poppet valve
and double vacuum wall
#33 | Encapsulated O-ring seals MLI
#48 | Encapsulated O-ring seals SOFI
#50 | Teflon seals MLI
Lauren Roche

## Slide 108
Department of Mechanical Engineering
108
Final Concept Selection
Force-held lock with double-poppet valve
and double vacuum wall
#33 | encapsulated O-ring seals MLI
Nicolas Sgammato

## Slide 109: Fall Design
Double poppet actuator and force held lock, seal with encapsulated seals, insulated by double vacuum wall and Multi-Layer Insulation (MLI) blanket

## Slide 110
Department of Mechanical Engineering
110
Final Concept Selection
Lauren Roche
Concept #33: Double poppet actuator and force held lock, seal with encapsulated seals, insulated by double vacuum wall and Multi-Layer Insulation (MLI) blanket

## Slide 111
Department of Mechanical Engineering
*We should fix this animation so that the receiver end (right piece) comes into frame while the probe end (left piece) is stationary
Name
Coupler Operation
Notes: Make this sexier and flip the direction

## Slide 112
Department of Mechanical Engineering
112
Concept #33
Lauren Roche

## Slide 113
Department of Mechanical Engineering
113
Concept #33
Lauren Roche

## Slide 114
Department of Mechanical Engineering
114
Concept #33
Lauren Roche

## Slide 115: Probe Half
Department of Mechanical Engineering
115
Sean Rodney
Static PTFE O-Rings
Stainless Steel Spring
Actuator
Spring-Energized PTFE Seals

## Slide 116: Sponsor Updates:
Insulation negligible for testing
SOFI: Smooth Exterior for future implementation
Flow rate should be low enough during fueling for pressure drop to be negligible.
Lubricant: Dry-film lube
Assume pressure in tanks is equalized.
Department of Mechanical Engineering
116
Sean Rodney

## Slide 117: Fall Design
Force-held
lock
Encapsulated seals
Double-poppet actuator​
F
Department of Mechanical Engineering
117
Valerie Rodriguez

## Slide 118: Initial Design Flaws
Department of Mechanical Engineering
118
Valerie Rodriguez

## Slide 119
Department of Mechanical Engineering
119
Flow Channel Misalignment and Size
Insertion Relief Port
Difficult Seal Location and Manufacturing
Valerie Rodriguez

## Slide 120: Updated Design
Department of Mechanical Engineering
120
Sean Rodney

## Slide 121: ASCC MK2
Department of Mechanical Engineering
10
Name

## Slide 122: Receiving Half
Department of Mechanical Engineering
122
Sean Rodney
Static PTFE O-Rings
Stainless Steel Spring
Spring-Energized PTFE Seals
Actuator

## Slide 123
Department of Mechanical Engineering
123
Sean Rodney
Static PTFE O-Rings
Stainless Steel Spring
Actuator
Spring-Energized PTFE Seals

## Slide 124: Design Revisions
Oversized flange dimensions
Multiple flow channels on receiver required alignment
Flange diameters and thicknesses decreased
Arbitrary dimensions based on previous design
Dimensions adjusted to match standard pipe sizes
Probe end fixed to outer surface
Single flow channel on receiver side
Department of Mechanical Engineering
12
Nicolas Sgammato
Probe split from outer surface and cap feature added

## Slide 125
Large and complex components created manufacturing difficulties
Components split up into multiple pieces
Flange seals located primarily within one flange half
Flange seal location moved to between flange surfaces
Gap formed between probe actuator and receiver cap upon mating
Cryogenic testing inhibited by open ends
Adapters added to connect KF fittings for testing
Chamfer added to outer edge of probe actuator
Department of Mechanical Engineering
13
Design Revisions Continued
Name

## Slide 126: Updated Sealing
Spring-energized seal
Implements a circular spring to exert outward pressure
Encapsulated by PTFE (Teflon) due to excellent performance in cryogenic applications
Seals translating cylindrical bodies
Static and low speed applications
Department of Mechanical Engineering
126
Sean Rodney
103A Omniseal​®
Note: Image for illustrative purposes only: The depicted seal is for stylization and a similar seal from McMaster-Carr will be implemented.

## Slide 127: Manufacturing
Department of Mechanical Engineering
127
Main components of probe and receiver will be CNC machined by the FAMU-FSU COE machine shop
Springs and seals will be ready to install from the manufacturer
Assembly of the coupler will be completed by the design team
Sean Rodney

## Slide 128: Anticipated Challenges + Solutions
Department of Mechanical Engineering
15
Design for less required machining and budget for extra materials in the event of irreparable fabrication errors
Machining Errors
Flow Channel Interference With Seals
If scraping of the seals by the flow channel holes is observed, a feature may need to be added to prevent significant seal damage
Order materials as soon as possible to allow time for re-order in case of a manufacturer issue
Material Issues
Name
Notes: - Make this look nicer, update with new challenges

## Slide 129
Department of Mechanical Engineering
129
Testing
Leakage
Status:
In Progress
Status:
Approved
Status:
Pending Approval
Status:
Approved
Cryogenic
Flow Rate
Durability
Sean Rodney

## Slide 130: Leakage Testing
Calculate leakage rates and use Nasa environment correction factors to obtain target rates
Identify design conflicts/areas of improvement
Apply calculated rates and developed solutions to improve design before cryogenic testing
Department of Mechanical Engineering
130
Sean Rodney

## Slide 131
Department of Mechanical Engineering
131
Sean Rodney
Initiation of NHMFL
on-boarding and training
KF fitting for compatibility with NHMFL equipment
Material-safety check with Dr. Wei Guo
Cryogenic Testing

## Slide 132: Flow Rate Testing
PIV testing will be conducted at the Florida Center For Advanced Aero-Propulsions
(FCAAP)
The design is to be sliced and placed in the low-speed wind tunnel to test flow rates
Particle Imaging Velocimetry will be used to analyze the flow inside the coupler
Department of Mechanical Engineering
132
Valerie Rodriguez

## Slide 133: Durability Testing
Department of Mechanical Engineering
133
Durability must be tested to identify any possible vulnerabilities in the design
The parts will be brushed with paint and tested at different forces
The paint will chip away exposing areas experiencing the most force
Leakage test will be preformed again to check for cracks and if design is reusable
Valerie Rodriguez

## Slide 134: Testing Validation
Department of Mechanical Engineering
134
Valerie Rodriguez
Leakage
Cryogenic
Flow Rate
Durability
External leakage: Less than 50 SCIM liquid nitrogen at 5 and 50 psig internal pressure
Internal leakage: Less than 500 SCIM liquid nitrogen at 15 and 50 psid while demated
Stainless steel springs can endure at least 10 N of force to keep tightly sealed connection
The valve can endure minimum 80 K temperatures
Less than 5% plastic deformation

## Slide 135: Testing Validation
Department of Mechanical Engineering
135
Valerie Rodriguez
Leakage
Cryogenic
Flow Rate
Durability
External leakage: Less than 50 SCIM liquid nitrogen at 5 and 50 psig internal pressure
Internal leakage: Less than 500 SCIM liquid nitrogen at 15 and 50 psid while demated
Stainless steel springs can endure at least 10 N of force to keep tightly sealed connection
The valve can endure minimum 80 K temperatures
Less than 5% plastic deformation

## Slide 136: Budget Breakdown
Chart: 
| Raw Materials | Seals | Springs | Miscellaneous | Remaining
% of Budget | 0.62 | 0.19 | 0.02 | 0.04 | 0.13
Department of Mechanical Engineering
16
Raw Materials - $1248.72
Seals - $380.00
Springs - $41.14
Miscellaneous - $66.36
Remaining Budget - $263.78
Total Budget - $2000.00
Name

## Slide 137
42
137
Summary
Jason Goldstein
The objective of this project was to create an actively sealed coupler that limits leakage during cryogenic fuel transfer for deep space missions.

## Slide 138
Summary
Jason Goldstein

## Slide 139
42
139
Summary
Jason Goldstein
Through discussions with our sponsor and machine shop, our team analyzed the constraints and developed a design that met our operation goals

## Slide 140
Complete manufacturing
Conduct testing at MagLab
Assemble coupler
Analyze and present data
Current Priorities
Jason Goldstein

## Slide 141
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 142: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 143: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 144
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 145
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 146
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136

## Slide 152: Team 520: NASA-MSFC Actively Sealed Cryogenic Coupler
Jason Goldstein, Lauren Roche, Sean Rodney,
Valerie Rodriguez, Nicolas Sgammato
Virtual Design Review 4