## Slide 1: DR 5
Team 520
John Baumann, Natalie Boggess, Cody Carlson,
Megan Jadush, Malik Jean-Baptiste, Anders Snell
02/20/2025

## Slide 2
John Baumann
Introduction – Project Mentors
Manager:
Dr. McConomy
Sponsor:
Dr. Rassweiler
Advisor:
Dr. Clark

## Slide 3: Introduction – Team 520
John Baumann
Design Engineer
Megan Jadush
Materials Engineer
Natalie Boggess
Marine Engineer
Cody Carlson
Software Engineer
Malik Jean-Baptiste
Robotics Engineer
Anders Snell
Mechatronics
Engineer
John Baumann

## Slide 4: Project Objective
The objective of this project is to create a system capable of recording a diver’s position while submerged.
John Baumann

## Slide 5: Project Summary
John Baumann
Dr. Rassweiler SCUBA dives and plots diseased corals on his map
Current system: location is within a 10m radius circle, wants to get more precise

## Slide 6: Overview
John Baumann
GPS
Dr. Rassweiler SCUBA dives and plots diseased corals on his map post dive, but the current method is not accurate
Error

## Slide 7: Background
John Baumann
GPS is incapable of penetrating through water
Relies on radio waves
Buoys will drift due to waves and current
Will be operating at up to 10m underwater
Can approximate a right triangle for diver position
Horizontal distance between diver and surface device is needed

## Slide 8: What This Is All For
John Baumann

## Slide 9: Assumptions
John Baumann
The user will be within 10 meters of the water's surface.
The user has access to a watch and a waterproof notepad.
The max duration of each dive will be no longer than 90 minutes.
  Weather conditions will consist of wind (15-20 knots),
  small waves (2-3 feet), and a water temperature of around
  82°F.

## Slide 10: Key Goals
John Baumann
The system will be able to reliably work at a depth underwater up to 10 meters
Pinpoint diver's position within 6 m. diameter
The system will be portable, capable of launching from the shore, and require minimal setup
The system's power should last at least 90 minutes at a time

## Slide 11: Functional Decomposition
John Baumann
Underwater Tracking System
Sensor
Power Source
Structure
Data

## Slide 12: Structure Changes
Cody Carlson
Above Surface System

## Slide 13: Technology
Cody Carlson
Global Positioning System (GPS)
Positioning data from satellites used to correct cumulative positional errors (drift) of the system
Compass

## Slide 14: Concept Selection
Cody Carlson
Table 1: Binary Pairwise Comparison Matrix

## Slide 15: Concept Selection
Cody Carlson

## Slide 16: Chosen Design: Concept 61
Cody Carlson

## Slide 17: First Prototype
Cody Carlson

## Slide 18: Second Prototype
Cody Carlson

## Slide 19: Current Prototype
Cody Carlson
Snap-on mounting bracket
Fins
Dive rope
Angle sensor or automatic reel
Water-tight surface box:
GPS
Arduino & SD Card
Portable charger

## Slide 20: Decisions Moving Forward
Cody Carlson
VS
Image 1: Reel [6]

## Slide 21: Dive Rope
Cody Carlson
Image 2: Dive Rope [7]

## Slide 22: Current GPS
Cody Carlson
Does not display correct heading
Very choppy when updating
Delayed from user

## Slide 23: New System
Cody Carlson

## Slide 24: Mounting
Anders Snell

## Slide 25: Mounting – Modular System
Can be used for fins, rotary encoder, or line reel
Anders Snell

## Slide 26: Testing
Anders Snell
Mini Pool

## Slide 27: Mini Pool Testing
Anders Snell
Tested stability and the watertight O-ring of the system with and without fins in a 4-foot-deep pool

## Slide 28: Testing
Anders Snell
Mini Pool
Morcom Aquatic Center
Springs/Ocean

## Slide 29: Testing Question
Anders Snell
OR

## Slide 30: Waterproofing
Anders Snell
Waterproof up to 1 m
This lasts 30 mins
Rotary encoder – rotary seal
Line measurer/tensioner
Epoxy to fill gaps

## Slide 31: Software
Anders Snell
Parses time-stamped latitude, longitude, and orientation data
Time, depth and line length of point of interest inputted
Calculates latitude and longitude displacement
Resultant coordinates outputted

## Slide 32: Project Budget
Anders Snell
$359.93
$1640.07

## Slide 33: References
[1] What is an Inertial Measurement Unit? (2024). VectorNav. https://www.vectornav.com/resources/detail/what-is-an-inertial-measurement-unit
[2] Garmin GPSMAP 78 Handheld Navigator - 010-00864-00. (2024). Marine Electronics Shop. https://www.marine-electronics-shop.com/garmin-gpsmap-78-handheld-navigator-010-00864-00/
[3] Bar02 Ultra High Resolution 10m Depth/Pressure Sensor. (n.d.). Blue Robotics. https://bluerobotics.com/store/sensors-cameras/sensors/bar02-sensor-r1-rp/
[4] SparkFun OpenLog Artemis - DEV-16832 - SparkFun Electronics. (2022, November 5). Sparkfun.com. https://www.sparkfun.com/products/16832
[5] Blue Robotics Watertight Box – Blue Robotics. (2024, April 30). BlueRobotics.com
https://bluerobotics.com/store/watertight-enclosures/watertight-boxes/watertight-box/
[6] 150ft Aluminum Dive Reel with Tension and Locking System - Rope Reel, Scuba Diving Reel, Kayak Anchor Reel, String Line Reel –Amazon https://www.amazon.com/SAEKODIVE-Aluminum-Tension-Locking-System/dp/B0CQ8FSPSV
Anders Snell

## Slide 34: Current/Future Work
Anders Snell
Buying and testing a reeling system
Designing and testing a completely external mounting system
Testing system in deeper pool/ spring, or ocean
Compare reel and angle sensor results
Waterproofing any connections needed
Work on coding different components together

## Slide 35: Stakeholder Matrix

## Slide 36: Stakeholders
Natalie Boggess
Dr. Andrew Rassweiler
Investor, Decision Maker, Receiver
Rassweiler Laboratory
Operator
Dr. Shayne McConomy
Manager
Dr. Jonathan Clark
Expert
RL

## Slide 37: Primary Market
Malik Jean Baptiste
Dr. Rassweiler
Oceanographers

## Slide 38: Secondary Market
Malik Jean Baptiste
Commercial Fishing
Underwater Exploration
Recreational Divers
Marine Sanctuary

## Slide 39: House of Quality
Cody Carlson
Track Diver Global Position
Track GPS Position
Data Transmission
Waterproofing
HoQ
Pressure Resistance

## Slide 40: Pugh Chart Iteration

## Slide 41: Concept Selection

## Slide 42: Concept Selection
Cody Carlson

## Slide 43: First High Fidelity Concept #33
Natalie Boggess
Inertial Navigation System (INS)
Barometer
Angle sensor
GPS
Cable instead of rope
Measurement of cable length

## Slide 44: Second High Fidelity Concept #55
Natalie Boggess
Long range radio communication (LoRa) triangular positioning technology
  Two nodes on shore and one on the ocean
Attitude & heading reference system (AHRS)
Angle sensors

## Slide 45: Third High Fidelity Concept #61
Inertial navigation system (INS)
Angle sensors
Attitude & heading reference system (AHRS)
GPS secured in a floating raft
Natalie Boggess

## Slide 46: Customer Needs
Natalie Boggess
The device can be packed into a carry-on bag.
The device can get a more precise reading of the diver’s location.
The device can operate with the user down to 10m.
The device is easy to carry straight from the shore into the ocean.
The device still operates normally when experiencing high winds.
The device can log a digital location.
The device’s battery lasts for at least 90 minutes.
The device consists of 1 or 2 small pieces.

## Slide 47: Inertial Navigation System (INS)
Natalie Boggess
Inertial Measurement Unit (IMU)
Global Positioning System (GPS)
Attitude and Heading Reference System (AHRS)
Linear accelerations and angular velocities are measured with accelerometers and gyroscopes
Orientation is determined with data from the IMU and a
magnetometer, ran through filter algorithms
Positioning data from satellites used to correct cumulative positional errors (drift) of the system
Attitude and Heading Reference System (AHRS)
Orientation is determined with data from the IMU and a
magnetometer, ran through filter algorithms
Global Positioning System (GPS)
Positioning data from satellites used to correct cumulative positional errors (drift) of the system
Picture of INS goes here
Figure 3: IMU + AHRS
Picture of INS goes here
Figure 4: GPS
20

## Slide 48: Project Updates
Megan Jadush
Tested device in a pool
Bought a new GPS and dive rope
Designed and implemented fins to device
Continuous Research
Coordinated with Morcom Aquatics Center
Figure out how to attach a reel

## Slide 49: Future Work Timeline
Megan Jadush
Tested device in a pool
Got New Dive rope and test new Tensioner
Designed and implemented fins to device
Continuous Research
Coordinated with Morcom Aquatics Center
Implement electronics to surface device

## Slide 50: GPS and INS Testing
Megan Jadush
Portable Charger
Pelican Case
Arduino
GPS
INS

## Slide 51: Angle Sensor Housing
Megan Jadush

## Slide 52
Megan Jadush
Materials Moving Forward
Below Surface System
Blue Robotics Watertight Box [5]

## Slide 53: Back Up Slides

## Slide 54: Barometer Testing
Megan Jadush
Barometer
Arduino Mega 2560
Level Converter

## Slide 56: Angle Sensor Testing
Megan Jadush
Angle Sensor
Arduino Mega 2560

## Slide 57: Targets
Natalie Boggess
Power Sources
Structures
Data
Sensors
  Tracks diver global position (6 m.)
  Lasts ≥ 90 minutes
  Waterproof
  Transportable
  Transmission (9600 baud)
  Storage (32 GB)

## Slide 58: Slide Headline
Try to keep text at 16 pt minimum.
Try to put as few words as possible on the slide if you’re using for a presentation.
Mix and match the backgrounds as shown in this template or just use one throughout.
You can put department/unit logos in slide master at Horizontal 0.89” Vertical 6.44” From top left corner

## Slide 59: Font Check
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 60: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 61: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 62
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 63
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 64
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136

## Slide 65
Border Line
Middle of Slide
Middle of White Space
Border Line
Border Line
Center of White Space
Center of Slide
Border Line
Edge of Branding
Notes: Vertical lines from top down.
Borderline and top of title. (0.5 inch)
Center of Slide (0 inch y-direction for the entire slide)
Center of Design Content (0 inch y-direction considering the title, footer, and negative space)
Bottom of Design Content (0.25 in gap to the footer. 0.75 to the bottom of the screen)
Horizontal lines from left to right
Borderline (0.5 inch)
Center of design content.
Center of slide (0 inch y-direction for the entire slide)
Borderline (0.125 inch all around)